## Slide 1: Conducting Reservoir Storage-Yield Analyses Using HEC-ResSim
Lecture #5 – Water Supply Details

## Slide 2: Introduction
What questions do we need to answer in water supply studies
Go over a few case studies of actual water supply studies
Discuss details that may impact how you set up your model for a study
Notes: In this lecture we will talk about what a water supply study is and why we might want to do one. We will also look at some of the different questions that a study can answer and look at some examples of real USACE studies.
Note that our workshops are going to use relatively simple model configurations in the interest of time and to focus on the main points for this training, but keep the discussion from this lecture in mind as we work through the rest of the training and you think about how you will apply it to the studies you may need to perform.

## Slide 3: Water Supply Analysis
Imagine a non-federal stakeholder needs additional water supply or maybe increased reliability, and this need results in a water supply study
What questions does the H&H analysis need to answer?
What percent of the conservation pool could be contracted to provide supply?
How reliably will that amount of storage meet the user’s needs?
Notes: We do water supply studies to look at the yield (firm or otherwise) of a storage volume. What primary questions does the H&H analysis need to answer?
This is one of the key takeaway points from this course. By the end of the course you should know how to answer these questions.

## Slide 4: Discussion
Class Discussion
  Review some case studies
  Review some specific modeling considerations
  What do you think?
Notes: Let’s talk about why you care about water supply, and what sort of studies you might have done or plan to do. There are many reasons to look at water supply and yield analysis. It is important to understand the purpose and the goals of each individual study to be able to design and execute the study effectively. Thinking about the goals at the beginning will pay dividends later.

## Slide 5: Case Study – Falls Lake
Falls Lake, North Carolina
Reallocation of conservation storage for additional water supply
Notes: This case study includes period of record and data consistency choices, a non-HEC operational model, and considered demand and basin conditions in the future.

## Slide 6: Falls Lake, North Carolina
Falls Lake is located on Neuse River in North Carolina
Notes: Falls Lake is located on the Neuse River in North Carolina. The Falls Lake project was authorized in the Rivers and Harbors Act of 1965 with construction substantially completed in 1981 and full impoundment completed by December 1983. The authorized project purposes of Falls Lake include flood risk management, water quality, water supply and recreation. Fish and wildlife enhancement was also included as a project purpose based on the Federal Water Project Recreation Act (Public Law 89-72). Based on 2007 survey data, the reservoir contains about 221,000 acre-feet (ac-ft) of storage for flood risk management, 106,000 ac-ft of conservation storage, for total active storage of 328,000 ac-ft (rounded), with an additional 25,000 ac-ft of sediment reserve storage. The table shows the elevation, area and storage capacities of the lake.

## Slide 7: Falls Lake Reallocation Study
Continuing regional growth, a severe drought in 2007-2008 and exploration of other alternatives, led the City of Raleigh to request additional water supply storage in Falls Lake.
Reallocation study examined feasibility of reallocating up to 17,300 acre-feet of storage from other authorized purposes to meet water supply needs.
The following alternatives were carried forward for additional analysis:
  No Action Plan
  Falls Lake - Reallocation of Storage within the Conservation Storage from Water Quality to Water Supply
  Construct a New Dam and Reservoir on the Little River
  Construct Offline Storage and New Water Intake on Neuse River near Richland Creek

## Slide 8: Falls Lake Observed Record
Annual runoff in the Falls watershed shows a declining trend.
Fourteen of the fifteen lowest minimum annual water supply storage amounts have occurred since 1980.
Therefore, period from April 1, 1980 to March 31, 2015 was inflow data set for the reallocation study.
Notes: One interesting aspect of the Falls Lake case is that the annual inflows for the period of record is not stationary. The District used the most recent period for the analysis.

## Slide 9: Falls Lake Storage-Yield Analysis
Hydrologic analysis for Falls Lake was performed using OASIS software, which is a proprietary water resources simulation and optimization model.
Study considered basin conditions in 2045 to calculate critical low-flow period.
Critical low flow period was June 2010 to February 2013.
Notes: The study considered basin conditions in 2045 to calculate the critical low-flow period. The critical low flow period was June 2010 to February 2013. Outflows for the yield analysis fully met the dam’s minimum release requirements and the downstream flow target for water quality. The daily return flow from the city of Raleigh also contributes to the downstream flow target. The reallocation study calculated both the City of Raleigh’s total system yield and the Falls Lake yield. The results are shown in Figure 3. An additional 17,300 ac-ft of water supply storage (an increase from 45,000 ac-ft to 62,300 ac-ft) is needed to fully satisfy the 2045 system demand of 97.9 MGD during the critical period.

## Slide 10: Case Study – Lake Texoma
Lake Texoma, Texas/Oklahoma
Analyzed reallocating storage space to water supply from both conservation storage and flood storage
Notes: The Lake Texoma study is an example of a study incorporating multiple benefit types and a variety of reallocation options. Reallocating water from flood storage to conservation storage was studied and considered.

## Slide 11: Lake Texoma, Texas and Oklahoma
Notes: Lake Texoma is located on the Red River on the border between Texas and Oklahoma. Lake Texoma was authorized for flood control and power by the Flood Control Act of 1938. The dam was completed in 1944. The authorized project purposes are flood control, hydroelectric power, navigation, Red River flow regulation, water supply, and recreation. The project also provides habitat for native and introduced sport fish and wildlife species. The elevation and capacity of the flood storage and conservation storage pools are shown in the Table.

## Slide 12: Lake Texoma Reallocation Study
Water Resources Development Act (WRDA) of 1986, Section 838 (Sec 838), authorized the reallocation of storage to water supply in increments as needed up to an additional 150,000 acre-feet each for Oklahoma and Texas.
North Texas Municipal Water District (NTMWD) requested 100,000 acre-feet of storage and Greater Texoma Utility Authority (GTUA) requested 50,000 acre-feet from Lake Texoma.
The study considered five alternatives for further evaluation:
  0) No action,
  Reallocation of 150,000 acre-feet from the conservation pool,
  Reallocation of 300,000 acre-feet from the conservation pool,
  Reallocation of 150,000 acre-feet from flood control storage,
  Reallocation of 300,000 acre-feet from flood control storage
Notes: The North Texas Municipal Water District (NTMWD) requested 100,000 acre-feet of storage and the Greater Texoma Utility Authority (GTUA) requested 50,000 acre-feet from Lake Texoma. The Water Resources Development Act (WRDA) of 1986, Section 838 (Sec 838), authorized the reallocation of storage to water supply in increments as needed up to an additional 150,000 acre-feet each for Oklahoma and Texas. The reallocation to NTMWD and GTUA would make up the full 150,000 acre-feet allocated to Texas, while Oklahoma has not yet identified an immediate need for their 150,000 acre-feet.
Alternatives
The preliminary screening of alternatives considered new groundwater wells, existing surface water sources other than Lake Texoma, new surface water sources, downstream Red River diversion, and conservation. Several of these alternatives were already accounted for in the Texas Water Plan, and the others were not feasible.
The study considered five alternatives for further evaluation: 0) no action, 1) reallocation of 150,000 acre-feet from the conservation pool, 2) reallocation of 300,000 acre-feet from the conservation pool, 3) reallocation of 150,000 acre-feet from flood control storage, 4) reallocation of 300,000 acre-feet from flood control storage.

## Slide 13: Lake Texoma Analysis of Alternatives
Since there were no immediate Oklahoma water supply needs, the selected plan was alternative 1, reallocation of 150,000 acre-feet from the conservation pool.
Notes: Reallocation from the conservation pool caused a reduction in hydropower benefits and a slight increase in flood risk reduction benefits. Reallocation from the flood pool caused some increase in flood damages (loss of flood damage reduction benefits) and also loss in hydropower benefits. Recreation benefits were assumed to not change. However, a reallocation from the flood pool would cause a rise in reservoir levels and would cause additional costs for cultural site mitigation and relocation of recreation and marina facilities. The cultural site mitigation includes cost of surveys and national register assessment.

## Slide 14: Lake Texoma Storage-Yield Analysis
Potential impacts of reallocation were evaluated using SUPER to model yield and impact analysis of reallocation alternatives.
Water supply yield run was made based on the 2002 sediment resurvey of Lake Texoma, with projected future sedimentation to the year 2044. This projected future storage is considered “usable storage”.
True yield of the conservation storage at Lake Texoma for the projected 2044 conditions was determined to be 1502.5 cfs (= Ytrue).
Critical dependable yield for the conservation storage allocated to water supply (Ycritical):
YCritical = Ytrue * SAllocated / STotal
  (SAllocated) = total allocated water supply storage
  (STotal) = total usable conservation storage
Notes: The potential impacts of reallocation were evaluated using SUPER to model yield and impact analysis of reallocation alternatives. The SUPER model is a predecessor to RiverWare that includes impact analysis modules in addition to hydrologic routing. The SUPER model was used to determine the yield of the conservation storage.
The water supply yield run was made using an elevation-area-capacity table based on the 2002 sediment resurvey of Lake Texoma, with projected future sedimentation to the year 2044. This projected future storage is considered “usable storage”. The true yield of the conservation storage at Lake Texoma for the projected 2044 conditions was determined to be 1502.5 cfs. The critical dependable yield for the conservation storage allocated to water supply (YCritical) is determined by multiplying true yield (Ytrue) of the conservation storage times the ratio of the total allocated water supply storage (SAllocated) to the total usable conservation storage (STotal). The results can be seen in Table.

## Slide 15: Case Study – John Redmond Dam
John Redmond Dam, Kansas
Included Kansas-specific yield criteria
Study and results affected strongly by projected future changes to reservoir
Approved reallocation of flood control storage to water supply, raising the normal conservation pool.

## Slide 16: John Redmond Dam and Reservoir, Kansas
Feature | Elevation | Area | Capacity | Equivalent Runoff
 | (feet) | (acres) | (acre-feet) | (inches)
Top of Dam | 1081.5 | - | - | -
Top of Gates and Flood Control Pool | 1068.0 | 34,331 | 574,918 | 3.36
Flood Control Storage | 1039.0-1068.0 | - | 524,417 | 3.68
Top of Conservation Pool | 1039.0 | 8,084 | 50,501 | 0.38
Conservation Storage | 1020.0-1039.0 | - | 50,501 | 0.38
Spillway Crest | 1033.0 | 4,801 | 9,980 | 0.01
Bottom of Conservation Pool | 1020.0 | 0 | 0 | -
Proposed Conservation Storage | 1041.0 | - | 67,700 | -
Notes: John Redmond Dam and Reservoir is on the Neosho River in Kansas. The Flood Control Act of 17 May 1950 authorized the construction of Strawn Dam and Reservoir, which was renamed the John Redmond Dam and Reservoir in 1958. Construction began in 1959, and the project became operational in 1964. The authorized purposes are flood control, water supply, water quality, and recreation, and it is also operated for wildlife.

## Slide 17: John Redmond Sedimentation Issues
USACE and Kansas Water Office (KWO) signed an agreement for 34,900 acre-feet of water supply, assuming 62,500 ac-ft of conservation storage remained after 50 years.
Conservation storage was impacted more by sedimentation than flood storage. Sedimentation survey in 2000 projected a 9% reduction in flood storage by 2014, while conservation storage would be reduced by over 50%.
Based on the 2000 study, there would be only 40,100 ac-ft of conservation storage by 2014.
Water supply uses include an operating nuclear power plant.
Notes: A sediment survey was conducted in 2000 and found there were 524,417 acre-feet of flood storage and 50,501 acre-feet of conservation storage remaining. The Kansas Water Office (KWO) had an agreement for 37,450 acre-feet of water supply storage. However, the sediment in the reservoir has increased at a higher rate than planned. The District estimated the total sediment deposited in the reservoir in year 2014 was approximately 95,000 acre-feet, which is almost twice the level projected when the water supply agreement was first signed in 1976. The report estimated that the conservation storage was reduced to only 40,100 acre feet in 2014, less than half of the original conservation storage space of 82,700. Only 9% of the flood storage space was reduced by sedimentation.

## Slide 18: John Redmond Yield Analysis
Kansas Water Statutes:
  "… the director shall not contract for withdrawals of water from a particular reservoir which in the director's opinion are in excess of the yield capability from the conservation storage water supply capacity in such reservoir committed to the state computed to provide water through a drought having a 2% chance of occurrence in anyone year with the reservoir in operation" (K.S.A. 82a-1305).
It can be inferred that statute refers to annual drought.
Existing KWO water supply agreement based on an expectation of 26.5 MGD yield throughout the 2%-annual chance drought
Approved reallocation study recommended raising the conservation pool by 2 feet to more equitably distribute the sedimentation losses and reduction in yield
  Note that KWO subsequently obtained a Section 404 permit to dredge the conservation pool (work is ongoing).
KWO had contracts for 26.5 MGD for use at Wolf Creek Nuclear Power Plant.
Notes: Another statute describes the quantity of water that the State may reserve to store in a reservoir (known as a water-reservation right) as:
"… an amount sufficient to insure a yield of water from the reservoir for beneficial use through a drought with a 2% chance of occurrence in any one year with the reservoir in operation" (K.S.A.82a-1303).
1997 yield analysis used LPOP5 computer model which simulated reservoir operations, which used a mass-balance method and a monthly time step.
Due to sedimentation, there was insufficient water supply storage available to satisfy the KWO’s existing water supply agreements with its customers. One of the customers is the Wolf Creek nuclear power plant downstream of the reservoir.

## Slide 19: Case Study – Apalachicola-Chattahoochee-Flint
The ACF system in Georgia, Alabama, and Florida has several federal reservoirs and complicated operations.
This study of the system yield was requested by Congress

## Slide 20: Apalachicola-Chattahoochee-Flint River Basin
Federal reservoir conservation storage by acre- feet and percent for the ACF basin.
Notes: The Apalachicola-Chattahoochee-Flint (ACF) River basin is located in the states of Alabama, Florida, and Georgia.
The 2010 reports accompanying the Energy and Water Development and Related Agencies Appropriations Act, 2010 (H.R. 3183; Public Law 111-85) included direction to update the critical yield of all the projects in the ACF basin.
“Alabama-Coosa-Tallapoosa [ACT], Apalachicola-Chattahoochee- Flint [ACF] Rivers, Alabama, Florida, and Georgia.—The Secretary of the Army, acting through the Chief of Engineers, is directed to provide an updated calculation of the critical yield of all Federal projects in the ACF River Basin and an updated calculation of the critical yield of all Federal projects in the ACT River Basin within 120 days of enactment of this Act.”

## Slide 21: ACF Storage-Yield Methods
This condition results in the maximum yield possible from the Federal projects.
This condition results in the most severe downstream impact and represents a conservative assessment of the critical yield available.
Notes: The critical yield study used the HEC-ResSim program for the calculations. The ResSim model for the ACF basin includes a net precipitation-evaporation rate for each reservoir. Evaporation values were from NOAA technical reports. The study also used an unimpaired flow data set that adjusted the historical observed flows for human influence.
The study calculated critical yield using different methods. Method A assumes that there are no withdrawals from or returns to the lake and there are no withdrawals from or returns to the river as it flows between projects. This condition results in the maximum yield possible from the Federal projects. Critical yield from an upstream reservoir is assumed to be permanently removed from the system and does not contribute to the inflow at downstream reservoirs.
Method B assumes net river withdrawals and returns are occurring; this method does not include withdrawals from the Corps reservoirs. Critical yield from an upstream reservoir is assumed to be permanently diverted from the system and does not contribute to the inflow at downstream reservoirs. This condition results in the most severe downstream impact. The results of Method B represent a conservative assessment of the critical yield available from Federal projects controlled by the Corps of Engineers.

## Slide 22: ACF Storage-Yield Methods
Method C computes a system yield for diversion from the most downstream storage reservoir.
Notes: Method C computes a system yield for diversion from the most downstream storage reservoir. It assumes upstream reservoirs operate in tandem to maximize the critical yield at the most downstream reservoir. Method C computes critical yield for the ACF River System with and without net river withdrawals. The “with net river withdrawals” condition results represent the Corps’ yield. The “without net river withdrawals” condition results represent the system theoretical maximum yield. Method C calculates the theoretical critical yield that might be observed if the upstream projects were operated solely to maximize yield at Walter F. George Lake. However, in reality the results could not be achieved because the Corps must operate in a balanced manner to achieve all authorized project purposes.

## Slide 23: ACF Storage-Yield Results
ACF projects critical yield using Method A (without diversions)
ACF projects critical yield using Method B (with diversions)
ACF river system yield without and with diversions
Notes: The study assumes that the upstream reservoir is the primary reservoir and its yield is met (maximized) before proceeding downstream. This is because upstream users can consumptively divert water, precluding the availability of water yield to a downstream user. Maximizing the yield of the upstream reservoir is consistent with current state-issued water withdrawal permits. Another assumption is that projects are full at the beginning of the drought period simulation. The pool level at the beginning of a drought simulation is important because it is a variable that directly affects the quantity or volume of water available as critical yield.
For methods A and B, it is assumed that none of the critical yield is returned to the system. Critical yield is permanently diverted from the system and assumed to be consumptively used. For example: Buford Dam critical yield is not counted as inflow to West Point Lake. Inflows to West Point Lake are assumed to derive only from the West Point Lake drainage basin. This methodology determines the conservative individual project yield. This assumption is not applicable to Method C.

## Slide 24: Additional Discussion
Notes: Spend the remainder of the lecture discussing any issues or points that have not yet been discussed. This slide links to several different topics that can guide further discussion.

## Slide 25: Possible Water Supply Study Goals
New water supply
  New water user
  Reallocation study
  Change in system operations
Changing conditions
  Re-evaluate hydrology
  Impact to existing agreements from new requirements
  Resilience to future uncertainty
  Dam safety measures (reduced pool elevation, etc.)
Notes: Here are some possible reasons for doing a water supply study. They may be the same or different than the reasons brought up during the class discussion, discuss any that have not been discussed yet through class discussion or case studies.

## Slide 26: Model Scope and Configuration
What model will you use?
What extent (spatial and temporal) do you need to include?
Timestep?
How many reservoirs?
Downstream points?
Different operating alternatives?

## Slide 27: Data
What will the period of record be? Does that period have consistent hydrology?
Synthetic/alternative hydrology?
Do you have historical operations data (outflow, elevation, etc.)?
Does your period include significant droughts?
Do you have evaporation data?
Will you need one or more demand patterns?

## Slide 28: Diversions
Is your diversion from the reservoir pool or downstream of the dam?
Are there minimum flow requirements between the dam and the diversion?
What about below the diversion?
Are there tributaries or other diversions you need to pay attention to?

## Slide 29: Physical Layout
Diversions from reservoir pool vs. downstream diversions
Res
Diversion from reservoir pool
Downstream diversion
City
Powerplant
Town
Notes: One example of competing vs. complementary uses is the location and method of a diversion. Diverting from the pool competes with uses that require downstream releases, while diverting below the reservoir can cooperate with those uses.

## Slide 30: Physical Layout
Diversions from storage typically compete with all uses except flood control
  Less water is available in the reservoir to release for other purposes
  The diverted water may not benefit other project purposes
Res
Diversion from reservoir pool
Downstream diversion
City
Powerplant
Town
Notes: In this example, we can see that diverting water from the reservoir pool causes that water to bypass the powerplant, the downstream reach, and the downstream city. In some cases (i.e. Falls Lake) diverted water may return to the downstream reach.
Note that competing uses such as this are not undesirable. They just need to be taken into account during modeling.

## Slide 31: Physical Layout
Downstream diversions can be complementary with some purposes
  Releasing for the diversion can also generate power
  Navigation or environmental benefits are created between the dam and the diversion point
Res
Diversion from reservoir pool
Downstream diversion
City
Powerplant
Town
Notes: We can see in this example that the diverted water first is passed through the powerplant, then flows along the downstream reach and through the city before being diverted.

## Slide 32: Other Requirements
Are there minimum instream flows?
Are there water quality requirements?
What benefits besides water supply need to be considered?
  Flood control?
  Navigation?
  Hydropower?
  Recreation?
  Environmental?
How will your model support assessments of those benefits?

## Slide 33: Changes Over Time
Will your study look at current or future conditions?
Will you model climate variability?
Will you model changes in demands?
How will you account for reservoir sedimentation?
Will you consider droughts outside the period of measured data?

## Slide 34: Water Allocation
What water rights regime does the study area have?
  “ ’True’ Riparian, Regulated Riparian, Prior Appropriation, Other?
How do water rights affect the operation of the project?
How are inflows and outflows apportioned between different rights?
How will water rights affect the model extent and study stakeholders?
Notes: The Corps does not have an official stance on how to model and account for water rights. Your study should make sense for your area and your specific water rights issues.

## Slide 35: Multiple Reservoirs
Are the flows in your study impacted by regulation besides the study reservoir?
Are there multiple reservoirs you want to study?
Do you want the yield of a single reservoir or the whole system?
Will the reservoirs operate together, or independently?

## Slide 36: Knowledge Check
What are some possible water supply study purposes?
  Determine the storage needed to meet a diversion demand, contribute to a reallocation analysis, and evaluating impacts and conflicts between different reservoir uses – Many other answers are possible
How would firm yield and reservoir benefits be affected by moving a diversion from the reservoir to a downstream intake?
  Yield may increase or decrease depending on how water supply is prioritized vs. other purposes. Flood control benefits could decrease, while hydropower and navigation benefits could increase.