## Slide 1: Scripting HEC-ResSim

## Slide 2: Topics
Scripts Executed During Simulations
  State Variable Scripts
  Scripted Rule Scripts
Scripts Executed Outside Simulations
  Static Scripts
Jython

## Slide 3: Two Categories of Scripts – 1 of 2
Scripts executed during simulations
  These scripts can:
    Compute and store the state of some (concrete or abstract) portion of the model at each simulation time step
    Compute a flow limit (minimum, maximum, specified, or free) at each simulation time step
  These scripts cannot:
    Know when they execute in relation to other scripts

## Slide 4: Two Categories of Scripts – 2 of 2
Scripts executed outside simulations
  These scripts can:
    Pre-process data for simulations
    Run simulations (some or all alternatives)
    Post-process data from simulations, generate plots, reports, etc…
  These scripts cannot:
    Interact with a running simulation

## Slide 5: Scripts Executed During Simulations – 1 of 2
There are two types of HEC-ResSim scripts that are executed during simulations
  State Variable Scripts
    Scripts that set the value of a state variable, which can be used by rules and IF-THEN-ELSE blocks to specify flow constraints
      A model variable represents the state of some element of the network with a value at each time step of the simulation (thus, a time series)
      A state variable is a model variable-like time series whose values are computed by a script instead of the static rule-based logic; it doesn’t necessarily represent the state of a single element
  Scripted Rules
    Scripts that directly specify flow constraints
Notes: State Variables have the benefit of being able to be used by multiple rules and also may be viewed in plots or tables.
Scripted Rules have the benefit of being able to set not just the value of a constraint, but the constraint type, and even whether a constraint exists at all – may need elaboration

## Slide 6: Scripts Executed During Simulations – 2 of 2
Common Properties of State Variable and Scripted Rule Scripts
  Scripts are executed at every iteration of every time step
  Computation at any time step may depend on any model variables at previous time steps, and may depend on other State Variables at the current time step
  Scripts are normally only executed when used in an active alternative, but can be forced to execute otherwise
Notes: Scripts that depend on other State Variables at the same time step must manually ensure they have been executed before the current script

## Slide 7: Limitations of Model Variables
Model variables provide the states of single elements within a ResSim model.
Therefore, model variables cannot represent abstract concepts that require analysis of more than one element such as:
  basin wetness
  drought level
  system storage utilization
  depth-area-duration considerations

## Slide 8: State Variables vs. Model Variables
Like model variables, state variables are time-series objects that belong to the Network.
Like model variables, state variables are globally accessible, so they may be used in multiple rules and in multiple reservoirs.
Unlike model variables, state variables are not associated with specific network elements (pools, junctions, etc…). As such, they can represent complex or abstract concepts.
Notes: The Network is the program object that holds all objects that make up the reservoir system being modeled. The GUI refers to it as the Reservoir Network.
Reservoirs, Reaches, Junctions, and Diversions are all objects within the Network. These objects are compound objects, each containing other objects. The reservoir object is the most complex. It contains the pool and outlet objects, as well as the operation sets, zones, and rules.

## Slide 9: State Variable Scripts
HEC-ResSim computes a state variable by executing a Jython script for that variable at every time step throughout the simulation period.
The script can access model variables and other state variables for the current and prior time steps.
  Scripts that depend on other State Variables at the same time step must be manually ensured to be executed after the script they depend upon
The script can also perform any function available to Jython to compute the variable.
  Care must be taken not to perform lengthy tasks (e.g. disk or network access) because of the number of times the script is executed!
Notes: Jython is a Java implementation of the Python programming language and provides the common basis for ResSim, DssVue, and CWMS scripting.
State Variable definition scripts do not return anything. They must “set” the value of the TimeSeries object for the current time step, or have set it in an earlier time step. The script may optionally set values into the future (through the end of the computation time window).

## Slide 10
ResSim
How To Implement Scripts….

## Slide 11: Creating New State Variable Scripts
To create a new State Variable script:
  Select EditState Variables from the Simulation Module menu bar.
  Select StateVariableNew from the State Variable Editor menu bar.
  Enter the desired name in the Name field of the New State Variable dialog.
  Press the OK button.
  Enter the desired parameter (DSS C Part) in the Parameter Name field.
  Select the desired parameter type from the Parameter Type list.
  Edit the script text as desired.
  Press the Compile Script button to check for syntax errors.
    Fix any errors and repeat this step.
  Save the script by selecting StateVariableSave from the menu bar or pressing Ctrl-S.
  Close the State Variable Editor dialog.

## Slide 12: Editing Existing State Variable Scripts
To edit an existing State Variable script:
  Select EditState Variables from the Simulation Module menu bar.
  Select the desired State Variable name from the Name field.
  Edit the script text as desired.
  Press the Compile Script button to check for syntax errors.
    Fix any errors and repeat this step.
  Save the script by selecting StateVariableSave from the menu bar or pressing Ctrl-S.
  Close the State Variable Editor dialog.

## Slide 13: Creating and Editing State Variable Scripts

## Slide 14: The State Variable Editor
Script Tabs
Script Pane (editor window)
Object Pane (API window)
API preview & Cursor Location

## Slide 15: Using the State Variable Editor API Pane
Selecting a node (not a folder) in the API Pane causes the API insertion text for the selected node to be displayed in the API preview bar.
Double-clicking on a node in the API Pane causes its API text to be inserted at the current cursor position in the Editor Pane.
  The same can be accomplished by selecting a node in the API and then selecting the Insert in Script button under the API Pane.
Dragging a node in the API Pane to some position in the Editor Pane causes its API text to be inserted at that location in the Editor Pane.

## Slide 16: State Variable Editor API Pane Example

## Slide 17: Creating New Scripted Rules
To create a Scripted Rule:
  Open the Reservoir Editor to the Zone-Rules tab of the Operations tab.
  Right-click the desired zone and select Add New Rule… from the context menu.
  Enter the desired name and select the desired release element in the New Operating Rule dialog.
    Select Script for the Rule Type.
  Press the OK button.
  Edit and check syntax as with a State Variable.

## Slide 18: Editing Existing Scripted Rules
To edit an existing Scripted Rule:
  Select the desired rule in the Zone-Rules tab of the Operations tab of the Reservoir Editor.
  Edit the script as desired. The editor is similar to the State Variable editor.

## Slide 19: Creating Scripted Rule Example

## Slide 20: Editing Scripted Rule Example

## Slide 21: Scripts Executed Outside Simulations
There is only one type of script executed outside simulations, which we call static scripts or utility scripts.
Static scripts resemble HEC-DSSVue scripts:
  They can be executed from the Script Selector, Script Pane, or Script Editor.
  They are edited and tested in the Script Editor.
  Their location in the Tree Pane of the Script Editor corresponds to a file on disk.
Static scripts go beyond HEC-DSSVue scripts:
  Script location in the Tree Pane determines script visibility.
  Scripts can have knowledge of the current module and current simulation.

## Slide 22: The Script Selector
The Script Selector is accessed by the ToolsScripts menu item in any module.
The Script Selector is titled according to the current module.
Execute a script by pressing its button.

## Slide 23: Accessing the Script Editor
The Script Editor is accessed by the ToolsScript Editor… menu item on the HEC-ResSim menu bar, or by ScriptScript Editor menu item on the Script Selector.

## Slide 24: The Script Editor
Tree Pane
Editor Pane
Script Name
File Name
Visibility Switches
Dismissal Buttons
Description Pane
Edit/Save/Test Buttons
Icon Selector
Pre-Defined Variables
Location / Mode Indicators

## Slide 25: Static Script Visibility
For a static script to be visible:
  its position in the Tree Pane:
    must be in the All Watersheds folder or Current Watershed folder
    must be in Modules folder or folder corresponding to the current module
  its Show in Script Selector switch must be checked to be visible in the Script Selector
  its Display Script to User switch must be checked to be visible in the script pane

## Slide 26: Creating a New Static Script
To create a new static script:
  right-click on one of the folders under either the All Watersheds or Current Watershed:
    Modules
    Watershed Setup
    Reservoir Network
    Simulation
  select New Script from the context menu
  enter a name in the Label field
  enter the script text in the Editor Pane
  press the Save or Save and Test button

## Slide 27: Editing Existing Static Scripts
To edit an existing Static Script, do one of the following:
  double-click on its entry in the Tree Pane
  right-click on its entry in the Tree Pane and select Edit Script from the context menu
  select its entry in the Tree Pane and do one of the following:
    select FileOpen from the menu bar
    press Ctrl-O
    press the Edit button

## Slide 28: Testing Existing Static Scripts
To test an existing Static Script from the Script Editor, select its entry in the Tree Pane and do one of the following:
  select FileTest from the menu bar
  press the Save and Test button

## Slide 29: Adding Scripts to the Simulation Module Script Pane
To add a script to the simulation module script pane:
  right-click in the scripts area
  select Edit Script List from the context menu
  use the Edit Scripts dialog to move desired scripts to the Selected list

## Slide 30: Static Script Access to ResSim Information
isWatershedOpened()
getWatershed()
getWatershedName()
openWatershed(watershedName)
closeWatershed()
getCurrentModule()
selectModule(moduleName)
getTimeWindow()
getTimeWindowString()
getSimulation() getSimulationName()
openSimulation(simulationName)
getSimulationRun(alternativeName)
getSimulationRuns() getSelectedSimulationRuns() getAlternativeNames() getSelectedAlternativeNames()
extractSimulationData()
computeSimulationRun(simulationRun)
getSimulationDSSFileName()
getFParts()
getFPart(alternativeName)
runSimulation(simulationName, newExtract=False, *alternativeNames)
These functions are included in the ResSimUtils module provided with this workshop.

## Slide 31: What is Jython?
Jython is a Java-based implementation of the Python programming language. This means:
  You learn the Python language to learn Jython.
  Jython code can work seamlessly with Java code.
Anybody programming experience will pick it up quickly.
Others can quickly become effective by mimicking examples.
http://jython.org

## Slide 32: What is Python?
Python is a programming language that is
  interpreted
  open source
  object oriented
and has
  simple syntax
  high level dynamic data types
http://python.org

## Slide 33: Some Books Available

## Slide 34: Review
Scripts Executed During Simulations
  State Variable Scripts
  Scripted Rule Scripts
Scripts Executed Outside Simulations
  Static Scripts
Jython