## Slide 1: Scripting HEC-ResSim

## Slide 2: Topics
Two Categories of Scripts
Scripts Executed Outside Simulations
  Utility Scripts (also called “static” scripts)
  We’ll use this for first two workshops!
Scripts Executed During Simulations
  State Variable Scripts
  Scripted Rule Scripts

## Slide 3: Two Categories of Scripts – 1 of 2
Scripts executed outside simulations
  These scripts can:
    Pre-process data for simulations
      modify input data
      modify models (What? Danger!)
    Run simulations (some or all alternatives)
    Post-process data from simulations,
      generate plots and reports, etc…
  These scripts cannot:
    Interact with a running simulation

## Slide 4: Scripts Executed Outside Simulations
There is only one type of script executed outside simulations, which we call static or utility scripts.
Utility scripts resemble HEC-DSSVue scripts:
  They can be executed from the Script Selector, Script Pane, or Script Editor.
  They are edited and tested in the Script Editor.
  Their location in the Tree Pane of the Script Editor corresponds to a file on disk.
Utility scripts go beyond HEC-DSSVue scripts:
  Script location in the Tree Pane determines script visibility.
  Scripts can have knowledge of the current module and current simulation.

## Slide 5: The Script Selector
The Script Selector is accessed by the ToolsScripts menu item in any module.
The Script Selector is titled according to the current module.
Execute a script by pressing its button.

## Slide 6: Accessing the Script Editor
The Script Editor is accessed by the ToolsScript Editor… menu item on the HEC-ResSim menu bar, or by ScriptScript Editor menu item on the Script Selector.

## Slide 7: The Script Editor
Also in DSSVue*!
Notes: DSS Vue has a different script tree on the side

## Slide 8: The Script Editor
Tree Pane
Editor Pane
Script Label
File Name
Visibility Switches
Description Pane
Edit/Save/Test Buttons
Icon Selector
Pre-Defined Config Variables
Location / Mode Indicators

## Slide 9: Utility Script Visibility
For a utility script to be visible:
  In the Tree Pane:
    must be in the All Watersheds folder or Current Watershed folder
    must be in Modules folder or folder corresponding to the current module
  its Show in Script Selector switch must be checked to be in the Script Selector
  its Display Script to User switch must be checked to be in the script pane

## Slide 10: Creating a New Utility Script
To create a new utility script:
  right-click on one of the folders under either the All Watersheds or Current Watershed:
    Modules
    Watershed Setup
    Reservoir Network
    Simulation
  select New Script from the context menu
  enter a name in the Label field
  enter the script text in the Editor Pane
  press the Save or Save and Test button

## Slide 11: Editing Existing utility Scripts
To edit an existing Utility Script, do one of the following:
  double-click on its entry in the Tree Pane
  right-click on its entry in the Tree Pane and select Edit Script from the context menu
  select its entry in the Tree Pane and do one of the following:
    select FileOpen from the menu bar
    press Ctrl-O
    press the Edit button

## Slide 12: Testing Existing Utility Scripts
To test an existing Utility Script from the Script Editor, select its entry in the Tree Pane and do one of the following:
  select FileTest from the menu bar
  OR press the Save and Test button

## Slide 13: Adding Scripts to the Simulation Module Script Pane
To add a script to the simulation module script pane:
  right-click in the scripts area
  select Edit Script List from the context menu
  use the Edit Scripts dialog to move desired scripts to the Selected list