## Slide 1: HEC-ResSim Scripting Applications Overview
Fauwaz hanbali
MMC HEC-ResSim Scripting
August 2023

## Slide 2: Agenda
HEC-ResSim Scripting Purposes
HEC-ResSim Scripting Applications

## Slide 3: Purposes
Preprocessing
  Parsing text input files and preparing DSS inputs
  Computing statistics and important criteria
Reservoir Operations
  Computing non-standard variables for use in decisions
  Non-standard and complex decision logic
Visualization
  Custom plot layouts, styles, and content
Post Processing
  Data transformations and datum shifts
  Byproduct variables and statistics
  Results plots and report generation
Automated Computes
Notes: Adding custom capability beyond HEC-ResSim generalized features:
  Driving computation
  State variable (pre, main, post)
  Global variable
  Scripted rule (pre, main, post)
  OSI
Depending on preference and application, can also use scripting editors in CAVI/DSS or ResSim for following:
  Plots and statistics for analysis
  Data preprocessing and post processing
  Report generation

## Slide 4: Customized Plotting
Notes: Multiple viewports
Reverse Axis and Multiple Axes
Markers and Labels
Colors (Curves and Symbols)
Filling Below/Above Curves
Legend Labels

## Slide 5: Forecast Reservoir Plot
Notes: Back computed observed reservoir inflows
Time of Forecast Axis
Observed vs. computed reservoir variables
  Elevation
  Inflow
  Outflow

## Slide 6: Scripted Conditional Minimum Releases
Notes: Preprocessed 25- and 50-percentiles using period of record and cyclic analysis
Time interval based checks on whether or not input inflows fall within or outside the range between the 25- and 50-percentiles

## Slide 7: Report Generation
Notes: Create a table from data lists using string manipulation

## Slide 8: Automated Computes
Example script and a document describing usage:
  https://drive.hecdev.net/share/SjQrzCH7
Notes: Use ResSim API for accessing and driving simulation and alternatives analysis
Use Java packages for building a convenient interface for driving the desired automated computes

## Slide 9: Applications
SPK – Folsom Dam
LRN – Jay Percy Priest Dam
LRN – Cumberland River System
SAM – ACF System
NWDMR – Missouri River System
NWD – Columbia River System

## Slide 10
Folsom Dam
Notes: Folsom dam’s outlet structures:
  Lower tier bottom outlets
  Upper tier bottom outlets
  Hydropower plant
  Main dam gated spillway group of 5
  Main dam gated spillway group of 3 with flip buckets
  Side spillway
  Emergency Spillway

## Slide 11: Outlet Release Allocations
Notes: Folsom reoperation study model included
  Stacked release allocations plot
    Use HEC Math to add up outlet flows
    Order the accumulated outlet flow curves and fill below curves
  Automated computes for hundreds of alternatives

## Slide 12
Jay Percy Priest Dam
Return Flow Via Dummy Reservoir
Notes: Workaround HEC-ResSim’s limitation in handling circular flow:
  Use a dummy reservoir with infinite storage
    Read the real reservoir’s diversion decision
    Apply a return flow ratio and feed back as inflow to the real reservoir

## Slide 13
Cumberland River System
Notes: Several scripts to assist with daily forecast modeling routine, including:
  Observed (USGS) data importing
  Plotting of real-time data and simulation results
  Interpreting reservoir release flow decisions and translating to gate change instructions

## Slide 14
Green River System
Notes: As a few reservoirs in the Green River system operate for stage criteria at a downstream location (Evansville, IN) along the Ohio River, real-time and forecast stages are simply read from the CWMS database for the downstream location without having to expand the model’s domain to include the Ohio River.

## Slide 15
ACF System
Notes: The composite storage of the three major reservoirs in the ACF Basin is checked against a handful of system levels that trigger drought operations from mild to severe measures.

## Slide 16
Missouri River System
Notes: Due to limitation in HEC-ResSim’s tandem system and downstream control operations, the entire Missouri River System operations are scripted:
  Several scripts that balance reservoir storages and release to meet downstream flow and stage targets
  ResSim Utils module with several HEC-ResSim API functions and user defined functions

## Slide 17: Questions
?