## Slide 1: System Operation
HEC-ResSim
Fauwaz Hanbali
Hydrologic Engineering Center

## Slide 3: Outline
Establish a system operation in ResSim
System storage balance concepts
Implicit (equal) system storage balance
Explicit (user-defined) system storage balance
Creating an explicit system storage balance operation set

## Slide 4: Establishing system operation

## Slide 5: Reservoir Systems in ResSim
ResSim supports two types of reservoir system operation
  Parallel
  Tandem
Both types rely on a System Storage Balance

## Slide 6: Parallel Operation
Two or more reservoirs operate together for minimum and/or maximum flow limits at common downstream locations
Releases made from each reservoir are determined by storage balance

## Slide 7: Defining Parallel Operation
In one reservoir…
  Create a Downstream Control rule for the common downstream location.

## Slide 8: Defining Parallel Operation
In a parallel reservoir…
  Apply the same Downstream Control Flow- Limit rule for the common downstream location

## Slide 9: Defining Parallel Operation
In the alternative editor…
  Select the operation set that includes the Downstream Control Rule for each reservoir in the system.

## Slide 10: Tandem Systems
A series of two or more reservoirs may be established by having each upstream reservoir operate for the next reservoir downstream
Tandem Operation occurs when an upstream reservoir makes releases to preserve the storage balance with a downstream reservoir

## Slide 11: Defining…Tandem Operation
Add a Tandem operation rule to the upstream reservoir of the tandem system

## Slide 12: Defining… Tandem Operation
In the alternative editor…
  Select the operation set that includes the Tandem operation rule for the upstream reservoir.

## Slide 13: Prioritizing System Operation
System Operating Rules are prioritized for each reservoir within its set of operating rules

## Slide 14: system Storage Balance concepts

## Slide 15: System Storage Balance
For every decision interval,
  End-of-period storage is estimated for each reservoir and the system total, accounting for:
    Beginning-of-period storages
    Total inflow volumes
    Total potential outflow volumes
  Total end-of-period system storage and system zone definitions are used to estimate a desired system storage level
  Priority to release is assigned to the reservoir that is farthest from the desired system storage level to achieve balance among reservoirs
  Desired system storage balance releases are compared against other rule priorities and constraints, then final release decisions are made
IN
IN
Loc
Div
Div
Loc
Loc

## Slide 16: System Storage Balance
System Storage is the sum of allocated storages in the system
Reservoir Level is % full in Reservoir Zone
Balance exists when each reservoir level equals the system level
Balance can be
  Implicit (default)
  Explicit (user-defined)
Project | Conserve Storage | Flood Storage
Res. 1 | 20,000 | 10,000
Res. 2 | 10,000 | 20,000
System | 30,000 | 30,000
%100
%0
%100
%0
Res. 1
Res. 2
System
%100
%0
%100
%0
F.C.
F.C.
Sys
F.C.
Con.
Con.
Sys
Con.

## Slide 17: Reservoir System Operation Equal (Implicit) Storage Balance Targets
Flood Control
Conservation
Res. 1
Res. 2
System

## Slide 18: Reservoir System Operation User-Defined (Explicit) Storage Balance Targets
Flood Control
Conservation
Res. 1
Res. 2
System

## Slide 19: Implicit (Equal) Storage Balance

## Slide 20: Implicit System Storage Balance
By default, ResSim uses an Implicit Storage Balance
Implicit Balance treats each reservoir storage equally toward its guide curve
System Storage
System Storage
Res1 Storage
Res2 Storage
Empty
Empty
Empty
Full
Full
Full
G.C.
G.C.
Sys
G.C.
Balance Line
Balance Line
Balance Line
Balance Line

## Slide 21: Implicit System Storage Balance
The reservoir that is the farthest above the desired storage balance has release priority
Here, Reservoir 2 should release to draw down to Desired Storage
System Storage
Estimated Storage
System Storage
Res1 Storage
Res2 Storage
Empty
Empty
Empty
Full
Full
Full
G.C.
G.C.
Sys
G.C.
Below Desired Storage
Above Desired Storage
Desired Storage

## Slide 22
System Flood Control Zone
System Conservation Zone

## Slide 23: Explicit (User-Def.) Storage Balance

## Slide 24: Explicit System Storage Balance
Explicit System Storage Balance is defined for specific zones
The %Storage desired for balance is defined
e.g. 70% in Res. 1 Con. is balanced with 33% in Res. 2 Con.
System Storage
System Storage
Res1 Storage
Res2 Storage
Empty
Empty
Empty
Full
Full
Full
Con.
Con.
F.C.
F.C.
Sys
Con
Sys
F.C.
70% Con
33% Con
25% F.C.
75% F.C.

## Slide 25: Explicit System Storage Balance
 | Example Explicit Storage Balance for the Conservation Storage |  |  | 
 | Reservoir 1 | Reservoir 2 | Equiv. System | Store Index
Storage at Top of Dam | 100,000 | 100,000 | 200,000 | 5.0
Storage at Top FC | 90,000 | 60,000 | 150,000 | 4.0
Storage at Top of Con | 70,000 | 30,000 | 100,000 | 2.0
Con Zone % Storage Balance | 100.0% | 100.0% | 100.0% | 2.0
 | 70.0% | 33.0% | 58.9% | 1.0
 | 0.0% | 0.0% | 0.0% | 0.0
Con Zone Storages: | 70,000 | 30,000 | 100,000 | 2.0
 | 49,000 | 9,900 | 58,900 | 1.0
 | 0 | 0 | 0 | 0.0
Estimated Con Storage | 62,000 | 8,000 | 70,000 | 
Con Zone %full | 88.6% | 26.7% | 70.0% | 
Index Level | 1.62 | 0.81 | 1.27 | = Target Index
Target Storage | 54,672 | 15,328 | 70,000 | 
Storage Adjustment | -7,328 | 7,328 |  | 

## Slide 26: Explicit System Storage Balance

## Slide 27: Explicit System Storage Balance

## Slide 28: Explicit System Storage Balance
Explicit System Storage Balance is defined for specific zones
The %Storage desired for balance is defined
e.g. 70% in Res. 1 Con.
is balanced with
33% in Res. 2 Con.
System Storage
System Storage
Res1 Storage
Res2 Storage
Empty
Empty
Empty
Full
Full
Full
Con.
Con.
F.C.
F.C.
Sys
Con
Sys
F.C.
Estimated Storage
Desired Storage
Below Desired Storage
Above Desired Storage

## Slide 29: Explicit Reservoir system creation

## Slide 30: Defining an Explicit Storage Balance
Explicit System Storage Balance is defined using the Reservoir Systems Editor
Here, Flood Control Storage is Balanced with Adam 90% full & Adam RG 10%

## Slide 31: Defining an Explicit Storage Balance
Components of a System Storage Balance
  Reservoir System (set of reservoirs)
  System Storage Balance (similar in concept to an Operation Set for an individual reservoir)
  System Storage Zones
  Allocation of %Storage for each reservoir in the system

## Slide 32: Defining an Explicit Storage Balance
Procedure
  Create a Reservoir System and edit the set of reservoirs included in the system.
  Create a System Storage Balance, selecting one Operation Set from each of the reservoirs included in the system.
  Create one or more System Storage Zones based on existing Reservoir Storage Zones and enter %Storage in the balancing table. (%Storage defines how you want to balance)

## Slide 33: Defining an Explicit Storage Balance
Edit > Reservoir System (to open the Reservoir System Editor)
Create a New Reservoir System

## Slide 34: Defining an Explicit Storage Balance
Next, Edit the Reservoir Set
Select the reservoirs that will use the Explicit Storage Balance

## Slide 35: Defining an Explicit Storage Balance
Next, create a new System Storage Balance
  The System Storage balance is effectively the “operation set” of the system
Select an Operation Set for each reservoir in the system

## Slide 36: Defining an Explicit Storage Balance
Create System Storage Zones

## Slide 37: Defining an Explicit Storage Balance
Select the corresponding Reservoir Storage Zone for each reservoir

## Slide 38: Defining an Explicit Storage Balance
Fill out the balance table for each zone

## Slide 39: Storage Zone Balance Table
System Storage
System Storage
Res1 Storage
Res2 Storage
Empty
Empty
Empty
Full
Full
Full
Con.
Con.
Sys
Con
100
0
100
0
Reservoir
Res 1
Res 2
Zone
Con
Con
Balance
100
100
90
50
50
10
50% Con
10% Con
90% Con
50% Con

## Slide 40: Applying…an Explicit Storage Balance
In the ResSim Alternative Editor, select one of the defined System Storage Balance sets (or NONE) for each Reservoir System defined in the Network

## Slide 41: Review

## Slide 42: Review
Parallel System Operations are defined by adding Downstream Control Flow-Limit Rules to all reservoirs operating for a common downstream location
Tandem System Operations are defined by adding a Tandem Operating Rule to the upstream reservoir in a tandem pair
System Operating Rules are prioritized for each reservoir along with other operating rules

## Slide 43: Review
Parallel and Tandem operations rely on a System Storage Balance to allocate releases among reservoirs
By default, ResSim applies an Implicit System Storage Balance that balances all reservoirs toward their respective guide curves
You can define an Explicit System Storage Balance that balances reservoirs based on System Storage Zones
Apply an Explicit System Storage Balance by selecting it in the Alternative Editor