## Slide 1: Analysis of Results
HEC-ResSim Output Options
Notes: HEC-ResSim
Simulation Module – Use Output Options to:
1. Verify Compute Complete (no errors)
2. Analyze Results (tabular and graphical)
3. Reasonable Operations?
4. Provide Evaluation Data & Reports

## Slide 2: Fundamental Questions
How do you review a simulation?
  Viewing Output
  Customizing Output
  Calibration v. Verification
    Testing different scenarios – “Trials”
How do you determine if one alternative is better than another?

## Slide 3: Reviewing Results
Revisit Purpose of Model
  Considerations such as Flood Damage Reduction, Water Supply, Environmental, Hydroelectric
Calibration
  Adjusting model parameters to match observed
Refinement
  Adjusting model parameters to produce desired operation
  Trials-Testing Different Scenarios
Verification
  Ascertaining that a model produces desired behavior/results under a variety of expected conditions

## Slide 4: ResSim Compute Complete …
CONGRATULATIONS !!!
Now What?…
Evaluate the simulation
Notes: Are the computational results “correct”? Just because you have a Successful Compute, that’s not necessarily an indication that the results are what you expected. Did the reservoir operations follow the rules that you input? If so, “great job” (by you and the program). If not, why not? More often than not, something unexpected occurs. The tabular and graphical tools in ResSim are intended to assist you in deciding if the results are “reasonable” (“not perfect”, since that would be unrealistic for “real” reservoir operation).

## Slide 5: ResSim Output Options
Informative Text
  Simulation Compute Window
  Compute Log for Alternatives
Summary Reports
  Basic Statistics
  Release Decisions
Time Series
  Plots
  Tables

## Slide 6: Compute Window
Notes: The Compute window provides Message Output that contains information regarding the status of each step of the computation process. The Progress Bar indicates the percentage of completion for each step. When the computation is finished, the Progress Bar is completely filled in and reads "100%" along with the message "Compute Complete" in the Message Bar of the Compute window.
If there are errors or any problems during the execution process, you can review the Message Output Text area of the compute window. The Compute Log can also provide information regarding any errors.

## Slide 7: Compute Report (or Log)
Notes: Can access Compute Reports from the Reports Menu.
Only Alternatives that have a checkmark to the left of the alternative name in the simulation tree will appear in the list for viewing Compute Reports. These checkmarks indicate the alternatives that you are interested in viewing results for.

## Slide 8: Compute Report (or Log)
Notes: If there are errors or any problems during the computation process, the Compute Log can provide information regarding the type of problem that exists. To view Compute Logs, select Compute from the Reports menu, then select the appropriate Alternative.
Only Alternatives that have a checkmark to the left of the alternative name in the simulation tree will appear in the list for viewing Compute Reports. These checkmarks indicate the alternatives that you are interested in viewing results for.

## Slide 9: Compute Information
Details of Compute
Verify
  Successful completion of Compute
  No Errors or Warnings
  No Exceptions
  Correct Time Window, No time-blocking
  Time Series data loaded correctly
  Proper routing window
  Proper number of passes
Notes: Compute Passes—Each time ResSim computes through the time window is referred to as a "pass". Each time you tell ResSim to compute an alternative it will perform at least two passes—the idea is that it can use the results from a prior pass to improve the results of the current pass. The option to set the Minimum Number of Compute Passes is provided to let you determine if a greater number of passes should be computed than what ResSim will do by default.

## Slide 10: Summary Reports: Reservoirs
Basic Statistics of Reservoir Parameters
  Average
  Maximum
  Minimum

## Slide 11: Summary Reports: Flows
Notes: Basic Statistics for All Locations
  Reservoirs
  Junctions
  Reaches
Flow Types
  Regulated
  Unregulated
  Cumulative Local

## Slide 12: Release Decision Report

## Slide 13: Release Decision Report
  Initial Conditions
  Active Zone
  Release “Rules”
    Objective
    Constraint
  Date & Time
  EOP Elevation
  Net Inflow
  Total Release
  Releases per Outlet

## Slide 14: Time Series Output
HEC-ResSim
  Plots & Tables
    Pre-defined (Default)
    User Defined
HEC-DSSVue
  Plots
  Tables
  Computations

## Slide 15: Pre-defined (Default) Plots
Select Location
Select “Plot” from Location Context Menu

## Slide 16: Default Reservoir Plot
Viewports
  Elevation
    Zones
    Computed Elev
  Flow
    Inflow
    Outflow
Start Time Marker
Pointer & Zoom Tools
Menu Edit  Edit Properties

## Slide 17: Default Junction Plot
Verification of Routing Criteria
  Inflow to Reach from upstream
  Local Flow
  Outflow
Inflow + Local = Outflow

## Slide 18: Plot Properties
Context Menu
  Edit Properties
  Callouts
File Menu
  Tabulate
  Save Template
  Apply Template
Edit Menu
  Plot Properties
  Default Line Styles
Plot Menu
  User Defined Plots

## Slide 19: Plot Menu: Select Variables
User Defined Plots
  Variables
  Region
  Axis
    Unit dependent
    Reversible
Notes: The Available Variables list shows the variables you can choose for your User Defined Plot. The Selected list shows variables you have selected.
To add variables to your User Defined Plot:
Click on the variable in the Available Variables list, then click on the appropriate Plot Region or component in the Selected list. This allows you to specify where you want variables to appear in your plot.
Click Add to add the variable you have chosen to the Selected list. If the added variable reflects different units, a separate Y-axis will be automatically added.
To remove a variable, click on its name in the Selected list then click Remove.
You can also Move a Plot Region up or down or Remove it by right-clicking on the plot region name and choosing the action desired from the context menu.

## Slide 20: Plot Menu: Open & Save Plot Type
Save Plot Type
Name of Plot
  All Watersheds, or
  Current Watershed
Open Plot Type

## Slide 21: Select and Display User-Defined Plots
Context Menu
  User Plots
    Select Your Plot
    View Your Plot

## Slide 22: Tabulating Time Series Results
FileTabulate from a plot’s Menu bar

## Slide 23: Options for Time Series Tables
File Menu Print & Plot | Edit Menu Clipboard Copy/Paste | View Menu Format Columns

## Slide 24: HEC-DSSVue
Tools Menu – HEC-DssVue
  Plots
  Tables
  Utilities
    Math Functions
    Statistics

## Slide 25: Math Functions: Arithmetic & General

## Slide 26: Math Functions: Time Functions & Hydrologic

## Slide 27: Math Functions: Smoothing & Statistics

## Slide 28: Analysis of Results for Studies

## Slide 29: Reservoir Operations Studies Metrics
Ultimately need to translate reservoir operations into impacts on the watershed!
FRM Impacts:
  May only need to simulate FRM
Other impacts often require continuous simulation
  Water Supply and Irrigation
  Hydropower
  Ecosystem
  Navigation
Notes: Ultimately need to translate reservoir operations into impacts on the watershed
No one cares about flow in the river! They care about what the flow (or change in flow) or the stage means for other things!
Analysis for other impacts beyond FRM often requires continuous simulation
Individual flood events
“Period of Record” compute
Monte Carlo compute
Synthetic Hydrology or synthetic streamflow records
Look at the two photos – what happens at the dam? What is ResSim modeling that might be important to other resources?
At the dam? Backwater stage behind the dam, hydropower plant, spill -> ecosystem, spill-> wear on components
Downstream? Loading on levees, water to the community and agriculture, recreation along the river, boating
Photos are Bluestone Dam (LRH) and levees near sacramento

## Slide 30: Coordinate with your PDT!
Reservoir modeling isn’t done in a vacuum! Expect to pass hydrologic results to other PDT members.
  For example: handing of boundary conditions to HEC-RAS!
Always review the metrics and information needed by other PDT members, and make sure your model is capable of producing meaningful results! Or communicate the model’s limits!
Notes: HEC, PR-21,1993 - Section 4.4.2 Measure of Performance (Page 34 of the pdf document)
“Columbia River Reservoir System Analysis,” report proposed four indices:
  Penalty, or Value – Impact to the Watershed
  Reliability
  Resiliency
  Vulnerability
  Robustness
  (see hidden slide for definitions)
Penalty is the raw economic impact derived from the economic and non-economic penalty functions used in HEC-PRM.
Reliability is the frequency that performance fails to meet a particular purposes' target.
Resiliency is a measure of a system's ability to recover from failure. The resiliency index used here is the number of recoveries divided by the number of failing months, expressed as a percent.
Vulnerability indicates the magnitude of typical failures, when they occur. Here, the average deviation from a performance target is used.
Analysis for other impacts beyond FRM often requires continuous simulation
Individual flood events
“Period of Record” compute
Monte Carlo compute
Synthetic Hydrology or synthetic streamflow records

## Slide 31: Economic Value from Reservoirs
Value or Penalty is the economic impact from the operation
  Flood-damage reduction = Damage without – with project operation
  Power benefits = Capacity value + Energy generated
  Difficult to put economic value on many objectives!
    Navigation? Goods moved by barge vs rail vs road?
    Value of ecosystem benefits?
    Recreation impacts?

## Slide 32: Reliability, Resilience, Vulnerability, Robustness
Reliability is the frequency that performance is able to meet a particular purpose's target.
  A reliability of 100% implies that the monthly target is always met.
  In simulation, instances of failure to meet target (shortages) imply a reliability less than 100%.
Resiliency is a measure of a system’s ability to recover from failure.
  A resiliency index was defined as the number of recoveries divided by the number of failing months.
  Resiliency of 100% implies that the system always recovers, that is the system does not fail to meet a target in two successive months.
Vulnerability indicates the magnitude of typical failures.
  The deviation is the difference between the target (e.g., diversion schedule) and the actual value.
  For storage, the average difference between the guide curve and the simulated pool elevation could be an indicator of vulnerability.
  The smaller the average the better, if the guide curve is the ideal.
Robustness – the ability of a reservoir operation to handle a bad forecast
  An alternative that handles a bad forecast better might be better than an alternative that has better performance elsewhere.
  Research is ongoing into how to define this; no policy guidance to give you here.
Notes: HEC, PR-21,1993 - Section 4.4.2 Measure of Performance (Page 34 of the pdf document)
“Columbia River Reservoir System Analysis,” report proposed four indices:
  Penalty, or Value – Impact to the Watershed
  Reliability
  Resiliency
  Vulnerability
  Robustness
Penalty is the raw economic impact derived from the economic and non-economic penalty functions used in HEC-PRM.
Reliability is the frequency that performance fails to meet a particular purposes' target.
Resiliency is a measure of a system's ability to recover from failure. The resiliency index used here is the number of recoveries divided by the number of failing months, expressed as a percent.
Vulnerability indicates the magnitude of typical failures, when they occur. Here, the average deviation from a performance target is used.

## Slide 33: Flow Frequency Curves
Notes: Flow frequency curves use the peak (or volume-over-duration) plotted as a statistical distribution, one value at a time.
Other ways to summarize metrics : peaks over threshold
Flow Frequency Analysis and Statistical Hydrology PROSPECT courses
HEC-SSP software
Other ways to analyze these
Require running many individual flood events or a period of record

## Slide 34: Statistical: Flow-Duration Curve
Water Years 1920-2018
Notes: Flow-duration for natural & regulated flow shows impact of regulation.
Seasonal duration shown for critical months of operation.
Percent chance of exceeding flow during season

## Slide 35: Statistical: Pool Elevation-Duration
Chart: Reservoir Elevation Duration
| 0.1 | 0.2 | 0.5 | 1 | 2 | 5 | 10 | 15 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 85 | 90 | 95 | 98 | 99 | 99.5 | 99.8 | 99.9
Elev | 1675.4 | 1673.9 | 1672.4 | 1671.6 | 1671.1 | 1670.7 | 1670.4 | 1669.8 | 1668 | 1664 | 1660 | 1655.7 | 1651 | 1650.5 | 1649 | 1646 | 1641.9 | 1635.5 | 1631.7 | 1629 | 1628.4 | 1627 | 1626.4
The Annual Pool Elevation-Duration for a reservoir provides a summary indicating the percent chance the pool is at or above an elevation during the year.

## Slide 36: Low-Flow Frequency
e.g., there is a 55% chance of a 1-day flow not exceeding 1.0 cfs in the year.

## Slide 37: Analysis of Results… HEC-ResSim Output Options
Questions?…

## Slide 38: User Defined Reports
ReportsUser Reports from Menu bar

## Slide 39: User Report Editor…Creating a Report Template
Notes: Use File menu to create a New report – Give it a name and description
The Report Header/Footer tab contains the Title block, Report Header block, and Report Footer block. The header and footer on this tab are for the overall report, not the printed pages of the report document. The title, header, and footer blocks are TEXT fields that can include the following special codes:
%R – run name
%A – alternative name
%N – network name
%L – lookback time
%B – simulation time
%E – end time
%V – build version
(yes, the case DOES matter – the codes are all UPPER CASE)
The text can be formatted with different font types and sizes. The text in the title block gets CENTER justified. The text in the header and footer blocks gets left justified.

## Slide 40: User Report Editor…Defining a Report Block
A report can have multiple tables.
Each table in a Report is a Report Block
Use the Edit button to define the contents of a table
Use the Add button to append more tables to your report.
Notes: More than one table can be placed in the report. These are called Report Blocks.
To add a table to the report, use the Add button to add a row to the Report blocks list.
To configure a table, select the report block in the list and press its Edit button.
The Label field is editable. Use it to give a title to the report block. The column headers field is not editable; it will fill with information from the data to place in the table when you Edit or configure the report block

## Slide 41: User Report Editor…Defining a Report Block
Options
Report Header/Footer
Page Header/Footer
Notes: More than one table can be placed in the report. These are called Report Blocks.
To add a table to the report, use the Add button to add a row to the Report blocks list.
To configure a table, select the report block in the list and press its Edit button.
The Label field is editable. Use it to give a title to the report block. The column headers field is not editable; it will fill with information from the data to place in the table when you Edit or configure the report block

## Slide 42: Editing a Report Block…Adding Columns
Select a Time Series
Add to Report Columns
Use Append to add a blank column for math operations

## Slide 43: Editing a Report Block…More About Columns
EOP=End of Period
SOP=Start of Period
PAVG=Period Average
PCUM=Period Cumulative
Notes: The Report Contents Selection editor is used to configure a report block. The basic idea here is to identify the data to place in the columns of the table or report block. The upper half of the editor is a model data browser (very much like the DSS browser except it you only get two fields, the location or “b part” and the parameter or “c part”. There are no other “parts” or filters to identify because the report builder only works on the currently active alternative in the current simulation so – the time window (d part), time step (e part), and alternative id (f part) are “known” (the a part is not used). Use the filters and the scroll bar to locate the time series that you want to include in the report block. When you find one, select it and press the Add to Report Columns button.
The selected time series will appear in the lower half of the editor. It will be identified by a column number and a default header will appear in the Column Header field. If you don’t like the Header that the program used, delete it and type in a new one. The code %S can be used to get the units of the data displayed in the column header of the table.

## Slide 44: New Columns Using Simple Math
Summary Statistics (Will list at End of Your Report):
  Maximum
  Time Maximum Occurred
  Minimum
  Time Minimum Occurred
  Average
  Sum
  Count

## Slide 45: Editing a Report Block… Column Options
Convert Units to (Units Multiplier)
Hidden Column
Notes: Interval Option – what does the data for each entry in the column represent?
SOP Start of Period
EOP End of Period
PAVG Period Average
PCUM Period Cumulative
Num. Decimal Places – how many digits after the decimal should be displayed?
Units Multiplier
1 – standard compute units: e.g. acre-ft
1000 – (the data is divided by 1000) e.g. Thousand acre-ft
1000000 – (data /1000000) e.g. Million acre-ft
Hidden Column – check this to keep this column from displaying
Value Range Limits – use this to truncate the data. E.g.: If you have negative values but you don’t want them displayed, put a zero in the Minimum box.
Summary Statistics – check the type of information you want added at the bottom of the column. See next slide for an example.

## Slide 46: Editing a Report Block…Column Summary Statistics
Notes: I checked Maximum, Average, and Sum for the Summary Statistics I wanted at each column.

## Slide 47: Report Options…The Defaults
Notes: Reporting Interval
  Each Step – produce a row in the report for each compute interval of the simulation
  Daily
  Weekly
  Monthly
  Yearly
The relevant entries below become active for each of the above four options
  Reporting Hour of Day
    Say you picked Daily - At what hour should it report? (what is the “end” of the day?)
  Day of Week
    Say you picked Weekly – At what day of the week should it report?
  Day of Month
  Month (of the year)
Minimum Column Width - this is in pixels
Date/Time Column
  Display Start of Period
Endo of Period
  or Both
  Should it include a label for the Day of the Week?
Report Size and Location
  This is pretty nit picky stuff – ignore it for now.
Table Font
  This should probably say Report Font or just Font. Use this to change the font style you want to be used in your report.

## Slide 48: Report Options…Changing a few
Notes: I picked:
Daily interval (the compute interval was hourly)
Report at 2400 (the end of the clock day)
Show the Day of Week

## Slide 49: Report Title…Page Headers & Footers…
Page Number and Date Buttons
Other useful codes:
%R – run name
%A – alternative name
%N – network name
%L – lookback time
%B – simulation time
%E – end time
%V – build version
Notes: Tables 14.1 and 14.2 in the Users Manual specify the available codes and their purposes.
The Report Header/Footer tab contains the Title block, Report Header block, and Report Footer block. The header and footer on this tab are for the overall report, not the printed pages of the report document. The title, header, and footer blocks are TEXT fields that can include the following special codes:
%R – run name
%A – alternative name
%N – network name
%L – lookback time
%B – simulation time
%E – end time
%V – build version
(yes, the case DOES matter – the codes are all UPPER CASE)
The text can be formatted with different font types and sizes. The text in the title block gets CENTER justified. The text in the header and footer blocks gets left justified.
The Page Header and Footer are only used when the report is printed.
The special codes I added in this example using the buttons:
%d - the date the report was printed
%p – the page number
%n – the number of pages