## Slide 1: If-Then-Else Blocks
Adding Conditional Logic to the HEC-ResSim Operation Scheme
Notes: Conditional logic can be added directly to the rule stack using “If Blocks”

## Slide 2: Need for IF-THEN-ELSE logic
Typically, reservoir operations follow conditional paths for decision-making
Conditions are used to determine the applicability of operational goals and constraints
Using the ResSim “IF-block” feature, you can define conditional tests that determine when and which rules apply in the release decision process.
Reservoir Elevation > 610 ft?
In Flood Control Space?
Max Release Constraint
New Release = Max Inflow
Flooding Downstream?
Yes
Yes
No
Hydropower Release
No
Yes
Min Release Constraint
No
Notes: Clear need for conditional statements in reservoir operation

## Slide 3: “IF Blocks” – Conditional Logic in HEC-ResSim
Conditional statements can be used with operation rules by adding IF Blocks to the rule stack.
{ } IF_Block: The top level describes the overall block
 Clauses: IF, ELSE IF, ELSE
Implied THEN: nest rules under the clauses
Notes: IF Blocks are used within the rule stack to add conditional logic around the rules.
The top level demarks the
Here is an example
IF
ELSE IF
ELSE

## Slide 4: Parts of an IF Block
IF Block Name
{ } IF Block
Conditional Expressions:
 Clauses: IF, ELSE IF, ELSE
(implied THEN): Rules
IF and ELSE IF Clauses require a Boolean Conditional Test:
IF (Value 1 operator Test Value 2)
Operator: =, >, >=,
Notes: IF Blocks are used within the rule stack to add conditional logic around the rules.
The top level demarks the
Here is an example
IF
ELSE IF
ELSE

## Slide 5: Parts of an IF Block
{ } IF_Block: Name
  Conditional Expression made up of clauses
   Clauses: IF, ELSE IF, ELSE IF (Value 1 operator Test Value 2)
    (implied THEN): Rules
IF Block Name
{ } IF Block
Conditional Expressions
Notes: IF Blocks are used within the rule stack to add conditional logic around the rules.
The top level demarks the
Here is an example
IF
ELSE IF
ELSE

## Slide 6: Ways of Applying IF Blocks
Simple If-Then
  basic IF-THEN statement
  ELSE is optional
Compound Conditional
  e.g., If ((x AND y) OR (z)) Then
  use parentheses and
  logical operators
Nested Conditionals
  If blocks can be nested within higher level if blocks. e.g.,
  If (x) Then
  If (y) Then
  Rule
Notes: The IF Block feature allows conditional statements that can be
Simple If – then
Compound – if x and if y or z
Nested – nest a secondary test within the first test

## Slide 7: How to…Create an IF Block
From the Operations tab of the Reservoir editor, select a zone in your current operation set
Right-click on the zone in the tree and Select Add IF Block…
Under the IF_Block menu, click New
Give the IF Block a name..

## Slide 8: Naming the IF Clause

## Slide 9: Add Condition(s)
Constant -> numeric value
Date/Time -> ddmmmyyyy, hh:mm
Current Time Step
Time Series ->
  External Variable
  Model Variable
  State Variable
Seasonal -> ddmmm
( ) -> group conditional tests

## Slide 10: Test Values – Time Series

## Slide 11: Test Operators

## Slide 12: Add rules to the IF block

## Slide 13: Add ELSE IF blocks

## Slide 14: Add ELSE blocks

## Slide 15: Nested If blocks

## Slide 16: Duplicate If Blocks

## Slide 17: Duplicate If Blocks, cont’d.

## Slide 18: Duplicate If-Blocks, cont’d.

## Slide 19: Complex Example