## Slide 1: Implementing Operation Sets Part 1
Assessing Operational Plans
Adding Operational Rules:
Rate of Change & Release Function Rules

## Slide 2: Implementing Operation Sets Part 1 Outline
Recap of Operations for Guide Curve & Physical Constraints
Considering Operational Objectives & Constraints
  Where/how to find operational constraints for a reservoir
    Identify the Operation Plan
    Identify the Zones and Rules
How to input operational rules in HEC-ResSim
  Creating Operation Sets
  Creating basic at-site Rules
    Rate of change rules
    Release rules

## Slide 3: How To…Create an Operation Set
In the Reservoir editor, select the Operations tab
From the Operations menu, select New.
Give it a name and description and click OK.
Notes: From prior presentation

## Slide 4: How To…Create Zones
Three default zones are created with each new operation set
Add more zones by selecting New from the Zone menu.
Enter the Top of Zone curve in the table.

## Slide 5: Prior to Adding Rules, ResSim Operations are based on:
physical release constraint
Notes: Results from prior presentation
Physical Properties - Pool
Physical Properties – Dam & Outlets
Operations – Zones
Results – showing Guide Curve operations & physical constraints only.

## Slide 6: Operational Constraints
Notes: Images reflect - Hydropower, water quality, fish & wildlife, flood risk reduction
Operational objectives and constraints

## Slide 7: Where to Find Operational Constraints

## Slide 8: Sources for Operational Constraints
Water Control Manual
  Best source for operational constraints for USACE reservoirs
No water control manual?
  Contact the operating agency
  Contact state water resources agency

## Slide 9: Pertinent Data
Become familiar with characteristics of the reservoir
Reservoir’s purpose and operating constraints
Keywords and phrases:
  Project Purposes
  Pool Levels
  Channel Capacity

## Slide 10: Table of Contents
Look at the table of Contents:
  Lists of Figures, Tables
  Plates and Exhibits
Keywords and phrases:
  Water Control Plan
  Instructions to Operators
  Operating Zones
  Operating Constraints
  Hydropower

## Slide 11: Water Control Plan
Read the plan CAREFULLY
Look for descriptions of requirements the reservoir must meet
Look for pool levels that will define your operating zones
Tables are great
  Some constraints are only mentioned in the text !

## Slide 12: Operational Constraints
Downstream Constraint (Maximum)
At-site Release Constraint (Maximum)
At-site Rate of Change Constraint (Increase/Decrease)

## Slide 13: Next, Convert to Operational Rules

## Slide 14: Turning Operating Objectives & Constraints into HEC-ResSim Operating Rules
Notes: Turning Operating Objectives & Constraints into HEC-ResSim Operating Rules

## Slide 15: Steps for Adding Operational Constraints
Use the Reservoir Editor Operations tab
Create Operation Set
Define Zones
Define Rules and add to appropriate Zones

## Slide 16: Create a New Operation Set
Operation Set: The set of zones and rules that describe a water control plan
  Instead of creating from scratch, use Duplicate…

## Slide 17: How to Create a Rule
Right click the Zone where you want to add the rule
    The rule will apply when the reservoir storage is in this Zone
Select Add New Rule… from the Rule Menu
1
2

## Slide 18: Creating a Rule: Release From
Select the reservoir element the rule will affect
  The pool (labeled as the reservoir itself)
  The dam
  An outlet group or a specific outlet
3
Notes: Next slides will depict options

## Slide 19
Pool
Dam
Inflow Junction
Outflow Junction
Reservoir
Dam Tailwater
Outlets
Elements of a ResSim Reservoir Element
Diverted Outlet

## Slide 20: Elements of a ResSim Reservoir Element
The Physical tab helps you visualize the elements within a reservoir

## Slide 21: Creating a Rule: Rule Type
Select the rule type
  Many different rule types to select
    Some elements can’t use certain rule types
    Drop down will update based on element
Finally, name the rule
4
5

## Slide 22: Rule Types
Rate of Change - Flow
Rate of Change - Elevation
Release Function
Downstream Control (covered in Part 2)
Tandem (covered in later lesson)
Induced Surcharge (covered in later lesson)
and more…

## Slide 23: Rate of Change Rules
Flow & Elevation

## Slide 24: Flow Rate of Change Rules
Evaluated instantaneously
Limits the rate of change (cfs/hr) of releases

## Slide 25: Interpolation Options
Step
Cubic
Linear
Notes: Shows different interpolation options for the relationship, although in this case we are looking at a relationship with respect to date, not a ROC

## Slide 26: Elevation Rate of Change Rules
Instantaneous or Period Average
Limits the rate of change (feet/hr) of reservoir elevation

## Slide 27: Release Function Rules
Release can be a Function of:
Date
Date & Time
Model Variable
External Variable
Scripted Variable
Notes: & soon additional types

## Slide 28: Release Function Rules
Set releases as a function of a variable
One of the most powerful and flexible rule types

## Slide 29: Function of: Date or Date & Time

## Slide 30: Function of: Model Variable
Makes releases based on a time series the model computes, or model input

## Slide 31: Function of: External Variable
Makes releases based on a user defined time series external to the model

## Slide 32: Additional Modifiers

## Slide 33: Period Average Limit
Period
  None
  Daily
  Weekly
Starting Day of Period
  For weekly only, set the start day of the week
Daily Pattern
  Acts as a weighting pattern for meeting the flow requirement
Sets the rule to meet a target averaged over a period

## Slide 34: Hour of Day & Day of Week Multipliers
Applies a multiplier to the release for specific days of the week, or hours of the day
  Can effectively turn off a rule with a 0.0 multiplier

## Slide 35: Rising/Falling Condition
Averaging Period
  Hours over which the condition will be determined
Tolerance
  The amount by which the beginning and end of the period can differ and still be considered constant
Sets the rule to only be applied during a rising or falling condition

## Slide 36: Seasonal Variation
Sets the rule to behave differently throughout the year
  Adds date columns to the existing tables
  Obviously, won’t work with a function of date rule

## Slide 37: Take-home Points
A reservoir’s Water Control Manual (or similar) can provide most of the information needed to model the reservoir operations
  Where else can you go for information on reservoir operations?
At-Site Rules limit the reservoir release explicitly
  What’s the difference between a physical constraint and an operational one?
Release Function Rules can be used to describe a vast array of operational constraints.
  Channel Capacity
  Water Supply
  Environmental Support
  Explicit (Specified) Releases
  Etc.

## Slide 38: Definitions
Physical Constraint – Outlet maximum discharge capacity and rate of increase or decrease constraints
Operational Constraint – A regulation. A requirement defined in the Water Control Plan. A limit on the release.
At-Site Constraint – An operational constraint specified for the reservoir itself or one of its outlets; not a downstream constraint.
Notes: At-site constraint in comparison with downstream.

## Slide 39: More Definitions
Operational Zone – A portion or range of the reservoir pool for which certain constraints have been specified.
Operation Rule – The ResSim data input form used to specify an operational constraint so that the constraint can be simulated.
Operation Set – The set of zones and rules the describe a water control plan
Rule Types – The specific kinds of rules that you can define with ResSim