## Slide 1: Implementing Operation Sets Part 2
Release Allocation, IF Blocks, Downstream Control Rules, Prioritizing Rules

## Slide 2: Implementing Operation Sets Part 2 Outline
Additional Operational Settings & Rules
Release Allocation
IF Blocks (Nesting rules in Conditional Statements)
Downstream Control Rules
Combining and Prioritizing Rules

## Slide 3: Release Allocation
Defined & Explained
How to use Release Allocation

## Slide 4: Release Allocation
What is Release Allocation?
    Which outlets should release first, next, and so on
    Balanced (weighted) approach
      Evenly weighted (e.g., 50:50 split (default))
      Unevenly weighted (e.g. 60:40 split)
    Sequential approach
    Stepped approach
Hydropower reservoirs often direct any release to the power plant first
Other outlets release water when the power plant reaches capacity
Release Allocation is an Operations setting
  Define the priority (or order) to the available outlets

## Slide 5: Specifying a Release Allocation
Operations Tab in Reservoir Editor
  Use Specified Release Allocation
  Specify Allocation Type
    Sequential
      Specify the component order
    Balanced
      Specify the component weighting
    Stepped
      Specify the release capacity balance
Always Active in v3.3
Notes: This is always turned on (no option) in v3.3

## Slide 6: IF Blocks
Making Rules Conditional with IF-THEN-ELSE
Conditional nature of operations
IF Blocks in HEC-ResSim
How to use IF Blocks in HEC-ResSim
Notes: Add conditional logic

## Slide 7: Need for IF-THEN-ELSE logic
Typically, reservoir operations follow conditional paths for decision-making
Conditions are used to determine the applicability of operational goals and constraints
Using the ResSim IF Block feature, you can define conditional tests that determine when and which rules apply in the release decision process.
Reservoir Elevation > 610 ft?
In Flood Control Space?
Max Release Constraint
New Release = Max Inflow
Flooding Downstream?
Yes
Yes
No
Hydropower Release
No
Yes
Min Release Constraint
No

## Slide 8: IF-THEN-ELSE in HEC-ResSim
Simple IF statement
  IF Block can be very simple, with a single conditional test
Compound conditional test
  using parentheses and logical operators
Nested IF statement
  A nested if is an if statement that is the target of another if statement

## Slide 9: How to…Create an IF Block
Operations tab of the Reservoir Editor, select a zone in your current operation set
Right-click on the zone in the tree and Select Add IF Block…
Under the IF_Block menu Click New
Name & Describe the IF Block…

## Slide 10: Naming & Describing IF Blocks

## Slide 11: IF Blocks: Adding Conditions
Constant -> numeric value
Date/Time -> ddmmmyyyy, hh:mm
Current Time Step
Time Series ->
  External Variable
  Model Variable
  State Variable
Seasonal -> ddmmm
( ) -> group conditional tests

## Slide 12: IF Block Test Values – Time Series

## Slide 13: IF Block Test Operators

## Slide 14: Adding rules to the IF Block

## Slide 15: Appending ELSE IF Statements

## Slide 16: Appending ELSE Conditions

## Slide 17: Nested IF Blocks

## Slide 18: Duplicate IF Blocks

## Slide 19: Duplicate IF Blocks, cont’d.

## Slide 20: Duplicate IF Blocks, cont’d.

## Slide 21: Complex Example

## Slide 22: Downstream Control Rules

## Slide 23: Creating a Downstream Rule…
From the Operations tab of the Reservoir Editor, select a Zone in your current Operation Set
Right click on the zone and select Add New Rule
Or, from the Rule menu, select New.
Notes: From the Reservoir Editor Operations tab,
…Choose an Operation Set
…Select a zone

## Slide 24: Creating a Downstream Rule…
Select the Reservoir from the “Operates Release From” list.
Select Downstream Control Function from the “Rule Type” list.

## Slide 25: Creating a Downstream Rule…
The New Rule dialog changes - a new list is added…
Select the Downstream Location from the “Downstream Location” list.
Name the rule
Press OK.

## Slide 26: Creating a Downstream Rule…
Define the rule in the same way as for a Release Function rule…
Additional field: Parameter..
    Flow
    Stage
…if specifying stage, you must enter a flow/stage rating curve at the downstream location

## Slide 27: More about… Downstream Control Rules
A grey square appears around each control point
Network Module: if a downstream control rule exists (even if not used)
Simulation Module: if a downstream control is used in the current operation set of the active alternative
A downstream control rule defined at one reservoir can be assigned to other reservoirs upstream of the control point
Select Use Existing from Rule Menu

## Slide 28: Prioritizing rules

## Slide 29: Defining Rule Priority
Rule Priority:
the order in which rules are evaluated and applied to the “allowable range”
In HEC-ResSim, rules appear in each zone of the Operations Tree in order of their priority (highest priority is at the top of the list)
Priority can differ by zone…

## Slide 30: Rule Logic - revisited
Rules refine the allowable range of release…
Rule 3:
F > 12,500 downstream, need R > 10,000
Rule 2:
R < 9,000
Rule 1:
R > 1,000
Max physical capacity
Release
0
allowable range
above guide curve
below guide curve
allowable range
1000
Rule 3 violated, but gets as close as possible
9000
allowable range
1000
9000
Notes: Rule 1 Minimum release of 1000 cfs
Rule 2 Maximum release of 9000 cfs
Rule 3 Minimum downstream flow of 12,500 cfs -> translates to min 10,000 release at reservoir

## Slide 31: Rule Logic - revisited
What if the rules were re-ordered?
Right-click on rule

## Slide 32: Rule Logic - revisited
What if the rules were re-ordered?
Rule 1:
F > 12,500 downstream, need R > 10,000
Rule 3:
R < 9,000
Rule 2:
R > 1,000
Max physical capacity
Release
0
allowable range
above guide curve
below guide curve
allowable range
10000
allowable range
10000
1000
Rule 3 violated, but gets as close as possible
10000
9000
Notes: Rule 3 is now Rule 1: Minimum downstream flow of 12,500 cfs -> translates to min 10,000 release at reservoir
Rule 2: Minimum release of 1000 cfs
Rule 3: Maximum release of 9000 cfs

## Slide 33: Take-home Points
Define the Release Allocation to express how releases will be distributed among outlets
The conditional application of operating rules can be accomplished using IF Blocks
Downstream Control Rules can be used to operate for conditions at a downstream location.
Rules are prioritized based on their position in each zone’s rule stack.