## Slide 1: HEC-RAS for CWMS
Andy Richter, P.E., PMP
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Objective
Identify basic concepts of using HEC-RAS in CWMS

## Slide 3: Outline
Purpose of Hydraulic Modeling in CWMS
HEC-RAS Capabilities Overview
HEC-RAS Program Essentials
HEC-RAS Model Development for Real-Time Forecasting
HEC-RAS CAVI Integration
Real-Time Forecasting using HEC-RAS

## Slide 4: HEC-RAS in sequence
Meteorological Processor (HEC-MetVue)
  Process meteorological data
  Provide input to the hydrologic model
Hydrologic Model (HEC-HMS)
  Transform precip, forecast flows
  Provide input for the reservoir and hydraulics models
Reservoir Simulation Model (HEC-ResSim)
  Determine reservoir system release decisions
  Provide input for the hydraulics model
Hydraulic Model (HEC-RAS)
  Determine stage and flood inundation
  Provide flow input for the flood impact model
Flood Impact Analysis (HEC-FIA)
  Estimate the economic and life loss consequences
  Report where action is required during high stages

## Slide 5: Purpose of Hydraulic modeling in CWMS

## Slide 6: Purpose of hydraulic modeling in CWMS
Predict critical and peak water surface elevations
Predict timing, depth, and extent of potential inundation

## Slide 7: Hydraulic Model Results
HEC-RAS results inform:
  Emergency management decisions
  Flood operations preparedness
  Post-flood impact analyses
When will the levee overtop?
Where are sandbags needed?
Will the road flood?
What areas need to evacuate, and when?
What were the consequences?

## Slide 8: HEC-RAS Capabilities overview

## Slide 9: HEC-RAS capabilities
1D Steady Flow Hydraulics
  Depth, velocity, and discharge treated as constant with respect to time
  Specify flowrates at all locations, compute stage
  Relies on hydrologic routing
1D Unsteady Flow Hydraulics
  Depth, velocity, and discharge change with respect to time
  Solves for flow and stage
  Computes hydraulic routing
2D Unsteady Flow Hydraulics
  Flow can vary in X and Y direction
  More detailed accounting of forces
https://www.hec.usace.army.mil/confluence/rasdocs

## Slide 10: HEC-RAS Program Essentials

## Slide 11: Components of an hec-RAS model
Project: *.prj
Plan: *.p##
Geometry: *.g##
US Flow : *.u##

## Slide 12: Geometry data
Cross Sections
Bridges and Culverts
Inline Structures (dams, weirs, spillways, etc.)
Lateral Structures (levees, storage area connections, etc.)
1D Storage Areas and 2D Flow Areas

## Slide 13: Terrain Data
Used to develop geometry data
  station/elevation data for cross sections, lateral structures, bridges, etc.
  elevation/storage curves for 1D storage areas
  computational mesh for 2D flow areas

## Slide 14: Boundary conditions
HEC-RAS needs boundary conditions (stored in the flow files)
  HEC-HMS flows
  HEC-ResSim outflows
  Observed/Forecasted data (tidal gages, NOAA/NWS, etc.)
  Output from other CWMS HEC-RAS models
  Rating Curves
  Normal Depth

## Slide 15: Inflow hydrographs

## Slide 16: Plan file
The Plan File controls the simulation
Combines a Geometry File with a Flow File
Sets the Time Window
Defines the Computation Options and Output Options
Becomes the HEC-RAS Model Alternative when imported into the CAVI

## Slide 17: Plan File

## Slide 18: HEC-RAS Mapper

## Slide 19: Dynamic Maps - animations

## Slide 20: Stored maps
Export results to GeoTiff raster file on disc
Allows HEC-RAS to pass results to other applications
  GIS for inundation maps
  HEC-FIA for consequences or flood damages reduced

## Slide 21: Model development for real-time forecasting

## Slide 22: Boundary conditions within HEC-RAS

## Slide 23: Model Calibration
Calibrate model to historic events
  Observed Stages/Flows
  Rating Curves
  Adjusting model parameters (Manning’s “n” values, ineffective flow areas, etc.)
Use HEC-RAS Mapper
  Compare model output to aerial photography
  Look for problems with inundated areas (abrupt cutoffs, missing areas, etc.)

## Slide 24: Stress testing
Why stress test our models?
  Ensure model stability at a variety of conditions
    High Flows
    Low Flows
    Levee Breaches

## Slide 25: Steady Flow Plan
Create a steady flow plan that can be used as a backup to the unsteady flow plan*
Consider steady flow limitations
not applicable when model has 2D elements

## Slide 26: Linking boundary Conditions in CAVI
Location/Parameter

## Slide 27: HEC-RAS CAVI Integration

## Slide 28: CAVI integration steps
Import HEC-RAS Project
Configure HEC-RAS Mapper
  Copy additional data (terrain and local HEC-DSS data)
  Create saved depth grid map
Run standalone simulation from base model (Setup Tab)
Verify Model Linking in CAVI

## Slide 29: Import HEC-RAS model
Only ONE HEC-RAS Project can be imported
HEC-RAS plans become CAVI alternatives

## Slide 30: Configure HEC-RAS Mapper
HEC-RAS Mapper needs more data than the CAVI import provides
  Terrain data
  Projection file
Copy data into the watershed directory
Create Saved Map

## Slide 31: Run standalone HEC-RAS Simulation
Compute HEC-RAS model in Base Directory
Generate Saved Map
Essential for HEC-RAS to HEC-FIA model linking

## Slide 32: Verify model linking in CAvi

## Slide 33: Real-Time Forecasting using HEC-RAS

## Slide 34: Running a forecast
Check incoming data
Run HEC-MetVue, HEC-HMS, and HEC-ResSim alternatives
  Adjust/calibrate until you are “happy”
Run HEC-RAS
  Review results
  Calibrate
  Generate depth grids (if needed)

## Slide 35: HEC-RAS Calibration Process
Run HEC-RAS model alternative
Compare results with observed data (flow and stage)
Adjust model parameters
  Manning’s “n” values
  Ineffective flow areas
Repeat
RUN
COMPARE
ADJUST

## Slide 36: Comparing model Results to observed
Use Stage and Flow hydrograph plots to compare model outputs to observed data
Use Profile plots to review overall shape of water surface (look for anomalies)

## Slide 37: Adjusting model parameters

## Slide 38: Adjusting model parameters
Set up Flow Roughness Factors for sections of your model around observed data locations
Similar approach to Zones for HEC-HMS
Good way to quickly adjust Manning’s “n” values within large sections of your model
Still need to check and fully calibrate your model a few times a year (especially if the factors start diverging)

## Slide 39: Validating Results
You should review results prior to creating an inundation map
Common Instability Locations
  Bridges
  Junctions
  Inline Structures
  Slope Changes/Steep Reaches

## Slide 40: Inundation mapping best practices
Run HEC-RAS, check results & calibrate, then generate saved map
Do not check the “Floodplain Mapping” box in the Unsteady Flow Analysis Options
Get in the habit of checking the results before publishing the maps

## Slide 41: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams