## Slide 1: HEC-ResSim in CWMS
Russell Errett, P.E.
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
  Learn basic concepts of using HEC-ResSim in CWMS for making real-time reservoir operation decisions
  Introduction to HEC-ResSim
    What is ResSim?
    What can ResSim do?
    Why do we want it in CWMS?
  Integrating an HEC-ResSim model into CWMS
    A brief review of importing, linking, etc.
  Using HEC-ResSim for Real-Time Decision Making
    Data Considerations
    How real-time modeling differs from planning studies
    Regulation Schedule/Plan
    The OSI

## Slide 3: Introduction to HEC-ResSim

## Slide 4: What is HEC-ResSim?
  HEC-ResSim is a software program designed for simulating the operations of one or more reservoirs in a river system for a variety of operational goals and constraints.
Notes: Introduction to ResSim
  What is ResSim?
    HEC-ResSim is a software program designed for simulating the operations of one or more reservoirs in a river system for a variety of operational goals and constraints.
      The acronym “ResSim” stands for Reservoir Simulation.
      ResSim is designed for modeling reservoir operations. It can handle one reservoir or many.
      It can handle at-site operations or system operations.
      And, because it is rule-based, it can handle multiple objectives at once.
    ResSim simulates the reservoir operations timestep by timestep.
      It is NOT an optimization model, so it doesn’t look at the whole time window and try to determine an “optimal” release plan.

## Slide 5: What can HEC-ResSim do?
  It can determine the releases of one or more reservoirs for an observed, synthetic, or predicted flow event using a defined operation scheme and/or a prescribed release schedule.
  It uses mass-balance computations to determine the resulting pool elevation and storage for each reservoir.
  It can route and combine inflows and the determined releases through the modeled river system using hydrologic routing.
Notes: Introduction to ResSim
  What can ResSim do?
    ResSim performs a variety of computations for determining reservoir operations
    It can determine the releases of one or more reservoirs for an observed, synthetic, or predicted flow event using a defined operation scheme and/or a prescribed release schedule.
    It uses mass-balance computations to determine the resulting pool elevation and storage for each reservoir.
    It can route and combine inflows and the determine flows through the modeled river system using hydrologic routing.
    More Informally…
    ResSim makes release decisions on a time-step by time-step basis
      It uses a rule-based operation scheme to make the release decisions -or-
      It uses a prescribed release schedule (release overrides)
    It computes the ending pool elevation and storage, time-step by time-step
    It routes and combines flows through the river network.
      It uses hydrologic routing (as opposed to hydraulic routing)
      Although not as physically accurate as hydraulic routing, it is faster and provides needed information for many operational decisions

## Slide 6: The Reservoir Network
The HEC-ResSim schematic…
  Reservoirs
    Pool Definition
    Hierarchical Outlet Structure
    Operation Plans
  Junctions/Control Points
    Inflows
    Outflow
    Stage lookup
  Routing Reaches & Diversions
    Provide Connectivity
    Hydrologic Routing
Notes: Introduction to ResSim
  Reservoir Networks
    The ResSim Schematic…
      ResSim’s Reservoir Network – is the key element of the ResSim model. It describes the model schematic and contains the physical and operational data for each model element of the schematic, including:
      Reservoirs
        Reservoir pool and outlet definitions
        Reservoir Operation Plans (the rules, zones, allocation, etc)
      Junctions
        Inflows - Inflows into the river system are identified at the Junctions.
        Outflow - Junctions sum up inflows to produce a single outflow
        Stage Lookup - Junctions can also be provide a rating curve for looking up Stage from the computed Flow.
      Routing Reaches and Diversions
        Provide Connectivity
        Hydrologic Routing
          Routing reaches and diversions move water through the river network (from one junction to the next) using hydrologic routing.
          Diversions take water away from a junction in the network… and may optionally return it elsewhere in the network.
        This slide includes a screen shot of the Model Schematic from the ResSim Network Module. Describe the visual clues included in the map schematic…
        Inflow, Control Points, Diversion arrowheads (connectivity)

## Slide 7: Rule-Based Reservoir Operations
  Guide-Curve
    A Seasonal or Variable Target Pool Elevation
  Basic Guide Curve Operation
    “Within physical limits, get the reservoir pool elevation to guide curve as fast as possible.”
  Operating Zones
    Divide the storage pool into operational zones.
    A prioritized set of rules within each zone limits or overrides basic guide curve operation.
Notes: Introduction to ResSim
  Rule-based Reservoir Operations
    The ResSim operation scheme is defined by 4 fundamental elements:
    A Guide-Curve
      A seasonal or Variable Target Pool Elevation
      the target pool elevation (or storage) throughout the year – thus, a curve (or annually repeating pattern)
    Basic Guide Curve Operation
      “Within physical limits, get the reservoir pool elevation to guide curve as fast as possible.”
        i.e., get to the target pool elevation and stay there
    Operating Zones
      Divide the storage pool into operational zones.
      A prioritized set of rules within each zone limits the basic guide curve operation
      Different layers of the reservoir pool (storage) have different operating objectives. The guide curve naturally divides the pool into two primary zones – Flood Control and Conservation (reserved space vs reserved water).
      The different operating objectives are represented by different sets of operating rules placed in each zone…

## Slide 8: Rule-Based Reservoir Operations
The Rules
  Release Function – local (at-site) objectives
  Downstream Control Function – downstream objectives
  Rates of Change – on release or elevation
  Induced Surcharge - Emergency Gate Regulation
  Hydropower – local and system
  Pump Schedule
  Tandem
  Prescribed Release
  User-Scripted
Notes: Introduction to ResSim
  Rule-based Reservoir Operations
    Rules
      ResSim has a variety of predefined rule types including:
      Complex Local & Downstream Flow Objectives
      Release or Pool Elevation Rates of Change
      Emergency Gate Regulation (Induced Surcharge)
      Local and System Hydropower Requirements
      Pump Schedule
      Parallel and Tandem Reservoir Systems
      Prescribed Release
      User-Scripted release objectives

## Slide 9: Reservoir Editor
Notes: Introduction to ResSim
  ResSim’s Reservoir Editor – Operations tab
    This slide is a screen shot of the Reservoir Editor, Operations tab, Zone-Rules subtab. Describe the features of this tab…
    Zone-Rules tree
      Bold zone is the guide curve
      Italic zone is the Inactive Zone (a special zone below which the reservoir cannot “operationally” release water)
    The Edit Pane – changes with the selection in the tree
    The Menus – change with the selection of the Major Tab
    The other subtabs – additional modifiers on the operations

## Slide 10: Alternatives
  Reservoir Network Selection
  Run Control
    Alternative Type , Compute Timestep, Compute Options
  Operations
    Operation set per Reservoir, System Storage Balance
  Lookback
    Starting Conditions – Pool Elevation, Releases
  Time Series
    Local Inflows, Lookback Time Series, External Variables
Notes: Introduction to ResSim
  ResSim Alternatives
    Reservoir Network Selection
    Alternatives …are based on a Reservoir Network. And include:
    Run Control data
      Alternative Type – Standard, Ensemble, Monte Carlo, etc.
      Compute Timestep – 5min to 1 day, 1 hour is typical for real-time
      Compute Options – instantaneous vs period average, plus unreg and holdouts.
    Operations
      (Select an) Operation set per Reservoir
      (Select a) Storage Balance plan per Reservoir System
    Lookback - aka…Initial Conditions
      Elevation or Storage
      Releases per outlet, Diversion flow, state variables.
        Each conditions can be defined with a Constant or Time Series.
        In Real-time modeling, use of Time Series for these Initial Conditions wherever you have real-time observed data in the database
    Time Series
      Local Inflows
      Lookback Time Series
      External Variables needed for the operations

## Slide 11: Alternative Editor
Notes: Introduction to ResSim
  ResSim’s Alternative Editor
    This slide shows a screen shot of the ResSim Alternative editor at the Time-Series tab. Describe the features of this tab…
    Upper panel: Existing Alternative list – includes the Reservoir Network identification, which it is the foundation of the alternative
    Lower Panel: The selected alternative “editor” made up of several tabs for specifying the various aspects of the alternative. The first four are the most important:
      Run Control
      Operations
      Lookback
      Time-Series
      Although each of the tabs are important, the Time-Series tab has some aspects worth noting:
        The time series list includes several different types of required input based on the information specified in the network and on the Operations and Lookback tabs. These include:
        Known Flows
        Lookback Elevation, Lookback Release
        Input Time Series
        Others… (Lookback Diversion, Input Evap,…)
        Inflow Multipliers button – for increasing or decreasing the inflows globally or one by one.

## Slide 12: Simulation and Analysis
  Simulation
    a specified Time Window
    a set of alternatives to analyze
  Analysis Tools
    Context-sensitive Plots
    Release Decision Report
    Summary Reports
    Customized Plots
    User-defined Reports
    HEC-DSSVue
    The Operations Support Interface (OSI)
Notes: Introduction to ResSim
  Simulation and Analysis
    To compute and analyze the results of an alternative, the user must create a “simulation” (A ResSim concept) or “forecast” (the equivalent in CWMS).
    A Simulation or Forecast is specified by:
      a Time Window
      a set of alternatives to be computed and analyzed.
    Once an alternative has been computed, a variety of tools are available to analyze the results
    Analysis Tools
      Context-sensitive Plots
      Release Decision Report
      Summary Reports
      Customized Plots
      User-defined Reports
      HEC-DSSVue/CWMSVue

## Slide 13: HEC-ResSim’s Major Features
  Graphical System Schematic, tightly integrated with CWMS (and HEC-WAT)
  Hierarchical Outlet Structure
  Diversions and Diverted Outlets
  Release Allocation – Outlet Prioritization
  Zone-Based Prioritized Operation Rule Set
  Compute Intervals: 5min – 1day
  Customizable Plots and Reports
  Induced Surcharge Operation
  Scheduled Local & System Hydropower
  Tandem and Parallel System Operations
  Pump-back Storage Operation
  Conditional (If-then-else) Rule Activation
  User-Scripted Rules & State Variables
  Customizable Operations Support Interface (OSI)
Notes: Introduction to ResSim
  ResSim’s Major Features allow users to model a wide variety of situations
    Graphical System Schematic, tightly integrated with CWMS. Includes an active schematic that provides access to model editors and output, from both ResSim and the CWMS
    Hierarchical Outlet Structure. The benefits and limitations of this feature include:
      Ability to separate power releases from spillway or sluice gate releases
      Inability to operate to gates settings, ResSim is presently all about flow
    Diversions and Diverted Outlets.
      Diversions are from the river
      Diverted outlets are from the (reservoir) pool.
      Diversions are single minded. In other models, when using diversions at a reservoir, they take water away before the reservoir can decide what to do with it. Diverted outlets allow the modeler to prioritize and determine the pool diversions with the other reservoir releases.
    Release Allocation – Outlet Prioritization
      When the rules don’t care where the water is released from, the release allocation can take over.
    Zone-Based Prioritized Operation Rule Set
      The operation rules are specified per reservoir “zone”. This allows the rules/objectives to change depending on how full (or empty) the reservoir is.
    Compute Interval Range: 5min – 1day
      Typical intervals for real-time operation are 1hr, 6hr, or 1day. But really flashy systems may need 15 min or less. 6hr may be used when the operations are coordinated with the Weather Service forecast (which is usually published on a 6hr interval)
    Customizable Plots and Reports
      A standard set of plots and reports are available.
      But, the standard plots allow the user to customize what they want to see and then save their custom plot configuration for later use as a “User Plot”
      And, a report builder is available for creating customized tables of output in a generalized report format.

## Slide 14: HEC-ResSim’s Role in CWMS
Simulate Real-Time Reservoir Operations
  Much of a water manager’s function is to operate the district’s reservoirs. CWMS is intended to support that effort.
  CWMS, therefore, needed a modernized and integrated reservoir simulation model.
  To meet that need, HEC-ResSim was developed in parallel with CWMS and its design requirements were strongly influenced by the water management community.
  A good HEC-ResSim model for CWMS should provide the water manager a good first guess to use when determining the upcoming release schedule for their reservoirs.
Notes: Introduction to ResSim
  ResSim’s Major Features allow users to model a wide variety of situations
    Graphical System Schematic, tightly integrated with CWMS. Includes an active schematic that provides access to model editors and output, from both ResSim and the CWMS
    Hierarchical Outlet Structure. The benefits and limitations of this feature include:
      Ability to separate power releases from spillway or sluice gate releases
      Inability to operate to gates settings, ResSim is presently all about flow
    Diversions and Diverted Outlets.
      Diversions are from the river
      Diverted outlets are from the (reservoir) pool.
      Diversions are single minded. In other models, when using diversions at a reservoir, they take water away before the reservoir can decide what to do with it. Diverted outlets allow the modeler to prioritize and determine the pool diversions with the other reservoir releases.
    Release Allocation – Outlet Prioritization
      When the rules don’t care where the water is released from, the release allocation can take over.
    Zone-Based Prioritized Operation Rule Set
      The operation rules are specified per reservoir “zone”. This allows the rules/objectives to change depending on how full (or empty) the reservoir is.
    Compute Interval Range: 5min – 1day
      Typical intervals for real-time operation are 1hr, 6hr, or 1day. But really flashy systems may need 15 min or less. 6hr may be used when the operations are coordinated with the Weather Service forecast (which is usually published on a 6hr interval)
    Customizable Plots and Reports
      A standard set of plots and reports are available.
      But, the standard plots allow the user to customize what they want to see and then save their custom plot configuration for later use as a “User Plot”
      And, a report builder is available for creating customized tables of output in a generalized report format.

## Slide 15: Integrating an HEC-ResSim model into CWMS

## Slide 16: Watershed Setup - A Process…
Notes: Integrating a ResSim model into CWMS
  Watershed Setup – A Process
    This slide shows the Next Steps dialog. This dialog is displayed by the CAVI after you (first) create a new watershed. It is a reminder of the steps you need to take to assemble a watershed for use in CWMS…
    Import any additional models
    Define the Program Order
      Note: steps 1 & 2 are swappable. It may be more logical to specify the program order before importing the models.
    Assign Key Letters
    Create a Forecast Run. Assemble the model alternatives into a sequence. Only “lettered” alternatives can be used
    Model Linking. Establish the data flow between the models
    Configure the Extract Groups. Create the extract groups so that the data needed by your models will be available for the compute
    Setup your Post Lists decide what you want to store back to the database from your forecasts. Complete this after models are up and running smoothly
    Create a Forecast. The forecast will exercise the extract. Test the data and model linking by computing, correct any problems, retest…
    Save. Talk about saving here, even though the illustration doesn’t…
      Save to Base – either the forecast run or the individual models. This will ensure that any changes you made to get the forecast running are available for the next forecast.

## Slide 17: Importing Models
Notes: Integrating a ResSim model into CWMS
  Importing Models
    This slide shows the Models menu from the CAVI, the submenu under import, and the query dialog you will see when you select ResSim to import.
    Models Menu, Import… Each model in the Program Order should be in the imported if available, but… If ResSim is going to be used, Import the ResSim model FIRST.
        a ResSim watershed and a CWMS watershed share a common framework. Because of this, a CWMS watershed can (and should) be created from a ResSim watershed
        When a ResSim watershed is imported, the CWMS watershed gets the ResSim watershed’s maps, stream alignment, and configuration information as well as the ResSim model data – networks, alternatives, & simulations
    When Importing a ResSim model, you will be asked if you want to import just an alternative or a whole watershed.
      If the CWMS watershed does not yet have a ResSim model, pick Watershed.
      If you have already imported a ResSim watershed but want to add a new alternative or update an existing one from the original source watershed, pick Alternative.
      “from the original watershed” should be stressed here. This is because there are a number of foundational aspects of the watershed that should be consistent between the existing CWMS watershed and the ResSim watershed you are importing from. These include the configurations and a variety of overlapping files – especially networks.

## Slide 18: Importing… Watershed versus Alternative
Watershed
Everything from the watershed is brought in – no questions asked…
  Stream Alignment
  Configurations & Elements
  Networks
  Alternatives
  Simulations
  Maps
  HEC-DSS Files
  More
Only the Alternative and its network files are brought in
  No Stream Alignment
  No Configurations & Elements
A valid stream alignment must already exist in the watershed
  Importer tries to place network elements on the correct streams…
  …and tries to tie them to existing configuration elements.
Alternative
Notes: Integrating a ResSim model into CWMS
  Importing Watershed vs Alternative
    Watershed – everything is brought in from the standard folders of the watershed, no questions asked. This includes the:
      Stream Alignment
      Configurations and Schematic Elements (not so sure about this one..)
      Reservoir Networks
      Alternatives
      Simulations.
      Maps
      Shared folder – DSS files.
      HOWEVER, any additional folders you’ve added to the watershed may not be imported (copied) into the CWMS watershed so review new watershed carefully.
    Alternative – only the files associated with the alternative and its network are imported (copied) into the CWMS watershed.
      No Stream Alignment
      No Configurations
    The Alternative Importer tries to associate all network elements to their streams so a valid stream alignment must already be in the watershed.
    The importer also tries to associate the network with its configuration, so if the configurations are not already in the watershed, the links to the configuration elements will be broken; this is not a problem for CWMS, but may be of concern if the CWMS watershed is later used as the basis for a study model.

## Slide 19: Revising a ResSim Alternative for CWMS
Revise Lookback settings (Use Observed Data):
  For each reservoir…
    Set Lookback Elevation to Time Series
    Set Lookback Release to Time Series
      If time series do not exist for every outlet
        Set ONE Controlled Outlet to Time Series
        Set all other outlets to Constant - Set those constants to zero
    If time series does not exist or are not reliable for pool elevation and/or outflow, advanced options exist to estimate one or both variables
      Lookback Elevation:
        Set to Guide Curve
        Function of Release (needs an initial pool elevation to start)
          Start with Constant
          Start with Time Series
          Start with Guide Curve
      Lookback Release
        Function of Elevation
Notes: Integrating a ResSim Model into CWMS
  Revising a ResSim Alternative for use in CWMS – Use Observed Data
  (before or after import, this is what you should consider to make the alternative appropriate for real-time use).
  But – we aware – in CWMS 3.x, ResSim alternatives can continue to be used in standalone, so some of your changes could affect how the alternative works in standalone.
    Revise the Lookback settings:
      The lookback settings are the Initial Conditions for your reservoirs. You should use current observed data for your real-time model.
      For each reservoir…
        Set Elevation to Time Series
        Set ONE outlet to Time Series
        Set all other outlets to Constant - Set those constants to zero
        Note – there are lots of caveats to these last two instructions. What are some of them?
          Controlled outlet – gates, spillway, power plant
          Observed total flow vs observed individual flow – is there a gage? Is the observed estimated?
          Uncontrolled outlets

## Slide 20: Revising an Alternative for CWMS
Notes: Integrating a ResSim Model into CWMS
  Revising a ResSim Alternative for use in CWMS, continued
  This slide contains 2 screen shots:
  one of the context menu from the Alternative in the CAVI setup tab’s model tree
  one of the Lookback Tab of the Alternative Editor
    If the ResSim modeler created the watershed for use in CWMS, then the alternatives may already be “ready to go”. Check ‘em anyway. To do so,
      right click on the ResSim alternative in the models tree and select Edit Alternatives…
      The ResSim alternative editor for the selected alternative will open. Go to the Lookback Tab.
      Make sure that for each reservoir, the reservoir pool elevation (or storage) and the release from at least one outlet are set to Time Series.
      Set the other outlet releases to zero (0.0)
    Explain WHY these entries should be set to Time Series and discuss data availability.
    Explain how constant vs time-series affects the real-time regulator. Talk about the exceptions.

## Slide 21: Assigning Model alternative Keys
Notes: Integrating a ResSim Model into CWMS
  Assigning Key Letters
    A “key” must assigned to each alternative that is going to be used in a CWMS forecast run
      It must be an single alpha-numeric character: A-Z and 0-9
      Not case sensitive
      Each character can only be used once per model but can be reused by another model. E.g., Both HMS and ResSim could have alts with the key “B”
    The forecast run assembles a “key string” from the individual alternatives’ keys that were selected to form the run
    Each alternative’s substring of the run’s key string is used to label the F-Part of the DSS pathname of each output record that they produce at compute time.

## Slide 22: Creating Forecast Runs
Notes: Integrating a ResSim Model into CWMS
  Creating Forecast Runs
  this slide contains 2 screen shots:
  one of the Models menu from the from the Modeling Tab of the CAVI
  one of the Forecast Run Editor
  Explain the following…
    To Create a Forecast Run Open the Forecast Run Editor from the Models menu (select Forecast Runs…)
    Click New.
    Give the new forecast run a Name. Be descriptive, but not too long
    Select the model alternatives
    Click Apply or OK.
    Not all models of the program sequence must be “filled in” with an alternative; you can decide which models you want to include or not include in a particular forecast run.
      For example you may just want a RAS/FIA forecast run to use only during flood events. This run might use data from other forecast runs. This would ensure you not running them unnecessarily in a daily forecast
      Another example could be to leave out HMS and MFP because you only want to use flows from the local RFC for ResSim’s inflows.

## Slide 23: Model Linking
Extract vs Model Input
  Known Flow
    More than likely is linked to HMS
    Could be extract if RFC flows are used
      The Know Flow time series must cover the entire simulation time window (lookback and forecast)
  Lookback Elevation and Release
    More than likely is linked to Extract
      Only needs to cover the lookback time window
Notes: Integrating a ResSim Model into CWMS
  Model Linking.
  This slide illustrates the Model Linking Editor. The model being linked is ResSim, the “Known Flow” rows are highlighted and the “Select Input Model Alternative but has been selected so that the dropdown dialog is shown
    Be careful – the list of input that ResSim generates is in sections…
    The local inflows, then the Lookback and Operations’ Input Time Series, then the Observed data. All listed inputs are required EXCEPT the observed.
    Set the “Input From” and set the source for each row of required input
      The first several rows of the list are the inflows (“Known Flow” is ResSim’s parameter name for inflow data).
        You should select these rows as a group,
        then click on the “Select Input Model Alternative” button.
        A small dialog with a dropdown list will appear
        Select the model in the sequence that will be producing the inflows for your ResSim model then press Ok.
        This data is usually produced (for the whole time window of the forecast or simulation) by HMS (a rainfall runoff model) which precedes ResSim in the CWMS program order.
        The NOAA-NWS RFC may be producing the forecasted inflows for your forecast run. In this condition, there is no preceding model that generates them, so “Input From” should be set to Extract List.
    When you perform a “mass” linking this way, another small dialog will appear that asks if you are sure you want to “link” all those rows to the selected alternative. Unless you accidently picked the wrong model alternative, click Yes.
    The other is a portion of the table in the model linking editor…

## Slide 24: Configuring the Extract
Notes: Integrating a ResSim Model into CWMS
  Configuring the Extract
  This slide is a screen shot of the Extract Editor
    Focus on the ResSim “required inputs”: Lookback Data! And maybe operational info…
    Discuss time step, time window, and data type.
      Time series, grids
      15 min data vs hourly or daily
      Instantaneous versus period average
    Explain how this affects which group a given record should be added to.
      Interpolation
      Extract Offsets

## Slide 25: Compute
Progress Dialog
  Watch for messages
    Red Text are ERRORs
    Yellow/Orange Text are Warnings
    Black Text is informational
  Most Errors are caused by the input data
    Fill in missing data
    Link to a different data source
    Adjust the extract time window, add offset.
    Re-Run the Extract
Notes: Integrating a ResSim Model into CWMS
  Compute, Continued
    Watch the Compute Progress Dialog. When Done (success or failure)…
    Spend some time reading the messages in the Compute Progress Dialog
      (usually) Red Text are ERRORs – a red message usually indicates a problem that halts the compute. The problem must be resolved before you can get a complete compute.
      Yellow/Orange Text are Warnings - understand the warnings – these usually won’t stop the compute but your results may be questionable
      Black Text is informational - become familiar with the messages, there’s important “progress” information in there
    Look for more information generated by the compute in:
      Message Box of the CAVI, Compute Log, Console Log, Model Server Log
    Most Errors are caused by the input data
    Analyze and Correct Any Errors
      For Example “known release TS empty or invalid”
      means: a time series record is empty, missing, or has “validity” flags raised. And…”known release”.. What’s that? A Lookback release? Or a local flow?
      But look deeper… at the messages around the error messages.
      See if you are being told which model element the TS is for.
      Do you know where ResSim is in its compute process? (Init, cumloc, unreg, reg, holdouts?)
      Is there a time window message or a date and time in the message?
        If so, check the message’s time info against the compute time window in the control panel (and at the beginning of the Progress dialog’s ResSim messages) Use DSSVue to check if the time-series record exists in the forecast.dss file and if it does, check if there’s missing data.

## Slide 26: Using HEC-ResSim for Real-Time Decision making

## Slide 27: Real-Time Modeling Procedure
Review Data
  Check status of the data streams and the basin’s gages
  Familiarize yourself with current basin conditions and weather forecast
  Review the current and forecasted precipitation (and snow?) grids
  Identify an appropriate forecast time window – esp. lookback and forecast times
Notes: ResSim for Real Time Decision Making
  Real Time Modeling Procedure
    Review Data
      Check Status of the data streams and the basin’s gages
      Familiarize yourself with Current Basin Conditions and Weather Forecast
      Review the current and forecasted precip (and snow?) grids
      Identify an appropriate forecast time window – esp lookback and forecast times

## Slide 28: Real-Time Modeling Procedure
Review Current Data
  Identify an appropriate forecast time window
Create a Forecast
  Use the time window you identified
  Recommend including at least two Forecast Runs
    No Future Precipitation
    Expected (Probable) and/or Possible Future Precipitation
  Add additional offsets to the Time Window, if needed
Compute all runs through HEC-ResSim
Notes: ResSim for Real Time Decision Making
  Real Time Modeling Procedure - continued
    Review Data
      Check Status of the data streams and the basin’s gages
      Familiarize yourself with Current Basin Conditions and Weather Forecast
      Review the current and forecasted precip (and snow?) grids
      Identify an appropriate forecast time window – esp lookback and forecast times
    Create a Forecast
      Use the time window you identified
      Include at least two Forecast Runs
        No Future Precip
        Expected (Probable) and/or Possible Future Precip
      Add additional offsets to the Time Window, if needed
    Compute all runs through ResSim

## Slide 29: Real-Time Modeling Procedure
  For each Forecast Run, Analyze the Reservoir Operations
    Review Standard and Custom Plots, Reports, OSI
  Make modifications to the HEC-ResSim model as needed to develop an appropriate Release Schedule
    Release Overrides - OSI
    Rule and/or Zone adjustments
    Physical Parameter updates
  Save to Base
    If changes made are needed for future forecast runs
      Rule and/or Zone adjustments
      Physical Parameter updates
Notes: ResSim for Real Time Decision Making
  Real Time Modeling Procedure, continued.
    For each Forecast Run, Analyze the Reservoir Operations
      Review Standard and Custom Plots, Reports, OSI
    Make modifications as needed to develop an appropriate Release Schedule
      Release Overrides
      Rule and/or Zone adjustments
      Physical Parameter updates
    Save – To – Base!
      At this point, saving is selective – do I or don’t I?
      Go over what gets saved for ResSim – Everything related to the Alternative ( including the overrides?)

## Slide 30: Tools for Analyzing Results
  Active Schematic
  Standard Plots & the Release Decision Report
    Element Specific
    Found on context menu from schematic elements
  Standard Reports
    Summary Reports – by Element Type, Some Statistics
    Found on the Reports tab when you’ve selected a HEC-ResSim alternative in the Forecast runs tree
  CWMS-Vue/HEC-DSSVue
    Access to more detailed ResSim output
    Filter by F part…
Notes: ResSim for Real Time Decision Making
  Tools for Analyzing ResSim Results…
    Active Schematic
    Standard Plots & the Release Decision Report
      Element Specific
      Found on shortcut (right click) menu from schematic elements
    Standard Reports
      Summary Reports – Flows per Element Type, Some Statistics
      Found on the Reports tab when you’ve selected a ResSim alternative in the Forecast runs tree
    CWMSVue/DSSVue
      Access to more detailed ResSim output
      Filter by F part

## Slide 31: Viewing Results
  Output is available from:
    Forecast Run Alternative modeling tree
    Reports Tab below modeling tree
    From the modeling schematic in the CAVI Modeling map window
    Opening the specific model from the standalone application
    Or opening the forecast.dss file via CWMS-Vue and sorting the results based upon the model results F-Part
View Results

## Slide 32: The Standard Reservoir Plot
Notes: ResSim for Real Time Decision Making
  The Standard Reservoir Plot
  This slide is a screen shot of a standard Reservoir plot. Describe how the plot is arranged (and how to interpret it.)
    In the upper viewport, the computed elevation of the selected reservoir and its operating zones are plotted
    In the lower viewport, the computed inflow and outflow from the reservoir (pool) are plotted.
    Other common option for reviewing results
      tabulating from the default plots – File menu
      customizing the plot – Edit and Plot menus
      Remind them about the CWMS graphics lecture and workshop on Wednesday

## Slide 33: The Standard Junction Plot
Notes: ResSim for Real Time Decision Making
  The Standard Junction Plot
  This slide is a screen shot of a standard Junction plot. Describe how the plot is arranged (and how to interpret it.) Point out how to read the plot, emphasize…
    The Junction’s (out)Flow
    Limiting Rules
    Flow-Cumloc

## Slide 34: The Reports Tab
Notes: ResSim for Real Time Decision Making
  The Reports Tab
  This slide is has two screen shots:
      One of the Forecast Control Panel (run tree and subtabs, with the Reports Tab selected)
      One of the Reservoir Summary Report
    Point out the sub-tabs of the Forecast Control Panel
    Explain that some are context sensitive to the selection in the Runs Tree
    For ResSim, the Reports tab contains links to ResSim’s Summary Reports

## Slide 35: The Reports Tab
  Summary Reports:
    Reservoir Summary report is available for any network with a reservoir
    Flow Summary report is available for any ResSim network
    Power Summary report requires a hydropower house to be associated to a reservoir
    Gates Summary Report is available if gates curves have been defined in the Physical Properties
    Stage Summary report is available for junctions with stage-discharge rating curves defined
Notes: ResSim for Real Time Decision Making
  The Reports Tab
  This slide is has two screen shots:
      One of the Forecast Control Panel (run tree and subtabs, with the Reports Tab selected)
      One of the Reservoir Summary Report
    Point out the sub-tabs of the Forecast Control Panel
    Explain that some are context sensitive to the selection in the Runs Tree
    For ResSim, the Reports tab contains links to ResSim’s Summary Reports

## Slide 36: The Release Decision Report
Notes: ResSim for Real Time Decision Making
  The Release Decision Report is designed to tell you what led to the release decisions at each timestep.
  This slide is a screen shot of the Release Decision Report. Describe how the report is arranged (and how to interpret it.)
    The start of the report = time of forecast
    The two lines/rows per timestep
      One row for what it did
      And one for why it did it
    The columns for zone, elevation, and each level of the outlet hierarch
    The bold vs std text – explain that bold text indicates a user specified rule
    The codes – like GC to be Guide Curve Operation, MinLim, PhysMaxCap

## Slide 37: Release Overrides

## Slide 38: Release Overrides
Notes: ResSim for Real Time Decision Making
  This slide contains a screen shot of the CAVI’s Actions tab and another of the ResSim Overrides Editor.
  Release Overrides allow the user to specify an exact operation constrained only by physical capacity (I.e., the rules, zones, and guide curve are ignored for the time step at which you have specified the overrides)
    Why override the Releases?
      Mimic gate settings
      Evaluate influence of a NOT by the book release schedule
      The rules “aren’t cutting it”.
    Trials vs Alternatives –
      Acknowledge that CWMS 3.0 cannot do trials
      Suggest possibility of a “base” alternative, and one or more to tinker with
    Process of defining overrides
      COMPUTE (if you haven’t already)
      Hand enter new values
      Enter value in selected cell, select range, fill-repeat
      Enter value in first and last cell of a range, fill-linear
      Use a Fill-Factor or Fill–add Constant option for a range
      Ok & RECOMPUTE

## Slide 39: Operations Support Interface (OSI)
Notes: ResSim for Real Time Decision Making
  Operations Support Interface (OSI)
    This slide shows a screen shot a fully setup OSI…
    The OSI is a fully configurable interface for building your own Release Overrides Editor – It is more like a ‘dashboard’ for defining your regulation schedule.
    Select the ResSim alternative in a Forecast. Launch the OSI from the Action buttons.
    If the OSI is blank, add a Tab from the Edit menu
    Add a Variable – this is the “variable” you are overriding, like a Reservoir Release.
      Give it a Name and Description, and Set the Element Type - Reservoir
      Select the Element and Select the Variable (Type) – Release, Press OK
      Click on a value in the column that was added for your variable in the OSI’s table. Notice what happens to the plot in the upper part of the OSI
    Edit your Variable
      Add Additional relevant Time Series to be displayed in plot
      Add a Max Target for your Variable.
      Press OK. Click to another variable’s column and then back to this one or Click Refresh Plot. Notice what happens to the plot.
    Enter an override of a reservoir release
      Use the graphical editing tool (the 4th one) and draw in your override or enter the override values in the table. (You end drawing by right-clicking on your last point)
      Press Compute to see the results of the overrides you entered
      Consider adding a second tab to show the elevation (and stage) at key control points in the watershed.
    A separate handout is available that covers these steps. Hand it out or go over it if you can’t do a demo.

## Slide 40: OSI – Operations Support Interface
  Configured by the User
  Intended for:
    Developing Overrides
  Tabs are for organizing variables
  Variables are for editing or displaying data
    Reservoir Overrides
    Computed Results

## Slide 41: OSI – Adding a Tab

## Slide 42: OSI – Adding a Variable

## Slide 43: OSI – Setting up the Variable

## Slide 44: OSI – Entering Overrides

## Slide 45: OSI – Configuration Examples

## Slide 46: OSI – Configuration Examples

## Slide 47: Capabilities & Limitations
Gates & Gate Operations
  Time Series of Gate Openings (with gate curves)
  Flows are what the program wants to be at the end of the timestep, not some reasonable gate setting for an ordered gate usage
Time Step
  Decision Interval
    Each Time-Step (default)
    Regular Interval
      1hr, 6hr, Daily, etc.
    Weekly Schedule
      Set the times of day based
        upon the day of week
        when changes can occur
Notes: ResSim Capabilities & Limitations
  Gates & Gate Operations
    Time Series of Gate Openings (with gate curves)
    Flows are what the program wants to be at at the end of the timestep, not some reasonable gate setting for an ordered gate usage
  Time Step
    New Decision each Time-Step
    Decision Interval, limited…
  Others?

## Slide 48: Summary
  HEC-ResSim is the integrated reservoir simulation model included in the CAVI’s suite of real-time decision support tools.
  HEC-ResSim Model Integration includes…
    Revising the ResSim Alternatives’ Lookback settings
    Establishing the model linking to HMS results and observed data
    Configuring the Extract groups
  Using HEC-ResSim for Real-time Decision Support involves…
    Analyzing the model’s releases
    Performing “What-if” analysis
    Developing a realistic release schedule
    Testing and revising your schedule
Notes: Summary
  ResSim is the integrated reservoir simulation model included in the CAVI’s suite of real-time decision support tools.
  ResSim Model Integration includes…
    Revising the ResSim Alternatives’ Lookback settings
    Establishing the model linking to HMS results and observed data
    Configuring the Extract groups
  Using ResSim for Real-time Decision Support involves…
    Analyzing the model’s releases
    Performing “What-if” analysis
    Developing a realistic release schedule
    Testing and revising your schedule

## Slide 49: ? ? ? Questions ? ? ?
Notes: Lake Sonoma outflow change instructions and stairwell to get down to where gate changes are made.