## Slide 1: Corps water management system (CWMS) overview
Fauwaz Hanbali
Hydrologic Engineering Center
CWMS Prospect Course
Notes: CWMS Overview

## Slide 2: Overview
Water Management in USACE
Corps Water Management System (CWMS)
CWMS National Implementation Program
Summary and Resources
Notes: Overview
  Water Management in USACE
  Corps Water Management System (CWMS)
  National CWMS Implementation Program
  Summary and Conclusion

## Slide 3: USACE Water Management Mission
Notes: CWMS Overview

## Slide 4: Usace water management mission
Collect, process, store, analyze and disseminate water resources data
Continuously monitor conditions in our systems (precipitation, temperature, flow, stage, melt)
Make daily operations decisions on over 600 USACE reservoirs
    Flood Risk Reduction
    Navigation
    Hydropower
    Water Supply
    Environment

## Slide 5: Usace water management mission
Support other USACE missions:
    Preparedness: Emergency and disaster response
    Planning: Systems based water resources approach
    Dam/Levee Safety: Risk informed decision making

## Slide 6: Importance of the water management mission
Water Management is a Mission Critical element within the Corps
  Increases public safety
  Benefits the economy
  Increases public quality of life
  Protects and restores the environment
Notes: III. Presentation
USACE Role in Water Management
  We are Stewards of our Nation’s Water (Water Management) Resources
    Water Management is a Mission Critical element within the Corps.
      Improves the public’s quality of life and safety
      Benefits the nations economy
    We are required to collect, process, store, analyze and disseminate water resource data.
    We directly support daily decisions at all 600+ Corps Reservoirs.
    These decisions, which are based on approved water control manuals and plans, directly impact most of the Corps business lines.
    We are also required to manage the flood storage of other federal, state and private dams during times of flooding. We must constantly monitor rain, snow, snow melt, lake levels and river levels.
    During Non-Flood time We must constantly make operation decisions to maintain navigation, generate hydropower and manage low flow and drought conditions.

## Slide 7: USACE Water Management Strategy and Policy
Strategic Vision: USACE Actions for Change: Comprehensive Systems Approaches that include sustainable solutions
Legislation: WRDA 1997 Sec. Army provide public access to USACE Water Resources Data
Civil Works Initiatives: Planning Transformation
Corps Policy on Water Control
  ER 200-1-5
  ER 1110-2-240
  EM 1110-2-3600
Notes: USACE Role in Water Management
  USACE Strategy for System/Watershed Requirements
    Corps Policy
      ER 1105-2-100, Planning Guidance Notebook, 22 April 2000, requires systems approaches, "The planning process shall address the Nation’s water resources needs in a systems context…”
      ER 1105-2-409, Planning in a Collaborative Environment, 31 May 2005, provides revised procedures for conducting Corps water resources planning, "Collaboration is the keystone of the Corps watershed approach…”
      EC 1110-2-6067, USACE Process for the National Flood Insurance Program (NFIP) Levee System Evaluation, 31 August 2010,
    Strategic vision: USACE Actions for Change
      required comprehensive systems approaches that include integrated sustainable solutions and decisions are risk-informed.
    Legislation: WRDA 1997 Sec. Army provide public access to USACE Water Resources Data.
    Civil Works Initiatives: Planning Transformation:
    CWMS is the tool to meet the Water Management Mission
      Is a modernized AIS set of Water Management tools designed to meet USACE initiatives, the WM mission, and any legislative or legal requirements.
      B. Corps Policy on Water Control
      Engineering Regulation ER 1110-2-240, Water Control Management
      Engineering Manual EM 1110-2-3600, Management of Water Control System
      Engineering Regulation ER 1110-2-8156, Preparation of Water Control Manuals
      Environmental Operating Principals ER 200-1-5.

## Slide 8: Corps Water management System (CWMS)
Notes: CWMS Overview

## Slide 9: Corps Water Management System (CWMS)
CWMS is the tool to help water managers meet the mission
An Automated Information System (AIS) to collect, process, and store real-time data
A suite of modeling tools to run real-time forecast simulations and help achieve a wide range of reservoir authorized purposes
Designed to meet USACE initiatives, the WM mission, and other legislative requirements

## Slide 10: Corps water management system (CWMS)
Observed Data
RTS Modeling & Water Management Decisions
Instructions
CWMS Database
Met Data
Data Dissemination
Notes: Explain the process
Explain that the piece we will be focusing on is RTS
CWMS Overview

## Slide 11: Real-time data acquisition
Collect
Decode
Transform
Validate
Make corrections
Use data for monitoring and forecasting
CWMS Server/Database
Notes: Components of CWMS
  Data Acquisition
    Collect: record and transmit (line of sight to satellite to receiving dish to CWMS server (database)
    Decode into usable format
    Transform decoded data
    Validate transformed data
    Make corrections
    Monitoring and Forecasting

## Slide 12: Station data
Stream gauging data used for water management
USGS provides USACE data for 2500 stations
Notes: Components of CWMS
  Common Data Acquired
    Real-Time Data
      Stream gauging data used for water management
      USGS provides USACE data for 2500 stations

## Slide 13: Observed & forecast met data
NOAA/NWS Support:
  Quantitative Precipitation Estimates (QPEs)
  Provides Quantitative Forecast Precipitation (QPFs)
  RFCs provide river stage/flow forecasts
Notes: Components of CWMS
  Common Data Acquired
    Forecasted Data
      Provides Precipitation Quantitative Estimates (QPE)
      Provides Precipitation Quantitative Forecast (QPF) for various durations such as 24, 48, and 72 hours
      RFCs (River Forecast Centers) provide river stage forecasts

## Slide 14: HEC-RTS
Hydrologic Engineering Center (HEC) Real-Time Simulation (RTS)
  The CWMS suite of modeling software with integrated real-time data
Instructions
Data

## Slide 15: CWMS Modeling Tools
Hydrology
Reservoir Operations
Hydraulics
Consequences
Meteorology
Notes: USACE Role in Water Management
  Corps of Engineers Water Management System
    CWMS Package
      The CWMS release package consists of a database (software and hardware) and a suite of models
        The database consists of software for data acquisition, visualization and dissemination
        The model suite consists of HEC-MetVue, HEC-HMS, HEC-ResSim, HEC-RAS, and HEC-FIA
        Real time data and weather forecasts are used with the models to generate streamflow forecasts and make release decisions

## Slide 16: Meteorological Scenarios: HEC-MetVue
Processes and Combines Observed and Forecast Meteorological Datasets
  Precipitation, Temperature, and more
Allows for:
  Observed Dataset Corrections
  Forecast Dataset Adjustments for additional “What-If” Scenarios
Observed
Precipitation
Forecast
Precipitation
Combined
Precipitation

## Slide 17: Hydrologic Modeling: HEC-HMS
Compute runoff and uncontrolled flows given input meteorological data
Predict inflows to reservoirs, and local-flows downstream of reservoirs
Model output used as input to reservoir operations and hydraulics models
Notes: Components of CWMS
  Hydrologic Modeling: Precipitation (HEC-HMS)
    Utilize GIS functionality for developing watershed input.
      Digital terrain model
    sub-basin delineation and drainage network
      development of a grid cell file

## Slide 18: Reservoir Operations: HEC-ResSim
Given stream flows and water control rules, simulate reservoir operations
Override operations to test operating plan scenarios
Model output used as input to hydraulics and consequences models
Notes: Components of CWMS
  Reservoir Operations
    Given streamflows and water control plans (reservoir operating rules) for a river basin simulate reservoir operations and computes downstream hydrographs
      Streamflows are observed and forecasted
      Streamflows include reservoir inflow and downstream local hydrographs
    Model (reservoir) output (regulated hydrographs) are used as input to hydraulic and flood inundation (consequence) models and impacts are evaluated

## Slide 19: River Hydraulics: HEC-RAS
Given flow hydrographs, compute water surface profiles
Predict resultant water surface elevations and inundation areas for events
Produce inundation maps
Model output used as input to consequences models
Notes: Components of CWMS
  River Hydraulics
    HEC-RAS Hydraulic Modeling Software
      Steady-flow or unsteady-flow analysis; 1-D and 2-D, water quality, sediment
      Channel friction adjusted through the CAVI and NMI (Native Model Interface)
      Given reservoir model hydrographs, computes water surface profiles and stage hydrographs
      Also computes river velocities, stages, and inundated areas given streamflow and river/floodplain geometry and hydraulic characteristics (river hydraulics).
19

## Slide 20: Consequences: HEC-FIA
HEC-FIA (Flood Impact Analysis) identifies the consequences from a flood event
Given river stages and damage data, computes damages to structures and estimates life loss
Computes project benefits
Response tables provide a list and of actions to take during an event, based on forecasted stages
Notes: Components of CWMS
  Consequence Analysis: HEC-FIA
    HEC-FIA (Flood Impact Analysis) identifies the consequences from a single event
    Accepts model output from HEC-ResSim and HEC-RAS
    Given river stages and damage data, computes damages to structures and other contents of the floodplain (including agricultural)
    Computes damages and benefits between different scenarios, including with and without project conditions
    Estimates Life Loss
    Commonly used FIA components
      "Action tables" provide a list and time of actions to take during an event, based on forecasted

## Slide 21: CWMS Modeling: Putting it all together
Real-time hydrometeorological data
Weather forecasts
Models for various forecast alternatives (scenarios) are calibrated based on real time conditions
Forecast alternatives for a variety of scenarios are simulated and evaluated for decision making purposes
Notes: USACE Role in Water Management
  Corps of Engineers Water Management System
    CWMS Modeling: Putting it all together
      Real time hydrometeorological data like rain, streamflow, temperature, snow water equivalent are acquired, validated, and transformed
      Weather forecasts (scenarios) for rain and temperature are input into CWMS
      Models for various forecast alternatives (scenarios) are calibrated based on real time conditions
        Typically use one week of observed data and evaluate results two weeks into the future.
        What models are needed? hydrologic, reservoir, hydraulic and flood inundation models?
      Forecast alternatives for a variety of scenarios are simulated and evaluated for decision making purposes
        No rain (rain on the ground)
        QPF’s or multiples of QPF
        Historical events
        Specified Reservoir operations
        Levee failures

## Slide 22: CWMS National implementation Plan
Notes: CWMS Overview

## Slide 23: CWMS National Implementation Plan
  Joint effort by MMC and HEC to strengthen water management capabilities of USACE
  Aims to develop CWMS models and databases for USACE Districts across the nations
    201 watersheds ranging in size from 50 to 100,000+ sq. mi.
    Total of 2,250,000+ sq. mi.
  Implement CWMS models into daily water management processes at district offices
    Consistent approach across the nation
Notes: National CWMS Implementation
  It is an investment in the Corps
    Supports Transformation of Civil Works, Preparing for Tomorrow, and Reducing Disaster Risks
    $124 million 10 year program depending on level of funding
    Working on basins in all 7 continental divisions.
    141 USACE personnel worked on CWMS including 109 modelers, 14 economist, and 18 GIS specialists.

## Slide 24: CWMS National Implementation Plan
  $124 million 10-year+ program (2012-2026)
  Build out of CWMS basin models in all 7 continental divisions and Alaska
  Around 200 USACE personnel per year worked on CWMS implementation including engineers, economist, and GIS specialists
Notes: The Corps Water Management System has been developed by HEC in an effort to streamline data collection, data validation, and data usage within hydrologic, reservoir simulation, hydraulic, and consequence models.
The CWMS Nationwide Implementation was started as an effort to fully integrate the CWMS platform within all watersheds for which there is a USACE interest. The total number of watersheds of interest exceeds 200 and range in size between 50 sq miles and 100,000+ sq miles. In total, 2.25 million sq miles falls under this umbrella.
Starting in 2012, two watersheds were used as part of a pilot program whereby models were constructed, data streams were established, and all products were integrated in a seamless fashion.
Since those first two successful implementations, CWMS has been implemented within an additional 190+ watersheds across the United States.
CWMS Overview

## Slide 25: 100% CWMS IMPLEMENTATION
An office with water management responsibility MUST have Corps Water Management System (CWMS) models developed and be fully capable to run the full suite of models (complete with meteorological and reservoir scenarios) to completion with consequences and inundation mapping being produced.
The office MUST regularly exercise the models to ensure they are sufficient in their operation/use/application and have an exercised Continuity of Operations Plan (COOP) in-place.
CWMS models MUST replace legacy systems since CWMS is the USACE standard across the enterprise.
It is expected that CWMS models will be used for daily operational planning in determining appropriate operational actions for reservoir operation.
It is not expected that consequence modeling and mapping be produced on a daily basis, but would need to be readily available in times of need or when requested.
Notes: CWMS Overview

## Slide 26: CWMS Implementation Map
Notes: National CWMS Implementation (Status as of January 2025)

## Slide 27: CWMS Beyond Water Management
Transform Civil Works
Reduce Disaster Risks
Planning
Planning Transformation
Watershed based budgeting
Watershed based analysis
UOC/FRM
Enhance Disaster Preparation
Strengthen interagency Support
Flood Risk Benefits
Risk Transference
Dam Safety
DSAC
Risk Assessments
EAP Maps
IRRMP
Levee Safety
LSAC
Risk Assessments
EAP Maps
CIPR
Consequence Assessment Studies
Consequence-Based Top Screen
Security Risk Assessments
Prepare for Tomorrow
Water Management
Operating Plans
Project Operation
Inundation Maps
What if Scenarios
Notes: National CWMS Implementation
  Who does CWMS implementation support?
    Transform Civil Works
      CIPR, Dam Safety
    Prepare for Tomorrow
      Levee Safety, Planning
    Reduce Disaster Risks
      Water Management
      UOC/FRM

## Slide 28: Summary and Resources
Notes: CWMS Overview

## Slide 29: Summary
CWMS is a basin wide comprehensive and integrated system for real time water management
Strong data management capabilities
A full range of hydrologic/hydraulic modeling software
Capability to evaluate operational decisions and compare the impact of various "what if?" scenarios
Comprehensive Training, Manuals and Full Technical Support
Notes: Conclusion
  CWMS is a basin wide comprehensive and integrated system for real time water management
  Strong data management capabilities
  A full range of hydrologic/hydraulic modeling software
  Capability to evaluate operational decisions and compare the impact of various "what if?" scenarios
  Comprehensive Training, Manuals and Full Technical Support

## Slide 30: CWMS INFO
CWMS Documentation Portal
  Users Manual, Release Notes, Training, and More
  Accessible from Sharepoint & the HEC Website
CWMS 3.4.0 Installation
  Database schema upgrade scheduled with all offices
  Client Software package available in Sharepoint
Notes: CWMS Overview

## Slide 31: CWMS Discourse & MS Teams
CWMS Discourse
MS Teams
  Primary CWMS support platform
  Community-wide questions/answers
  Group or one-on-one Chats & Meetings
  Live & Recorded Webinars
  Virtual Working Sessions & Workshops
  In-person Workshop Materials Archives
Notes: CWMS Overview

## Slide 32: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
Notes: CWMS Overview