## Slide 1: Corps water management system (CWMS) overview
Fauwaz Hanbali
Hydrologic Engineering Center
CWMS Prospect Course
Part B – CWMS Introduction
Notes: CWMS Overview

## Slide 2: Overview
Water Management in USACE
Corps Water Management System (CWMS)
CWMS National Implementation Program
Summary and Resources
Notes: Overview
  Water Management in USACE
  Corps Water Management System (CWMS)
  National CWMS Implementation Program
  Summary and Conclusion

## Slide 3: Corps Water Management System (CWMS)
CWMS is the tool to help water managers meet the mission
An Automated Information System (AIS) to collect, process, and store real-time data
A suite of modeling tools to run real-time forecast simulations and help achieve a wide range of reservoir authorized purposes
Designed to meet USACE initiatives, the WM mission, and other legislative requirements

## Slide 4: Corps water management system (CWMS)
Observed Data
RTS Modeling & Water Management Decisions
Instructions
CWMS Database
Met Data
Data Dissemination
Notes: Explain the process
Explain that the piece we will be focusing on is RTS
CWMS Overview

## Slide 5: Real-time data acquisition
Collect
Decode
Transform
Validate
Make corrections
Use data for monitoring and forecasting
CWMS Server/Database
Notes: Components of CWMS
  Data Acquisition
    Collect: record and transmit (line of sight to satellite to receiving dish to CWMS server (database)
    Decode into usable format
    Transform decoded data
    Validate transformed data
    Make corrections
    Monitoring and Forecasting

## Slide 6: Station data
Stream gauging data used for water management
USGS provides USACE data for 2500 stations
Notes: Components of CWMS
  Common Data Acquired
    Real-Time Data
      Stream gauging data used for water management
      USGS provides USACE data for 2500 stations

## Slide 7: Observed & forecast met data
NOAA/NWS Support:
  Quantitative Precipitation Estimates (QPEs)
  Provides Quantitative Forecast Precipitation (QPFs)
  RFCs provide river stage/flow forecasts
Notes: Components of CWMS
  Common Data Acquired
    Forecasted Data
      Provides Precipitation Quantitative Estimates (QPE)
      Provides Precipitation Quantitative Forecast (QPF) for various durations such as 24, 48, and 72 hours
      RFCs (River Forecast Centers) provide river stage forecasts

## Slide 8: HEC-RTS
Hydrologic Engineering Center (HEC) Real-Time Simulation (RTS)
  The CWMS suite of modeling software with integrated real-time data
Instructions
Data

## Slide 9: CWMS Modeling Tools
Hydrology
Reservoir Operations
Hydraulics
Consequences
Meteorology
Notes: USACE Role in Water Management
  Corps of Engineers Water Management System
    CWMS Package
      The CWMS release package consists of a database (software and hardware) and a suite of models
        The database consists of software for data acquisition, visualization and dissemination
        The model suite consists of HEC-MetVue, HEC-HMS, HEC-ResSim, HEC-RAS, and HEC-FIA
        Real time data and weather forecasts are used with the models to generate streamflow forecasts and make release decisions

## Slide 10: Meteorological Scenarios: HEC-MetVue
Processes and Combines Observed and Forecast Meteorological Datasets
  Precipitation, Temperature, and more
Allows for:
  Observed Dataset Corrections
  Forecast Dataset Adjustments for additional “What-If” Scenarios
Observed
Precipitation
Forecast
Precipitation
Combined
Precipitation

## Slide 11: Hydrologic Modeling: HEC-HMS
Compute runoff and uncontrolled flows given input meteorological data
Predict inflows to reservoirs, and local-flows downstream of reservoirs
Model output used as input to reservoir operations and hydraulics models
Notes: Components of CWMS
  Hydrologic Modeling: Precipitation (HEC-HMS)
    Utilize GIS functionality for developing watershed input.
      Digital terrain model
    sub-basin delineation and drainage network
      development of a grid cell file

## Slide 12: Reservoir Operations: HEC-ResSim
Given stream flows and water control rules, simulate reservoir operations
Override operations to test operating plan scenarios
Model output used as input to hydraulics and consequences models
Notes: Components of CWMS
  Reservoir Operations
    Given streamflows and water control plans (reservoir operating rules) for a river basin simulate reservoir operations and computes downstream hydrographs
      Streamflows are observed and forecasted
      Streamflows include reservoir inflow and downstream local hydrographs
    Model (reservoir) output (regulated hydrographs) are used as input to hydraulic and flood inundation (consequence) models and impacts are evaluated

## Slide 13: River Hydraulics: HEC-RAS
Given flow hydrographs, compute water surface profiles
Predict resultant water surface elevations and inundation areas for events
Produce inundation maps
Model output used as input to consequences models
Notes: Components of CWMS
  River Hydraulics
    HEC-RAS Hydraulic Modeling Software
      Steady-flow or unsteady-flow analysis; 1-D and 2-D, water quality, sediment
      Channel friction adjusted through the CAVI and NMI (Native Model Interface)
      Given reservoir model hydrographs, computes water surface profiles and stage hydrographs
      Also computes river velocities, stages, and inundated areas given streamflow and river/floodplain geometry and hydraulic characteristics (river hydraulics).
13

## Slide 14: Consequences: HEC-FIA
HEC-FIA (Flood Impact Analysis) identifies the consequences from a flood event
Given river stages and damage data, computes damages to structures and estimates life loss
Computes project benefits
Response tables provide a list and of actions to take during an event, based on forecasted stages
Notes: Components of CWMS
  Consequence Analysis: HEC-FIA
    HEC-FIA (Flood Impact Analysis) identifies the consequences from a single event
    Accepts model output from HEC-ResSim and HEC-RAS
    Given river stages and damage data, computes damages to structures and other contents of the floodplain (including agricultural)
    Computes damages and benefits between different scenarios, including with and without project conditions
    Estimates Life Loss
    Commonly used FIA components
      "Action tables" provide a list and time of actions to take during an event, based on forecasted

## Slide 15: CWMS Modeling: Putting it all together
Real-time hydrometeorological data
Weather forecasts
Models for various forecast alternatives (scenarios) are calibrated based on real time conditions
Forecast alternatives for a variety of scenarios are simulated and evaluated for decision making purposes
Notes: USACE Role in Water Management
  Corps of Engineers Water Management System
    CWMS Modeling: Putting it all together
      Real time hydrometeorological data like rain, streamflow, temperature, snow water equivalent are acquired, validated, and transformed
      Weather forecasts (scenarios) for rain and temperature are input into CWMS
      Models for various forecast alternatives (scenarios) are calibrated based on real time conditions
        Typically use one week of observed data and evaluate results two weeks into the future.
        What models are needed? hydrologic, reservoir, hydraulic and flood inundation models?
      Forecast alternatives for a variety of scenarios are simulated and evaluated for decision making purposes
        No rain (rain on the ground)
        QPF’s or multiples of QPF
        Historical events
        Specified Reservoir operations
        Levee failures

## Slide 16: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
Notes: CWMS Overview