## Slide 1: HEC-ResSim in CWMS
Russell Errett, P.E.
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
  Learn basic concepts of using HEC-ResSim in CWMS for making real-time reservoir operation decisions
  Introduction to HEC-ResSim
    What is ResSim?
    What can ResSim do?
    Why do we want it in CWMS?
  Integrating an HEC-ResSim model into CWMS
    A brief review of importing, linking, etc.
  Using HEC-ResSim for Real-Time Decision Making
    Data Considerations
    How real-time modeling differs from planning studies
    Regulation Schedule/Plan
    The OSI

## Slide 3: Using HEC-ResSim for Real-Time Decision making

## Slide 4: Real-Time Modeling Procedure
Review Data
  Check status of the data streams and the basin’s gages
  Familiarize yourself with current basin conditions and weather forecast
  Review the current and forecasted precipitation (and snow?) grids
  Identify an appropriate forecast time window – esp. lookback and forecast times
Notes: ResSim for Real Time Decision Making
  Real Time Modeling Procedure
    Review Data
      Check Status of the data streams and the basin’s gages
      Familiarize yourself with Current Basin Conditions and Weather Forecast
      Review the current and forecasted precip (and snow?) grids
      Identify an appropriate forecast time window – esp lookback and forecast times

## Slide 5: Real-Time Modeling Procedure
Review Current Data
  Identify an appropriate forecast time window
Create a Forecast
  Use the time window you identified
  Include at least two Forecast Runs
    No Future Precipitation
    Expected (Probable) and/or Possible Future Precipitation
  Add additional offsets to the Time Window, if needed
Compute all runs through HEC-ResSim
Notes: ResSim for Real Time Decision Making
  Real Time Modeling Procedure - continued
    Review Data
      Check Status of the data streams and the basin’s gages
      Familiarize yourself with Current Basin Conditions and Weather Forecast
      Review the current and forecasted precip (and snow?) grids
      Identify an appropriate forecast time window – esp lookback and forecast times
    Create a Forecast
      Use the time window you identified
      Include at least two Forecast Runs
        No Future Precip
        Expected (Probable) and/or Possible Future Precip
      Add additional offsets to the Time Window, if needed
    Compute all runs through ResSim

## Slide 6: Real-Time Modeling Procedure
  For each Forecast Run, Analyze the Reservoir Operations
    Review Standard and Custom Plots, Reports, OSI
  Make modifications to the HEC-ResSim model as needed to develop an appropriate Release Schedule
    Release Overrides - OSI
    Rule and/or Zone adjustments
    Physical Parameter updates
  Save to Base
    If changes made are needed for future forecast runs
      Rule and/or Zone adjustments
      Physical Parameter updates
Notes: ResSim for Real Time Decision Making
  Real Time Modeling Procedure, continued.
    For each Forecast Run, Analyze the Reservoir Operations
      Review Standard and Custom Plots, Reports, OSI
    Make modifications as needed to develop an appropriate Release Schedule
      Release Overrides
      Rule and/or Zone adjustments
      Physical Parameter updates
    Save – To – Base!
      At this point, saving is selective – do I or don’t I?
      Go over what gets saved for ResSim – Everything related to the Alternative ( including the overrides?)

## Slide 7: Tools for Analyzing Results
  Active Schematic
  Standard Plots & the Release Decision Report
    Element Specific
    Found on context menu from schematic elements
  Standard Reports
    Summary Reports – by Element Type, Some Statistics
    Found on the Reports tab when you’ve selected a HEC-ResSim alternative in the Forecast runs tree
  CWMS-Vue/HEC-DSSVue
    Access to more detailed ResSim output
    Filter by F part…
Notes: ResSim for Real Time Decision Making
  Tools for Analyzing ResSim Results…
    Active Schematic
    Standard Plots & the Release Decision Report
      Element Specific
      Found on shortcut (right click) menu from schematic elements
    Standard Reports
      Summary Reports – Flows per Element Type, Some Statistics
      Found on the Reports tab when you’ve selected a ResSim alternative in the Forecast runs tree
    CWMSVue/DSSVue
      Access to more detailed ResSim output
      Filter by F part

## Slide 8: Viewing Results
  Output is available from:
    Forecast Run Alternative modeling tree
    Reports Tab below modeling tree
    From the modeling schematic in the CAVI Modeling map window
    Opening the specific model from the standalone application
    Or opening the forecast.dss file via CWMS-Vue and sorting the results based upon the model results F-Part
View Results

## Slide 9: The Standard Reservoir Plot
Notes: ResSim for Real Time Decision Making
  The Standard Reservoir Plot
  This slide is a screen shot of a standard Reservoir plot. Describe how the plot is arranged (and how to interpret it.)
    In the upper viewport, the computed elevation of the selected reservoir and its operating zones are plotted
    In the lower viewport, the computed inflow and outflow from the reservoir (pool) are plotted.
    Other common option for reviewing results
      tabulating from the default plots – File menu
      customizing the plot – Edit and Plot menus
      Remind them about the CWMS graphics lecture and workshop on Wednesday

## Slide 10: The Standard Junction Plot
Notes: ResSim for Real Time Decision Making
  The Standard Junction Plot
  This slide is a screen shot of a standard Junction plot. Describe how the plot is arranged (and how to interpret it.) Point out how to read the plot, emphasize…
    The Junction’s (out)Flow
    Limiting Rules
    Flow-Cumloc

## Slide 11: The Reports Tab
Notes: ResSim for Real Time Decision Making
  The Reports Tab
  This slide is has two screen shots:
      One of the Forecast Control Panel (run tree and subtabs, with the Reports Tab selected)
      One of the Reservoir Summary Report
    Point out the sub-tabs of the Forecast Control Panel
    Explain that some are context sensitive to the selection in the Runs Tree
    For ResSim, the Reports tab contains links to ResSim’s Summary Reports

## Slide 12: The Reports Tab
  Summary Reports:
    Reservoir Summary report is available for any network with a reservoir
    Flow Summary report is available for any ResSim network
    Power Summary report requires a hydropower house to be associated to a reservoir
    Gates Summary Report is available if gates curves have been defined in the Physical Properties
    Stage Summary report is available for junctions with stage-discharge rating curves defined
Notes: ResSim for Real Time Decision Making
  The Reports Tab
  This slide is has two screen shots:
      One of the Forecast Control Panel (run tree and subtabs, with the Reports Tab selected)
      One of the Reservoir Summary Report
    Point out the sub-tabs of the Forecast Control Panel
    Explain that some are context sensitive to the selection in the Runs Tree
    For ResSim, the Reports tab contains links to ResSim’s Summary Reports

## Slide 13: The Release Decision Report
Notes: ResSim for Real Time Decision Making
  The Release Decision Report is designed to tell you what led to the release decisions at each timestep.
  This slide is a screen shot of the Release Decision Report. Describe how the report is arranged (and how to interpret it.)
    The start of the report = time of forecast
    The two lines/rows per timestep
      One row for what it did
      And one for why it did it
    The columns for zone, elevation, and each level of the outlet hierarch
    The bold vs std text – explain that bold text indicates a user specified rule
    The codes – like GC to be Guide Curve Operation, MinLim, PhysMaxCap

## Slide 14: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams