## Slide 1: CWMS CAVI Orientation
Matt Fleming, P.E.
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Objective
  Learn about the Control and Visualization Interface

## Slide 3: Overview
Introduce the CWMS Control and Visualization Interface (CAVI)
  Screen Components
  Layers
  Time-Series Icons
  Scripts
Introduce CAVI components and modules
  Modules
    Purpose and use
  Available tools

## Slide 4
General CAVI Components

## Slide 5: CAVI Purpose
Serves as the main interface to CWMS
Access and manipulate data and models:
  View status of data feeds and gauge quality
  Validate data
  View hydro-meteorological conditions of the watershed
  Plot, tabulate, and edit data
  Run models and view results
CAVI organizing unit is called the “Watershed”, which contains data and models

## Slide 6: Screen components
Menu
Module Tab
Tool bar buttons
Map Panel
Control Panel
Map mouse functionality and tools
Map status line
Message area

## Slide 7: Layers
A “Layer” is a set of objects drawn in the CAVI map(s).
Example layers include:
  Background images or map layers
    Internet Map
    Aerial photos or other geo-referenced images
    Subbasin, stream outline maps (e.g., shapefiles)
    County/political boundaries
  Grids (precipitation, temperature, etc.)
    From the visualization tab
  “Stream Alignment”
  Model representation
Time-series icons can be divided into sub-layers:
  Flow, stage, or precipitation layers
  Raw or validated data layer
  Thumbnail plot or color bar layer

## Slide 8: Time-series icons
A time-series icon represents a location that is associated with one or more data sets
The data sets are usually time-series data and can be from Oracle or HEC-DSS
  Observed raw data from Oracle
  Validated data from Oracle
  Model results from HEC-DSS
Paired curve data may be displayed from an icon (but not with time-series data in the same icon).
Icons can show an image, document, a live video with the icon, etc

## Slide 9: Time-series icons
Each time-series icon data set is associated with an icon style for each module:
  Graphic Symbol
  Dot
  Thumbnail Plot
  Quality Color Bar
  Threshold Color Bar
  None
For example, a flow data set may be represented by:
  A quality color bar in Data Acquisition
  A thumbnail plot in Data Visualization
  A graphic symbol in Model Interface

## Slide 10: Time-series plots and Tables

## Slide 11: scripts
Scripts are a set of text instructions to perform common tasks:
  Plots of data from different locations (e.g., main steam gages)
Setup/edit scripts from the “Scripts” menu
Run scripts from:
  “Script Buttons” in a separate window or in the lower portion of the control panel
  From a “script schedule” for automatic execution

## Slide 12
CAVI Modules

## Slide 13: Cavi login
You can login to access data from the CWMS Oracle database on the server or run locally if you have the data (already downloaded or from some other source)

## Slide 14: Data acquisition module purpose
View status of the data streams
  Status for each data stream represented by the color of a corresponding button on the control panel
  Last data stream status shown in the alert message line
View status and quality of data from individual gauges
  Quality color bar time-series icons reflect data quality at primary gauge locations
  Time window identified and set in the control panel
  Icons can be set to update automatically (e.g., every 5 minutes)
Validate (edit) data from gauges
Identify usable observed data time window for modeling (i.e., select forecast time and lookback time)

## Slide 15: Data status summary table
Provides a quality color bar, number missing, and time of last value for each data set in a list of data sets
Can have as many different lists as desired, with no limit to the number of data sets in a list
Use by data analyst to evaluated data for all locations
Used by modelers to choose the forecast time

## Slide 16: Data validation editor
Combined graphical/tabular editor
Used to accept/reject/estimate/enter gage data
Run in “ad hoc” mode or list driven
  “ad hoc” by selecting series icons (shift-right mouse click), then press Validation button
  Pre-defined list
Filter list (selections) according to quality
Plot other gages for comparison

## Slide 17: Data visualization module
View hydro-meteorological state of the watershed
Animation of precipitation or temperature
  Combined “slider bar” and “VCR controls” allow user to play, fast forward, step through, etc. through gridded precipitation hours
  Placing the mouse over a grid cell shows the amount of rain for that cell for that hour
“Thumbnail” plots of data at key locations (flow, stage, reservoir data)

## Slide 18: Data visualization module
Threshold color bars depict data values over time as colors are compared to defined limits
Example:
  Green – below warning stage
  Orange – above warning, below flood stage
  Red – above flood stage
User defined threshold limits and colors
Limits and colors given in the time-series icon legend

## Slide 19: Modeling module
Model watershed and projects to:
  Forecast future flows and stages
  Determine inundation areas and flood depths
  Simulate reservoir operations
  Evaluate economic impacts
  Evaluate “what if” alternatives:
    What if there is more rain than forecasted?
    How does a change in my reservoir operation affect downstream locations?
  Results can be posted to Oracle

## Slide 20: Modeling Module
Model run:
  Meteorology (HEC-MetVue)
  Hydrology (HEC-HMS)
  Reservoir Analysis (HEC-ResSim)
  Hydraulics (HEC-RAS)
  Economics (HEC-FIA)
  Inundation maps (RAS Mapper)
Adjust model parameters native editors
View and compare results from plots or tables (via time-series icons) or from model reports
Parameters can be adjusted to improve results
  Loss rates/baseflow
  Reservoir release overrides
  Manning's n values

## Slide 21: Watershed Setup Module
Load background maps
Import models
Setup “run alternatives”
Link models (data from a  data to)
Build extract/post lists
Add and configure time-series icons

## Slide 22: Summary
CAVI (Control and Visualization Interface) serves as the front end of CWMS
CAVI is organized into functional modules
Time-series icons represent data sets at a location
A layer represents a set of objects drawn on the CAVI screen (such as background maps or a set of icons)
Each module has several tools available to aid the user
Modeling module provides a mechanism to forecast flows/stages, operate reservoirs, evaluate “what if” alternatives, etc.
Scripts provide a mechanism to perform repeated tasks

## Slide 23: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
“Just keep CWMS’ing”