## Slide 1: CWMS CAVI Orientation
Matt Fleming, P.E.
Hydrologic Engineering Center
CWMS Prospect Course
CAVI Components

## Slide 2: Overview
Introduce the CWMS Control and Visualization Interface (CAVI)
  Screen Components
  Layers
  Time-Series Icons
  Scripts
Introduce CAVI components and modules
  Modules
    Purpose and use
  Available tools

## Slide 3: CAVI Purpose
Serves as the main interface to CWMS
Access and manipulate data and models:
  View status of data feeds and gauge quality
  Validate data
  View hydro-meteorological conditions of the watershed
  Plot, tabulate, and edit data
  Run models and view results
CAVI organizing unit is called the “Watershed”, which contains data and models

## Slide 4: Screen components
Menu
Module Tab
Tool bar buttons
Map Panel
Control Panel
Map mouse functionality and tools
Map status line
Message area

## Slide 5: Layers
A “Layer” is a set of objects drawn in the CAVI map(s).
Example layers include:
  Background images or map layers
    Internet Map
    Aerial photos or other geo-referenced images
    Subbasin, stream outline maps (e.g., shapefiles)
    County/political boundaries
  Grids (precipitation, temperature, etc.)
    From the visualization tab
  “Stream Alignment”
  Model representation
Time-series icons can be divided into sub-layers:
  Flow, stage, or precipitation layers
  Raw or validated data layer
  Thumbnail plot or color bar layer

## Slide 6: Time-series icons
A time-series icon represents a location that is associated with one or more data sets
The data sets are usually time-series data and can be from Oracle or HEC-DSS
  Observed raw data from Oracle
  Validated data from Oracle
  Model results from HEC-DSS
Paired curve data may be displayed from an icon (but not with time-series data in the same icon).
Icons can show an image, document, a live video with the icon, etc

## Slide 7: Time-series icons
Each time-series icon data set is associated with an icon style for each module:
  Graphic Symbol
  Dot
  Thumbnail Plot
  Quality Color Bar
  Threshold Color Bar
  None
For example, a flow data set may be represented by:
  A quality color bar in Data Acquisition
  A thumbnail plot in Data Visualization
  A graphic symbol in Model Interface

## Slide 8: Time-series plots and Tables

## Slide 9: scripts
Scripts are a set of text instructions to perform common tasks:
  Plots of data from different locations (e.g., main steam gages)
Setup/edit scripts from the “Scripts” menu
Run scripts from:
  “Script Buttons” in a separate window or in the lower portion of the control panel
  From a “script schedule” for automatic execution

## Slide 10: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
“Just keep CWMS’ing”