## Slide 1: CWMS CAVI Orientation
Matt Fleming, P.E.
Hydrologic Engineering Center
CWMS Prospect Course
CAVI Modules

## Slide 2: Overview
Introduce the CWMS Control and Visualization Interface (CAVI)
  Screen Components
  Layers
  Time-Series Icons
  Scripts
Introduce CAVI components and modules
  Modules
    Purpose and use
  Available tools

## Slide 3: Cavi login
You can login to access data from the CWMS Oracle database on the server or run locally if you have the data (already downloaded or from some other source)

## Slide 4: Data acquisition module purpose
View status of the data streams
  Status for each data stream represented by the color of a corresponding button on the control panel
  Last data stream status shown in the alert message line
View status and quality of data from individual gauges
  Quality color bar time-series icons reflect data quality at primary gauge locations
  Time window identified and set in the control panel
  Icons can be set to update automatically (e.g., every 5 minutes)
Validate (edit) data from gauges
Identify usable observed data time window for modeling (i.e., select forecast time and lookback time)

## Slide 5: Data status summary table
Provides a quality color bar, number missing, and time of last value for each data set in a list of data sets
Can have as many different lists as desired, with no limit to the number of data sets in a list
Use by data analyst to evaluated data for all locations
Used by modelers to choose the forecast time

## Slide 6: Data validation editor
Combined graphical/tabular editor
Used to accept/reject/estimate/enter gage data
Run in “ad hoc” mode or list driven
  “ad hoc” by selecting series icons (shift-right mouse click), then press Validation button
  Pre-defined list
Filter list (selections) according to quality
Plot other gages for comparison

## Slide 7: Data visualization module
View hydro-meteorological state of the watershed
Animation of precipitation or temperature
  Combined “slider bar” and “VCR controls” allow user to play, fast forward, step through, etc. through gridded precipitation hours
  Placing the mouse over a grid cell shows the amount of rain for that cell for that hour
“Thumbnail” plots of data at key locations (flow, stage, reservoir data)

## Slide 8: Data visualization module
Threshold color bars depict data values over time as colors are compared to defined limits
Example:
  Green – below warning stage
  Orange – above warning, below flood stage
  Red – above flood stage
User defined threshold limits and colors
Limits and colors given in the time-series icon legend

## Slide 9: Modeling module
Model watershed and projects to:
  Forecast future flows and stages
  Determine inundation areas and flood depths
  Simulate reservoir operations
  Evaluate economic impacts
  Evaluate “what if” alternatives:
    What if there is more rain than forecasted?
    How does a change in my reservoir operation affect downstream locations?
  Results can be posted to Oracle

## Slide 10: Modeling Module
Model run:
  Meteorology (HEC-MetVue)
  Hydrology (HEC-HMS)
  Reservoir Analysis (HEC-ResSim)
  Hydraulics (HEC-RAS)
  Economics (HEC-FIA)
  Inundation maps (RAS Mapper)
Adjust model parameters native editors
View and compare results from plots or tables (via time-series icons) or from model reports
Parameters can be adjusted to improve results
  Loss rates/baseflow
  Reservoir release overrides
  Manning's n values

## Slide 11: Watershed Setup Module
Load background maps
Import models
Setup “run alternatives”
Link models (data from a  data to)
Build extract/post lists
Add and configure time-series icons

## Slide 12: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
“Just keep CWMS’ing”