## Slide 1: CWMS Real-Time Modeling
Russell Errett, P.E.
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
  Identify basic concepts for building a new CAVI watershed and about running real-time forecast simulation models in CWMS
  Quick overview on CAVI watershed model development
    Steps to create new CAVI watershed for use in real-time modeling
  Using CWMS for real-time modeling
    Creating a forecast
    Time windows and forecast times
    Data Status Summary Report
    Editing and running models
    Evaluating results
    Time-series icons for model results
    Saving models and results

## Slide 3: CWMS Modeling

## Slide 4: Defining CAVI Watershed Locations
X

## Slide 5: CAVI Modeling SETUP

## Slide 6: CWMS Modeling Setup
  These are the key steps if you are building a CWMS watershed from scratch
  From the Setup Tab create a watershed from FileNew Watershed
  Import all the standalone models into the CAVI
    MetVue, HMS, ResSim, RAS, FIA
  Define Program Order
  Define Model Alternative Keys
    MetVue requires additional steps prior to assigning a model alternative key (discussed later)
  Create Forecast Run Alternatives (i.e., what models to run together)
  Setup Model Linking
  Setup Extract Lists
  Setup Post Lists (can be done later)
  Create a Forecast and test and resolve any steps above

## Slide 7: Creating a New CAVI Watershed

## Slide 8: CAVI Modeling Setup

## Slide 9: CAVI Model Imports

## Slide 10: CAVI Program Order

## Slide 11: CAVI Model Alternative Keys

## Slide 12: CAVI Forecast Run Alternatives

## Slide 13: CAVI Model Linking

## Slide 14: CAVI Extract Lists

## Slide 15: CWMS Real-Time Modeling

## Slide 16: CWMS Modeling

## Slide 17: Create a Forecast
  A forecast can be created once:
    All the necessary models are imported
    A forecast run alternative is created
    Model linking is accomplished
      This step can be done from the modeling tab within an active forecast
    Extract lists are developed
  Forecast directory will be created
    Default name is Forecast Time in YYYY.MM.DD-HHMM TZ
  Model alternative files used in the forecast run alternatives selected are copied to the forecast directory
  Data will be extracted from source location to the forecast.dss file (as defined in extract list)
    Oracle
    CDA
    Cumulus
    Local and/or Remote DSS files

## Slide 18: Time Windows
OBS
No QPF
QPF
Extract Start
Start Time
Forecast Time
End Time
Observed Data
Forecast Data
Model Simulation Window

## Slide 19: Start Time
  Start Time is the time that the models begin simulating
  Choose a time that:
    Is far enough before time of forecast so that water has time to route through the routing reaches (i.e., time for water to flow from upper junction to lowest junction)
    Prior to start of event in question
    Typically, 4-10 days
Notes: Time Windows and Forecast Times
4. Starting date/time of the simulation. AKA – lookback time.
    Where the observed data used in the simulation begins. HMS and RAS start simulating at this time.
    CWMS is event-oriented. In order to calibrate HMS loss rate and base flow parameters, the start time should be prior to the start of the rainfall for the initial forecast of the event.
      Typically greater than 6 hours, and less than 2 weeks.
    For HMS, If it’s been raining for an extended period:
      Select an appropriate lull in the storm.
Set your initial loss rate low, close to the constant loss rate.
Set your base flow to what it was prior to the event. (it won’t have much effect at this point)
Set an appropriate recovery rate in the “Deficit-Constant” HMS/HFP editor
If it hasn’t rained yet:
  Generally, set the starting time to greater than the routing time from the top of the watershed to the outlet.
  Long enough to estimate base flow parameters.
For ResSim, the lookback window should be at least as long as it takes to route flow from the upstream-most reservoir to the downstream-most control point.
For RAS, the lookback period should reflect a period of reasonably steady flows throughout the basin.

## Slide 20: Extract Start
  Extract Start is often the same as the Start Time
  Typically used when a value just before the start time is needed for a computation.
    Observed data is in varying time steps, some longer than the compute interval
    Observed data has an offset from the interval so a value is not extracted at the start time.
    Your compute is period average, but your data is instantaneous, so a “start of period” value is needed to compute the first period’s average.
  Or you just want to see more observed data than will be used in the simulation.

## Slide 21: Data Status Summary Report

## Slide 22: Forecast Time
  Forecast Time is the time at which observed data runs out and you are predicting stream flow and river and reservoir stages
  For real-time forecasting, typically not earlier than previous hour
    Need time for all the stream gage data within the watershed to be transmitted and processed
    Time for all the gridded data to be processed
  Many offices have a default/standardized initialization time used for daily forecasting
    For example 07:00 am local time
      12:00 UTC for Central Time Zone

## Slide 23: End Time
  End Time is the time where models stop simulating (i.e., end of forecast)
  Many offices have a default/standardized initialization time used for End Time
    For example, the length of forecast will dictate the End Time
      i.e., Forecast length of 5-days, 7-days, or 14-days
  Other questions and data constraints can influence length of forecast or End Time
    How long to evacuate flood storage
    Drought forecasting
    How much and accuracy of existing meteorological forecast data
    Limitations in model computational time
      i.e., detailed 2D RAS models running for 2 weeks versus 6 months of data

## Slide 24: Default Time Window

## Slide 25: CAVI Watershed Folder Structure
  The CAVI works only with files in preselected folders called Watershed Locations
  There are 3 sets of folders created within a Watershed Location
    watershed
      Watersheds are created and stored in a folder named “watershed”
      The watershed folder is often referred to as “Base” or “Setup”
        Watershed = Base = Setup
    forecast
      When a forecast is created, a subset of the watershed is copied to the forecast folder
    database
      Folder to store supplemental DSS records (i.e. ratings, cumulus grids, USGS downloaded data, etc.) or any other reference material to support modeling (SOPs, contact list, etc.)

## Slide 26: CAVI Watershed Folder Structure

## Slide 27: Computing the Models

## Slide 28: Computing the Models
  3 ways to compute CWMS models from a forecast:
    Highlight forecast run alterative OR individual model alternative:
      Right click and Compute
      Compute from Actions Tab below
        Hold Control to force recompute for either option
    Navigate to ForecastCompute Manager
      Select one or multiple forecast alternatives to have the CAVI compute
        These are not computed simultaneously, rather in sequence
Notes:   Editing And Running Models
  Run all models for a forecast run by selecting the forecast, and then:
    Right clicking and selection the “Compute” menu.
    Selecting the Compute Button in the Actions Panel.
  Run an individual model by selecting the model in the Forecast run panel, then pressing the “Compute” button in the Actions panel.
    Will run any models in the sequence before it that needs to be run.
    Select “Force Recompute” checkbox to force all prior models to be re-computed.
      You can also hold the Control key on the keyboard when you click the compute button to force a recompute.

## Slide 29: Computing the Models
Notes:   Editing And Running Models
  After choosing to compute, the compute progress dialog will open.
    This dialog box gives useful output detailing any issues found throughout the forecast run for any of the models being computed.

## Slide 30: Viewing the Results

## Slide 31: Viewing Results
  Output is available from:
    Forecast Run Alternative modeling tree
    Reports Tab below modeling tree
    From the modeling schematic in the CAVI Modeling map window
    Opening the specific model from the standalone application (i.e., HMS, ResSim, RAS)
    Or opening the forecast.dss file via CWMS-Vue and sorting the results based upon the model results F-Part
View Results

## Slide 32: Edit Model Parameters
  Multiple ways to get to access model editors

## Slide 33: Saving and Posting Results

## Slide 34: Saving to Base & Replace From Base
Save To Base
  If you have made changes and want them available for future forecast creations
    Changes such as:
      Adjustments to guide curve or zones
      Adjustments to Max-Min Release rules
      Rating curve updates with models
      HMS zonal parameters
      RAS roughness coefficient calibrations
  If you make changes and cannot undo them
    Too many changes in the HMS zonal parameter editor
    Modifications to ResSim rules or zones that you want undo
    RAS model modifications that need undone
      Cross-Sectional edits
      Manning's n changes
      Roughness coefficients
Replace From Base
  Check with your office’s procedure on leveraging these options
    Some offices prohibit Saving to Base to preserve the Base directory

## Slide 35: SavE to Base & Replace From Base

## Slide 36: Posting Results
  Posting results allow for other CAVI watersheds to extract modeled data and to exchange data to other users for other purposes
    Posting to CDA GIS dashboards to access (EOC, EMs, Division, etc.)
    Posting to CDA or CWMS database allows for exchange with other downstream watersheds for boundary conditions
      Inter-district watersheds, downstream district, or exchange with NWS via shef
  Posting to database or remote DSS file for evaluating forecast accuracy
    Versioning of time-series (i.e., many forecast under same time-series)

## Slide 37: Posting Results

## Slide 38: CWMS Forecasting Methodologies

## Slide 39: CWMS Forecasting Methodologies
  There are a couple competing methodologies for performing daily CWMS forecasting (not a competition…or is it)
    Create a new forecast each day
      Fresh extract of data (time-series and gridded data)
      Many offices set the lookback is at least 30 days back (i.e., initial conditions have less influence on current conditions
      This methodology is advantageous if you have multiple watersheds to run and manage as keeping up with various start times and when to reset can be difficult
    Continuous forecasting
      Initialize the CAVI forecast at a time between events when initial baseflow is at it’s lowest
      Move Forecast Time and End Time by one day for daily forecasting
      Extract only the missing data needed (i.e., last 24 hrs)
      This methodology is advantageous if you have only one or a limited number of watersheds to run and manage

## Slide 40: Team Forecasting
  Team forecasting improves:
    The ability to sync CAVI watershed updates amongst multiple Water Managers
    Syncing and sharing active forecasts with Water Managers and H&H modelers
      Hydrology Team  Reservoir Regulation Team  Hydraulic Team  Economist
  Team Forecasting can be used for archiving CAVI watershed models as a backup

## Slide 41: Team Forecasting

## Slide 42: ? ? ? Questions ? ? ?