## Slide 1: CWMS Real-Time Modeling
Russell Errett, P.E.
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
  Identify basic concepts for building a new CAVI watershed and about running real-time forecast simulation models in CWMS
  Quick overview on CAVI watershed model development
    Steps to create new CAVI watershed for use in real-time modeling
  Using CWMS for real-time modeling
    Creating a forecast
    Time windows and forecast times
    Data Status Summary Report
    Editing and running models
    Evaluating results
    Time-series icons for model results
    Saving models and results

## Slide 3: Computing the Models

## Slide 4: Computing the Models
  3 ways to compute CWMS models from a forecast:
    Highlight forecast run alterative OR individual model alternative:
      Right click and Compute
      Compute from Actions Tab below
        Hold Control to force recompute for either option
    Navigate to ForecastCompute Manager
      Select one or multiple forecast alternatives to have the CAVI compute
        These are not computed simultaneously, rather in sequence
Notes:   Editing And Running Models
  Run all models for a forecast run by selecting the forecast, and then:
    Right clicking and selection the “Compute” menu.
    Selecting the Compute Button in the Actions Panel.
  Run an individual model by selecting the model in the Forecast run panel, then pressing the “Compute” button in the Actions panel.
    Will run any models in the sequence before it that needs to be run.
    Select “Force Recompute” checkbox to force all prior models to be re-computed.
      You can also hold the Control key on the keyboard when you click the compute button to force a recompute.

## Slide 5: Computing the Models
Notes:   Editing And Running Models
  After choosing to compute, the compute progress dialog will open.
    This dialog box gives useful output detailing any issues found throughout the forecast run for any of the models being computed.

## Slide 6: Viewing the Results

## Slide 7: Viewing Results
  Output is available from:
    Forecast Run Alternative modeling tree
    Reports Tab below modeling tree
    From the modeling schematic in the CAVI Modeling map window
    Opening the specific model from the standalone application (i.e., HMS, ResSim, RAS)
    Or opening the forecast.dss file via CWMS-Vue and sorting the results based upon the model results F-Part
View Results

## Slide 8: Edit Model Parameters
  Multiple ways to get to access model editors

## Slide 9: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams