## Slide 1: CWMS Real-Time Modeling
Russell Errett, P.E.
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
  Identify basic concepts for building a new CAVI watershed and about running real-time forecast simulation models in CWMS
  Quick overview on CAVI watershed model development
    Steps to create new CAVI watershed for use in real-time modeling
  Using CWMS for real-time modeling
    Creating a forecast
    Time windows and forecast times
    Data Status Summary Report
    Editing and running models
    Evaluating results
    Time-series icons for model results
    Saving models and results

## Slide 3: Saving and Posting Results

## Slide 4: CAVI Watershed Folder Structure
  The CAVI works only with files in preselected folders called Watershed Locations
  There are 3 sets of folders created within a Watershed Location
    watershed
      Watersheds are created and stored in a folder named “watershed”
      The watershed folder is often referred to as “Base” or “Setup”
        Watershed = Base = Setup
    forecast
      When a forecast is created, a subset of the watershed is copied to the forecast folder
    database
      Folder to store supplemental DSS records (i.e. ratings, cumulus grids, USGS downloaded data, etc.) or any other reference material to support modeling (SOPs, contact list, etc.)

## Slide 5: CAVI Watershed Folder Structure

## Slide 6: Saving to Base & Replace From Base
Save To Base
  If you have made changes and want them available for future forecast creations
    Changes such as:
      Adjustments to guide curve or zones
      Adjustments to Max-Min Release rules
      Rating curve updates with models
      HMS zonal parameters
      RAS roughness coefficient calibrations
  If you make changes and cannot undo them
    Too many changes in the HMS zonal parameter editor
    Modifications to ResSim rules or zones that you want undo
    RAS model modifications that need undone
      Cross-Sectional edits
      Manning's n changes
      Roughness coefficients
Replace From Base
  Check with your office’s procedure on leveraging these options
    Some offices prohibit Saving to Base to preserve the Base directory

## Slide 7: SavE to Base & Replace From Base

## Slide 8: Posting Results
  Posting results allow for other CAVI watersheds to extract modeled data and to exchange data to other users for other purposes
    Posting to CDA GIS dashboards to access (EOC, EMs, Division, etc.)
    Posting to CDA or CWMS database allows for exchange with other downstream watersheds for boundary conditions
      Inter-district watersheds, downstream district, or exchange with NWS via shef
  Posting to database or remote DSS file for evaluating forecast accuracy
    Versioning of time-series (i.e., many forecast under same time-series)

## Slide 9: Posting Results

## Slide 10: CWMS Forecasting Methodologies

## Slide 11: CWMS Forecasting Methodologies
  There are a couple competing methodologies for performing daily CWMS forecasting (not a competition…or is it)
    Create a new forecast each day
      Fresh extract of data (time-series and gridded data)
      Many offices set the lookback is at least 30 days back (i.e., initial conditions have less influence on current conditions
      This methodology is advantageous if you have multiple watersheds to run and manage as keeping up with various start times and when to reset can be difficult
    Continuous forecasting
      Initialize the CAVI forecast at a time between events when initial baseflow is at it’s lowest
      Move Forecast Time and End Time by one day for daily forecasting
      Extract only the missing data needed (i.e., last 24 hrs)
      This methodology is advantageous if you have only one or a limited number of watersheds to run and manage

## Slide 12: Team Forecasting
  Team forecasting improves:
    The ability to sync CAVI watershed updates amongst multiple Water Managers
    Syncing and sharing active forecasts with Water Managers and H&H modelers
      Hydrology Team  Reservoir Regulation Team  Hydraulic Team  Economist
  Team Forecasting can be used for archiving CAVI watershed models as a backup

## Slide 13: Team Forecasting

## Slide 14: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams