## Slide 1: Forecasting with Ensembles in CWMS
Simon Evans, P.E., CFM
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
Sources of Ensemble Forecasts
HEC-ResSim Ensemble Compute
CAVI Ensemble Compute
Ensemble Forecast Processor
Ensemble Viewer

## Slide 3: CUMULUS
CWMS supports Cumulus directly:
CorpsNet/VPN access with CAC authentication
https://cumulus.corps.cloud/
HRRR – 1hr
NBM – 1hr
NDFD – 6hr
WPC – 6hr
NAEFS – 6hr

## Slide 4
Deterministic Forecast
Ensemble Forecast - 5 Day
Ensemble Forecast - 10 Day
Russian River – Hopland
California Nevada RFC
March Ensemble Forecast

## Slide 5
Deterministic Forecast
Ensemble Forecast - 5 Day
Ensemble Forecast - 10 Day
Russian River – Guerneville
California Nevada RFC
March Ensemble Forecast

## Slide 6: HEC-ResSIm Ensemble Compute
DSS
HEC-ResSim
DSS
1
2
3
n
1
2
3
n
Ensemble
of Input
Reservoir Inflows
Ensemble
of Computed Reservoir Outflows

## Slide 7: CAVI Ensemble Compute
What does it do?
  Each trace used sequentially in an isolated pass through the Program Order
  Each trace generates a separate watershed “run” folder in the forecast
  Results in separate forecast.dss files, then rolled into a master forecast.dss at end.
  Current Limitations
  Ensemble input data only from HEC-DSS, not CWMS Database
  Gridded ensembles not yet supported
  Lacks dedicated tools for reviewing and analyzing results

## Slide 8: Ensemble Forecast Processor (EFP)
What does it do?
  New plugin first available in CWMS 3.4
  Based on HEC-WAT FIRO Forecast Processor
  Part of the Program Order
  Allow user to specify locations within the watershed to calculate statistical metrics from ensemble time series.
  Metrics can be used as input to other applications within the CWMS forecast

## Slide 9: Ensemble Forecast Processor
  Metrics to be computed can either be Scalar or time series
  Scalar metrics:
  Can be used to influence rules in ResSim Alternative (FIRO)
  User defined alternatives
  Based on Prado FIRO Case Study approach

## Slide 10: Ensemble Forecast Processor
  Time Series metrics
  Allow for reduced number of ensemble members to be used for input to other models
  For a chosen metric(s) return the specific ensemble member that has the closest volume
  If applicable merge observed time series with the returned ensemble member

## Slide 11: Summarized ensemble forecast
Raw
HEFS Data
Extract
Ensemble Forecast
Processor (EFP)
HEC-RAS + HEC-FIA
DSS
Ensemble DSS
Ensemble DSS
Regulated Flows
Ensemble CSV
Regulated Flows
Metric Data + Uncontrolled Flows
Metric Data
HEC-MetVue
+
HEC-HMS
HEC-ResSim
Gridded DSS
Uncontrolled Flows

## Slide 12: Regulated ensemble forecast
Raw
HEFS Data
Extract
Ensemble
HEC-ResSim
HEC-RAS + HEC-FIA
DSS
Ensemble DSS
Ensemble DSS + Uncontrolled Flows
Ensemble Summary
Ensemble CSV
Ensemble Summary
Regulated Ensemble DSS
HEC-MetVue
+
HEC-HMS
Ensemble Forecast
Processor (EFP)
Gridded DSS
Uncontrolled Flows
Regulated Ensemble DSS

## Slide 13: Ensemble Viewer
Allows user to view ensemble time series
Ability to view ensemble metrics that summarize the ensembles as a single summary time series, single value for each ensemble, or as a single summary value
Available from the CAVI under > Tools

## Slide 14: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams