## Slide 1: Real Time Data IN CWMS
Kat Feingold
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: objective
Identify the types of real-time data and their management in CWMS

## Slide 3: Overview
  CWMS Real-Time Data Types & Viewing
  CWMS Data Sources
  CWMS Data Processing
  CWMS Data Storage Systems
  CWMS Data Acquisition
Notes: Overview
  There are two categories of real-time data:
    Time Series
    Grids
  CWMS Data Sources include:
    USGS and USACE gaging station networks
    National Weather Service meteorological data products
      USACE Cumulus gridded data web service
    Other agencies gaging station networks
  CWMS Data Processing is done through manual and automated means for:
    Time Series Data
      Manual Data Quality Control through the CWMS/CWMSVue Validation Editor
      OpenDCS CWMS Computational Processor (CCP)
      DSS Scripting
    Gridded Data
      Manual Edits using HEC-MetVue Interactive Features
      Automatic Processing based on HEC-MetVue project and session settings
        Missing Data Filing
        Dataset Merging
        Temporal Aggregation/Disaggregation
        Spatial Aggregation/Averaging
        MetInterp Point-to-TIN/Grid Spatial Interpolation
  Data is stored in two different storage systems:
    CWMS Oracle database
    Remote and Local DSS files
  CWMS Data Acquisition and Access Modes
    Data Acquisition is based on:
      Realtime telemetry
      Federal/State/Local Direct Data Exchange
      Federal/State/Local/Public Web Services
    CWMS can run in two different “modes” to access data:
      Client-Server Mode (requires authentication)
      Local (HEC-RTS) mode

## Slide 4: CWMS Real-time data types & Viewing

## Slide 5: Real-time Data Types in CWMS
Time Series
Grids
  Examples:
    Flow at a gage
    Elevation of a reservoir
  Storage
    HEC-DSS files
    CWMS Oracle Database
  Examples:
    Precipitation estimates from RADAR
    Precipitation Forecasts
    Snow state grids from SNODAS
  Storage:
    HEC-DSS files
    Other Files (GRIB, NetCDF, etc)
Notes: III. Presentation
Real-Time Data Types
  There are two categories of real-time data in CWMS
    Time Series Data
      Examples: Flow at a Gage, Elevation of a Reservoir
      Time series data can be stored in:
        HEC-DSS files
        CWMS Oracle Database
    Grids
      Examples: RADAR precipitation estimates, Snow state grids from SNODAS
      Grids are stored in DSS files (Not in ORACLE database)
        CWMS separates large grid data sets into monthly DSS files with standard naming
        For example, Precipitation grids: “precip.yyyy.mm.dss”, “precip.2017.01.dss”
      Grids can be stored in other file formats (GRIB, netCDF)

## Slide 6: DSS/CWMS Display of Time Series
Notes:   DSS/CWMS Display of Time Series
    Time series data can be tabulated or graphed in DSSVue / CWMS-Vue
    Many HEC model programs share a common graphics / display library
    Graphs and tables can be customized or produced by scripts

## Slide 7: DSS File – Time Series Catalog
Notes: Real-Time Data Types
    DSS File Time Series Catalog
      DssVue shows a list or “catalog” of contents of a DSS file
      DSS record types (including Time Series) are identified by a 6-part “path name” (A, B, C, D, E, F)

## Slide 8: CWMS Database Time Series Catalog
Notes:     CWMS Database Time Series Catalog
      CWMS-Vue shows a list of time series stored in CWMS Oracle database
      Time Series are identified by 6-part “time-series identifier”
      In CWMS 3.3, CWMS-Vue can display location metadata, rating curves, and other information

## Slide 9: DSS Display of Grids
Notes:   DSS Display of Grids
    Grids are stored in DSS files. DSSVue and CWMS-Vue are capable of displaying grids and metadata
    Grids can be displayed graphically
      Accomplished by clicking the “plot” icon
      Background maps are not displayed in DSSVue or CWMS-Vue
    Grid metadata (text format) can be viewed
      Accomplished by clicking the “tabulate” icon
      “Tabulate” shows grid metadata and summary, not array of cell values

## Slide 10: Standard hydrologic grid (SHG)
  Based on Albers Equal-Area map of the US
  Same coordinate system used by USGS for nation-wide mapping
  Locations are identified by cell indices (row and column numbers)
Notes:     Standard Hydrologic Grid (SHG)
      Coordinate system is valid in the contiguous United States
      Based on Albers Equal-Area map of US
      Same coordinate system used by USGS for nationwide mapping
      Locations are identified by cell indices (row and column numbers)

## Slide 11: Cavi display of time series and grids
Notes: Real-Time Data Types
    CAVI Display of Time Series and Grids
      Grids can be displayed in map context in Data Visualization and Modeling modules of CAVI

## Slide 12: HEC-MetVue Display of Grids
  MetVue Map Window
  CAVI Map Window

## Slide 13: DSS File – grids catalog
Notes:     DSS File Catalog of Grids
      Grids are displayed similarly to time-series data in DSSVue and CWMS-Vue
      Grids are stored using a 6-part pathname (A, B, C, D, E, F)
        A-Part: Coordinate System Reference (Typically SHG for “Standard Hydrologic Grid”)
        B-Part: Location
        C-Part: Parameter
        D-Part/E-Part: Timestamp
        F-Part: Version

## Slide 14: HEC-MetVue – Data Reader

## Slide 15: CWMS Data Sources

## Slide 16: Time Series data Sources
  USACE
  USGS https://waterdata.usgs.gov/nwis/rt https://dashboard.waterdata.usgs.gov/
  Other (Federal/State/Local)

## Slide 17: Gridded data sources - Cumulus
  https://cumulus.corps.cloud
  Web service single point of meteorological data access available to USACE WM and HH&C
  Requires CorpsNet Access
    Either Direct or VPN
  Direct Cumulus extract via the CAVI
    Watershed or Area of Interest extents
Notes: Cumulus is a gridded meteorological data repository that serves the Corps Water Management and Hydrologic and Hydraulic Communities of Practice. Cumulus is a web service that provides on-demand data access through its primary website https://www.cumulus.corps.cloud as well as an (API) that can be used by software programs or other web services to access through custom interface or automated means.
Product – Provides a list of all available historic, real-time, and forecast meteorological parameters
Filtered by
  Corps Office – Filter the applicable watersheds for the selected office
  Watershed – Determines the clipping extents for the dataset download
  Time Window – Defines the start and end dates and times for the dataset download
Cumulus is only available through CorpsNet. And requires, CAC authentication is required to download datasets.

## Slide 18: Additional Gridded data sources
  RFC – River Forecast Center
    https://water.weather.gov/ahps/rfc/rfc.php
  NBM – National Blend of Models
    https://vlab.noaa.gov/web/mdl/nbm
  NCEP – National Center for Environmental Predictions
    https://nomads.ncep.noaa.gov
  NDFD – National Digital Forecasting Database
    https://vlab.noaa.gov/web/mdl/ndfd
Notes:   Gridded Precipitation and Temperature Data Sources
    Data Sources Overview
      River Forecast Centers distribute grids of QPE and QPF (Quantitative Precipitation Estimate/Forecast)
      Nationwide grids are available from several sources
        National Digital Forecast Database (NDFD)
        National Digital Guidance Database (NDGD)
        National Center for Environmental Predictions (NCEP)
        Weather Prediction Center (WPC)
        National Operational Hydrologic Remote Sensing Center (NOHRSC)
      Nationwide grids are collected and processed for use in CWMS at the Central Processing Center and can be distributed to your office for use in CWMS modeling

## Slide 19: Precipitation forecast (QPF)
Notes:     Data Sources Details
      NDFD Precipitation Forecast (QPF)
        From National Weather Service National Digital Forecast Database
        Resampled to 2km SHG and stored in DSS records at CPC
        Can be distributed to division/district offices
        Supplement to QPF from River Forecast Center

## Slide 20: Temperature Forecast (QTf)
Notes:       NDFD Temperature Forecast
        From National Weather Service National Digital Forecast Database
        Resampled to 2km SHG and stored in DSS records at CPC
        Can be distributed to division/district offices
        Available for use in snow forecasts or with Gridded Hamon evaporation

## Slide 21: Example Snodas
  Snow Data Assimilation System (SNODAS)
Notes:       SNODAS grids from NOHRSC
        SNODAS is the primary source of gridded snow data used in CWMS snowmelt models in the Corps
        Hourly/Daily gridded snow products for conterminous U.S.
        Based on an energy balance snow model combined with multi-sensor snow observations
        Spatial Resolution: 1 sq km resolution
        Available period of record: October 2003 – Present
        Additional information available at http://www.nohrsc.noaa.gov/

## Slide 22: CWMS Data Processing

## Slide 23: Time-series Data processing
Data Types
Data Processing
  Observation
    Stage gage
    Rain gage
    Thermometer
  Derived
    Flow from stage & rating
    Storage from elevation & rating
    Model Results
  CWMS/CWMSVue Validation Editor
  CWMS Computational Processor (CCP)
  DSS Math functions and Scripts
Notes: Real-Time Data Types
    Time-Series are obtained and transformed in a variety of ways
      Time-series can be obtained from direct observation or derived
        Examples of time-series data from direct observations
          River stage gage
          Precipitation gage
          Thermometer
        Examples of time-series derived using direct observations and computations
          Flow from stage & stage-flow rating
          Storage from elevation & elevation-storage curve
      There are several tools available for processing and modifiying time series data.
        CWMS and CWMSVue Data Validation Editor
        CWMS Computational Processor (CCP)
        DSS Math functions and Scripts

## Slide 24: CAVI/CWMSVue Validation Editor
  Interactive Data Review & Editing
    Set value as missing
    Set specified value
    Fill – Linear
    Fill – Repeat
    Fill – Raw
    Add a constant value
    Multiply by a factor

## Slide 25: OpenDCS Cwms Computational Processor (CCP)
  Example Functions
    Average
    Fill Forward
    Disaggregate
    Inflow computation
  References
    Main Documentation https://opendcs-env.readthedocs.io/en/latest/
    Standard Algorithms https://opendcs-env.readthedocs.io/en/latest/resources-algorithms.html
    Custom Python Algorithms https://opendcs-env.readthedocs.io/en/latest/resources-algorithms.html#opendcs-custom-python-algorithms

## Slide 26: Hec-dss Math functions & Scripts
  Example Functions
    Estimate Missing Values
    Replace Specific Values
    Screen using Minimum and Maximum
    Change Time Interval
    Irregular to Regular
    Rating Table
    Reverse Rating Table
    Moving Average
  References
    HEC-DSSVue Users Manual https://www.hec.usace.army.mil/confluence/dssdocs/dssvueum/math-and-statistical-functions https://www.hec.usace.army.mil/confluence/dssdocs/dssvueum/scripting/math-functions
    HEC-DSSVue Github Scripts Repo https://github.com/HydrologicEngineeringCenter/DSSVue-Example-Scripts/tree/master/src
https://github.com/HydrologicEngineeringCenter/DSSVue-Example-Scripts/blob/master/src/change-interval.py

## Slide 27: Grid Data processing
Data Types
Data Processing
  Observation
    RADAR
    Aircraft and Satellite Remote Sensing
  Derived
    Interpolation from point measurements
    Model Results
  HEC-MetVue
    Missing Data Filing
    Dataset Merging
    Temporal Aggregation/Disaggregation
    Spatial Aggregation/Averaging
    TIN-to-Grid and Grid-to-TIN
    MetInterp
      Point-to-TIN/Grid Spatial Interpolation
Notes:     Grids are obtained and transformed in a variety of ways
      Grids can be obtained from direct observations
        RADAR
        Remote Sensing (from Satellite or Aircraft)
      Grids can be derived from direct observations (point or gridded).
        Interpretation of Remote Sensing products
        Interpolation from point measurements to TIN (Triangulated Irregular Network) and Grid.
        There are many derived grids available from Weather Service Models/Processes
          RTMA (Real-Time-Mezzoscale-Analysis)
          MRMS (Multi-Radar-Multi-Sensor)
          SNODAS (SNOw Data Assimilation System)
          HRRR (High-Resolution-Rapid-Refresh)
          Others
      HEC-MetVue offers a number of spatial data processing methods:
      Missing Data Filing
      Dataset Merging
      Temporal Aggregation/Disaggregation
      Spatial Aggregation/Averaging
      TIN-to-Grid and Grid-to-TIN
      HEC-MetVue also provides for Point-to-TIN or Point-to-Grid spatil interpolation with a methods, including
        Inverse-Distance
        Inverse-Distance Squared
        Nearest Neighbor
        Bilinear

## Slide 28: HEC-MetVue Data Processing
Temporal Disaggregation
Dataset Merging
Missing Data Filling
Spatial Interpolation

## Slide 29: Data storage Systems

## Slide 30: Data storage systems in cwms
CWMS Database
HEC-DSS Files
  Runs on a CWMS T7 Server or Cloud Server
  Oracle-Based Relational Database System
  Supports enterprise-scale data operations
  AIS (Automated Information System)
  Requires authenticated login
  Stored on
    Windows PC
    CWMS server
  Optimized for data sequences like time series
  Local DSS requires no login
Notes: Data Storage Systems in CWMS
  Data in CWMS is stored in two forms, CWMS Oracle Database and DSS Files
    CWMS Database:
      Runs on CWMS server (locally or in the cloud)
      Oracle Relational Database System
      Supports enterprise-scale data operations
      Army AIS (Automated Information System)
      Requires Authenticated Login
    DSS Files:
      Stored on CWMS server (locally or in the cloud)
      Stored on PC or Server file system
      Optimized for data sequences like time series
      No login required for local DSS file operations

## Slide 31: Files and directories for cwms data
Notes: Data Storage Systems in CWMS
  Files and Directories for CWMS Data
    Top directCWMS server the top directory is set by $CWMS_HOME environment variable
    config directory holds relatively static setup for data acquisition (da) processes
      MetInterp configuration files are saved in the config directory
      ProcessSheffit criteria files
    ory (CWMS_CLASS here) is left to user choice
    On dated directory contents change as data collection and transformation processes run
      DSS files for grids are stored in dated/db/grid
      Temporary files required by data processing programs
      Log files
    database directory hold DSS files for time series in “Local Mode” (RTS)
      In Corps production systems, this is replaced by the CWMS Oracle database
      There is no “database” directory on CWMS server

## Slide 32: Cwms data Acquisition

## Slide 33: District/division data acquisition
Federal/state/Local Agency
Satellite
Telemetry
Data
VHF
Line-of-
Sight
Data
Dedicated Line
Data Exchange
Internet
Data Exchange
Server-based
Water
Management
System
Instructions To and
From Dam Operator
Local Water Management Office
Federal/State/Local Agency
Hydrometeorological Automated Data System
CWMS Client-Server Mode
(Authentication Required)
Notes: CWMS Data Modes
  Client-Server Mode
    Data Acquisition for Corps Office in Production
      Data comes from both public and proprietary sources
      Data is acquired continuously through automated processes
      Data is transmitted over internet, dedicated data exchange lines, line-of-site radio, satellites, and more
      Time-series data is stored in CWMS Oracle database on CWMS server(s)
      Grids come from National Weather Service and other sources
      Grids are stored in server-side DSS files with precip.yyyy.mm.dss naming convention
      Many validation/transformation processes may be used

## Slide 34: Client-Server CAVI Data Extracts
  CAC authentication required for server access

## Slide 35: HEC-RTS CAVI Data Extracts
  No authentication required for local DSS file access

## Slide 36: Summary
  CWMS data supporting real-time modeling includes both time series and grids from a variety of sources
  Time-series data is stored in CWMS Oracle database and HEC-DSS

## Slide 37: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams