## Slide 1: Real Time Data IN CWMS
Kat Feingold
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: objective
Identify the types of real-time data and their management in CWMS

## Slide 3: Overview
  CWMS Real-Time Data Types & Viewing
  CWMS Data Sources
  CWMS Data Processing
  CWMS Data Storage Systems
  CWMS Data Acquisition
Notes: Overview
  There are two categories of real-time data:
    Time Series
    Grids
  CWMS Data Sources include:
    USGS and USACE gaging station networks
    National Weather Service meteorological data products
      USACE Cumulus gridded data web service
    Other agencies gaging station networks
  CWMS Data Processing is done through manual and automated means for:
    Time Series Data
      Manual Data Quality Control through the CWMS/CWMSVue Validation Editor
      OpenDCS CWMS Computational Processor (CCP)
      DSS Scripting
    Gridded Data
      Manual Edits using HEC-MetVue Interactive Features
      Automatic Processing based on HEC-MetVue project and session settings
        Missing Data Filing
        Dataset Merging
        Temporal Aggregation/Disaggregation
        Spatial Aggregation/Averaging
        MetInterp Point-to-TIN/Grid Spatial Interpolation
  Data is stored in two different storage systems:
    CWMS Oracle database
    Remote and Local DSS files
  CWMS Data Acquisition and Access Modes
    Data Acquisition is based on:
      Realtime telemetry
      Federal/State/Local Direct Data Exchange
      Federal/State/Local/Public Web Services
    CWMS can run in two different “modes” to access data:
      Client-Server Mode (requires authentication)
      Local (HEC-RTS) mode

## Slide 4: CWMS Real-time data types & Viewing

## Slide 5: Real-time Data Types in CWMS
Time Series
Grids
  Examples:
    Flow at a gage
    Elevation of a reservoir
  Storage
    HEC-DSS files
    CWMS Oracle Database
  Examples:
    Precipitation estimates from RADAR
    Precipitation Forecasts
    Snow state grids from SNODAS
  Storage:
    HEC-DSS files
    Other Files (GRIB, NetCDF, etc)
Notes: III. Presentation
Real-Time Data Types
  There are two categories of real-time data in CWMS
    Time Series Data
      Examples: Flow at a Gage, Elevation of a Reservoir
      Time series data can be stored in:
        HEC-DSS files
        CWMS Oracle Database
    Grids
      Examples: RADAR precipitation estimates, Snow state grids from SNODAS
      Grids are stored in DSS files (Not in ORACLE database)
        CWMS separates large grid data sets into monthly DSS files with standard naming
        For example, Precipitation grids: “precip.yyyy.mm.dss”, “precip.2017.01.dss”
      Grids can be stored in other file formats (GRIB, netCDF)

## Slide 6: DSS/CWMS Display of Time Series
Notes:   DSS/CWMS Display of Time Series
    Time series data can be tabulated or graphed in DSSVue / CWMS-Vue
    Many HEC model programs share a common graphics / display library
    Graphs and tables can be customized or produced by scripts

## Slide 7: DSS File – Time Series Catalog
Notes: Real-Time Data Types
    DSS File Time Series Catalog
      DssVue shows a list or “catalog” of contents of a DSS file
      DSS record types (including Time Series) are identified by a 6-part “path name” (A, B, C, D, E, F)

## Slide 8: CWMS Database Time Series Catalog
Notes:     CWMS Database Time Series Catalog
      CWMS-Vue shows a list of time series stored in CWMS Oracle database
      Time Series are identified by 6-part “time-series identifier”
      In CWMS 3.3, CWMS-Vue can display location metadata, rating curves, and other information

## Slide 9: DSS Display of Grids
Notes:   DSS Display of Grids
    Grids are stored in DSS files. DSSVue and CWMS-Vue are capable of displaying grids and metadata
    Grids can be displayed graphically
      Accomplished by clicking the “plot” icon
      Background maps are not displayed in DSSVue or CWMS-Vue
    Grid metadata (text format) can be viewed
      Accomplished by clicking the “tabulate” icon
      “Tabulate” shows grid metadata and summary, not array of cell values

## Slide 10: Standard hydrologic grid (SHG)
  Based on Albers Equal-Area map of the US
  Same coordinate system used by USGS for nation-wide mapping
  Locations are identified by cell indices (row and column numbers)
Notes:     Standard Hydrologic Grid (SHG)
      Coordinate system is valid in the contiguous United States
      Based on Albers Equal-Area map of US
      Same coordinate system used by USGS for nationwide mapping
      Locations are identified by cell indices (row and column numbers)

## Slide 11: Cavi display of time series and grids
Notes: Real-Time Data Types
    CAVI Display of Time Series and Grids
      Grids can be displayed in map context in Data Visualization and Modeling modules of CAVI

## Slide 12: HEC-MetVue Display of Grids
  MetVue Map Window
  CAVI Map Window

## Slide 13: DSS File – grids catalog
Notes:     DSS File Catalog of Grids
      Grids are displayed similarly to time-series data in DSSVue and CWMS-Vue
      Grids are stored using a 6-part pathname (A, B, C, D, E, F)
        A-Part: Coordinate System Reference (Typically SHG for “Standard Hydrologic Grid”)
        B-Part: Location
        C-Part: Parameter
        D-Part/E-Part: Timestamp
        F-Part: Version

## Slide 14: HEC-MetVue – Data Reader

## Slide 15: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams