## Slide 1: Real Time Data IN CWMS
Kat Feingold
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: objective
Identify the types of real-time data and their management in CWMS

## Slide 3: Overview
  CWMS Real-Time Data Types & Viewing
  CWMS Data Sources
  CWMS Data Processing
  CWMS Data Storage Systems
  CWMS Data Acquisition
Notes: Overview
  There are two categories of real-time data:
    Time Series
    Grids
  CWMS Data Sources include:
    USGS and USACE gaging station networks
    National Weather Service meteorological data products
      USACE Cumulus gridded data web service
    Other agencies gaging station networks
  CWMS Data Processing is done through manual and automated means for:
    Time Series Data
      Manual Data Quality Control through the CWMS/CWMSVue Validation Editor
      OpenDCS CWMS Computational Processor (CCP)
      DSS Scripting
    Gridded Data
      Manual Edits using HEC-MetVue Interactive Features
      Automatic Processing based on HEC-MetVue project and session settings
        Missing Data Filing
        Dataset Merging
        Temporal Aggregation/Disaggregation
        Spatial Aggregation/Averaging
        MetInterp Point-to-TIN/Grid Spatial Interpolation
  Data is stored in two different storage systems:
    CWMS Oracle database
    Remote and Local DSS files
  CWMS Data Acquisition and Access Modes
    Data Acquisition is based on:
      Realtime telemetry
      Federal/State/Local Direct Data Exchange
      Federal/State/Local/Public Web Services
    CWMS can run in two different “modes” to access data:
      Client-Server Mode (requires authentication)
      Local (HEC-RTS) mode

## Slide 4: CWMS Data Sources

## Slide 5: Time Series data Sources
  USACE
  USGS https://waterdata.usgs.gov/nwis/rt https://dashboard.waterdata.usgs.gov/
  Other (Federal/State/Local)

## Slide 6: Gridded data sources - Cumulus
  https://cumulus.corps.cloud
  Web service single point of meteorological data access available to USACE WM and HH&C
  Requires CorpsNet Access
    Either Direct or VPN
  Direct Cumulus extract via the CAVI
    Watershed or Area of Interest extents
Notes: Cumulus is a gridded meteorological data repository that serves the Corps Water Management and Hydrologic and Hydraulic Communities of Practice. Cumulus is a web service that provides on-demand data access through its primary website https://www.cumulus.corps.cloud as well as an (API) that can be used by software programs or other web services to access through custom interface or automated means.
Product – Provides a list of all available historic, real-time, and forecast meteorological parameters
Filtered by
  Corps Office – Filter the applicable watersheds for the selected office
  Watershed – Determines the clipping extents for the dataset download
  Time Window – Defines the start and end dates and times for the dataset download
Cumulus is only available through CorpsNet. And requires, CAC authentication is required to download datasets.

## Slide 7: Additional Gridded data sources
  RFC – River Forecast Center
    https://water.weather.gov/ahps/rfc/rfc.php
  NBM – National Blend of Models
    https://vlab.noaa.gov/web/mdl/nbm
  NCEP – National Center for Environmental Predictions
    https://nomads.ncep.noaa.gov
  NDFD – National Digital Forecasting Database
    https://vlab.noaa.gov/web/mdl/ndfd
Notes:   Gridded Precipitation and Temperature Data Sources
    Data Sources Overview
      River Forecast Centers distribute grids of QPE and QPF (Quantitative Precipitation Estimate/Forecast)
      Nationwide grids are available from several sources
        National Digital Forecast Database (NDFD)
        National Digital Guidance Database (NDGD)
        National Center for Environmental Predictions (NCEP)
        Weather Prediction Center (WPC)
        National Operational Hydrologic Remote Sensing Center (NOHRSC)
      Nationwide grids are collected and processed for use in CWMS at the Central Processing Center and can be distributed to your office for use in CWMS modeling

## Slide 8: Precipitation forecast (QPF)
Notes:     Data Sources Details
      NDFD Precipitation Forecast (QPF)
        From National Weather Service National Digital Forecast Database
        Resampled to 2km SHG and stored in DSS records at CPC
        Can be distributed to division/district offices
        Supplement to QPF from River Forecast Center

## Slide 9: Temperature Forecast (QTf)
Notes:       NDFD Temperature Forecast
        From National Weather Service National Digital Forecast Database
        Resampled to 2km SHG and stored in DSS records at CPC
        Can be distributed to division/district offices
        Available for use in snow forecasts or with Gridded Hamon evaporation

## Slide 10: Example Snodas
  Snow Data Assimilation System (SNODAS)
Notes:       SNODAS grids from NOHRSC
        SNODAS is the primary source of gridded snow data used in CWMS snowmelt models in the Corps
        Hourly/Daily gridded snow products for conterminous U.S.
        Based on an energy balance snow model combined with multi-sensor snow observations
        Spatial Resolution: 1 sq km resolution
        Available period of record: October 2003 – Present
        Additional information available at http://www.nohrsc.noaa.gov/

## Slide 11: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams