## Slide 1: Real Time Data IN CWMS
Kat Feingold
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: objective
Identify the types of real-time data and their management in CWMS

## Slide 3: Overview
  CWMS Real-Time Data Types & Viewing
  CWMS Data Sources
  CWMS Data Processing
  CWMS Data Storage Systems
  CWMS Data Acquisition
Notes: Overview
  There are two categories of real-time data:
    Time Series
    Grids
  CWMS Data Sources include:
    USGS and USACE gaging station networks
    National Weather Service meteorological data products
      USACE Cumulus gridded data web service
    Other agencies gaging station networks
  CWMS Data Processing is done through manual and automated means for:
    Time Series Data
      Manual Data Quality Control through the CWMS/CWMSVue Validation Editor
      OpenDCS CWMS Computational Processor (CCP)
      DSS Scripting
    Gridded Data
      Manual Edits using HEC-MetVue Interactive Features
      Automatic Processing based on HEC-MetVue project and session settings
        Missing Data Filing
        Dataset Merging
        Temporal Aggregation/Disaggregation
        Spatial Aggregation/Averaging
        MetInterp Point-to-TIN/Grid Spatial Interpolation
  Data is stored in two different storage systems:
    CWMS Oracle database
    Remote and Local DSS files
  CWMS Data Acquisition and Access Modes
    Data Acquisition is based on:
      Realtime telemetry
      Federal/State/Local Direct Data Exchange
      Federal/State/Local/Public Web Services
    CWMS can run in two different “modes” to access data:
      Client-Server Mode (requires authentication)
      Local (HEC-RTS) mode

## Slide 4: CWMS Data Processing

## Slide 5: Time-series Data processing
Data Types
Data Processing
  Observation
    Stage gage
    Rain gage
    Thermometer
  Derived
    Flow from stage & rating
    Storage from elevation & rating
    Model Results
  CWMS/CWMSVue Validation Editor
  CWMS Computational Processor (CCP)
  DSS Math functions and Scripts
Notes: Real-Time Data Types
    Time-Series are obtained and transformed in a variety of ways
      Time-series can be obtained from direct observation or derived
        Examples of time-series data from direct observations
          River stage gage
          Precipitation gage
          Thermometer
        Examples of time-series derived using direct observations and computations
          Flow from stage & stage-flow rating
          Storage from elevation & elevation-storage curve
      There are several tools available for processing and modifiying time series data.
        CWMS and CWMSVue Data Validation Editor
        CWMS Computational Processor (CCP)
        DSS Math functions and Scripts

## Slide 6: CAVI/CWMSVue Validation Editor
  Interactive Data Review & Editing
    Set value as missing
    Set specified value
    Fill – Linear
    Fill – Repeat
    Fill – Raw
    Add a constant value
    Multiply by a factor

## Slide 7: OpenDCS Cwms Computational Processor (CCP)
  Example Functions
    Average
    Fill Forward
    Disaggregate
    Inflow computation
  References
    Main Documentation https://opendcs-env.readthedocs.io/en/latest/
    Standard Algorithms https://opendcs-env.readthedocs.io/en/latest/resources-algorithms.html
    Custom Python Algorithms https://opendcs-env.readthedocs.io/en/latest/resources-algorithms.html#opendcs-custom-python-algorithms

## Slide 8: Hec-dss Math functions & Scripts
  Example Functions
    Estimate Missing Values
    Replace Specific Values
    Screen using Minimum and Maximum
    Change Time Interval
    Irregular to Regular
    Rating Table
    Reverse Rating Table
    Moving Average
  References
    HEC-DSSVue Users Manual https://www.hec.usace.army.mil/confluence/dssdocs/dssvueum/math-and-statistical-functions https://www.hec.usace.army.mil/confluence/dssdocs/dssvueum/scripting/math-functions
    HEC-DSSVue Github Scripts Repo https://github.com/HydrologicEngineeringCenter/DSSVue-Example-Scripts/tree/master/src
https://github.com/HydrologicEngineeringCenter/DSSVue-Example-Scripts/blob/master/src/change-interval.py

## Slide 9: Grid Data processing
Data Types
Data Processing
  Observation
    RADAR
    Aircraft and Satellite Remote Sensing
  Derived
    Interpolation from point measurements
    Model Results
  HEC-MetVue
    Missing Data Filing
    Dataset Merging
    Temporal Aggregation/Disaggregation
    Spatial Aggregation/Averaging
    TIN-to-Grid and Grid-to-TIN
    MetInterp
      Point-to-TIN/Grid Spatial Interpolation
Notes:     Grids are obtained and transformed in a variety of ways
      Grids can be obtained from direct observations
        RADAR
        Remote Sensing (from Satellite or Aircraft)
      Grids can be derived from direct observations (point or gridded).
        Interpretation of Remote Sensing products
        Interpolation from point measurements to TIN (Triangulated Irregular Network) and Grid.
        There are many derived grids available from Weather Service Models/Processes
          RTMA (Real-Time-Mezzoscale-Analysis)
          MRMS (Multi-Radar-Multi-Sensor)
          SNODAS (SNOw Data Assimilation System)
          HRRR (High-Resolution-Rapid-Refresh)
          Others
      HEC-MetVue offers a number of spatial data processing methods:
      Missing Data Filing
      Dataset Merging
      Temporal Aggregation/Disaggregation
      Spatial Aggregation/Averaging
      TIN-to-Grid and Grid-to-TIN
      HEC-MetVue also provides for Point-to-TIN or Point-to-Grid spatil interpolation with a methods, including
        Inverse-Distance
        Inverse-Distance Squared
        Nearest Neighbor
        Bilinear

## Slide 10: HEC-MetVue Data Processing
Temporal Disaggregation
Dataset Merging
Missing Data Filling
Spatial Interpolation

## Slide 11: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams