## Slide 1: Real Time Data IN CWMS
Kat Feingold
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: objective
Identify the types of real-time data and their management in CWMS

## Slide 3: Overview
  CWMS Real-Time Data Types & Viewing
  CWMS Data Sources
  CWMS Data Processing
  CWMS Data Storage Systems
  CWMS Data Acquisition
Notes: Overview
  There are two categories of real-time data:
    Time Series
    Grids
  CWMS Data Sources include:
    USGS and USACE gaging station networks
    National Weather Service meteorological data products
      USACE Cumulus gridded data web service
    Other agencies gaging station networks
  CWMS Data Processing is done through manual and automated means for:
    Time Series Data
      Manual Data Quality Control through the CWMS/CWMSVue Validation Editor
      OpenDCS CWMS Computational Processor (CCP)
      DSS Scripting
    Gridded Data
      Manual Edits using HEC-MetVue Interactive Features
      Automatic Processing based on HEC-MetVue project and session settings
        Missing Data Filing
        Dataset Merging
        Temporal Aggregation/Disaggregation
        Spatial Aggregation/Averaging
        MetInterp Point-to-TIN/Grid Spatial Interpolation
  Data is stored in two different storage systems:
    CWMS Oracle database
    Remote and Local DSS files
  CWMS Data Acquisition and Access Modes
    Data Acquisition is based on:
      Realtime telemetry
      Federal/State/Local Direct Data Exchange
      Federal/State/Local/Public Web Services
    CWMS can run in two different “modes” to access data:
      Client-Server Mode (requires authentication)
      Local (HEC-RTS) mode

## Slide 4: Data storage Systems

## Slide 5: Data storage systems in cwms
CWMS Database
HEC-DSS Files
  Runs on a CWMS T7 Server or Cloud Server
  Oracle-Based Relational Database System
  Supports enterprise-scale data operations
  AIS (Automated Information System)
  Requires authenticated login
  Stored on
    Windows PC
    CWMS server
  Optimized for data sequences like time series
  Local DSS requires no login
Notes: Data Storage Systems in CWMS
  Data in CWMS is stored in two forms, CWMS Oracle Database and DSS Files
    CWMS Database:
      Runs on CWMS server (locally or in the cloud)
      Oracle Relational Database System
      Supports enterprise-scale data operations
      Army AIS (Automated Information System)
      Requires Authenticated Login
    DSS Files:
      Stored on CWMS server (locally or in the cloud)
      Stored on PC or Server file system
      Optimized for data sequences like time series
      No login required for local DSS file operations

## Slide 6: Files and directories for cwms data
Notes: Data Storage Systems in CWMS
  Files and Directories for CWMS Data
    Top directCWMS server the top directory is set by $CWMS_HOME environment variable
    config directory holds relatively static setup for data acquisition (da) processes
      MetInterp configuration files are saved in the config directory
      ProcessSheffit criteria files
    ory (CWMS_CLASS here) is left to user choice
    On dated directory contents change as data collection and transformation processes run
      DSS files for grids are stored in dated/db/grid
      Temporary files required by data processing programs
      Log files
    database directory hold DSS files for time series in “Local Mode” (RTS)
      In Corps production systems, this is replaced by the CWMS Oracle database
      There is no “database” directory on CWMS server

## Slide 7: Cwms data Acquisition

## Slide 8: District/division data acquisition
Federal/state/Local Agency
Satellite
Telemetry
Data
VHF
Line-of-
Sight
Data
Dedicated Line
Data Exchange
Internet
Data Exchange
Server-based
Water
Management
System
Instructions To and
From Dam Operator
Local Water Management Office
Federal/State/Local Agency
Hydrometeorological Automated Data System
CWMS Client-Server Mode
(Authentication Required)
Notes: CWMS Data Modes
  Client-Server Mode
    Data Acquisition for Corps Office in Production
      Data comes from both public and proprietary sources
      Data is acquired continuously through automated processes
      Data is transmitted over internet, dedicated data exchange lines, line-of-site radio, satellites, and more
      Time-series data is stored in CWMS Oracle database on CWMS server(s)
      Grids come from National Weather Service and other sources
      Grids are stored in server-side DSS files with precip.yyyy.mm.dss naming convention
      Many validation/transformation processes may be used

## Slide 9: Client-Server CAVI Data Extracts
  CAC authentication required for server access

## Slide 10: HEC-RTS CAVI Data Extracts
  No authentication required for local DSS file access

## Slide 11: Summary
  CWMS data supporting real-time modeling includes both time series and grids from a variety of sources
  Time-series data is stored in CWMS Oracle database and HEC-DSS

## Slide 12: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams