## Slide 1: CWMS GRAPHICS AND SCRIPTING
Oskar Hurst,
Hydrologic Engineering Center
CWMS Prospect Course
Scripting

## Slide 2: Uses for Scripting
Notes: CWMS Scripting Overview

## Slide 3: What is Scripting?
Scripting is the process of automating the actions of an interactive program for the purpose of being able to execute a prescribed set of actions with a simple trigger.
May involve small to large amount of initial effort.
Trivially repeatable.
Notes: CWMS Scripting Overview
  What is Scripting
    Scripting is the process of automating the actions of an interactive program for the purpose of being able to execute a prescribed set of actions with a simple trigger.
      May involve small to large amount of initial effort.
      Trivially repeatable.

## Slide 4: Why Use Scripting?
To simplify user operation
To ensure repeatability and consistency of results
To reduce time required to generate results
Notes: CWMS Scripting Overview
  Why Use Scripting?
    To simplify user operation
    To ensure repeatability and consistency of results
    To abstract complexity
    To reduce time required to generate results

## Slide 5: Scripting in CWMS
CWMS includes a scripting facility that can be used to customize and/or automate tasks:
  Create and execute forecasts.
  Analyze and process data stored in Oracle or DSS.
  Create custom plots and tables.
CWMS scripts are written using the combination of a scripting language and the CWMS Application Programming Interface (API)
  There is no way to record interactive operations (i.e., no macro recorder)
  The scripting language is Jython – a version of the Python programming language
Notes: CWMS Scripting Overview
  Scripting in CWMS
    CWMS includes a scripting facility that can be used to customize and/or automate tasks:
      Create and execute forecasts.
      Analyze and process data stored in Oracle or DSS.
      Create custom plots and tables.
    CWMS scripts are written using the combination of a scripting language and the CWMS Application Programming Interface (API)
      There is no way to record interactive operations (i.e., no macro recorder)
      The scripting language is Jython – a version of the Python programming language

## Slide 6: Scripting Components
Notes: Scripting Components

## Slide 7: Script Editor
The main scripting component in CWMS is the Script Editor. It is used for:
  Creating new scripts
  Editing existing scripts
  Testing scripts
Notes: Scripting Components
  Script Editor
    The main scripting component in CWMS is the Script Editor. It is used for:
      Creating new scripts.
      Editing existing scripts.
      Testing scripts.

## Slide 8: Opening the Script Editor
Select “ScriptsEditor…” from the CAVI menu bar.
Notes: Scripting Components
  Script Editor
    Opening the Script Editor
      Select “ScriptsEditor…” from the CAVI menu bar.

## Slide 9: Script Editor – Tool Bar
New Script
Print Script
Cut
Copy
Paste
Same functions available via menu bar
Select “FileDelete” to delete a script (no tool for this)
Notes: Scripting Components
  Script Editor
    Script Editor Toolbar
      New Script
      Print Script
      Cut
      Copy
      Paste
      Same functions available via menu bar
      Select “FileDelete” to delete a script (no tool for this)

## Slide 10: Script Editor – Tree Pane
Lists scripts for watershed
Double-click on script name to edit it
Notes: Scripting Components
  Script Editor
    Script Editor – Tree Pane
      Lists scripts for watershed
      Double-click on script name to edit it

## Slide 11: Script Editor – API Pane
Lists CWMS API methods
To insert code in editor pane:
  Double-click node (inserts at current position)
  Drag node to desired position
  Select node and click “Insert in Script” button (inserts at current position)
Notes: Scripting Components
  Script Editor
    Script Editor – API Pane
      Lists CWMS API methods
      To insert code in editor pane:
        Double-click node (inserts at current position)
        Drag node to desired position
        Select node and click “Insert in Script” button (inserts at current position)

## Slide 12: Script Editor – Editor Pane
Displays code for script
Syntax highlighting
Highlights all occurrences of word at current position
Notes: Scripting Components
  Script Editor
    Script Editor – Editor Pane
      Displays code for script
      Syntax highlighting
      Highlights all occurrences of word at current position

## Slide 13: Script Editor – Editor Pane Details
context menu
current line (highlighted)
word at current position (highlighted)
line numbers
Ctrl-F – search
Uses normal select/cut/copy/paste keystroke combinations
Notes: Scripting Components
  Script Editor
    Script Editor – Editor Pane Details
      Context menu contains editing operations.
      Ctrl-F opens search dialog
      Standard editing shortcut keys can be used.

## Slide 14: Script Editor – Action Buttons
Insert in Script
  Inserts code for selected API method into script at current position
Compile Script
  Compiles the script without saving
Save
  Compiles and saves the script
Save/Run
  Compiles, saves, and executes the script
Select
  Notifies other CWMS components of current script selection
Notes: Scripting Components
  Script Editor
    Script Editor – Action Buttons
      Insert in Script – inserts code for selected API method into script at current position
      Compile Script – compiles the script without saving
      Save – compiles and saves the script
      Save/Run – compiles, saves, and executes the script
      Select – notifies other CWMS components of current script selection

## Slide 15: Script Selector
Select “ScriptsRun” from CAVI menu bar.
Displays scripts for watershed.
Double-click on name to run, or select name and click “Run” button.
Notes: Scripting Components
  Script Editor
    Script Selector
      Select “ScriptsRun” from CAVI menu bar.
      Displays scripts for watershed.
      Double-click on name to run, or select name and click “Run” button.

## Slide 16: Modeling Scripts Panel
Select the Modeling tab.
At the bottom of the tab, select the Scripts tab.
Right-click in the Scripts panel and select “Edit…”
Use the “Select Scripts” dialog to choose which scripts to add to the panel
Notes: Scripting Components
  Modeling Scripts Panel
    Select the Modeling tab.
    At the bottom of the tab, select the Scripts tab.
    Right-click in the Scripts panel and select “Edit…”
    Use the “Select Scripts” dialog to choose which scripts to add to the panel

## Slide 17: Modeling Scripts Panel

## Slide 18: Assigning Scripts To Time Series Icons
Switch to Watershed Setup Module.
Right-click the icon and select “Edit” from the context menu.
Select the “Scripts/HTML” tab on the properties dialog.
Populate the scripts dialog with the appropriate information.
  Put a variable assignment statement in the “Arguments” column. That variable with its assigned value will be available in the script.
    This allows a common script to be used on many icons, as each icon will have its unique assignment to the same variable
Dismiss dialogs and save configuration.
Notes: Scripting Components
  Time Series Icons Scripts
    Assigning Scripts to Time Series Icons.
      Switch to Watershed Setup Module.
      Right-click the icon and select “Edit” from the context menu.
      Select the “Scripts/HTML” tab on the properties dialog.
      Populate the scripts dialog with the appropriate information.
        Put a variable assignment statement in the “Arguments” column. That variable with its assigned value will be available in the script.This allows a common script to be used on many icons, as each icon will have its unique assignment to the same variable
      Dismiss dialogs and save configuration.

## Slide 19: Assigning Scripts To Time Series Icons

## Slide 20: Section 5 Review
What component is used to create and edit scripts?
What are three ways to execute a script?
What is the API pane used for?
How can multiple time series icons use a common script and produce individual results?
Notes: Scripting Components
  Section 5 Review
    What component is used to create and edit scripts?
      Script Editor
    What are three ways to execute a script?
      From the Script Editor (Save/Run)
      From the Script Selector
      From the Modeling Scripts Panel
      From a Time Series Icon
    What is the API pane used for?
      To insert code for a CWMS API method into the script
    How can multiple time series icons use a common script and produce individual results?
      By assigning different values to the same variable in the “Arguments” column of the “Scripts/HTML” tab

## Slide 21: Scripting Language
Notes: Scripting Language

## Slide 22: What is Jython?
Jython is a Java-based implementation of the Python programming language. This means:
  You learn the Python language to learn Jython. Python tutorials and book references can be found at http://www.python.org.
  Jython code can interface seamlessly with Java code. The CWMS API is written in Java, but Jython can use it as if it were written in Python.
Notes: Scripting Language
  What is Jython?
    Jython is a Java-based implementation of the Python programming language. This means:
      You learn the Python language to learn Jython.
        Python tutorials and book references can be found at http://www.python.org.
      Jython code can interface seamlessly with Java code.
        The CWMS API is written in Java, but Jython can use it as if it were written in Python.

## Slide 23: Jython Scripting Resources
HEC-DSSVue User’s Guide
  Scripting (army.mil)
  Available from within HEC-DSSVue by selecting “HelpHelp” from the menu bar.
  HEC-DSSVue shares the same API as CWMS for many items, including plots, tables, and HEC-DSS file access.
Examples
  Some examples are installed with HEC-DSSVue in the “samples” directory
  https://github.com/HydrologicEngineeringCenter/DSSVue-Example-Scripts
  The CWMS wiki (https://cwms.usace.army.mil/dokuwiki/) contains many scripting examples, including accessing the CWMS database.
  HEC Monolith documentation https://www.hec.usace.army.mil/software/javadocs/hec-monolith/
Notes: Scripting Language
  Jython Scripting Resources
    Chapter 8 of the HEC-DSSVue User’s Guide
      HEC-DSSVue shares the same API as CWMS for many items, including plots, tables, and HEC-DSS file access.
      Interactive documentation is available from within HEC-DSSVue by selecting “HelpHelp” from the menu bar.
    Examples
      Many examples are installed with HEC-DSSVue in the “samples” directory
      The CWMS wiki (https://cwms.usace.army.mil/dokuwiki/) contains many scripting examples, including accessing the CWMS database.
  For general Java and Python, Army Civilians in the Scientist, Engineer and Analyst (CP16) Career Field have access to Udemy for Business.
    Create an account with your usace.army.mil at Udemy for Business (armyciv.udemy.com)
    Should be emailed instructions on how to setup
    100 days of code course has been highly recommended.
      https://armyciv.udemy.com/course/100-days-of-code/

## Slide 24: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
“Just keep CWMS’ing”