## Slide 1: CWMS GRAPHICS AND SCRIPTING
Oskar Hurst,
Hydrologic Engineering Center
CWMS Prospect Course
Overview & Plotting

## Slide 2: Objective
Identify graphics (plotting) capabilities in CWMS
Identify scripting capabilities in CWMS
Notes: Objectives
  Identify graphics (plotting) capabilities in CWMS
  Identify scripting capabilities in CWMS

## Slide 3: Outline
Opening Plots
Plot Components
Customizing Plots
Uses for Scripting
Scripting Components
Scripting Language
Notes: Outline
  Creating Plots
  Plot Components
  Customizing Plots
  Uses for Scripting
  Scripting Components
  Scripting Language

## Slide 4: Opening Plots
Notes: III. Presentation
Creating Plots

## Slide 5: Setup Tab
Select setup table to enter the setup view
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 6: Setup View
To create an Icon Select time series Icon tool then
CTRL + Left Click
Time Series Icon
Organizes Time series data for plotting
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 7: Setup view
To create an Icon Select time series Icon tool then
CTRL + Left Click
Time Series Icon
Organizes Time series data for plotting
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 8: Setup view
To create an Icon Select time series Icon tool then
CTRL + Left Click
Time Series Icon
Organizes Time series data for plotting
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 9: Setup view
Right Click Time series icon to edit data
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 10: Time Series icon
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 11: Visualization tabs
Select the Visualization tab to open plots
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 12: Visualization Tab
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 13: Visualization Tab
Right Click graph icon and select plot
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 14: Example Plot
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 15: Plot Components
Viewport (1,1)
Viewport (2,1)
Y1 Axis
Y1 Axis
X1 Axis
Y2 Axis
Curves
Legend
Notes: Plot Components

## Slide 16: Viewports
Viewport (1,1)
Viewport (2,1)
Y1 Axis
Y1 Axis
X1 Axis
Y2 Axis
Curves
Legend
Notes: Plot Components
  Viewports are components that include axes, gridlines, and curves.
    Plots can have multiple viewports.
      Multiple viewports are always stacked vertically (one column, multiple rows)
      Viewports are indexed by (row, column) with the top row being 1 and the column always being 1.
    Viewports can show major and/or minor grid lines

## Slide 17: Axes
Viewport (1,1)
Viewport (2,1)
Y1 Axis
Y1 Axis
X1 Axis
Y2 Axis
Curves
Legend
Notes: Plot Components
  Axes show the scale for values and date/time.
    Each viewport has two or three axes: one or two Y axes labeled Y1 (left) and Y2 (right), and an X axis labeled X1
    A single X axis is shared by all viewports.
    X axes can be numeric (e.g., ratings) or date/time (time series).
      Numeric X axes can be linear, logarithmic, or probability
    Y axes can only be numeric (linear or logarithmic)
    Numeric axes can have labels, which default to parameter and unit.
    Date/time axes can have 1, 2, or 3 levels of labeling.
    Axes can show major and/or minor tic marks, which correspond with the major and minor viewport gridlines.

## Slide 18: Curves
Viewport (1,1)
Viewport (2,1)
Y1 Axis
Y1 Axis
X1 Axis
Y2 Axis
Curves
Legend
Notes: Plot Components
  Curves are the datasets plotted in the viewports.
    Each curve is associated with the Y1 or Y2 axis of the viewport.
    Each Y axis can be associated with multiple curves of the same parameter and unit.

## Slide 19: Legend
Viewport (1,1)
Viewport (2,1)
Y1 Axis
Y1 Axis
X1 Axis
Y2 Axis
Curves
Legend
Notes: Plot Components
  The legend contains identifying items for each curve. Each item contains:
    Line. The legend line has the same visual properties as the curve it identifies.
    Label. For time series curves, the label is normally a concatenation of the location, version, and parameter of the dataset.
    The legend can be placed in various locations in or outside the plot.

## Slide 20: Tools
Selector Tool
Zoom Tool
Tool Bar
Notes: Plot Components
  A tool bar is found in each plot. The tool bar contains:
    Select tool. This is used to select components of the plot for editing. To edit a component, right-click on it.
    Zoom too. This tool is used to zoom-in viewports by dragging the extents to fill the plot. Right-click to zoom-out.

## Slide 21: Callout and Marker Lines
Marker Lines
Callout

## Slide 22: Customizing Plots
Notes: Customizing Plots

## Slide 23: Arranging the Plot
“EditConfigure Plot Layout…”
  Control number, order, and relative sizes of viewports
  Add, remove, and reverse Y axes
Notes: Customizing Plots
  Arranging the Plot
    Select “EditConfigure Plot Layout…” from plot menu bar.
    Opens “Configure Plot” dialog which allows you to:
      Control the number, order, and relative sizes of viewports.
      Add, remove, and reverse Y axes.

## Slide 24: Managing Viewports
Adding & Removing
Sizing (relative weights)
Ordering
Notes: Customizing Plots
  Managing Viewports
    Select “EditAdd Viewport” or “EditRemove Viewport” from the Configure Plot menu bar to add or remove viewports
    Select “EditSet Viewport Weights…” to open the “Set Viewport Weights” dialog, which lets you set the relative sizes (height) of viewports (Must sum to 100%)
    Select a viewport and use the up or down button to reorder the viewports.

## Slide 25: Managing Y Axes
Adding & Removing
Moving
Reversing
Notes: Customizing Plots
  Managing Y Axes
    Select a viewport and then select “EditAdd Axis” from the “Configure Plot” menu bar to add a Y axis.
    Select an axis and then select “EditRemove Axis” from the “Configure Plot” menu bar to remove a Y axis.
    Select an axis and then click on the up or down button to reorder axes.
      You can move viewport (2,1) left axis up and it becomes a secondary axis for viewport (1,1) and removed viewport (2,1)
    Right-click on an axis and select “Reverse” from the context menu to reverse an axis.

## Slide 26: Adding Callouts and Marker Lines
Add a Callout
  Right-click on curve using select tool.
  Select “Add Callout” from the menu.
  Enter info on Callout dialog.
  The callout will be place at the point you clicked. You cannot move the callout once placed (but you can delete it and make another one).
Callout
Notes: Customizing Plots
  Adding Callouts and Marker Lines
    Add a callout by right-clicking on a curve and selecting “Add Callout” from context menu.
      Cannot be edited
    Add a marker line by right-clicking in a viewport and selecting “Add Marker” from the context menu.
      Adding a marker line on the X axis of a viewport will not add the marker line to all viewports.
      Can edit line style, location and label

## Slide 27: Adding Callouts and Marker Lines
Add a Marker Line
  Right-click in viewport using select tool.
  Select “Add MarkerOn ...-Axis” from menu.
  Enter info on marker dialog.
  Marker line will be placed at the location you selected, but you can edit that.
Marker Lines
Notes: Customizing Plots
  Adding Callouts and Marker Lines
    Add a callout by right-clicking on a curve and selecting “Add Callout” from context menu.
      Cannot be edited
    Add a marker line by right-clicking in a viewport and selecting “Add Marker” from the context menu.
      Adding a marker line on the X axis of a viewport will not add the marker line to all viewports.
      Can edit line style, location and label

## Slide 28: Plot With Callout and Marker Lines
Marker Lines
Callout

## Slide 29: Plot With Callout and Marker Lines
Right Click Title Area
Right Click Legend Area

## Slide 30: Editing the Title and Legend
Adding a Title
  Right-click above top viewport with the select tool
  Select “Edit Properties” from the menu.
Customizing the Legend
  Right-click in legend with select tool
  Select “Edit Properties” from the menu.
Notes: Mention that you can also right click within the legend or top viewport to also get to these specific properties
If too close to graph, will edit spacing.

## Slide 31: Plot With Title and Legend Edits

## Slide 32: Plot Properties Editor
Select “EditPlot Properties…” from plot menu bar.
Editor dialog has same editors as context menus, each in its own tab.
Viewport and curve selected from lists.
Edits apply only to current plot.
Notes: Customizing Plots
  Plot Properties Editor
    Select “EditPlot Properties” from the plot menu bar to open the Properties dialog.
    Every editor available by right-clicking on plot components is also available in this dialog.
    Each tab contains a component editor
    Specific viewports and curves are selected from lists at the top of the dialog.
    Like edits made via right-clicking on components, the edits apply only to the current plot.

## Slide 33: Templates
The current layout and properties of any plot can be save to a template by selecting “FileSave Template…” from the plot’s menu bar and saving to a template file.
The same layout and properties can later be applied to another plot by selecting “FileApply Template…” from the plot’s menu bar and selecting the previously saved template file.
Templates are intended be applied to plots with the same parameters and number of curves as the plot from which the template was created.
Notes: Customizing Plots
  Templates
    Templates can save all edits to a plot made using the previous methods so they can be applied to another plot
      Select “FileSave Template…” from the plot menu bar to save a template to a file.
      To apply the same edits to another plot, select “FileApply Template…” from the plot menu bar.
      Templates are intended to be applied only to plots similar to the one the template was created from (same parameters and number of curves).

## Slide 34: Templates in Time Series Icon Layers
A Template can be imposed on a time-series icon layer in order to force icons in that layer to plot their datasets in a fashion different from the default.
  From the tab where you want to see the custom plot, plot the icon, modify it to look the way you want, then save the template.
  Switch to the Setup tab and open the Map Layers dialog (MapsMap Layers…)
  Expand the Time Series Icons layer, right-click on the desired layer and select Properties from the context menu.
  Use the Template tab on the Time Series Icon Layer Properties dialog to select the template.
Notes: Customizing Plots
  Templates in Time Series Icon Layers
    Customize a plot opened from a time series icon, and save the customization as a template.
    Open the Map Layers dialog from the Setup tab.
    Right-click on the desired time series icon layer and select “Properties” from the context menu.
    Use the “Template” tab on the Time Series Icon Layer Properties dialog to select the template.

## Slide 35: Templates in Time Series Icon Layers

## Slide 36: Default Plot Properties
User-editable default plot properties.
Specifies properties that will be applied to every future plot (not applied to any open plots).
Uses editor dialog that resembles the plot properties editor.
  Doesn’t specify default properties for individual curves – these are specified using default line styles.
Individual edits cannot be undone, but deleting the data file for a tab restores that tab to program default properties.
The current default plot properties can be exported to a zip file, and later be re-imported from the zip file.
Notes: Customizing Plots
  Default Plot Properties
    Default plot properties are user-editable properties that are applied to future plots only.
    Default plot properties are specified using a dialog that resembles the plot properties editor.
      Default line styles are not specified in this editor.
    Each tab of the editor saves the specified defaults to a file in the C:\Users\<username>\.gfx2d\ directory.
    Individual edits cannot be undone, but deleting a tab’s data file restores the program defaults for that tab.
    Default plot properties can be exported to, and imported from, zip files.

## Slide 37: Default Plot Properties Editor
Select “Edit Default Plot Properties…” from plot menu bar.
Notes: Customizing Plots
  Default Plot Properties Editor
    Select “EditDefault Plot Properties” from the plot menu bar to open the Default Plot Properties dialog.

## Slide 38: Default Line Styles
User-editable default styles for curves based on:
  Parameter
  Data Type
  Order (1st curve, 2nd curve, etc…)
Default styles will not be applied to any open plots, but only be applied to future plots.
All default styles saved in one file specified on bottom of editor.
Individual edits cannot be undone, but deleting the file will restore program default styles.
Notes: Customizing Plots
  Default Line Styles
    Default line styles are user-editable default properties for curves based on parameter, date type, and order.
    Default styles will not be applied to any open plots, but only be applied to future plots.
    All default styles saved in one file specified on bottom of editor.
    Individual edits cannot be undone, but deleting the file will restore program default styles.

## Slide 39: Default Line Style Editor
Select “EditDefault Line Styles…” from plot menu bar
Notes: Customizing Plots
  Default Line Styles Editor.
    Select “EditDefault Line Styles” from the plot menu bar to open the Default Line Styles dialog.

## Slide 40: Uses for Scripting
Notes: CWMS Scripting Overview

## Slide 41: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
“Just keep CWMS’ing”

## Slide 42: What is Scripting?
Scripting is the process of automating the actions of an interactive program for the purpose of being able to execute a prescribed set of actions with a simple trigger.
May involve small to large amount of initial effort.
Trivially repeatable.
Notes: CWMS Scripting Overview
  What is Scripting
    Scripting is the process of automating the actions of an interactive program for the purpose of being able to execute a prescribed set of actions with a simple trigger.
      May involve small to large amount of initial effort.
      Trivially repeatable.

## Slide 43: Why Use Scripting?
To simplify user operation
To ensure repeatability and consistency of results
To reduce time required to generate results
Notes: CWMS Scripting Overview
  Why Use Scripting?
    To simplify user operation
    To ensure repeatability and consistency of results
    To abstract complexity
    To reduce time required to generate results

## Slide 44: Scripting in CWMS
CWMS includes a scripting facility that can be used to customize and/or automate tasks:
  Create and execute forecasts.
  Analyze and process data stored in Oracle or DSS.
  Create custom plots and tables.
CWMS scripts are written using the combination of a scripting language and the CWMS Application Programming Interface (API)
  There is no way to record interactive operations (i.e., no macro recorder)
  The scripting language is Jython – a version of the Python programming language
Notes: CWMS Scripting Overview
  Scripting in CWMS
    CWMS includes a scripting facility that can be used to customize and/or automate tasks:
      Create and execute forecasts.
      Analyze and process data stored in Oracle or DSS.
      Create custom plots and tables.
    CWMS scripts are written using the combination of a scripting language and the CWMS Application Programming Interface (API)
      There is no way to record interactive operations (i.e., no macro recorder)
      The scripting language is Jython – a version of the Python programming language

## Slide 45: Scripting Components
Notes: Scripting Components

## Slide 46: Script Editor
The main scripting component in CWMS is the Script Editor. It is used for:
  Creating new scripts
  Editing existing scripts
  Testing scripts
Notes: Scripting Components
  Script Editor
    The main scripting component in CWMS is the Script Editor. It is used for:
      Creating new scripts.
      Editing existing scripts.
      Testing scripts.

## Slide 47: Opening the Script Editor
Select “ScriptsEditor…” from the CAVI menu bar.
Notes: Scripting Components
  Script Editor
    Opening the Script Editor
      Select “ScriptsEditor…” from the CAVI menu bar.

## Slide 48: Script Editor – Tool Bar
New Script
Print Script
Cut
Copy
Paste
Same functions available via menu bar
Select “FileDelete” to delete a script (no tool for this)
Notes: Scripting Components
  Script Editor
    Script Editor Toolbar
      New Script
      Print Script
      Cut
      Copy
      Paste
      Same functions available via menu bar
      Select “FileDelete” to delete a script (no tool for this)

## Slide 49: Script Editor – Tree Pane
Lists scripts for watershed
Double-click on script name to edit it
Notes: Scripting Components
  Script Editor
    Script Editor – Tree Pane
      Lists scripts for watershed
      Double-click on script name to edit it

## Slide 50: Script Editor – API Pane
Lists CWMS API methods
To insert code in editor pane:
  Double-click node (inserts at current position)
  Drag node to desired position
  Select node and click “Insert in Script” button (inserts at current position)
Notes: Scripting Components
  Script Editor
    Script Editor – API Pane
      Lists CWMS API methods
      To insert code in editor pane:
        Double-click node (inserts at current position)
        Drag node to desired position
        Select node and click “Insert in Script” button (inserts at current position)

## Slide 51: Script Editor – Editor Pane
Displays code for script
Syntax highlighting
Highlights all occurrences of word at current position
Notes: Scripting Components
  Script Editor
    Script Editor – Editor Pane
      Displays code for script
      Syntax highlighting
      Highlights all occurrences of word at current position

## Slide 52: Script Editor – Editor Pane Details
context menu
current line (highlighted)
word at current position (highlighted)
line numbers
Ctrl-F – search
Uses normal select/cut/copy/paste keystroke combinations
Notes: Scripting Components
  Script Editor
    Script Editor – Editor Pane Details
      Context menu contains editing operations.
      Ctrl-F opens search dialog
      Standard editing shortcut keys can be used.

## Slide 53: Script Editor – Action Buttons
Insert in Script
  Inserts code for selected API method into script at current position
Compile Script
  Compiles the script without saving
Save
  Compiles and saves the script
Save/Run
  Compiles, saves, and executes the script
Select
  Notifies other CWMS components of current script selection
Notes: Scripting Components
  Script Editor
    Script Editor – Action Buttons
      Insert in Script – inserts code for selected API method into script at current position
      Compile Script – compiles the script without saving
      Save – compiles and saves the script
      Save/Run – compiles, saves, and executes the script
      Select – notifies other CWMS components of current script selection

## Slide 54: Script Selector
Select “ScriptsRun” from CAVI menu bar.
Displays scripts for watershed.
Double-click on name to run, or select name and click “Run” button.
Notes: Scripting Components
  Script Editor
    Script Selector
      Select “ScriptsRun” from CAVI menu bar.
      Displays scripts for watershed.
      Double-click on name to run, or select name and click “Run” button.

## Slide 55: Modeling Scripts Panel
Select the Modeling tab.
At the bottom of the tab, select the Scripts tab.
Right-click in the Scripts panel and select “Edit…”
Use the “Select Scripts” dialog to choose which scripts to add to the panel
Notes: Scripting Components
  Modeling Scripts Panel
    Select the Modeling tab.
    At the bottom of the tab, select the Scripts tab.
    Right-click in the Scripts panel and select “Edit…”
    Use the “Select Scripts” dialog to choose which scripts to add to the panel

## Slide 56: Modeling Scripts Panel

## Slide 57: Assigning Scripts To Time Series Icons
Switch to Watershed Setup Module.
Right-click the icon and select “Edit” from the context menu.
Select the “Scripts/HTML” tab on the properties dialog.
Populate the scripts dialog with the appropriate information.
  Put a variable assignment statement in the “Arguments” column. That variable with its assigned value will be available in the script.
    This allows a common script to be used on many icons, as each icon will have its unique assignment to the same variable
Dismiss dialogs and save configuration.
Notes: Scripting Components
  Time Series Icons Scripts
    Assigning Scripts to Time Series Icons.
      Switch to Watershed Setup Module.
      Right-click the icon and select “Edit” from the context menu.
      Select the “Scripts/HTML” tab on the properties dialog.
      Populate the scripts dialog with the appropriate information.
        Put a variable assignment statement in the “Arguments” column. That variable with its assigned value will be available in the script.This allows a common script to be used on many icons, as each icon will have its unique assignment to the same variable
      Dismiss dialogs and save configuration.

## Slide 58: Assigning Scripts To Time Series Icons

## Slide 59: Section 5 Review
What component is used to create and edit scripts?
What are three ways to execute a script?
What is the API pane used for?
How can multiple time series icons use a common script and produce individual results?
Notes: Scripting Components
  Section 5 Review
    What component is used to create and edit scripts?
      Script Editor
    What are three ways to execute a script?
      From the Script Editor (Save/Run)
      From the Script Selector
      From the Modeling Scripts Panel
      From a Time Series Icon
    What is the API pane used for?
      To insert code for a CWMS API method into the script
    How can multiple time series icons use a common script and produce individual results?
      By assigning different values to the same variable in the “Arguments” column of the “Scripts/HTML” tab

## Slide 60: Scripting Language
Notes: Scripting Language

## Slide 61: What is Jython?
Jython is a Java-based implementation of the Python programming language. This means:
  You learn the Python language to learn Jython. Python tutorials and book references can be found at http://www.python.org.
  Jython code can interface seamlessly with Java code. The CWMS API is written in Java, but Jython can use it as if it were written in Python.
Notes: Scripting Language
  What is Jython?
    Jython is a Java-based implementation of the Python programming language. This means:
      You learn the Python language to learn Jython.
        Python tutorials and book references can be found at http://www.python.org.
      Jython code can interface seamlessly with Java code.
        The CWMS API is written in Java, but Jython can use it as if it were written in Python.

## Slide 62: Jython Scripting Resources
HEC-DSSVue User’s Guide
  Scripting (army.mil)
  Available from within HEC-DSSVue by selecting “HelpHelp” from the menu bar.
  HEC-DSSVue shares the same API as CWMS for many items, including plots, tables, and HEC-DSS file access.
Examples
  Some examples are installed with HEC-DSSVue in the “samples” directory
  https://github.com/HydrologicEngineeringCenter/DSSVue-Example-Scripts
  The CWMS wiki (https://cwms.usace.army.mil/dokuwiki/) contains many scripting examples, including accessing the CWMS database.
  HEC Monolith documentation https://www.hec.usace.army.mil/software/javadocs/hec-monolith/
Notes: Scripting Language
  Jython Scripting Resources
    Chapter 8 of the HEC-DSSVue User’s Guide
      HEC-DSSVue shares the same API as CWMS for many items, including plots, tables, and HEC-DSS file access.
      Interactive documentation is available from within HEC-DSSVue by selecting “HelpHelp” from the menu bar.
    Examples
      Many examples are installed with HEC-DSSVue in the “samples” directory
      The CWMS wiki (https://cwms.usace.army.mil/dokuwiki/) contains many scripting examples, including accessing the CWMS database.
  For general Java and Python, Army Civilians in the Scientist, Engineer and Analyst (CP16) Career Field have access to Udemy for Business.
    Create an account with your usace.army.mil at Udemy for Business (armyciv.udemy.com)
    Should be emailed instructions on how to setup
    100 days of code course has been highly recommended.
      https://armyciv.udemy.com/course/100-days-of-code/

## Slide 63: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams
“Just keep CWMS’ing”