## Slide 1: HEC-MetVue overview
Fauwaz Hanbali
Hydrologic Engineering Center
CWMS Prospect Course

## Slide 2: Overview
HEC-MetVue Program Interface
HEC-MetVue Key Features Orientation
HEC-MetVue Interactive and Automated Data Processing and Analysis
HEC-MetVue in CWMS
HEC-MetVue

## Slide 3: HEC-MetVue Program Interface

## Slide 4: HEC-METVUE Meteorological Visualization Utility Engine

## Slide 5: Map Panel Features
Visualization Layers
  Contour, Basin Avg., TIN Mesh, Point Measurement, & Gage Interpolation Layers
Interactive zoom:
  Encompass Data or background map extents
  Previous zoom levels
Map Panel tiling and zoom level syncing
Mouse tracking (point coordinate & value)

## Slide 6: Layer Visualization Options
Contour Layer
Basin Average Layer
TIN Layer
Web Map Layer

## Slide 7: HEC-MetVue File & Data Management
A Project File (*.metvue) is in XML format and contains project configuration and settings information
A Session is the work area for the user to organize work units (Map Windows)
A Map Window is the work unit that contains the information the user views and edits
Session
Session
Map Window

## Slide 8: HEC-MetVue Key Features Orientation

## Slide 9: HEC-MetVue Temporal Aggregation
Hourly Radar TINs for N-Hours of Duration
Aggregate TIN for the N-Hours Duration

## Slide 10: HEC-MetVue Basin Average Computation

## Slide 11: Save Time Series
96 aggregated (Hourly) TINs
21July2003 – 25July2003
Spring Creek
1.37 in
24809 ac-ft

## Slide 12: Save Modified Image as a Projection on a Grid
Translating and/or rotating an image will require reprojection of the image for saving the output.
Original Image
Translated and Rotated Image

## Slide 13: HEC-MetVue Spatial Aggregation

## Slide 14: HEC-METVUE Analysis & Manipulation
Refine Storms
  Trim & Correct
Translate Storms
  Spatially
  Temporally
Rotate Storms
  Temporally
Scale Storms
  Factor & Resize
Animate Storms
Original Image
Trimmed Image

## Slide 15: Image Rotation
  Map Center
  TIN Geometric Center
  TIN Weighted Center
Rotating 45 degrees
Rotating 45 degrees
Rotating 45 degrees

## Slide 16: DSS Grid Selection

## Slide 17: Sample PRISM Data
Defined Rectangle
Mask
Polygon
Mask

## Slide 18: Ad-hoc Polygon Clipping

## Slide 19: Time Zone Handling
Input Zone
  DSS and other data types typically have Time Zone Information in their metadata.
  If input data lacks meta data, PC Time Zone assumed by default, but user can override the time zone setting.
Display Time Zone is a user setting to convert the input dataset’s time zone.
MetVue allows for writing output datasets in any desired time zone.
Input
Display
Output

## Slide 20: Dataset Meta Data

## Slide 21: Supported Meteorological Variables
Precipitation
Temperature
Snow Water Equivalent
Snow Melt
Snow Depth
Liquid Water
Cold Content
Cold Content ATI
Metlrate ATI
Air Pressure
Humidity
Dew Point
Sky Cover
Wind Speed
Wind Direction
Solar Radiation
Sunshine
Energy
Albedo
Evapotranspiration
Moisture Deficit
Percolation Rate
Impervious Area
Crop Coefficient
Storage Capacity
Water Content
Water Potential

## Slide 22: Supported Data Products

## Slide 23: Hec-MetVue Interactive and Automated Data Processing

## Slide 24: Combined Dynamic Time Window/Animation

## Slide 25: Quality Control of Interpolated Precipitation Grids

## Slide 26: Image Translation
3-Day QPF issued on 2019.09.06-1800 GMT

## Slide 27: Image Translation
What if?
3-Day QPF issued on 2019.09.06-1800 GMT
(Translated over area of interest to prepare for potential consequences)

## Slide 28: Basin Average Comparison Quantitative Forecast Precipitation (QPF)
NDFD QPF
NCEP QPF
http://www.nws.noaa.gov/ndfd/anonymous_ftp.htm
  ftp://ftp.hpc.ncep.noaa.gov/5km_qpf/

## Slide 29: Ad Hoc Time Series Plotting
Hurricane Florence (September 2018)

## Slide 30: MetInterp
  Inverse Distance Squared (IDW2)
  Inverse Distance (IDW)
  Nearest Neighbor (NN)
  Bilinear (BL)
IDW2
NN
IDW
BL

## Slide 31: HEC-MetVue Command Line Operations
Command Line Utilities for automating HEC-MetVue operations
Batch File | Description
GridReader.cmd | Read/Write supported Gridded Data Formats (e.g. ESRI ASCII Grid & HEC-DSS)
NCGribExtractor.cmd | Extract individual variables from multi-variable NetCDF or GRIB files
AddTin.cmd | Aggregate multiple TINs or Grids
BasinComps.cmd | Compute basin averages
ProjectTinToGrid.cmd | Generate projected Grids from TINs or modified Grids
MetInterp.cmd | Use time series measurements at point locations to generate interpolated grids.
TriangulateTin.cmd | Use aggregate measurements at point locations to generate an interpolated TIN
CalRad.cmd | Adjust Radar grids based on interpolated Gage TINs

## Slide 32: District Daily Precipitation Reports Automated Processing of Real-Time Precipitation Basin Averages

## Slide 33
  uCOP MetVue Dashboard
USACE Projects HW Basin Averages
Automated Processing of Real-Time NWS Products

## Slide 35: HEC-MetVue in CWMS

## Slide 36: HEC-MetVue in CWMS
Data Acquisition & Processing
Data Transformation
Missing Data Filling
Historic Data Time Shifting of analog years
Report Generation
Visualization & Interactive Analysis
Modeling & Forecast Scenarios
HRRR
&/or QPF
MetVue
HMS
ResSim
FIA
RAS
MetInterp or NEXRAD
Observed
Precipitation
& Temperature
Flow
Flow
Flow
Stage
Automated Processing
Forecast
Precipitation
&Temperature
Storm Totals
Product Comparisons
Quality Control
Animation & Dynamic Time Window Scanning
What-if Scenarios
Observed & Forecast
Gridded and/or Non-Gridded Precipitation and Temperature
Observed & Forecast
Gridded and/or
Non-Gridded
Precipitation, Wind Velocity/Direction and Temperature

## Slide 37: RTS-MetVue Model Alternative
HEC-MetVue Session = RTS-MetVue Model Alternative
HEC-MetVue Sessions
RTS-MetVue Alternatives

## Slide 38: QPF Temporal Disaggregation
6 HOUR Input Dataset
1 HOUR Output Dataset

## Slide 39: MetVue Model Alternative Input settings

## Slide 40: MetVue Model Alternative Output settings

## Slide 41: CWMS RTS-MetVue Simulation

## Slide 42: Simulation Alternatives
Observed
Forecast
  Interpolated Grids
  RTMA
  MRMS
  RFC QPE
  Zero Forecast
  HRRR
  3Day NDFD QPF
  7Day WPC QPF

## Slide 43: Summary
HEC-MetVue allows for the display, verification, and editing of spatial data through interactive and visual means.
HEC-MetVue is designed to process and edit precipitation and other meteorological data sets including operations such as: spatial extents trimming, spatial and temporal translation, scaling and resizing, and animations.
HEC-MetVue provides a variety of data transformation and analysis tools, as well as batch processing utilities that can be used in CWMS real-time decision support, in particular:
  Weather/Watershed Monitoring and Assessment and Report Generation
  Scenario Development for Forecast Modeling

## Slide 44: Questions Help additional Training
https://usace.dps.mil/sites/KMP-WM/SitePages/Corps-Water-Management-System-(CWMS).aspx
https://www.hec.usace.army.mil/confluence/cwmsdocs
https://discourse.hecdev.net/c/cwms/5
TDL-CELRH-EC-GW-W-USACE CWMS Modeling | General | Microsoft Teams