## Slide 1: 3.2. Estimation of Economic Uncertainty
Jordan Lucas

## Slide 2: Sources of Uncertainty
First Floor Elevation
Asset Values
  Structure Value
  Contents Value
  Vehicle Value
  Other Value
Depth-Percent Damage Relationships
  Structure Damage
  Contents Damage
  Vehicle Damage
  Other Damage
Notes: Three sources
FFE is approximately where damages begin
Asset values tell us what can be damaged
DDFs tell us at what rate damages increase as stages increase

## Slide 3: Sources of Uncertainty
First Floor Elevation
Asset Values
  Structure Value
  Contents Value
  Vehicle Value
  Other Value
Depth-Percent Damage Relationships
  Structure Damage
  Contents Damage
  Vehicle Damage
  Other Damage
Notes: Let’s talk a bit more about FFE

## Slide 4: First Floor Elevation
First Floor Elevation = Ground Surface Elevation + Foundation Height
Notes: FFE=GSE+FH
Damages generally begin when water surface is above the first floor
Some distance between the ground and the first floor
We want to know that, foundation height

## Slide 5: First Floor Elevation
Uncertainty
  Ground Surface Elevation
    LIDAR
  Foundation Height
    Windshield Survey
      Google Maps Street View
      Site Visit
Distribution Types in FDA 2.0
  Deterministic
  Normal
  Triangular
  Uniform
Notes: Two sources of uncertainty: GSE and Foundation Height
Lidar and eyeballs
Different types allowed in FDA
So, understanding where damages begin on a given structure helps inform the stage-damage relationship

## Slide 6: Ground Surface Uncertainty
May be provided by the source
Can reference FDA Manual (Table 9.1)
Can reference EM 1110-2-1619 (Table 6-5)
Both FDA manual and EM represent uncertainty distributions ~40 years old
FDA Manual (Table 9.1)
Notes: We’re mostly using aerial survey in the form of LIDAR
Table from manual and EM
Very old
  Could be updated

## Slide 7: Methods of Survey
Site Visit – uses human eyeballs to count steps from a vehicle approximately 50 feet away
Google Maps Street View Survey – uses human eyeballs to count steps from street view imagery approximately 50 feet away
  Slightly more uncertainty than site visit due to potentially low res imagery
Hand Level/Stadia – compares multiple points against a reference to find a horizontal distance.
Conventional/Auto Level – uses GPS and reference systems with a stable tripod to triangulate horizontal distance.
Notes: How do we measure foundation height?

## Slide 8: Foundation Height Uncertainty
Google Maps Street View ?? ??????? ??????
FDA Manual (Table 9.1)
Notes: Also very old
Nothing about naked eye or Google Maps Street View
I usually call it .3 or .4
  More uncertainty than Stadia

## Slide 9: How to combine multiple Uncertainties?
Ground El measurement std. dev (σ) = 0.6
Found Ht measurement std. dev. (σ) = 0.4
Notes: Beth showed you this
This is the value you’d enter in FDA

## Slide 10: EM 1110-2-1619
“Alternatively, professional judgment can be used to determine the most-likely, minimum, and maximum values, and a triangular distribution can be fitted.”

## Slide 11: Statistically Significant Sample Size
, where
n = Sample size
Z = Z-Value (1.96)
E = Allowable error (0.20)
Notes: Now we need to determine survey sample
Not one way to do this, this is what we use in MVD
Z is for 95% confidence
S is a proxy of KU based on NV
E is allowable error, or desired level of precision (very sensitive to this)

## Slide 12: Developing a Stratified Sample
Sample Size Source Calculations
Notes: Some examples of stratified samples
Best to split by occ type
Can also split by foundation type
Generally want to stratify by attributes that may impact foundation height
I typically round up to the nearest hundred or 500 depending on the size of the study area
May do separate stratification by floodplain

## Slide 13: Sources of Uncertainty
First Floor Elevation
Asset Values
  Structure Value
  Contents Value
  Vehicle Value
  Other Value
Depth-Percent Damage Relationships
  Structure Damage
  Contents Damage
  Vehicle Damage
  Other Damage
Notes: We know damages begin approx. at FFE
Let’s talk asset value
Helps us understand what can be damaged

## Slide 14: Asset Values
Structure Value
  RS Means
  Marshall & Swift
  Parcel Data
Contents Value
  EGMs (RES)
  Regional Studies
Vehicle Value
  Edmunds or KBB
Other Value
  Regional Studies
  Pretty open-ended
Same distribution types
Notes: Look at the pics
RS Means/M&S
Parcel data (no uncertainty, maybe professional judgment or some other source; DOCUMENT IT)
Regional studies
Edmunds/KBB (no uncertainty)
Other: open-ended
Same distro types

## Slide 15: Asset Value Entry
Structure Value
  Entered directly in structure inventory
Contents Value
  May be entered directly in structure inventory
  May use CSVR
Vehicle Value
  Entered directly in structure inventory
Other Value
  May be entered directly in structure inventory
  May use OSVR

## Slide 16: RS Means
Inputs Convert NSI occupancy types to match RS Means
  Select location factor
  Select level of depreciation
    Estimated age in years
    Poor, Average, Good condition
  Estimated sq ft (assumes we know with certainty)
Outputs
  Used as inputs in FDA
  Depreciated replacement dollar value per sq ft
    Min
    Most Likely
    Max

## Slide 17: Sources of Uncertainty
First Floor Elevation
Asset Values
  Structure Value
  Contents Value
  Vehicle Value
  Other Value
Depth-Percent Damage Relationships
  Structure Damage
  Contents Damage
  Vehicle Damage
  Other Damage
Notes: Last source of uncertainty
We know approx. where damages begin
We know what will be damaged
We need to know at what rate damages occur as stages increase

## Slide 18: Asset Depth Percent-Damage
Structure Damage
  EGMs
  Regional Studies
Contents Damage
  EGMs
  Regional Studies
Vehicle Damage
  EGMs
Other Damage
  Regional Studies
  Other studies or reports
Notes: There’s uncertainty around the asset values, but also the percent-damage for a given depths
The table shows an example of a depth percent-damage relationship
  Normal dist, 5 ft, 60% mean, 4% st dev
EGMs
Regional studies
Vehicle damages come from the EGM
Regional studies fill in the rest of the blanks
Other: open-ended

## Slide 19: EGMs
EGM 01-03: Generic Depth-Damage Relationships for Residential Structures (no basements)
  Structure and Content Depth-Percent Damage
  One Story
  Two+ Story
  Split Level
  AMAZINGLY, allows for negative values
    Mean 2.5%, st dev 2.7%
EGM 09-04: Generic Depth-Damage Relationships for Vehicles
  Sedan
  Pickup
  SUV
  Sport
  Mini Vans
EGM 04-01: Generic Depth-Damage Relationships for Residential Structures (with basements)
  Same as EGM 01-03, but with basements
https://planning.erdc.dren.mil/toolbox/library.cfm?Option=Listing&Type=EGM&Search=Policy&Sort=YearDesc

## Slide 20: Regional Studies
Not commonly conducted today
  Expensive
Sometimes short vs long duration and salt vs fresh water
Will provide example studies for workshop
Expert Elicitation
  Consultants
  Contractors
  Insurance Appraiser/Adjusters
  Construction Executives
  Restoration Construction Experts
  USACE Advisors
Structure Surveys
Structure Owner Interviews