## Slide 1: Reservoir Modeling Methodologies
Advanced Applications of HEC-HMS
March 2023
Gregory S. Karlovits, P.E., PH, CFM
Statistical Hydrologist
US Army Corps of Engineers
Hydrologic Engineering Center

## Slide 2: Purpose
Understand and apply appropriate reservoir modeling techniques in HEC-HMS

## Slide 3: Outline
Reservoir element overview
Specified release
Outflow curves
Outflow structures
Rule-based routing
Reservoir volume reduction (sediment)

## Slide 4: Reservoir Element Overview

## Slide 5: Reservoir Element
One of the seven basin model element types
One upstream element
Up to two downstream elements
  Main
  Auxiliary
Five routing methods
  None, Outflow Curve, Outflow Structures, Rule-Based Operations, Specified Release

## Slide 6: Geometry (Storage Method)
Reservoir computes the continuity equation
Outflow Curve | Outflow Structures | Rule-Based Operations | Specified Release
Elevation-Area-Discharge | Elevation-Area | Elevation-Area | Elevation-Area
Elevation-Storage-Area-Discharge | Elevation-Storage | Elevation-Storage | Elevation-Storage
Elevation-Storage-Discharge | Elevation-Storage-Area | Elevation-Storage-Area | 
Storage-Discharge |  |  | 

## Slide 7: Initial Conditions
State information required for simulation start
Available options depend on selected storage method
  Storage (simplest)
  Elevation
  Discharge
  Inflow = Outflow
Notes: The Discharge method is available for outflow curves – since storage and outflow are 1:1 related, the initial storage can be determined
The Inflow = Outflow method takes the inflow to the reservoir at the beginning of the simulation and determines the pool elevation necessary to cause that outflow through the outlet structures. The pool elevation is then used in the elevation-storage curve to determine the matching storage.

## Slide 8: Simulation Results
Notes: The top plot is for geometry – it shows the reservoir’s storage and elevation for the simulation. Not all routing methods will have an elevation plot, but all of them must compute storage.
The bottom is for flow – the reservoir inflow is dashed, and outflow is solid.

## Slide 9: Reservoir Options Tab
Notes: Observed outflow allows you to set a discharge gage as an observed flow series that you can compare your results to
Observed tailwater stage lets you set a stage gage as an observed stage time series that you can compare computed tailwater stages to (requires a tailwater rating curve)
Observed pool elevation is pretty self-explanatory
Tailwater stage-discharge lets you set a rating curve for the tailwater – this can be important for computing hydraulic structure submergence.
The reference flow and label are for making a nice label on your simulation results graph.

## Slide 10: Best Practices
Use a junction upstream and downstream of your reservoir
Calibrate/validate your model isolating out the reservoir first
  Use Specified Release method to pass the right flows downstream
Keep it simple
  HMS is not ResSim

## Slide 11: “None” Routing Method
“--None--” will pass flow downstream with no routing

## Slide 12: Specified Release

## Slide 13: Specified Release
Used when the outflow from a reservoir is known
Elevation/storage computed from simulated inflow and specified outflows

## Slide 14: Specified Release
Outflow specified as a discharge gage
Optional settings: Max Release, Max Capacity
  Settings do not alter outflows, only produce warnings

## Slide 15: Specified Release – When to Use?
Calibration/validation phase of model construction
Releases are determined by something external to HMS

## Slide 16: Outflow Curves

## Slide 17: Outflow Curves
Reservoir outflow is determined solely by storage
Ideal for reservoirs with no gates/operations
Can be “calibrated” to represent more complex reservoirs
Notes: This gets quite a bit of use for detention basin design – most have simple geometry and outflow relationships that makes modeling them very easy.

## Slide 18: Outflow Curves – Storage Method
Simplest option is the Storage-Discharge storage method
Other methods will compute elevation
Notes: The “Primary” setting just determines the interpolation scheme. The Outflow Curve method builds a big table for all the geometry variables involved, and the one set as “primary” determines the initial configuration of the table (what rows the other tables are interpolated to.)

## Slide 19: Outflow Curve Calibration
Works best when operations are simple
Iterative process
  Build curve
  Run simulation
  Check stage/storage/ outflow
  Modify curve

## Slide 20: Outflow Curves – When to Use?
Outflow is always the same for a given storage
  Ungated outlets/spillways, dam tops, etc.
Operations can be reasonably simplified to a single curve
Long Term Reservoir Volume Reduction Analysis

## Slide 21: Outflow Structures

## Slide 22: Outflow Structures
Outflow computed by a collection of hydraulic structures
  Outlets
  Spillways
  Dam tops
  Pumps
Simulate other kinds of outflows
  Dam breaks
  Dam seepage
  Time-series releases
  Evaporation

## Slide 23: Outlets
Orifice Outlet
Culvert Outlet
Always submerged
Can flow partially full

## Slide 24: Spillways
Broad-Crested
Ogee
Specified

## Slide 25: Spillway Gates
Sluice Gate
Radial Gate
Notes: Note that the only control method is “Fixed Opening” – the gates do not move during the simulation. This will compute the hydraulics through a gate at a fixed setting.

## Slide 26: Dam Tops
Level
Non-Level

## Slide 27: Pumps

## Slide 28: Tailwater
Controls determination of submergence for structures
5 options:
  Assume None
  Reservoir Main Discharge (requires rating curve)
    Computed at outlet – no backwater
  Downstream of Main Discharge (requires rating curve)
    Computed at next element downstream
  Specified Stage (requires stage time series)
  Fixed Stage

## Slide 29: Outflow Structures – When to Use?
Complex combination of ungated hydraulic structures
Need to compute dam breaks, seepage, or evaporation

## Slide 30: Rule-Based Reservoir Routing

## Slide 31: Guide Curve Operations
Notes: There are three states in guide curve ops.
You can be right on the guide curve (see the yellow dot.) For the day of the year, the reservoir has the desired storage.
You can be above the guide curve (see the blue dot.) For the day of the year, the reservoir is storing more than desired.
You can be below the guide curve (see the orange dot.) For the day of the year, the reservoir is storing less than desired.

## Slide 32: Basic Guide Curve Operation
Above the Guide Curve
  increase releases as necessary (or possible) to lower the pool elevation to the Guide Curve.
Below the Guide Curve
  reduce releases as necessary (or possible) to raise the pool elevation to the Guide Curve.
At the Guide Curve
  release “just enough” to maintain the pool elevation at the Guide Curve
Notes: Basic Guide Curve Operations
1.5-L-04
Klipsch 1.5-L-04
32
From HEC-ResSim Slide

## Slide 33: Rule-Based Reservoir Routing
Extension of Outflow Structures routing method
Uses rules and operable structures to determine releases
Zones determine what rules are applied
  Reservoir elevation
  Day of the year

## Slide 34: Rule-Based Reservoir Routing
Based on Outflow Structures
Additional control for Zones

## Slide 35: Zones
A grouping of homogeneous rules
Defined by an elevation range and day of year for each zone
  Finds first Maximum Elevation curve above the current elevation/day
Need at least one for operations to work

## Slide 36: Maximum Elevation

## Slide 37: Maximum Elevation
Daily Elevation Pattern Paired Data
Top zone should cover entire range of elevations and dates
Curve does not need to be defined for every day of the year
  If nothing defined, zone will not be used for that day
Schedule A Non-Growing Season
Schedule A Growing Season
Notes: In the example on the right, a regulation manual calls its basic flood operations “Schedule A”. The dam has the potential to cause agricultural damages, so maximum releases are limited during the growing season compared to the non-growing season, so despite these having the same overall elevation (707 ft) the rules they contain would be different.

## Slide 38: Storage Objective (Guide Curve)
For every day of the year, what is the desired storage?
Currently able to be defined for each zone
  May change to a single guide curve in the future
  Recommend using only one unless you have really specific needs
Flood Pool
Conservation Pool

## Slide 39: Storage Pattern
Interpolates between points
Needs to cover entire year

## Slide 40: Rules
Added via Zone
Rules are specific to a single zone

## Slide 41: Rule Types (10)
Type | Limits | Operation
Main Release | Min, Max, Specified | Sets a target for releases in the main direction
Auxiliary Release | Min, Max, Specified | Sets a target for releases in the auxiliary direction
Downstream Flow* | Min, Max, Specified | Sets a target for an element downstream
Rate of Flow Change | Max | Limits how much releases can change
*requires iterative trial releases

## Slide 42: Rules
No limit to what you can specify
Try not to make them conflict

## Slide 43: Downstream Controls
Require iterative trial releases
Significantly add to simulation time
Keep them as simple as possible

## Slide 44: Outflow Structures
All features of Outflow Structures method available
Only some structures have parts that can be operated
  Outlets
    General Outlet
    Gated Orifice
  Broad-Crested and Ogee Spillways
    Radial Gates
    Sluice Gates

## Slide 45: Gate Control Methods
Adjustable Gate Control
Fixed Opening
Percent Annual Pattern
Percent Time Series
Notes: Adjustable gate control is what allows the rule-based operations to work.
Some structures (e.g. gated orifice, spillway gates) have a fixed opening option.

## Slide 46: General Outlet
Simplified outlet based on rating curves
Min and max rating
  Gates at 0% and 100% open
Specify from a regulation manual

## Slide 47: General Outlet

## Slide 48: Gated Orifice Outlet

## Slide 49: Gated Spillway
Operable sluice and radial gates for Broad-Crested and Ogee spillways

## Slide 50: Calibration
Isolate reservoir by using a source element with a timeseries gage
Calibration by adjusting rules
  These may deviate from the regulation manual
  Add other rules or settings for stability
    Rate of change rules help even if not included in WCM
Calibration by adjusting structures
  Adjust rating curves for outlets or spillways using simple methods

## Slide 51: Rule-Based Reservoir Routing – When to Use?
Storage target and releases vary seasonally
Complex rules and operable structures determine releases
You will be surprised how far you can get with simple guide curve operations for many models!

## Slide 52: Reservoir Volume Reduction
Slides by Dr. Jay Pak

## Slide 53: Reservoir Volume Reduction Process

## Slide 54: Reservoir Volume Reduction Chen & Brune Trap Efficiency
Notes: Sediment must be turned on in the basin model in order to use these capabilities.

## Slide 55: Tuttle Creek Results with Reservoir Volume Reduction

## Slide 56: Questions?