## Slide 1: Continuous Simulation
Lauren Coe, P.E.
Slides by Thomas Brauer, P.E.
Hydrologic Engineering Center

## Slide 2: Overview
Learn about the differences between event and continuous simulation.
Learn about the structure of the soil moisture accounting loss rate method.
Learn about the deficit constant loss rate method and how it is similar and differs from soil moisture accounting.
Learn about the layered Green Ampt loss method and how it represents infiltration in a physically based way.

## Slide 3: Soil Water Basics
Soil is a porous media with solids and voids, containing air or water.
Richard's Equation – Water moves through an unsaturated soil chiefly due to matric forces.
Darcy's Law – Water moves through a saturated soil chiefly due to hydrostatic forces.
Hydrophobic compounds in the soil particles may affect water movement.
In general, soil properties are highly heterogeneous.
Notes: Matric forces bond water to solid particles
Hydraulic conductivity for saturated soils

## Slide 4: Continuous versus Event

## Slide 5: Available Loss methods
Loss Method | Event | Continuous
Deficit and constant |  | Yes
Exponential | Yes | 
Green and Ampt | Yes | 
Gridded deficit and constant |  | Yes
Gridded Green and Ampt | Yes | 
Gridded SCS curve number | Yes | 
Gridded soil moisture accounting |  | Yes
Initial and constant | Yes | 
Layered Green and Ampt |  | Yes
Linear Deficit and Constant | Yes | Yes
SCS curve number | Yes | 
Smith Parlange | Yes | 
Soil moisture accounting |  | Yes

## Slide 6: Soil Water Basics
The soil is unsaturated when precipitation starts.
If the rain rate is large enough, water ponds on the soil surface.
Hydrostatic force pushes the ponded water into the soil, while matric forces pull the water into the soil.
Water redistributes due to matric forces when ponding ceases.

## Slide 7: Modeling requirements
The meteorologic model must be configured with precipitation and evapotranspiration. Add snowmelt in cold climates.
Subbasins must use a canopy method. The plant canopy is the mechanism for extracting water from the soil moisture state.
Subbasins must use a loss method that tracks soil moisture state, i.e. Soil Moisture Accounting, Deficit and Constant, or Layered Green and Ampt.

## Slide 8: Deficit Constant
Notes: Canopy storage
Surface Depression (optional)
Infiltrate to Soil Storage
Deficit is zero  percolation
Precipitation > percolation direct runoff

## Slide 9: Deficit Constant
The meteorologic model should be configured with precipitation and evapotranspiration. Add snowmelt in cold climates.
Initial conditions:
  Initial deficit.
Parameters:
  Maximum deficit (soil storage, tension storage, canopy interception)
  Infiltration/Percolation rate.
  Percent impervious area (directly connected)
Notes: Directly connected impervious areas are surfaces where runoff is conveyed directly to a waterway or stormwater collection system. These surfaces differ from disconnected impervious areas where runoff encounters permeable areas which may infiltrate some (or all) of the runoff prior to reaching a waterway or stormwater collection system.
Constant rate ( can be estimated as hydraulic conductivity)
The maximum deficit is typically defined using the product of the effective soil porosity and an assumed active layer depth, but it should be calibrated using observed data.
The constant rate defines the rate at which precipitation will be infiltrated into the soil layer after the initial deficit has been satisfied in addition to the rate at which percolation occurs once the soil layer is saturated.

## Slide 10: Precipitation and Infiltration
Fill canopy interception. Precipitation that exceeds the canopy storage capacity will overflow and be added to the surface
Infiltrate from surface depression. Infiltration is not limited by a maximum rate, but will cease when soil storage is full.
The current deficit is the amount of water that will infiltrate before surface runoff can begin.
Notes: Precipitation through-fall from the canopy, or direct precipitation if there is no canopy, impacts on the surface. The net precipitation accumulates in the depression storage and infiltrates as the soil has capacity to accept water. Surface runoff will begin when the precipitation rate exceeds the infiltration rate of the soil layer (loss method), and the surface storage is filled.
If precipitation occurs during the interval, ET is not modeled. Precipitation contributes first to canopy-interception storage. Precipitation in excess of canopy-interception storage, combined with water already in surface storage, is available for infiltration. If the volume available is greater than the available soil storage, or if the calculated potential infiltration rate is not sufficient to deplete this volume in the determined time step, the excess goes to surface-depression storage. When surface-depression storage is full, any excess is surface runoff.

## Slide 11: Percolation and Evapotranspiration
Percolation only occurs when the soil is saturated. That is, the moisture deficit = 0 due to sufficient infiltration.
Percolated water can be split between contribution to linear reservoir baseflow, and aquifer recharge.
Evapotranspiration is computed by the plant canopy component.
Percolation stops as soon as evapotranspiration creates a moisture deficit in the soil.

## Slide 12: Soil Moisture Accounting
Question: Which parameter in Deficit and Constant is roughly equivalent to soil storage?
Notes: Canopy storage
Surface depressions (optional)
Infiltrate to soil storage
ET from Upper Zone
ET from Tension Storage
Soil Moisture > Tension Storage  Percolation to GW1
GW1 to GW 2 or Baseflow
GW2 to Aquifer or Baseflow
Precipitation rate > infiltration rate direct runoff

## Slide 13: Soil Moisture Accounting
The meteorologic model should be configured with precipitation and evapotranspiration. Add snowmelt in cold climates.
Initial conditions:
  Percent soil storage.
  Percent groundwater storage.
Parameters:
  Soil storage and tension storage.
  Groundwater storage.
  Maximum infiltration rate.
  Maximum soil percolation.
  Maximum groundwater percolation.
  Groundwater storage coefficients.
  Percent impervious area.

## Slide 14: Precipitation and Infiltration
Fill canopy interception. Precipitation that exceeds the canopy storage capacity will overflow and be added to the surface.
Precipitation storage on the surface:
  Infiltrate to soil profile.
  Calculate the precipitation remaining in surface depression.
  Water exceeding surface storage becomes precipitation excess.
Soil storage:
  Add infiltration to the soil storage.
  Percolation occurs only when soil storage exceeds tension storage.
Notes: The Maximum Infiltration Rate sets the upper bound on infiltration from the surface storage into the soil. This is the upper bound on infiltration; the actual infiltration in a particular time interval is a linear function of the surface and soil storage, if a Surface Method is selected. Without a selected Surface Method, water will always infiltrate at the maximum rate.
Soil Storage represents the total storage available in the soil layer. It may be zero if you wish to eliminate soil calculations and pass infiltrated water directly to groundwater.
Tension Storage specifies the amount of water storage in the soil that does not drain under the affects of gravity. Percolation from the soil layer to the upper groundwater layer will occur whenever the current soil storage exceeds the tension storage. Water in tension storage is only removed by evapotranspiration. By definition, tension storage must be less that soil storage.
I = infiltration
Imax = maximum infiltration
Ssurf = surface storage
Ssurfmax = maximum surface storage
Ssoil = soil storage
Ssoilmax = maximum soil storage

## Slide 15: Percolation
Soil percolation only occurs when soil storage exceeds the tension zone storage.
Groundwater percolation occurs as long as there is storage.
Notes: The Soil Percolation sets the upper bound on percolation from the soil storage into the upper groundwater. The actual percolation rate is a linear function of the current storage in the soil and the current storage in the upper groundwater.
Groundwater 1 Storage represents the total storage in the upper groundwater layer. It may be zero if you wish to eliminate the upper groundwater layer and pass water percolated from the soil directly to the lower groundwater layer.
The Groundwater 1 Percolation Rate sets the upper bound on percolation from the upper groundwater into the lower groundwater. The actual percolation rate is a linear function of the current storage in the upper and lower groundwater layers.
The Groundwater 1 Coefficient is used as the time lag on a linear reservoir for transforming water in storage to become lateral outflow. The lateral outflow is available to become baseflow.
Psoil = soil percolation
Psoilmax = maximum soil percolation
Ssoil = soil storage
Ssoilmax = maximum soil storage
Pgw1 = groundwater 1 percolation
Sgw1 = groundwater 1 storage
Sgw1max = maximum groundwater 1 storage
Pgw2 = groundwater 2 percolation
Sgw2 = groundwater 2 storage
Sgw2max = maximum groundwater 2 storage

## Slide 16: Evapotranspiration
Evapotranspiration removes water from the soil layer at the potential rate while the current storage exceeds the tension storage. During this phase the soil water will also be percolating to groundwater.
Evapotranspiration from the soil layer while in the tension zone is controlled by the canopy’s tension reduction method.
Notes: If tension reduction is selected, the amount of evapotranspiration from the tension zone is a function of the storage. It represents the fact that water is increasingly difficult for plants to remove from the soil as the soil dries out.

## Slide 17: Groundwater
Percolation into groundwater 1 is a function of current storage in the soil and groundwater 1.
Percolation from groundwater 1 into groundwater 2 depends on the storage in both layers.
Both groundwater layers convert a portion of water in storage to lateral outflow that connects to the linear reservoir baseflow.
  Add incoming percolation.
  Subtract outgoing percolation.
  Calculate portion of remaining storage that becomes lateral outflow.
  Transform lateral outflow to become baseflow.
Percolation out of groundwater 2 can be split between contribution to linear reservoir baseflow, and aquifer recharge.

## Slide 18: Layered Green Ampt
Question: What water volume in the soil cannot be drained by gravity?
Notes: It may also be used in combination with a Surface Method that will hold water on the land surface. The water in surface storage infiltrates to the soil layer. The infiltration rate is determined by the capacity of the soil layer to accept water. When both a Canopy and Surface Method are used in combination with the Layered Green and Ampt Method, the system can be conceptualized as shown in the following figure.
Canopy storage
Surface depressions (optional)
Infiltrate to soil storage
Layer 1 saturated  infiltration = seepage rate
L1 Soil moisture > field capacity  seepage to L2
ET extracts L1 then L2
ET extracts from both, until wilting point
Layer 1 and Layer 2 saturated  infiltration = percolation rate
Precipitation rate > infiltration rate  direct runoff

## Slide 19: Layered Green Ampt
The meteorologic model should be configured with precipitation and evapotranspiration. Add snowmelt in cold climates.
Initial Conditions:
  Layer 1 initial content.
  Layer 2 initial content.
Parameters:
  Saturated water content.
  Field capacity, wilting point.
  Layer thickness.
  Wetting front suction.
  Saturated hydraulic conductivity.
  Maximum seepage, percolation.
  Percent impervious area.
  Dry period duration (for reset).
Notes: Layer 1 and 2 thicknesses [in or mm], field capacity [in/in or mm/mm], wilting point [in/in or mm/mm], layer 1 maximum seepage rate [in/hr or mm/hr], layer 2 maximum percolation rate [in/hr or mm/hr], and dry duration [days].
The layer 1 and 2 thicknesses define the bulk depth of soil and are typically estimated using soil maps.
The field capacity content specifies the point where the soil naturally stops seeping under gravity while the wilting point content specifies the amount of water remaining in the soil when plants are no longer capable of transpiring infiltrated water. Both parameters are typically estimated using predominant soil texture and literature values.
The dry duration sets the amount of time that must pass after a storm event in order to recalculate the initial condition. An initial estimate of 12 hours has been found to be reasonable for the dry duration. However, this parameter should be calibrated using observed data.
Finally, the percentage of the subbasin which is directly connected impervious area can be specified. Directly connected impervious areas are surfaces where runoff is conveyed directly to a waterway or stormwater collection system. These surfaces differ from disconnected impervious areas where runoff encounters permeable areas which may infiltrate some (or all) of the runoff prior to reaching a waterway or stormwater collection system. No loss calculations are carried out on the specified percentage of the subbasin; all precipitation that falls on that portion of the subbasin becomes excess precipitation and subject to direct runoff.

## Slide 20: Precipitation and Infiltration
Fill canopy interception. Precipitation that exceeds the canopy storage capacity will overflow and be added to the surface.
Precipitation storage on the surface:
  Infiltrate to soil profile.
  Calculate the precipitation remaining in surface depression.
  Water exceeding surface storage becomes precipitation excess.
Layer 1:
  Add infiltration to the layer storage.
  Infiltration is limited to maximum seepage rate when saturated.
  Seepage occurs only when storage exceeds field capacity.
Notes: Precipitation fills the canopy storage. Precipitation that exceeds the canopy storage will overflow onto the land surface. The precipitation is added to any water already in surface storage. The infiltration rate from the surface into Layer 1 is calculated with the Green and Ampt Equation so long as Layer 1 is below saturation. The infiltration rate changes to the current seepage rate when Layer 1 reaches saturation.
f = Infiltration
Ksat = Saturated Hydraulic Conductivity
h = Wetting Front Suction Head
ΘSAT = Saturated Water Content
Θinit = Initial Water Content
F = Cumulative Infiltration

## Slide 21: Percolation and Evapotranspiration
Seepage only occurs if Layer 1 storage exceeds field capacity.
Percolation only occurs if Layer 2 storage exceeds field capacity.
Seepage is limited when Layer 2 is saturated.
Percolation can be split between contribution to linear reservoir baseflow, and aquifer recharge
Evapotranspiration is computed by the plant canopy component.
Notes: The infiltration rate changes to the current seepage rate when Layer 1 reaches saturation. Infiltrated water is added to the storage in Layer 1. Seepage out of Layer 1 only occurs when the storage exceeds field capacity. Maximum seepage occurs when Layer 1 is at saturation and declines to zero at field capacity. The seepage rate changes to the percolation rate when Layer 2 is saturated. Seepage is added to the storage in Layer 2. Percolation out of Layer 2 only occurs when the storage exceeds field capacity. Maximum percolation occurs when Layer 2 is at saturation and declines to zero at field capacity.
RSEEP = Rate of Seepage
Seepmax = Maximum Seepage
RSEEP = Rate of Percolation
Percmax = Maximum Percolation
Θ = Water Content
ΘSAT = Saturated Water Content
ΘFC = Field Capacity Water Content

## Slide 22: Plant Canopy
No ET from soil without Canopy Method (w/Canopy Uptake Method)
The uptake method determines how water is extracted from the soil:
  Simple approach extracts at the potential evapotranspiration rate provided by the meteorologic model. It works with all three methods.
  Tension reduction reduces extraction as the soil becomes drier. Typically applied with soil moisture accounting, but can use with Layered Green Ampt.

## Slide 23: Surface Depression
The surface depression component captures precipitation or canopy overflow for eventual infiltration.
Allows for infiltration after the rain has stopped, thus increasing total potential infiltration.
Soil moisture accounting with no surface:
  Precipitation or canopy overflow infiltrates at the maximum infiltration rate when soil is unsaturated.
  Infiltration reduces to the maximum percolation rate when the soil is saturated.
  Precipitation exceeding the infiltration/percolation becomes excess precipitation.
Deficit constant with no surface is essentially unchanged except total infiltration is reduced.
Layered Green Ampt with no surface will reset the initial water content quicker after the end of precipitation.

## Slide 24: Gridded Loss Methods
A regular grid is overlaid on the subbasin to break it into grid cells.
Each grid cell receives a separate precipitation value.
The state variables in each grid cell evolve separately from surrounding grid cells.
"Gridded" loss methods have separate parameter values and initial conditions for each grid cell.
"Lumped" loss methods use the same properties at all cells.

## Slide 25: Method Differences
Deficit constant method lumps soil and groundwater together.
  A larger water store is available for evapotranspiration and so it may be overestimated.
Deficit constant method does not separate gravity and tension zones in the soil profile.
  Soil moisture is only removed by evapotranspiration.
Soil moisture accounting method uses a reduction function for evapotranspiration.
  Evapotranspiration is better modeled in soils that regularly dry out.
Layered Green Ampt is more physically based.
  Less parsimonious
  Infiltration is more clearly linked to the soil moisture content.

## Slide 26: Review
Learned about the differences between event and continuous simulation.
Learned about the structure of the soil moisture accounting loss rate method.
Learned about the deficit constant loss rate method and how it is similar and differs from soil moisture accounting.
Learned about the layered Green Ampt loss method and how it represents infiltration in a physically based way.
Technical Reference Manual is a great resource: Available Loss Methods - HEC-HMS Technical Reference Manual - HEC Confluence (army.mil)