## Slide 1: Snowmelt Modeling Methodologies
Advanced Applications of HEC-HMS
June 2024
Avital Breverman, P.E.
Slides borrowed from:
Mike Bartles, P.E.
US Army Corps of Engineers
Hydrologic Engineering Center

## Slide 2: Overview
Review energy transfer in, out, and within a snowpack
Describe the available snowmelt modeling approaches within HEC-HMS
  Energy Budget
  Hybrid
  Temperature Index
Discuss snowmelt parameter sensitivity and calibration techniques
2
Notes: Guess what spillway this is

## Slide 3: Snowpack Energy Inputs/Output
In order to melt snow, energy is required.
This energy comes from radiation, wind, air temperature, rain, etc.
Typically snow melts in three phases:
  Warming: Frozen snow absorbs energy which causes the snowpack temperature to rise to 32 degrees F.
  Ripening: Snow absorbs energy which causes melt to occur where water fills the pores in the snowpack.
  Melt/Runoff: More energy absorbed into snow causes melt water to leave the snowpack.
All three phases must be represented in order to produce runoff.
3

## Slide 4: Available Snow Modeling Methods
Multiple modeling approaches are available to represent energy transfer:
  Temperature Index
    Use air temperature as a surrogate for the total heat transfer
    Banded and gridded implementations
  Radiation-derived TI (RTI)/Hybrid
    Account for some modes of heat transfer but not all
    Gridded implementation (no banded)
  Energy Budget
    Explicitly account for each mode of heat transfer
    Banded and gridded implementations
4
Notes: In version 4.10, snow methods were migrated from the Meteorologic Model to the Basin Model.

## Slide 5: Temperature Index Method
5

## Slide 6: Temperature Index Method
Derived from the TI model within SSARR (USACE, 1987)
  Streamflow Synthesis and Reservoir Regulation (SSARR) was based upon TI method in Snow Hydrology (USACE, 1956)
Great flexibility in describing the melt rate
  Deep cold snowpack melting for months -> melt rate changes to account for snow metamorphism and seasonal change in meteorology
  Shallow, seasonal snowpack that melts in a few days -> constant melt rate
Though simple, it has been widely used with good results throughout the world
6
Notes: USACE. (1987) SSARR Model, Streamflow Synthesis and Reservoir Regulation. User Manual. (Reprinted 1991) US Army Corps of Engineers, North Pacific Division, PO Box 2810, Portland, OR 97208-2870
USACE. (1956) Snow Hydrology. Summary Report Of The Snow Investigations. North Pacific Division, Corps of Engineers, U.S. Army, Portland, Oregon. 30 June 1956

## Slide 7: Temperature Index Method
Uses a melt rate times the linear difference between the air temperature and base temperature to estimate melt:
  Melt = Mf (Ta – Tbase)
Dry melt rate, Mf, serves as an index of the total heat transfer at the snow surface
Can be influenced by wind speed, aspect, slope, vegetation, etc.
Mf can be a constant, a function of the accumulated thawing days, or a function of the day/time of year
7

## Slide 8: Temperature Index Method
8

## Slide 9: Temperature Index Method
LWASS
Precipitation
SWE
Temperature
9
Notes: HMS calculates SWE and liquid water at the soil surface (LWASS)

## Slide 10: Temperature Index Parameters
PX Temperature
Base Temperature
ATI Coefficient
Wet Melt
  Constant, Pattern
Rain Rate Limit
Dry Melt
  Constant, Function, Pattern
Cold Limit
Coldrate Function
Coldrate Coefficient
Water Capacity
Groundmelt Method
Groundmelt
10

## Slide 11: PX Temperature
The discrimination temperature between precipitation falling as rain or snow.
When the air temperature is less than the specified PX temperature, any precipitation is assumed to be snow.
When the air temperature is above the specified PX temperature, any precipitation is assumed to be rain.
This discrimination temperature is usually pretty close to freezing (32oF-34oF).
11

## Slide 12: Base Temperature
The difference between the base temperature and the air temperature defines the temperature index used in calculating snowmelt.
The melt rate is multiplied by the difference between the air temperature and the base temperature to estimate the snowmelt amount.
If the air temperature is less than the base temperature, then the amount of melt is assumed to be zero.
The base temperature is usually pretty close to freezing (32oF-34oF).
Be careful using a base temperature > PX temperature.
12

## Slide 13: PX / Base Temperature
PX Temperature
Base Temperature
13
Notes: On this slide, subbasin-specific PX and Base temperatures for water year 2017 are compared against one another
It’s evident that there are large differences in PX and Base temperature throughout the watershed

## Slide 14: Temperature Index Parameters
PX = 32 deg F
PX = 34 deg F
Base = 32 deg F
Base = 34 deg F
14
Notes: PX temperature discriminates between precipitation falling as rain vs. snow
  Higher PX temperature means that there is a wider range of temperatures at which precipitation falls as snow which allows more snow to accumulate
Base temperature is the temperature above which snow melts
  Lower base temperature means that there is a wider range of temperatures at which snow melts which reduces the snowpack

## Slide 15: Dry Melt Rate
Constant, annual pattern, or function
A variable melt rate function recognizes that as the snowpack matures the heat transfer rates change AND/OR different components of heat transfer change in importance.
Clean Snow
Dirty Snow
15

## Slide 16: Dry Melt Rate
Constant
  Using a constant allows for this parameter to be included in optimization and uncertainty calculations.
ATI-Melt Rate Function
  The seasonal variation of melt rate is indexed by an antecedent temperature function.
  The initial melt ATI should be thought of as “the accumulated thawing degree days” at the start of the simulation.
  Using a function allows the melt rate to change as the snowpack matures and ages.
Annual Pattern
  An alternate method of entering the melt rates as a function of the day/time of year.
16

## Slide 17: ATI-Melt Rate Function
ATI-Melt Rate: Melt rate values associated with ATI values in depth per degree-day.
Typical range of melt rate values is 0.015-0.2 in/oF-day.
ATI-Melt Rate Coefficient for updating the antecedent temperature index. Set to 0.98 – 1.0
Automating the Development of ATI-Meltrate Functions
17

## Slide 18: Annual Pattern
Entered as a Parameter Value Pattern:
  ddMMM, HH:mm vs. Melt Rate
Parameters can be estimated using techniques like these: Empirical Radiation Snow Model
  Giovando, et al. (2023)
18
Notes: Giovando, et al. (2023): https://doi.org/10.1016/j.jhydrol.2023.129290

## Slide 19: Dry Melt Rate
Slow Meltrate
Fast Meltrate
19
Notes: PX temperature = 34 deg for both

## Slide 20: Dry Melt Rate
Questions to ask yourself when setting dry melt rates:
How long does it take the snow to melt away at any one location?
  A few days – use a constant melt factor
    Melt rate is independent of ATI
    Typical of the eastern U.S.
  A month or more – use a variable melt factor
    Melt rate is dependent upon ATI or is a Function of Date/Time
    Typical of the western U.S.
20

## Slide 21: Dry Melt Rate
Questions to ask yourself when setting dry melt rates:
How much SWE is typically on the ground?
  A few inches or less – use a constant melt factor
    Melt rate is independent of ATI
    Typical of the eastern U.S.
  10 inches or more – use a variable melt factor
    Melt rate is dependent upon ATI or is a Function of Date/Time
    Typical of the western U.S.
21

## Slide 22: Wet Melt Rate
Greatest cause of snowmelt during rain-on-snow is from heat transfer to the snowpack during condensation of water vapor on the snowpack surface
Lesser cause of snowmelt during rain-on-snow is due to melting from warm rain by direct contact
Constant or annual pattern
22

## Slide 23: Wet Melt Rate
Wet Melt Rate
The wet melt rate should not be less than the dry melt rate
Usually, the wet melt rate is set to the higher end of the dry melt rate function, 0.05 - 0.2 in/oF-day.
Rain Rate Limit
The discrimination rain rate in inches/day between dry melt and wet melt.
The wet melt rate is applied as the melt rate when it is raining at rates greater than the rain rate limit.
If the rain rate is less than the rain rate limit, the melt rate is computed as if there were no precipitation. (0.1 – 1 in/day)
23
Notes: Third viewport is SWE. Notice the dip in SWE that corresponds with a ton of runoff and flooding.

## Slide 24: Cold Rate
ATI-Coldrate Function
Cold Content is the amount of energy required to bring the snowpack to 32 deg F (sensible heat).
Expressed as a depth of frozen water
The ATI for cold content is an index to the snow temperature near the surface.
It is calculated assuming an approximation to the transient heat flow equations.
Typically set as a constant function (i.e. coldrate doesn’t change with ATI).
Typical range of values is 0.01 - 0.05.
ATI-Coldrate Coefficient.
Coefficient for weighting previous values when updating the ATI-Coldrate.
Typical value 0.2-0.5.
Base Coldrate
Delayed Coldrate
24
Notes: Base and PX temperature = 34 deg for both
Notice that each time the “Base Coldrate” curve melts, the “Delayed Coldrate” curve doesn’t. That’s because the “Delayed Coldrate” curve builds cold content at a greater rate and gets it through the short periods when temperatures are above the base temperature

## Slide 25: Water Capacity
The maximum liquid water capacity specifies the amount of melted water that must accumulate in the snowpack before liquid water becomes available at the soil surface for infiltration or runoff
Typically, the maximum liquid water capacity is 3%-5% of the SWE
Liquid water can persist in the snow only if the snowpack temperature is at 32oF (0oC); at which point the cold content is zero
Water content affected by age of snowpack to the largest extent
25

## Slide 26: Groundmelt
Snow melt that occurs due to heat transfer from the ground beneath the snowpack.
Almost always set to zero, especially for relatively shallow, seasonal snow covers (SWE < 10 inches)
May not always be zero…
Mount St. Helens, 1982
26

## Slide 27: Temperature Index Method
27
Advantages
"Mature" method that has been used successfully in thousands of studies throughout the U.S.
Easy to set up and use
Only requires precipitation and air temperature boundary conditions
More parsimonious than other methods
Disadvantages
May be too simple for some situations
Limited snowpack outputs compared to other methods
Notes: Parsimony/parsimonious is relative to the user
In this instance, I’m comparing this snow method against the other snow methods within HEC-HMS (e.g. hybrid and energy balance)
Temperature index offers both lumped and gridded implementations

## Slide 28: Hybrid / RTI Method
28

## Slide 29: Hybrid / RTI Method
Derived from Follum, et al. (2015)
Instead of using air temperature, use a proxy that includes short and longwave radiation
Incorporates topographic, cloud cover, vegetation, and albedo affects
Requires additional meteorologic boundary conditions
Relatively new method
29

## Slide 30: Hybrid / RTI Method
30
Notes: Radiation is generally the largest contributor to melting the snowpack

## Slide 31: Hybrid / RTI Method
31
Air Temperature
Longwave
Shortwave
Radiation Temperature

## Slide 32: Hybrid / RTI Parameters
Rain Threshold Air Temperature
Snow Threshold Air Temperature
Base Temperature
Melt Factor
Max Negative Melt Factor
ATI Coefficient
Wind Function
Water Capacity
32

## Slide 33: Rain and Snow Threshold Temperatures
Discrimination temperatures above/below which precipitation falls as rain or snow.
Rain temperature must be equal to or greater than snow temperature
If the two aren’t equal, precipitation goes to both liquid and snow
Rain (32oF - 40oF)
Snow (30oF - 35oF)
33

## Slide 34: Melt Factor and Max Negative Melt Factor
Melt factor = Dry melt rate
  0.001 in / oF-6hr – 0.01 in / oF-6hr
Wet melt rate is calculated using relative humidity, saturation vapor pressure, and atmospheric pressure
  If 6 hr precip. accum. > 1.5 mm (0.06 in) && current precip. rate > 0.25 mm/hr (0.01 in/hr)
  These are not user-entered parameters. They are hard coded.
Max Negative Melt Factor (NMF)
  Used to update snowpack heat deficit
  Positive value despite its name
  0.001 in / oF-6hr – 0.05 in / oF-6hr
34
Notes: Increasing the Max Negative Melt Factor increases the heat deficit and delays the initiation of snow melt
Decreasing the Max Negative Melt Factor decreases the heat deficit and causes snow melt to initiate sooner

## Slide 35: Melt Factor and Max Negative Melt Factor
35
MF = base
MF = -66%
MF = +66%
NMF = base
NMF = -66%
NMF = +66%
Notes: Melt Factor
Decreasing Melt Factor results in less melt
Increasing Melt Factor results in more melt
Max Negative Melt Factor
Decreasing Max Negative Melt Factor results in more melt
Increasing Max Negative Melt Factor results in less melt

## Slide 36: Hybrid / RTI Method
36
Advantages
Incorporates factors such as short and longwave radiation into snowmelt equations
Can incorporate terrain slope, aspect, and shading
More snowpack outputs than TI method
Disadvantages
Requires additional meteorologic boundary conditions
Less mature than other methods

## Slide 37: Energy Budget Method
37

## Slide 38: Energy Budget Method
Based upon University of Utah Energy Budget model
  Tarboton, et al. (1995)
Method balances energy stored within a single snow layer and upper part of the ground
Change in energy content affects snow water equivalent
Requires lots of additional meteorologic boundary conditions
Largely an academic method
38
Notes: The Energy Budget method incorporates many more sources of energy that can potential melt (or grow) the snowpack
Image is of the Susquehanna River at Harrisburg, PA during the January 1996 flood
The January 1996 flood affected the Ohio River, Susquehanna River, Delaware River, and everything in between. Primary causes were large amounts of precipitation, high temperatures, large antecedent snow water equivalents, but also extremely high wind speeds. High wind speeds causes turbulent heat transfer. In essence, this allows for warm air to constantly be in contact with the snowpack. Normally, the air immediately above the snowpack is pretty cold. This drastically increases the rate at which the snowpack melts.
However, this method, especially when compared against the temperature index and RTI methods, requires a significant amount of additional boundary condition data.

## Slide 39: Energy Budget Method
39
Notes: Radiation is generally the largest contributor to melting the snowpack

## Slide 40: Energy Budget Method
Requires iterative solver to balance mass/energy inputs and outputs, snowpack temperature, surface temperature, etc.
More computationally intensive than other snow methods
40
inner loop B computes surface temperature
B
A
outer loop A computes energy and mass flux for a time step

## Slide 41: Energy Budget Method
41
Compute State Change
Compute Energy and Mass Flux
Compute Surface Fluxes
Compute Surface Temperature
Compute Melt Rate
Update Snowpack State
A
B
Met Boundary Conditions
Generate Outputs
Notes: Use previous time step for initial SWE and snowpack energy content
Update each guess for SWE and energy content after each iteration
Iterate outer loop until guessed SWE and energy = computed SWE and energy (within tolerance):
  deltaSwe > 0.025 mm
  deltaEnergy > 2000 J
  Max # iterations < 15
Iterate inner loop until surface temperature balances

## Slide 42: Energy Budget Parameters
Rain Threshold Air Temperature
Snow Threshold Air Temperature
New Snow Albedo
Min Snow Albedo
Albedo Refresh Depth
Albedo Decay
Snow Thermal Conductivity
Liquid Water Retention Fraction
Snow Hydraulic Conductivity
Soil Depth for Energy Balance
42

## Slide 43: New Albedo, Min Albedo, and Albedo Refresh Depth
Albedo of fresh snow
  When new snow depth > albedo refresh depth
  0.6 – 0.95
Minimum albedo
  0.1 – 0.5
Depth at which albedo is reset
  0.02 inches – 0.2 inches
43
Clean Snow
Dirty Snow
Notes: Albedo is the reflectivity (0 to 1)
  Albedo = reflected light/incident light
The maximum possible albedo value is 1.0 (all incident light is reflected)
But brand-new snow rarely has an albedo of 1.0

## Slide 44: New Albedo and Min Albedo
44
New Albedo = base
New Albedo = -66%
New Albedo = +66%
Min Albedo = base
Min Albedo = -66%
Min Albedo = +150%
Notes: New Albedo
Decreasing New Albedo means less incident light is reflected resulting in less accumulation/less SWE
Increasing New Albedo means more incident light is reflected allowing for more accumulation/more SWE
Min Albedo
Decreasing Min Albedo means less incident light is reflected resulting in less accumulation/faster melt out
Increasing Min Albedo means more incident light is reflected resulting in more accumulation/slower melt out

## Slide 45: Albedo Decay Coefficient
Describes how albedo decays from new snow albedo to min snow albedo
Constant or Annual Pattern
40 hrs – 600 hrs
45
Actual Observations
Model Results
Notes: Three winters of albedo measurements and snow depth observations in the Senator Beck basin in Colorado.
  solid blue circles are the daily average snow albedo
  open blue circles are the daily average albedo when the snow depth was reported as zero
  orange line is the daily average snow depth.

## Slide 46: Albedo Decay Coefficient
46
Albedo Decay = base
Albedo Decay = -50%
Albedo Decay = +50%
Notes: Albedo Decay Coefficient
  Increasing albedo decay coefficient decreases the rate of snowmelt
  Decreasing albedo decay coefficient increases rate of snowmelt

## Slide 47: Snow Thermal Conductivity
Describes how efficiently heat is transferred within the snowpack
0.01 btu / ft / oF / hr – 0.1 btu / ft / oF / hr
47
Thermal Cond. = base
Thermal Cond. = -66%
Thermal Cond. = +66%
Notes: Increasing snow thermal conductivity allows heat to be transferred more efficiently through the snowpack resulting in higher snow accumulations
Decreasing the snow thermal conductivity causes heat transfer to be less efficient which results in less accumulation and faster melt out

## Slide 48: Energy Budget Method
48
Advantages
Incorporates factors such as short and longwave radiation, sensible heat flux, sublimation, condensation, and wind into snowmelt equations
Can incorporate terrain slope, aspect, and shading
Lots of snowpack outputs available including SWE, snow density, snow depth, snowpack temperature, snowpack energy, albedo, etc.
Disadvantages
Requires lots of meteorologic boundary conditions
Computationally intensive
Solution isn’t guaranteed to converge
Much less parsimonious than other methods

## Slide 49: Boundary Condition Requirements
49
Process | Temperature Index | Hybrid | Energy Budget
Precipitation | X | X | X
Temperature | X | X | X
Shortwave Radiation |  | X | X
Longwave Radiation |  | X | X
Wind Speed |  |  | X
Atmospheric Pressure |  | X | X
Relative Humidity |  | X | X

## Slide 50: Snow Parameter Calibration
50

## Slide 51: Calibration
Two approaches:
  Calibrate parameters for times with both accumulation and melt
  Calibrate parameters only during times of melt
The goal for both is to modify parameters to reduce the difference between the calculated and observed SWE
Computed SWE
Observed SWE
51

## Slide 52: Calibration
Two approaches:
  Calibrate parameters for times with both accumulation and melt
  Calibrate parameters only during times of melt
The goal for both is to modify parameters to reduce the difference between the calculated and observed SWE
Computed SWE
Observed SWE
52

## Slide 53: Calibration Metrics
Metrics to use:
  Rate of melt
  Peak SWE
  Date of Peak SWE
  Melt Out Date
  NSE
  RSR
  PBIAS
  Etc.
Water Year | Peak SWE (in) |  |  | Peak SWE Date |  | SWE Meltout Date |  | NSE | RSR | PBIAS
 | Model | Obs. | Diff. | Model | Obs. | Model | Obs. |  |  | 
2008 | 48.9 | 59.0 | -10.1 | 13May | 12Jun | 30Jun | 14Jul | 0.68 | 0.53 | 29.6
2009 | 44.6 | 55.9 | -11.3 | 01May | 06May | 25Jun | 06Jul | 0.79 | 0.34 | 18.6
2010 | 45.2 | 47.0 | -1.8 | 25May | 29May | 11Jul | 11Jul | 0.99 | 0.12 | 6.5
2011 | 68.0 | 72.9 | -4.9 | 30May | 12Jun | 21Jul | 23Jul | 0.99 | 0.05 | 2.2
2012 | 40.4 | 39.6 | 0.8 | 19Apr | 19Apr | 25Jun | 24Jun | 1.00 | 0.03 | 0.9
2013 | 43.1 | 41.8 | 1.3 | 05May | 25Apr | 25Jun | 23Jun | 0.98 | 0.13 | 5.8
2014 | 56.6 | 55.6 | 1.0 | 12May | 27Apr | 05Jul | 04Jul | 0.99 | 0.05 | 1.4
2015 | 41.9 | 37.8 | 4.1 | 26Apr | 16Apr | 19Jun | 18Jun | 0.96 | 0.17 | 7.9
2016 | 41.0 | 43.0 | -2.0 | 18Apr | 14Apr | 19Jun | 20Jun | 0.99 | 0.08 | 1.7
2017 | 54.2 | 60.4 | -6.3 | 02May | 04May | 30Jun | 30Jun | 0.85 | 0.44 | 21.0
Overall | - | - | - | - | - | - | - | 0.91 | 0.18 | 6.1
53

## Slide 54: Calibration
Peak SWE
Melt Out
54

## Slide 55: Calibration
USACE Snow Course
NCDC Hydromet Station
55
Notes: SNOTEL is not the only source of point data for snow
SNOTEL stations (~900) are located at high elevations in the western 11 states
Left: National Climatic Data Center (NCDC, now part of National Centers for Environmental Information (NCEI) hydromet station
Right: USACE snow course station, often located near dams

## Slide 56: Snowmelt Graph
56
Precipitation
Air Temperature
SWE

## Slide 57: Calibration Strategies
If available, calibrate point SWE using multiple SNOTEL gages/snow sites in the watershed, each with its own set of observed data
Calibrate to a number of events/water years
Use a large time step (e.g. 1 day)
Very fast!
Point Calibration Workshop
57

## Slide 58: Calibration Strategies
Calibrate basin-average SWE against SNODAS or UofA data
Need to extract basin-average SWE
Calibrate to a number of events and/or water years
Use a smaller time step (e.g. 1 hr)
Can be slow
Gridded Snowmelt Workshop
HMS
SNODAS
58

## Slide 59: Grid-to-Point Tool
Extract subbasin-average time series from gridded data using the grid to point tool
Working with Gridded Data Workshop
59

## Slide 60: Calibration Strategies
Calibrate runoff using snowmelt parameters
This is more important than any other calibration step!
Modify snowmelt, loss, transform, baseflow, etc parameters, as necessary
Calibrate to a number of events and/or water years
Use a smaller time step (e.g. 1 hour)
Will be slow
60

## Slide 61: Optimization
Can optimize parameters using both gridded and banded approaches
  Only constants are allowed
  No Annual Patterns or Functions
THIS IS NOT AUTO CALIBRATION!!!
Only use this feature after you’ve figured out reasonable parameter ranges
61

## Slide 62: Optimization
62

## Slide 63: Uncertainty
How much uncertainty in SWE, flow, volume, reservoir pool stage, etc. is due to snowmelt parameters?
Can use both gridded and banded approaches
  Only constants are allowed
  No Annual Patterns or Functions
63

## Slide 64: Uncertainty
64
Martis Creek Dam
Pool Elevation
Uncertainty due *solely* to wet melt rate!
Flow at Reno, NV
Notes: Results generated by randomly sampling a uniform distribution of wet meltrates ranging between 0.05 and 0.2 in/degF-day and applying uniformly throughout the modeling domain (i.e. wet meltrate is the same for each subbasin element)
Then, apply the precipitation and temperature sequences observed during the Jan 1997 flood event
Large amount of uncertainty due to just this single parameter!
This uncertainty needs to be incorporated within reservoir regulation manual and infrastructure design decisions!

## Slide 65: Parameter Sensitivity
65
Notes: Use the Uncertainty Analysis and multiple linear regression to assess parameter sensitivity
In this case, we are examining how sensitive SWE is to 10 Energy Budget parameters
The left plot is a tornado plot and shows the magnitude of the regression coefficient
Higher absolute values indicate that SWE is more sensitive to that parameter and can help you decide which parameters to focus on during calibration
Positive regression coefficient means that increasing that parameter value increases SWE
Negative regression coefficient means that decreasing that parameter value increases SWE
The right plot shows a comparison of a single model parameter, new snow albedo, to SWE
We’ve standardized the parameter values and SWE values so that everything has a common scale and large standard deviation values do not exert outside influence on the results
The regression coefficient of 0.723 indicates that this parameter has a significant impact on computed SWE

## Slide 66: Review
Reviewed energy transfer in, out, and within a snowpack.
Described the available snow modeling methods within HEC-HMS along with important model parameters.
Detailed how to calibrate snow method parameters.
Discussed optimization and uncertainty.
66

## Slide 67: Questions?
67