## Slide 1: Model Calibration
Hydrologic Modeling with HEC-HMS
Instructor:
Jay Pak
Notes: I’ll be presenting on model calibration. Model is set up with our components and methods, now we want to calibrate or adjust the parameters to the model so results make sense

## Slide 2: Outline
Calibration Theory
Calibration Strategies
Calibration Metrics

## Slide 3: Calibration Theory

## Slide 4: Hydrologic Modeling
We can’t experiment on a real watershed
Our model stands in for reality
Goal: represent our watershed accurately using algorithms
Notes: Why do we go about creating hydrologic models?
Often, hydrologic modelers are interested in performing experiments on a watershed so we can see how its behavior changes when some property of it is changed. We can’t experiment on a real watershed for many reasons. We can’t apply design rainfall; we can’t evaluate engineering project impacts without building them; we can’t have a side-by-side comparison of a control and an experiment. In order to experiment on a watershed, we need to use a model as a stand-in for the real thing.
Instead of soil and plants, we have equations that govern how much water goes where. These equations represent the physical world in a deterministic way.

## Slide 5: Hydrologic Modeling
Models contain approximations and simplifications
Simpler model → parameters represent more → more parameter uncertainty
Notes: It is necessary for a model of something as complex as the flow of water through the environment to contain approximations and simplifications of the real world. Even if we could represent the entire watershed at the atomic level, the measurement of the physical properties of the watershed necessary to model all the physics would contain uncertainty. Then, applying the physics at that scale would be computationally prohibitive.
Models should be as simple of a representation of the system being modeled as needed to answer the question or perform the experiment. When several related processes are rolled into one algorithm to represent them, the parameters of that algorithm become more and more abstract and uncertain. While the parameters become more uncertain, their level of abstraction also lends them well to being determined empirically.

## Slide 6: What is Calibration?
Adjustment of model parameters
Manual or automatic
Goal: match output with observed data
Notes: Our hydrologic model is a collection of parametric algorithms that simulate the hydrologic cycle. It is up to us as modelers to determine what the appropriate parameters for those algorithms are. We want to make our algorithmic representation of the watershed match the actual watershed across a wide range of conditions. Usually, we determine if our model matches reality by comparing model output for observed past events and seeing if key results match. We may consider whether the simulation of streamflow at locations where we have flow observations match reasonably well. We may also compare observations for other hydrologic processes such as snowmelt and accumulation, and evapotranspiration.
There are some so called “automated” tools for performing calibration, but the most reliable way to produce a calibrated model with reasonable parameters is to change the parameters yourself until the model results match observed data.

## Slide 7: Why Calibrate?
Uncertainty abounds
Models are simplifications
Initial estimates are only estimates
Boundary Conditions
Hydrologic Model
Observed Data
Notes: There is uncertainty inherent in all parts of the hydrologic modeling process. The data used to define the model has measurement error – everything from elevation data and land use data to meteorologic and hydrologic boundary conditions. Process simplifications can create parameters that represent several things all rolled into one number. Models are also abstractions of the real world. Even the most detailed so-called physical models are simplifications of the hydrologic cycle.
When we make an initial estimate of a parameter from physical data, it is just that – an estimate. Using the same technique across many watersheds will on average get you close to a good value, but each individual estimate may be off.
We assume that any mismatch between the hydrologic results and the observed data are due to mis-specification of hydrologic model parameters. There are more advanced techniques involved in jointly assessing uncertainty in boundary conditions, hydrologic model parameters, and the observed data – but that’s out of scope here.
What we want in the end is a model that represents our watershed well even when we change the boundary conditions out from underneath it.

## Slide 8: Observed Data
Observed data are necessary for calibration
  Precipitation Gages
  USGS stream gages
  Snow observations or models
  Evaporation data
Notes: Observed data are the key to knowing if our model represents reality or not. A known standard that we can compare the model to, will give us an assessment of its performance.
Usually, we are interested in calibrating flow, so we reach for instantaneous streamflow data when we can. Occasionally only coarse timestep data such as daily-average data are available, and we can aim for that instead.
Other times, the processes are more complicated. In snow-dominant watersheds we may want to calibrate the snow processes independently using observed (or modeled) snow data. For continuous calibration, it might be beneficial to calibrate the evapotranspiration process – although data to do so may be rare.

## Slide 9: HMS Calibration
Basin model parameters
  Subbasins
  Reaches
  Reservoirs/diversions
  Snowmelt
Met model parameters
  ET
Notes: When calibrating an HEC-HMS model, we are changing the parameter values for the processes inside the basin model and the meteorologic model.
In the basin model, the primary location we will make adjustments is in the subbasin elements. They handle the majority of the rainfall-runoff process.
We changed to model snowmelt as a basin process, so the snowmelt parameters are now also handled in the subbasin elements. The temperature index method has several tunable parameters that can improve model performance not only in the explicit snowmelt and accumulation processes, but also in the resulting runoff. ET may be adjusted in a fine sense to match observations, or more coarsely to address mismatches in overall discharge volume.
For more complicated watersheds where elements are connected with reaches, we may adjust reach parameters to get channel routing correct. In order to model historical events correctly, we may also need to make changes to reservoir or diversion operations.

## Slide 10: Model Parameters
Any numeric value or functional relationship that controls model behavior
Notes: Some model parameters are typically treated as fixed, while others are allowed to freely vary during the calibration process.
For example, the area of a subbasin element is a model parameter, but it isn’t changed while calibrating.
On the left is a subbasin element, and the parameters for the loss process are shown. The user has selected the Deficit and Constant loss method as the most appropriate method for modeling the loss process in this watershed.
The method is not initially parameterized with any values and it is up to the user to provide initial estimates for those parameter values. Then, during the calibration process, these values are adjusted in order to improve model performance.
On the right is the subbasin settings for the temperature index snow model. This is a highly-parameterized model process and can include more than single-numeric-value parameters. ATI-meltrate functions and ATI-coldrate functions are an empirical representation of a mathematical function and can be calibrated to improve model performance. It is again up to the user to initially parameterize the model with parameter values, and then to adjust those parameters to improve model performance.

## Slide 11: Calibration Process
Initial parameter estimates
Adjustment of parameters
Assessment of agreement
Validation
Iterate
Notes: There is a four-step process to calibrating a hydrologic model.
First you must determine a set of initial parameters to get the model to run and assess the initial performance of the model. There are helpful tools for getting useful parameters based on data about the watershed.
Next you will begin to adjust the model parameters so that the agreement between the model and observed data begins to improve.
With each change in parameters, take the time to assess how the model performance changes. Then, go back to the parameter adjustment, and iterate. You will loop between step 2 and 3 many times, even if the initial parameter estimates aren’t bad.
Finally, once you have a candidate set of calibration parameters, you will run a validation simulation, which helps ensure your parameters are useful outside of the event you used for calibration.

## Slide 12: Initial Parameter Estimates
Gather informative data
  Soils
  Land use/imperviousness
  Basin characteristics
Estimate starting values from data
  Experience
    Utilize knowledge from local history, past projects, and site visits to inform initial estimates.
  Regression
  Regional values
  Other heuristics
Notes: HMS does not provide default values for model parameters. It is up to the user to provide reasonable starting values for model process parameters.
Experienced modelers can draw on knowledge of similar models to choose reasonable starting parameters. Models for similar watersheds may have similar parameters and parameter values from previous model calibrations may provide good starting points.
Data-driven approaches use physical information to estimate model parameter values. Typically, these estimates are driven by data such as soil surveys, land use/land cover and imperviousness data, basin physical characteristics, and so on.

## Slide 13: Parameter Regression
Calibrate models in a region
Predict calibrated parameters from physical data
Notes: Regression equations are sometimes developed from regional studies. Several models are calibrated, and their physical properties retained. Then, a regression model is fit to the data so that the physical properties explain the variability in the calibrated parameters. These equations can then be used to estimate parameters in other watersheds. An example of a predictor equation for time of concentration based on basin drainage area and drainage density is shown on the right. Time of concentration tends to be easier to predict using regional regression than some other parameters are.
Over time, modelers have developed other useful guidelines for estimating starting parameters. Some parameters are easier to estimate from physical data, such as constant loss rate, percent impervious, time of concentration, and so on. Then, simple rules can be applied to these estimated parameter values to estimate other parameter values. Two examples of this are shown in the lower right. After estimating time of concentration, the storage coefficient can be estimated using an empirical relationship such as this. Typical values for this ratio are in the range of 0.5-0.8. For linear reservoir groundwater parameters, the fast-response layer coefficient can be initially estimated by 30 times the time of concentration.
DD is the drainage density.

## Slide 14: Adjustment of Parameters
Work upstream to downstream
Keep realistic ranges in mind
Consider physical evidence
Change one parameter at a time
S1
S2
S4
S3
Marion
Outlet
Notes: Here are some simple rules for a successful calibration.
First, work upstream to downstream. Get a small area performing well, and then move downstream – and leave the smaller areas alone when adjusting parameters further downstream. In the image shown, you would calibrate S1 and S2 above the Marion junction first, and then calibrate S3, S4 and the Indian Creek reach next at the Outlet junction. When calibrating for the Outlet junction you should leave everything above the Marion junction alone once the performance at Marion is satisfactory.
When calibrating, keep in mind what ranges for a parameter are reasonable. If you are pushing against the boundary of reasonable values in your calibration, perhaps you need to be adjusting something else to bring that parameter back into range.
Consider why the model is behaving the way it is and consider the physical explanation for hydrologic behavior. Look at physical information to explain why the model behaves differently in different parts of the watershed. For example, parts of the watershed with poorly drained soils should probably have a lower infiltration rate than areas with well drained soils.
To really get a sense of the magnitude and direction of change on model performance you get by changing a parameter, change one parameter at a time and re-run the model. Then when you feel good about the model performance in one aspect (such as timing or volume) you can move on to another parameter to change that parameter. This isolates the effects of the parameters and gives you feedback on how sensitive the model performance is to it.

## Slide 15: Assessment of Agreement
Visual agreement
Goodness-of-fit metrics
  Nash-Sutcliffe Model Efficiency
  Volume Error
  Root-Mean-Square Error
  Coefficient of determination (R2)
Notes: In order to assess model agreement, you need to be able to compare the model output to observed data. In HEC-HMS, observed data is shown in black, with the simulated results in blue.
Visual agreement is the first step. It lets you qualitatively assess things like timing, volume, hydrograph shape, and so on. When you’re calibrating you can get a long ways just by using a visual comparison. Eventually you get to a point where it’s hard to know objectively whether one parameter set is better than another, and goodness-of-fit metrics can help. They can also give you an idea of how good your agreement is numerically.
Four common goodness-of-fit metrics are shown here.
There are guidelines for what values of these goodness-of-fit metrics describe good agreement between the model and observed data. These concepts will be discussed in another video.

## Slide 16: Validation
Use calibrated parameters on another event
Do not adjust the parameters
Assess goodness of fit
Notes: Validation is an extremely important and often overlooked step. It assures that you have not overfit your parameters to a single event, and that the model has predictive power outside of just the calibration period. A mistake often made is that a modeler will start to alter parameters during the validation process, but then the independent assessment of the model performance is ruined. The only parameters that MIGHT change in a situation like this are initial conditions (e.g., initial deficit, initial baseflow, etc.) Things like constant rate, unit hydrograph parameters, baseflow coefficients, and so on, should not change. The best way to represent the performance of a model for general use is to report its validation statistics.

## Slide 17: Calibration Strategies

## Slide 18: Objectives
Setting Initial Model Parameters
  Data Sources
  Estimation Methods
Setting Calibration Goals
  Calibration Metrics
Notes: This lecture will cover how to set some of the more common initial model parameters—including data sources & estimation methods that you can use.
We’ll also cover how to set calibration goals and the calibration metrics that HMS provides.

## Slide 19: Setting Initial Model Parameters
Loss
Transform
Baseflow
Routing
Evapotranspiration/Snowmelt
Notes: Setting initial model parameters—Where do those values come from?
We’ll discuss how you might estimate the initial loss, transform, baseflow & routing parameters for your model and will also touch briefly on ET & Snowmelt as well.

## Slide 20
Initial Model Parameters - Loss
Loss Parameters
Regulate Infiltration
Various Methods Available
Depend On:
  Rainfall
  Soil Compaction
  Slope
  Cracks
  Roots
  Vegetation
  Soil Moisture
  Litter
  Temperature
  Soil Porosity
  Soil Type
  Urban Areas
  & More!
Source: (Top)- http://ftp.comet.ucar.edu/memory-stick/hydro/basic_int/runoff/navmenu.php_tab_1_page_2.1.0.htm, (Bottom)-https://cals.arizona.edu/extension/riparian/chapt3/p07.html
Notes: Loss parameters are very important within HMS—they regulate how much precipitation infiltrates into the soil and what becomes runoff.
There are several loss methods available within HMS. Loss parameters are physically-based and really depend on the soil properties and condition of your watershed.

## Slide 21
Initial Model Parameters - Loss
Loss Parameter Data Sources:
Gridded Soil Survey Geographic (gSSURGO) Database
Digital General Soil Map of the U.S. (STATSGO2)
*Gridded Nat'l Soil Survey Geo. Database (gNATSGO)*
National Land Cover Database (NLCD)
Local Resource Agencies/Studies
Source: https://www.nrcs.usda.gov/wps/portal/nrcs/detail/soils/survey/geo/?cid=nrcseprd1464625
Notes: There are a number of nationwide, online products available that provide detailed soil information such as gSSURGO, STATSGO and gNATSGO that compiles the “best available” data to eliminate gaps.
The National Land Cover Database (NLCD) also provides valuable information on land use which can be used in estimating initial loss parameters.
Local resource agencies and nearby soil or watershed studies may also provide valuable information.

## Slide 22
Initial Model Parameters - Loss
Initial Estimate Example:
Deficit and Constant Method
  Initial Loss: Dependent on Antecedent Conditions
    Fully Saturated? 0.0 in
    Very Dry? > 0.0 in
  Constant Loss
    Estimate using soil texture from gSSURGO and lit. values
  Maximum Deficit
    gSSURGO Available Water Storage
  Impervious (%): Dependent on Land Cover/Use
    NLCD Urban Imperviousness
    NLCD Impervious Estimate by Type of LC
      Assign each type a %-impervious value, ratio by area within subbasin
Source: https://www.nrcs.usda.gov/wps/PA_NRCSConsumption/download?cid=nrcs142p2_051847&ext=pdf
Notes: As mentioned earlier, there are several loss methods available within HMS, but here’s an example of how you might estimate initial loss parameters for the Deficit & Constant method.
Initial loss is very dependent on antecedent conditions within the watershed. This value ranges from Zero—when soils are already fully saturated—to higher values if the simulation is starting during a dryer period.
Constant loss rates can be estimated using soils data (such as gNATSGO)—use the soil texture from gSSURGO and literature values.
The Maximum Deficit value can also be estimated using soils data by estimating the average available water storage within each subbasin.
The Percent Impervious values can be estimated using the NLCD Urban Imperviousness data or by deriving values from the regular NLCD data by estimating the impermeability of each land class and deriving an estimate from spatial statistics.

## Slide 23: Initial Model Parameters - Transform
Transform Parameters Impact Hydrograph Timing & Attenuation within Subbasins
Compute Initial Estimate with Regression:
Time of Concentration (Tc):
Tc = Time of Concentration (hr)
L = Longest Flowpath (mi)
Lca = Centroidal Longest Flowpath (mi)
S10-85 = 10-85 Stream Slope (ft/mi)
Storage Coefficient (R):
R = Storage Coefficient (hr)
Tc = Time of Concentration (hr)
Try Constant=0.5 to start
Other Initialization Methods:
Previous Models
Other Regression Equations
Time
Flow
Tc:
Time
Flow
Tc:
Time
Flow
R:
R:
Time
Flow
= Constant
Notes: Transform parameters are also critical within HMS—they impact the timing & attenuation of subbasin hydrographs.
You can compute initial estimates of the Time of Concentration (Tc) using subbasin physical properties.
The Storage Coefficient (R) is usually associated as a ratio with Tc and that ratio is usually set equal to a constant value. A good initial estimate would be setting the R/(Tc+R) ratio to 0.5 and solving for an initial R value.
Other methods to estimate these initial parameters include referencing previous models or referring to regression equations and studies from within your region as well. Some regions have even identified typical ranges of the R/(Tc+R) ratio—so local resources can be extremely helpful if you can find them!

## Slide 24: Initial Model Parameters - Baseflow
Baseflow Parameters Impact Hydrograph Attenuation & Recession within Subbasins
Common Baseflow Methods:
Recession:
  Recession Constant
    Baseflow recession slope
    Typically 0.7 to 1
    ↓ Value = ↑ Slope
    Start with 0.9, adjust in calibration
  Ratio to Peak
    Threshold at which BF recession begins
    Start with 0.2, adjust in calibration
Linear Reservoir:
  Conserves Volume (No Loss)
GW1 coefficient = 3 x Tc
GW2 coefficient = 10 x Tc
Tc = Time of Concentration
Flow
Time
Flow
RTP=0.5
Time
Flow
RTP=0.2
Time
Flow
Time
Flow
RC=1
RC<1
1.0
0.5
0.0
1.0
0.2
0.0
Notes: HMS Baseflow parameters impact the hydrograph’s attenuation & recession within each subbasin.
HMS offers several baseflow methods, but we’ll focus on a couple of the most common.
The figures on this slide help illustrate the key components of the recession baseflow method—that has two primary parameters—the Recession Constant—which essentially defines the slope of the receding hydrograph. Recession constant values typically range from 0.7 to 1.0. A recession constant of 1 results in a completely horizontal tail. The further the value is from 1.0, the steeper the slope. Assuming an initial value of 0.9 & further adjusting in calibration is a good starting point for this parameter.
The Ratio to Peak parameter is essentially the threshold at which the Baseflow Recession begins—the pivot point of the hydrograph. Looking at the 2nd row of figures here—a Ratio to Peak of 0.5 places the pivot point at 50% of the peak flow value. A Ratio to Peak value of 0.2 lowers the pivot point to the 20% (of peak flow) value on the receding limb of the hydrograph.
Initial RTP values can be estimated by examining observed flow data or through adjustment during calibration.
The Linear Reservoir method is another popular HMS baseflow method and is particularly relevant when groundwater interaction is occurring within a watershed as it conserves volume throughout the simulation event. Rules of thumb for estimating the Groundwater Coefficients are shown here as 3 times the time of concentration for the 1st Coefficient and about 10 times Tc for the 2nd coefficient.

## Slide 25: Initial Model Parameters - Routing
Routing Parameters Impact Hydrograph Timing & Attenuation within Reach Elements
Common Routing Methods:
Lag: Directly translates hydrograph as specified
Modified-Puls: Uses HEC-RAS to compute storage-discharge relationships in specified reaches.
Muskingum:
  Muskingum X = Attenuation Factor (0 to 0.5, try starting with 0.25 & adjust in calibration)
  Number of Subreaches
  t = time step (hr)
Notes: The HMS Routing parameters impact the hydrograph timing & attenuation within Reach Elements.
Several routing methods are available, but we’ll touch on a few of the common ones.
The Lag method directly staggers the hydrograph by the specified Lag Time and does not include any attenuation or storage.
The Modified-Puls method uses HEC-RAS to determine storage-discharge relationships within specified reaches.
The Muskingum method uses the length and slope of each reach to estimate its travel time. Attenuation can be adjusted by adjusting the Muskingum X value between 0 and 0.5—I suggest starting with 0.25 and adjusting further during calibration. The number of subreaches for this method is estimated by dividing the Travel Time by the simulation timestep.

## Slide 26: Initial Model Parameters – ET & Snow
Evapotranspiration (ET)
Accounts for water vaporization & plant absorption.
Data Sources:
  National Climatic Data Center (NCDC)
  Water Control Manuals/Local Reports
Snowmelt Parameters
Includes Temperature, Snow & Melt Parameters
Data Sources:
  Snow Data Assimilation System (SNODAS)
  Snow Telemetry (SNOTEL)
  Add’l Local & Nationwide Sources
ET & Snow can be calibrated independently of streamflow.
Notes: Evapotranspiration (ET) and Snowmelt Parameters can also be applied within HMS.
ET accounts for water vaporization & plant absorption—initial ET values can be derived from Evaporation Data found on the NCDC website. ET estimates are also often included in USACE Water Control Manuals or reports on other local studies.
Snowmelt parameters include temperature, Snow and Melt components. Snowmelt data sources include SNODAS—which is national snow modeling output or SNOTEL which includes direct snow measurements and is widely available in the Western US.
Both the ET & Snowmelt components can be calibrated independently from the runoff/streamflow calibration within HMS.

## Slide 27: Setting Calibration Goals
Goals Vary by Project Objective
Goal Examples:
  Quantitative Goodness-of-Fit
    Statistics
  Timing
  Volume
  Magnitude
Notes: Now that you’ve developed initial parameters for your model--It’s very helpful to set goals when calibrating an HMS model. Calibration goals might include:
-Quantitative goodness-of-fit goals—using statistics
and goals for how important it is to capture the timing, volume and magnitude of the calibration events.
Examples of goals are included in the next few slides, but goals should be determined based on the objectives of the HMS project.

## Slide 28: Calibration Goals
Quantitative Goodness-of-Fit
  Coefficient of Determination, Nash-Sutcliffe Efficiency, Root Mean Square Error, Percent Bias
Performance Ratings for Evaluation Metrics for a daily and weekly time step |  |  |  | 
Performance Rating | R2 | NSE | RSR | PBIAS
Very Good | 0.65<R2≤1.00 | 0.65<𝑁𝑆𝐸≤1.00 | 0.00<𝑅𝑆𝑅≤0.60 | 𝑃𝐵𝐼𝐴𝑆< ±15
Good | 0.55<𝑅2≤0.65 | 0.55<𝑁𝑆𝐸≤0.65 | 0.60<𝑅𝑆𝑅≤0.70 | ±15≤𝑃𝐵𝐼𝐴𝑆<±20
Satisfactory | 0.40<𝑅2≤0.55 | 0.40<𝑁𝑆𝐸≤0.55 | 0.70<𝑅𝑆𝑅≤0.80 | ±20≤𝑃𝐵𝐼𝐴𝑆<±30
Unsatisfactory | 𝑅2≤0.40 | 𝑁𝑆𝐸≤0.40 | 𝑅𝑆𝑅>0.80 | 𝑃𝐵𝐼𝐴𝑆≥±30
Performance Ratings for Evaluation Metrics for a monthly time step |  |  |  | 
Performance Rating | R2 | NSE | RSR | PBIAS
Very Good | 0.75<𝑅2≤1.00 | 0.75<𝑁𝑆𝐸≤1.00 | 0.00<𝑅𝑆𝑅≤0.50 | 𝑃𝐵𝐼𝐴𝑆< ±10
Good | 0.65<𝑅2≤0.75 | 0.65<𝑁𝑆𝐸≤0.75 | 0.50<𝑅𝑆𝑅≤0.60 | ±10≤𝑃𝐵𝐼𝐴𝑆<±15
Satisfactory | 0.50<𝑅2≤0.65 | 0.50<𝑁𝑆𝐸≤0.65 | 0.60<𝑅𝑆𝑅≤0.70 | ±15≤𝑃𝐵𝐼𝐴𝑆<±25
Unsatisfactory | 𝑅2≤0.50 | 𝑁𝑆𝐸≤0.50 | 𝑅𝑆𝑅>0.70 | 𝑃𝐵𝐼𝐴𝑆≥±25
Source: Moriasi et al (2007) |  |  |  | 
Notes: Statistics used for model evaluation:
  Coefficient of Determination (R2)
  Nash-Sutcliffe Efficiency (NSE)
  Root Mean Square Error (RSR)
  Percent Bias (PBIAS)
Instead of simply using the “eyeball test” to visually look at whether or not model results match observed data, it is helpful to set quantitative goodness-of-fit goals using statistics such as R2, Nash-Sutcliffe & more.
Shown here is a handy table by Moriasi that proposes a range of statistical values that quantitatively categorize how well the calibration mirrors the observed event.
For example, to be satisfactory, the Nash-Sutcliffe efficiency for models with a daily or weekly timestep should be greater than 0.40 and if it’s above 0.65 it is considered a Very Good fit.

## Slide 29
Right-Click!
Calibration Goals
Notes: Thankfully, if you have observed flow data linked to a junction in HMS, the program will compute several goodness-of-fit statistics for you!
These statistics can be found in the junction’s Summary Table by right-clicking on the junction, selecting “View Results” and then “Summary Table.”

## Slide 30
Performance Ratings for Evaluation Metrics for a daily and weekly time step |  |  |  | 
Performance Rating | R2 | NSE | RSR | PBIAS
Very Good | 0.65<R2≤1.00 | 0.65<𝑁𝑆𝐸≤1.00 | 0.00<𝑅𝑆𝑅≤0.60 | 𝑃𝐵𝐼𝐴𝑆< ±15
Good | 0.55<𝑅2≤0.65 | 0.55<𝑁𝑆𝐸≤0.65 | 0.60<𝑅𝑆𝑅≤0.70 | ±15≤𝑃𝐵𝐼𝐴𝑆<±20
Satisfactory | 0.40<𝑅2≤0.55 | 0.40<𝑁𝑆𝐸≤0.55 | 0.70<𝑅𝑆𝑅≤0.80 | ±20≤𝑃𝐵𝐼𝐴𝑆<±30
Unsatisfactory | 𝑅2≤0.40 | 𝑁𝑆𝐸≤0.40 | 𝑅𝑆𝑅>0.80 | 𝑃𝐵𝐼𝐴𝑆≥±30
Source: Moriasi et al (2007) |  |  |  | 
Calibration Goals
Notes: For example, this location has a Nash-Sutcliffe efficiency of 0.888 which falls into the Very Good category—so this would be considered quantitatively well-fit to the observed data.

## Slide 31
  Timing
    Ex: +/- 12 hours of Observed Peak
Calibration Goals
Notes: Beyond simple statistics, it’s also very useful to set calibration goals for other event components based on the objectives and needs of your project.
For example, in some of our forecasting HMS models, we’ve set an initial goal of calibrating the timing of events to within 12 hours of the observed peak.
Again, timing goals may vary significantly based on what the objectives of your project are.
HMS makes it very easy to compare the modeled and observed peak timing by displaying both timestamps within the Summary table window as shown here.

## Slide 32
  Volume
    Ex: +/- 10% of Observed Event Volume
Calibration Goals
Notes: Volume is another key component that you should consider setting calibration goals for---particularly if you’ll be using the HMS model for forecasting models or reservoir studies, the event volume is a critical component you’ll want to capture as closely as possible.
For some of my forecasting models, we set an initial goal of capturing total event volume within 10% of the observed event volume.
Again, HMS makes it very easy to obtain the modeled and observed volumes for the event from directly within the Summary Table.

## Slide 33
  Peak Magnitude
    Ex: +/- 10% of Observed Peak
Calibration Goals
Notes: Event Magnitude is another component you may consider setting calibration goals for—often peak magnitude corresponds to peak stage and inundation levels, so depending on the scope of your study, the magnitude goal may vary.
In the past, for forecasting models, we’ve set an initial calibration goal of coming within 10% of the observed peak magnitudes.
Again, looking at the Summary table again here, HMS makes it easy to do a quick peak magnitude comparison between modeled results and observed values if you have the gage data linked to the junction.

## Slide 34: Takeaways
Setting Initial Model Parameters
  “Best Guess” Starting Values
  Parameters Will Evolve Throughout Calibration
Setting Calibration Goals
  Quantifying Fit (vs. “Eyeball Test”)
  Goals Depend on Scope of Project
Notes: Let’s wrap up with the key takeaways from this lecture—
When setting initial parameters, it’s important to remember that these as simply your “best guess” numbers—the parameters will evolve further as you calibrate and hone in on the processes within your watershed.
When setting calibration goals—it’s helpful to set quantifiable goodness-of-fit goals vs. relying on the “eyeball test.” We provided some examples of goals, but the goals you set definitely depend on the scope and objectives of each unique project.

## Slide 35: Calibration Metrics

## Slide 36: Setting Computation Points
Why?
Where?
How?
Notes: Setting Computation Points within HMS—
Why might this be helpful to you?
Where should they be set?
How to set them…

## Slide 37
Setting Computation Points
Why Set Computation Points?
  Creates Element “Groups”
    Includes Subbasins between Computation Points
    Easy Parameter Table Filtering
  Enables “Compute to Point”
Notes: How are computation points helpful to an HMS modeler? Computation points create element “groups” that include all subbasins & elements between computation points. The first handy computation point feature is that it enables fast & easy parameter table filtering—For example, heading to Paremeters > Loss > Deficit & Constant….

## Slide 38
Setting Computation Points
Why Set Computation Points?
  Creates Element “Groups”
    Includes Subbasins between Computation Points
    Easy Parameter Table Filtering
  Enables “Compute to Point”
Notes: …brings up the Deficit & Constant parameter table—filtering by Computation Point and selecting the point of interest shows just those subbasins within that computation point group. This is helpful for viewing & comparing nearby parameter values—and can even be useful for calibration which we’ll touch on a bit later.

## Slide 39
Setting Computation Points
Why Set Computation Points?
  Creates Element “Groups”
    Includes Subbasins between Computation Points
    Easy Parameter Table Filtering
  Enables “Compute to Point”
    Only Re-Computes Elements Upstream of Computation Point (vs. Entire Model)
    Time Saver!
Right-Click!
Notes: Another useful feature of computation points is the ability to “Compute to Point.” By right-clicking on a computation point and “Computing to Point,” HMS will only recompute the elements upstream of that computation point (instead of re-computing the entire model) which can save a lot of time during calibration—particularly if you’re working in a large watershed!

## Slide 40
Setting Computation Points
Where to Set Computation Points?
  Junctions
    Gages
    Key Locations
! Gage Location !
Notes: Where should computation points be set? They can be set at any junction, however, Gage Locations are a great place to use computation points since you’ll be adjusting and re-running the model frequently during calibration at these locations. Setting computation points are other key locations such as tributary junctions or areas where watershed features change rapidly may also be useful.

## Slide 41
Setting Computation Points
How to Set Computation Points?
Right-Click!
Notes: How do you set a computation point? It’s as simple as right-clicking on the intended junction element and “Selecting Computation Point!”

## Slide 42
Setting Computation Points
How to Set Computation Points?
  Junction Icon Turns Red Once CP Set
Notes: Once the computation point has been set, the junction icon will have a red background.

## Slide 43: Summary Tables & Metrics
Where?
What?
How?
Notes: Let’s talk about the Summary Tables & Metrics available within HMS—
Where are they located?
What useful information does it have?
How can I use the information?

## Slide 44
Right-Click!.
Summary Tables & Metrics
Where to Access Summary Tables?
  Right-Click Junction Elements
Notes: Where are the HMS summary tables located? Summary tables can be found at every junction element within HMS by right-clicking on the junction element > View Results > Summary Table

## Slide 45
Summary Tables & Metrics
What’s in the Summary Tables?
Simulation
Info
Notes: What’s included in the summary tables?
Every summary table provides information about the simulation you’re running such as start/end date, which models the simulation is using…

## Slide 46
Summary Tables & Metrics
What’s in the Summary Tables?
Computed Results
Observed Data
Volume
Unit
Selection
Notes: Summary tables always summarize the computed timing and magnitude of the peak discharge as well overall modeled event volume—which can be displayed in inches or acre-feet (English Units, Metric is also available).
Another great summary table feature is if you have observed flow data linked to the junction, HMS will also summarize the same metrics from the observed data and…

## Slide 47
Summary Tables & Metrics
What’s in the Summary Tables?
Computed Results
Observed Data
Calibration Metrics
Notes: …it will also compute several goodness-of-fit statistics for you!

## Slide 48
Summary Tables & Metrics
How Can I Use Them?
  Reference Goodness-of-Fit Statistics
  Compare Observed vs. Modeled:
    Timing
    Volume
    Magnitude
Performance Ratings for Evaluation Metrics for a daily and weekly time step |  |  |  | 
Performance Rating | R2 | NSE | RSR | PBIAS
Very Good | 0.65<R2≤1.00 | 0.65<𝑁𝑆𝐸≤1.00 | 0.00<𝑅𝑆𝑅≤0.60 | 𝑃𝐵𝐼𝐴𝑆< ±15
Good | 0.55<𝑅2≤0.65 | 0.55<𝑁𝑆𝐸≤0.65 | 0.60<𝑅𝑆𝑅≤0.70 | ±15≤𝑃𝐵𝐼𝐴𝑆<±20
Satisfactory | 0.40<𝑅2≤0.55 | 0.40<𝑁𝑆𝐸≤0.55 | 0.70<𝑅𝑆𝑅≤0.80 | ±20≤𝑃𝐵𝐼𝐴𝑆<±30
Unsatisfactory | 𝑅2≤0.40 | 𝑁𝑆𝐸≤0.40 | 𝑅𝑆𝑅>0.80 | 𝑃𝐵𝐼𝐴𝑆≥±30
Source: Moriasi et al (2007) |  |  |  | 
Notes: How can you use the summary table information?
Summary statistics provide a quantitative assessment of how well the model matches the observed data. The suggested performance metrics table by Moriasi shown here can be referenced--for example, this location has a Nash-Sutcliffe value of 0.888 which falls into the Very Good category—so this would be considered quantitatively well-fit to the observed data and HMS computed the metrics for us!

## Slide 49
Summary Tables & Metrics
How Can I Use Them?
  Reference Goodness-of-Fit Statistics
  Compare Observed vs. Modeled:
    Timing
    Volume
    Magnitude
Computed Results
Observed Data
Notes: Summary tables are also very useful for comparing other modeled vs. observed event characteristics—such as timing, volume and magnitude. This is useful when setting and tracking calibration goals which we’ll talk more about in the calibration strategies discussion.

## Slide 50
Zonal Calibration
Sliders
Group Tables
Notes: Let’s touch on Zonal Calibration—I’ll mention two ways to calibrate HMS parameters by zone, including using the HMS Slider Bars feature as well as by groups within the Parameter Tables…

## Slide 51
Zonal Calibration
Sliders
  Right-Click CP > Calibration Aids
Notes: One great approach to Zonal Calibration is using the Slider Bar Calibration option. Elements, parameters and ranges must first be set up to enable slider bar use. To access the slider bar feature, right click on a Computation Point junction and select “Calibration Aids.”

## Slide 52
Zonal Calibration
Sliders
  User-Set Parameters, Ranges, Plots
Notes: The slider bar Calibration Editor dialog box will open. The sliders should be set up to reflect the calibrated range of each parameter with the option to include custom plots to track calibration progress.

## Slide 53
Zonal Calibration
Sliders
  Auto-Recompute by Sliding
Notes: Selecting “Compute with each slider change” will re-compute the model and update the associated plots each time the slider is adjusted. The re-computation is typically fairly quick for a nearly real-time cause/effect update as parameters are adjusted…

## Slide 54
Zonal Calibration
Sliders
  User-Set Parameters, Ranges, Plots
  Auto-Recompute by Sliding
Pros
  Rapid Response to Adjustment
  Pre-Defined Parameter Ranges
Notes: The prep work to set up the ranges for slider bar parameters can be time-consuming, but using them in real-time is efficient with rapid re-computation as parameters are adjusted. Having the pre-defined ranges is also useful for ensuring adjustments stay within reasonable ranges for each parameter.

## Slide 55
Zonal Calibration
Parameter Tables
Notes: Another approach to Zonal Calibration is adjusting multiple elements at once by viewing the parameters by Group in the parameter summary tables. For example, here we’re viewing the Loss parameters for the “Martin” computation point in this basin…

## Slide 56
Zonal Calibration
Group Tables
  Scale/Factor Parameters by Computation Point or Zone
    Highlight & Right-Click > Fill
Notes: Multiple subbasin parameters can be set or scaled at once by highlighting the parameter > Right-Clicking > Selecting Fill…

## Slide 57
Zonal Calibration
Group Tables
  Scale/Factor Parameters by Computation Point or Zone
    Highlight & Right-Click > Fill
    Select Operation > OK
Pros
  View & Adjust Multiple Subbasins at Once
  Especially useful for large watersheds
Notes: …which pops up the Table Fill Options dialog…from here, the initial parameters can be adjusted all at once.
Adjusting parameters within the parameter tables by group is particularly useful when working in a large watershed. The slider bar dialog for 10+ (or even 100+) subbasins can get a little overwhelming. Focusing on one Computation Point Groups at a time within the parameter tables and being able to scale/adjust multiple parameters all at once can be efficient when tackling larger watersheds.

## Slide 58: Takeaways
Computation Points Enable:
  Element Grouping
  Compute-to-Point
  Slider Bar & Group Calibration
Summary Tables Provide:
  Model Results Overview
  Valuable Calibration Metrics
Zonal Calibration
  Slider Bars or by Table
  Efficient Calibration Tools
Notes: Key takeaways from this Calibration Metrics & Tools lecture are:
Setting Computation Points enables:
  Element grouping
  Compute to Point feature
  Slider Bar & Calibration by Group within Tables
The HMS Summary Tables Provide:
  An overview of model results and observed data
  Valuable calibration metrics
Zonal Calibration options include:
  Slider bars or Scaling by Groups within the Parameter Tables
  Both are efficient calibration tools

## Slide 59: Model Calibration
Hydrologic Modeling with HEC-HMS

## Slide 60
References
Moriasi, D. N., J.G. Arnold, M.W. Van Liew, R.L. Bingner, R.D. Harmel, and T.L. Veith, Model evaluation guidelines for systematic quantification of accuracy in watershed simulations, Transactions of the ASABE 50 (3), 885-900, 2007