## Slide 1: Meteorologic Models
Hydrologic Modeling with HEC-HMS
February 2025
David Ho, P.H.
US Army Corps of Engineers
Hydrologic Engineering Center
Slides by:
Greg Karlovits (HEC), Emily Moe (MVP)

## Slide 2: Objectives
Review the Meteorologic Model and its components
Discuss methods for precipitation, evapotranspiration, and other meteorologic processes
Gain an understanding of when to apply each method and what data is needed

## Slide 3
Precipitation Model
Combined Losses
Excess Precip Transform
Total Runoff
Channel Routing
Watershed Outlet
Baseflow

## Slide 4: Meteorologic Model Overview
Overview
Historic Precipitation
Hypothetical Storm
Evapotranspiration
Precipitation Methods

## Slide 5: Simulation Run
Basin Model
Meteorologic Model
Control Specification
Notes: The simulation run is one type of simulation available in HEC-HMS and is the most used one. All simulation types require a basin model and a meteorologic model (the control specification is unique to the simulation run).

## Slide 6: Meteorologic Model
Basin Model
Meteorology Model
Atmospheric boundary conditions
Notes: Water can only enter the system in two ways in HMS: through a hydrologic element that produces discharge (e.g. source elements) or through the atmosphere.
A meteorologic model can be used with any number of basin models, as long as they are set up to do so.
The name is deliberate. The met model is more than just a set of data. It contains several models for representing atmospheric processes. However, it is not an atmospheric model in the vein of a weather forecast model or GCM.
For example, there are precipitation methods that take precipitation gages as inputs and compute area averages from them in a couple of different ways. There are methods for computing potential evapotranspiration from atmospheric data. And so on.

## Slide 7: Meteorologic Model
Basin Model
Meteorology Model
Atmospheric boundary conditions
Notes: Here are all the meteorologic processes that can be simulated using the HMS Meteorologic Model.

## Slide 8: Creating a Meteorologic Model
Notes: Met models can be created through the Components menu. All simulation types require a basin model and a meteorologic model. Precipitation is one of the modeling methods inside of a meteorologic model. The meteorologic model is meant to manage all the atmospheric boundary conditions necessary for hydrologic modeling.

## Slide 9: Meteorologic Model
User chooses methods for modeling each process
Notes: To access the component editor for the met model, click on the met model in the watershed explorer.
For each of the boundary conditions, there is a collection of methods for modeling it. Not all processes are necessary for all models, and the simplest models may only use precipitation. As methods are added, generally the data requirements increase. Some methods are more complex than others and require more types of data.
Each of these process are more than just data – they are models for representing states of the atmosphere and require data as an input. For example, note that there is no “temperature” process in the met model. However, temperature is a data input for snowmelt, evapotranspiration, etc.
You may notice there is no snowmelt option in the met model. As of HMS version 4.10, snowmelt has been migrated to the basin model since it is a land surface process.

## Slide 10: Include Subbasins
Notes: Met models are independent of basin models – since they are general representations of atmospheric boundary conditions and can be set up to work with any basin model, they don’t know anything about a basin model unless you tell them.
In the component editor for the met model, there is a “Basins” tab. Here you will see all the basin models in your project. If you want a basin model to be usable with this met model, you must select “include subbasins – yes” in this menu. Otherwise two things will happen. 1) you will not be able to set any subbasin-level settings or parameters if your methods have them and 2) the simulation run will fail and inform you that the met model is not set up to work with the basin model.
This is a common pitfall – it is easy to forget to set your met model and basin model to work together.

## Slide 11: Watershed Explorer
Settings for entire Met Model
Met Model settings for subbasins
Notes: You can specify whichever methods are appropriate for your modeling goals. Typically, at minimum a precipitation method will be specified.
In the Watershed Explorer, the selected methods will appear beneath the met model. Clicking on any of those will open the component editor below.
The topmost set of icons are for the processes that have been selected in the met model component editor. Clicking on any of these will let you edit settings for that method. The settings at this level are used across all hydrologic elements. However, some processes are controlled in a much more granular way, such as Gage Weights. Gridded methods will eliminate a lot of granularity because they already explicitly handle the atmospheric process in space.

## Slide 12: Global Editors
Hamon (Met Model)
Notes: Here is an example of a global editor for the temperature index snowmelt method. Because the TI method has parameters that are controllable at the subbasin level, it can be cumbersome to click through each node of the watershed explorer tree to set them. The global editor is a faster way to enter these parameters. You can open the global editor for snowmelt by selecting the met model in the watershed explorer, then choosing the Parameters menu, and selecting Snowmelt then temperature index (or gridded temperature index.)

## Slide 13: Data Requirements
Non-gridded
  At the Met Model or Subbasin level
Gridded
  At the Met Model level
  Should cover entire modeling domain
Notes: For non-gridded methods each met variable has a few methods for specifying information. For example here in temperature, the “Specified Thermograph” method lets you link a temperature gage directly to a subbasin. For precipitation there’s “Gage Weights” that lets you combine up multiple gages for a subbasin. There are also interpolated methods for many met variables that allow you to specify how to interpolate several gages to a subbasin.
For gridded methods, grids of meteorologic data should cover the entire modeling domain. These models are explicitly georeferenced, meaning the location of all the hydrologic elements and the meteorologic data are known, and referenced to a common datum. Gridded precipitation and temperature (and other gridded met variables) link directly to a gridset.
Processes like ET or snow look to the met model for the variables they need in order to compute – for example gridded Hamon and gridded TI require temperature data. In this met model they would look to the temperature gridset specified in the Gridded Temperature method.
Creating the required data, and details on the meteorological methods are covered in other tutorials.

## Slide 14: Precipitation Methods
Overview
Historic Precipitation
Hypothetical Storm
Evapotranspiration
Precipitation Methods

## Slide 15: Setting a Precipitation Method
Set the method in your Meteorologic Model
Notes: If there are subbasin elements in your basin model, you will be required to choose a precipitation method in order to run the model. It can be selected in the meteorologic model component editor.
Let’s take a look at the most important precipitation methods in HEC-HMS.

## Slide 16: What is my modeling goal?
I am trying to reproduce a precipitation event that occurred in the past.
   Historical storm methods
I am trying to design something, perform a risk analysis, or otherwise model an idealized event.
   Hypothetical storm methods
Notes: There are two categories of precipitation methods in the HEC-HMS meteorologic model. HMS doesn’t label the methods with these categories, but it’s valuable to know which methods are related and what they are intended for.
Historical storm methods help you create precipitation boundary conditions for a storm or a period of time that has already occurred, so that you can simulate the hydrology for some time in the past. They may also be used creatively to model future forecasted conditions or other hypotheticals, but their primary purpose is representing past precipitation.
When you are designing something, performing a risk analysis, or doing any other kind of hydrologic analysis that makes many simplifying assumptions about the behavior of precipitation in space or time, hypothetical storm methods are the precipitation methods to use. These are also sometimes called design storms, or synthetic storms, but the idea is that they do not represent a specific storm event that has occurred. Instead, it is a generalization of storm behavior that allows the user to specify something interesting for design or analysis purposes.

## Slide 17: Historical Storm Methods
Gridded precipitation
Gage weights
Interpolated precipitation
Inverse distance
Specified hyetograph
→ Key: driven by observed precipitation data
Notes: Historical storm methods are means for providing precipitation boundary conditions to a basin model in a way that it reasonably represents an event that occurred in the past. Historical events are unique like fingerprints or snowflakes, varying in precipitation depth, temporal and spatial pattern, and so on. These methods intend to capture the things that make an event unique.
When you are calibrating a hydrologic model so that it represents a real watershed, use of a historical storm method is necessary. You need to represent the input precipitation as well as you can in order to isolate the uncertainty in the model to just the hydrologic parameters.
These are listed in the order HMS shows them. The first two we will cover in more detail later in the presentation.
Gage weights is a method for combining information from multiple precipitation gages and can vary the combination of gages for each subbasin in the model.
The controls for the gage weights method are at the subbasin level, since each subbasin has its own combination of gages that you can set. The selections tab lets you choose which of the precipitation gages to use for the selected subbasin. The weights tab lets you set the depth weight and time weight for each gage.
You would use this method when you have gage data scattered across your watershed, and you want control over how each one is used to estimate the volume and timing of precipitation for each subbasin.
The controls for gridded precipitation are very simple – choose a precipitation gridset. If there are time zone issues (for example your observed flow data and precipitation data are in different time zones) you can shift the precipitation grid times by whole hours.
The gridded precipitation method is very simple to set up, because most of the hard work is handled by the data itself. These grids are at a regular time interval, so that controls any temporal patterning. The grids themselves contain spatial patterns. The data are spatially-referenced, and the sub-basins know their locations if the model is georeferenced. This means that setting up the model is very simple.
If you have gridded precipitation data, you should use it. This is the method we recommend today.
Gridded precipitation is just what the name says: a way to use gridded precipitation products as a boundary condition.

## Slide 18: Historical Storm Methods
Gridded precipitation
Gage weights
Interpolated precipitation
Inverse distance
Specified hyetograph
Notes: Interpolated precipitation is a generalized framework for interpolating precipitation gages to a grid

## Slide 19: Creating Precipitation Gridsets from Point Data
Interpolated Meteorology method
  Converts observation points to grids
  Available for all Meteorologic Model processes
Notes: When creating precipitation grids from observed gage data, the gageInterp program is useful.
gageInterp takes point values, like those from precipitation gages, and creates grids by interpolation. GageInterp estimates the value at each grid cell by calculating a weighted average of all gages located within a certain distance. The weights are computed by taking a simple average or using distance to gages. The figures on this slide show two examples of distance being used to compute a weight. The figure on the left was computed by giving more weight to the closest gage. Grid cell values become similar to gage values the closer they are to the gage (bulls-eye). The figure on the right was computed by assigning grid cell values using only the closest gage--using the Thiessen Polygon method (any point, or grid cell in this case, within a polygon is closer to that gage than any other).

## Slide 20: Historical Storm Methods
Gridded precipitation
Gage weights
Interpolated precipitation
Inverse distance
Specified hyetograph
Notes: Finally, the specified hyetograph method is a simple way to represent precipitation for each subbasin in the model. Each subbasin gets its own precipitation gage. This can be a “real” gage, i.e. a weather station, or you can externally compute the subbasin-averaged precipitation using another method, and feed it in this way.
The specified hyetograph method is very straightforward – for each subbasin, choose a precipitation gage.
This method is very flexible and you might use it for a number of reasons. The most common usage today is when precipitation timeseries for each subbasin are computed externally to HEC-HMS, and you want HMS to apply exactly that precipitation data. The biggest advantage is that this method is the most performant method in HMS, requiring no additional computation steps to apply precipitation to a subbasin.
One other application that isn’t strictly a “historic” event would be using HMS for forecasting – however, the input data is probably from a model that reasonably represents the coming precipitation, and a good model will be close to the precipitation that actually occurs.

## Slide 21: Hypothetical Storm Methods
Frequency Storm
HMR52 Storm
Standard Project Storm
Hypothetical Storm
→ Key: intended to model highly idealized storms, usually for design
Notes: Hypothetical storms are also called design storms, or synthetic storms. They control for a small number of design criteria, and then make a large number of simplifying assumptions about the remainder of a storm’s properties. These methods will not be covered in detail during this course, but more information can be found in the HMS user’s manual, and with the HMS tutorials and guides online.
Frequency storm is a very specific method for defining a storm pattern using precipitation-frequency information. It was designed to work with older precipitation-frequency information, such as HYDRO35, TP40, or TP49. Today, the recommendation is to use the hypothetical storm method instead.
The HMR52 storm is meant to perform probable maximum flood analyses for the central and eastern United States. It has a very specific application and is not intended for general use.
The standard project storm is no longer used in practice; however, HEC-HMS maintains this capability in order to support older projects where it may still be necessary. This storm has an extremely specific application and should not be used for general modeling.

## Slide 22: Hypothetical Storm Methods
Frequency storm
HMR52 storm
Standard project storm
Hypothetical storm
Notes: The hypothetical storm method is a flexible and generalized modeling method that subsumed the old SCS storm methods of HMS 4.2.1 and prior. It allows a user full control over the storm temporal pattern, point-to-area conversion, and can be used directly with precipitation-frequency grids from NOAA Atlas 14. I highly recommend this method for all idealized storm modeling needs. Tutorials on this method are available online with the HMS tutorials and guides.
The hypothetical storm method offers the user a lot of control, so there are many settings to be specified for it to run. This instance of the hypothetical storm requires the user to specify a dimensionless storm temporal pattern, a storm duration, a precipitation-frequency grid to pull depth information from, an area reduction method, an area reduction function, and a computation point to compute the storm area for.
Of the hypothetical or synthetic storm methods, this is the most flexible and applicable one. Unless you have specific project needs that require one of the other methods, it is recommended to use this method.

## Slide 23: Gridded Precipitation
Overview
Historic Precipitation
Hypothetical Storm
Evapotranspiration
Precipitation Methods

## Slide 24: Gridded Precipitation
Pros
  Spatially distributes precipitation
    Ex: RADAR vs. precip gage
  Increasing number of sources available
    National & Local Availability
0
50
Precip Depth (in)
Notes: The primary benefit of applying gridded precipitation to an HMS model is that the precipitation is then spatially distributed across the watershed as it’s been observed by RADAR or other products (versus a lump measurement being applied homogenously across the entire basin). Another positive note is that an increasing number of gridded precipitation sources are becoming available.

## Slide 25: Gridded Precipitation
Cons
  May require file format conversion
  Quality of data varies
    Quality control recommended
      Gage comparison
      RADAR coverage
Notes: One slight drawback is that available gridded datasets may require conversion from their native format to an HEC-DSS record to be usable within HMS. However, conversion tools are available to make most conversions quick & easy!
It’s also important to note that the quality of the various available gridded datasets will vary. When selecting a gridded precipitation source, it’s recommended to perform spot-checks against established precipitation gage sites to determine how accurate that particular source is within your watershed. If applying RADAR data, a visual of RADAR coverage throughout the watershed may help with product quality control as well.

## Slide 26: Gridded Precipitation Sources
National Products
  National Digital Guidance Database (NDGD)
Regional Products
  NWS River Forecast Centers NEXRAD
CWMS
  USACE Water Management data
Additional Products
  Gridded Data Sources Tutorial & Guide
Notes: There are an increasing number of gridded precipitation products available. This includes both nationwide products as well as more locally developed sources such as from your local National Weather Service River Forecast Centers. Some of the most popular products include:
The National Digital Guidance Database (NDGD) has Real-Time Mesoscale Analysis (RTMA) hourly precipitation available for CONUS for download from 2007 to present.
NEXRAD RADAR data is a NWS product available regionally. There are currently 160 operational NEXRAD radar systems deployed throughout the United States and at selected overseas locations. Stage III and Multisensor Precipitation Estimator (MPE) products are hourly precipitation estimates that are computed by taking raw radar measurements and applying corrective algorithms. Rain gage data and satellite images are used to “correct” the raw data. Estimates from multiple radars are mosaicked together to create a precipitation grid (HRAP) for the entire river forecast center region. The period of record for NEXRAD data varies regionally.
There are several more gridded precipitation products available than those listed here and the quality of each product can greatly vary by region. As part of the USACE Corps Water Modeling System (CWMS) efforts, most USACE districts currently have real-time gridded precipitation products included within their Water Management server databases. It’s highly recommended to discuss the data available through CWMS with your local water management staff when searching for gridded precipitation products as there has likely already been some searching and testing of the available precipitation products within your region completed.
Also, as part of the USACE CWMS model development, many districts have gridded precipitation data available for their region on their water management servers.
Dipper.nws.noaa.gov/hdsb/data/nexrad/nexrad.html

## Slide 27: Converting & Creating Precipitation Gridsets
Utilities available:
  HMS – certain file types can be imported directly within HMS
    Generalized Data Reader coming soon!
  Vortex Utilities – converts several formats to HEC-DSS records
    NetCDF, Grib, HDF, ASC & more
    Also allows for clipping, re-projecting, resampling, etc.
  Interpolated Meteorology methods
Notes: Once you’ve decided to apply gridded precipitation to your model, how do you convert the raw precipitation data to an HEC-DSS file for use in HMS?
There are a few options available for converting formats or creating grids—
HMS can actually import select gridded file formats directly into HMS—(File > Import > Import Gridded Data…for more information, please see the Shared Data Components: Grid Data lecture).
VORTEX tool which can convert several native data formats to HEC-DSS, allows for additional spatial manipulation during the processing and is also user-friendly. More information on the VORTEX tool is included in a later lecture.
Interpolated Precipitation Methods takes point precipitation data (such as rain gage data) and creates a grid where the value for each cell is computed by weighting values from all gages within a specified distance (radius of influence). Multiple interpolation methods are available.

## Slide 28: Gridded Precipitation
DSS Pathnames for Grids in HEC-HMS
/A-part/B-part/C-part/D-part/E-part/F-part/
A – grid system (SHG, HRAP)
B – region or watershed name
C – the data variable (precip, temp, …)
D – starting time for grid (ex: 04JAN2021:1500)
E – ending time for grid (ex: 04JAN2021:1600)
F – additional identification (e.g. obs, radar, NWS, …)
Notes: When converting or creating gridded datasets, it’s important to clearly name the resulting DSS-file pathnames so that it is clear where the data came from, the extent of the data and—most importantly—the data type and time.
The recommended naming convention for gridsets and parameter grids are shown on this slide. HEC-HMS requires specific C-part names. The program will not use the grid unless the C-part name is correct (the next slide shows correct C-part names for each grid type).
Gridsets, precipitation, temperature, solar radiation and crop coefficient will have both D and E-part pathnames. The parameter grids do not need E-part pathnames and only the parameter grids used by snowmelt require D-parts.

## Slide 29: Gridded Precipitation
Grids must have:
  Correct C-part pathname
  Correct units
  Valid Data type
  Values for each grid cell
Grid Type | C-Part | Units | Data Type
Precipitation | PRECIPITATION | MM, IN | PER-CUM
Temperature | TEMPERATURE | DEG C DEG F | PER-AVER INST-VAL
Solar Radiation | SOLAR RADIATION | WATT/M2 LANGLEY/M IN | PER-AVER INST-VAL
Crop Coefficient | CROP COEFFICIENT | UNSPECIF | PER-AVER INST-VAL
Storage Capacity | STORAGE CAPACITY | MM, IN | INST-VAL
Percolation Rate | PERCOLATION | MM/HR IN/HR | INST-VAL
Storage Coefficient | STORAGE COEFFICIENT | HR | INST-VAL
Moisture Deficit | MOISTURE DEFICIT | MM, IN | INST-VAL
Impervious Area | IMPERVIOUS AREA | % | INST-VAL
SCS Curve Number | CURVE NUMBER | UNSPECIF | INST-VAL
Elevation | ELEVATION | M, FT | INST-VAL
Cold Content | COLD CONTENT | MM, IN | INST-VAL
Cold Content ATI | COLD CONTENT ATI | DEG C DEG F | INST-VAL
Meltrate ATI | MELTRATE ATI | DEGC-DAY DEGF-DAY | INST-VAL
Liquid Water | LIQUID WATER | MM, IN | INST-VAL
Snow Water Equivalent | SWE | MM, IN | INST-VAL
Notes: HEC-HMS will not load a grid if the C-part pathname, Units or Data Type is incorrect. The table on this slide contains the correct C-part pathnames, Units and Data Type for each grid type in HEC-HMS.

## Slide 30: Adding Gridded Precipitation to HMS
Notes: Once gridded precipitation has been converted to the HEC-DSS format and clearly labeled, it is ready to be added to the HMS model.
To create a precipitation gridset in HMS: Components > Create Component > Grid Data…
Within the Create a Parameter Grid Data dialog, ensure Precipitation Gridsets is selected as the Data Type and be sure to name and describe the precipitation data you are importing.
Select Create to add the grid to the Gridded Data Manager

## Slide 31: Gridded Data Manager
Notes: Once the precipitation gridset is created and named, it is added to the Gridded Data Manager within the watershed explorer dialog.
Now, the gridded DSS record must be linked to the precipitation gridset by navigating to the dss file and selecting the appropriate pathname.

## Slide 32: Linking Gridded Precipitation to Met Model
Notes: Next, the meteorologic model must be configured to use gridded precipitation by highlighting the Meteorologic Model name and selecting Gridded Precipitation
The gridded precipitation data must then be linked to that Meteorologic Model by highlighting Gridded Precipitation and selecting the name of the precipitation grid in the dialog box below.

## Slide 33: Defining Discretization
Required to run HMS with gridded components
Spatially relates gridded datasets to subbasins
Specified by subbasin
Four Discretization Methods:
  Structured
  Unstructured
  File-Specified
  None
Notes: Defining a discretization method is required to run HMS with spatially-discrete components such as precipitation gridsets. Defining the discretization allows the HMS model to spatially relate gridded components (precip, storage, etc.) to subbasin elements, enabling spatial variability within each subbasin vs. applying a singular value throughout the entire subbasin (ie, lumped-parameter).
Discretization is defined by subbasin and has four methods to choose from.

## Slide 34: Defining Discretization
Four Discretization Methods:
  Structured*
    “Automatic” Method
    Defaults to standard SHG grid & 2-km cell size
  Unstructured
    Any coordinate system
    Allows unstructured grid such as RAS plan files (ex: *.p##.hdf)
  File-Specified
    Points to HEC-HMS “Grid Cell Files” (*.mod)
  None
    “Lumped-Parameter”
    No variation within subbasin
Notes: The “Structured” discretization method is a quick & easy approach to discretizing the model as it applies the Standard Hydrologic Grid (SHG) at a resolution. The structured method can also be used to apply a Universe Transverse Mercator (UTM) projection and various grid cell sizes ranging from 50 to 10,000 meters.
The Unstructured Method allows the application of any coordinate system (not just SHG or UTM) and can be easily defined with HEC-RAS plan files.
File-Specified allows the user to point directly to the HEC-HMS grid cell file (that was required in HMS version 4.2 & older).
Defining a “None” discretization assumes no variation of variables within the subbasin, resulting in a “lumped-parameter,” non-gridded approach.
Once the Discretization has been defined, the gridded precipitation can be added to a Simulation and the HMS model can be run.

## Slide 35: Hypothetical Storm
Overview
Historic Precipitation
Hypothetical Storm
Evapotranspiration
Precipitation Methods

## Slide 36: Flow-Frequency Modeling
Key assumption:
  Probability of rainfall equals probability of flow
  “AEP neutral”
Model flow with a combination of met and basin model
Notes: The AEP neutral technique assumes you can calibrate the hydrologic model so that this is true.

## Slide 37: Hypothetical Storm Method
Precipitation method in the meteorologic model
3 sub-methods:
  Area-Dependent Pattern
  SCS Storm
  User-Specified Pattern
Creates a synthetic storm based on a single duration
Assumes you choose the right duration for AEP neutrality

## Slide 38: User-Specified Pattern
User-defined time pattern
Ability to read PF grids
Depth-Area Analysis magic
  Computes precipitation above each comp. pt.
  Gets drainage area
  Computes area reduction
Average = 7.50 in
Computation Point

## Slide 39: Data

## Slide 40: Frequency Storm Data

## Slide 41: Importing Data

## Slide 42: Temporal Patterns
Probabilistic analysis of time patterns of heavy rainfall
4 durations: 6-hour, 12-hour, 24-hour, 96-hour
Classified by “quartile” and “percentile”
Quartile = which quarter of storm has the most volume
Percentile = ranking of peakedness of storms in a quartile
Q1 Q2 Q3 Q4

## Slide 43: Temporal Patterns
Percentage curve paired data
Atlas 14 has data
Notes: I copy the right column from the A14 temporals CSV file and paste it into the table. Then I set the first to 0.000 and 100.0000 and use the interpolation function to fill in the left column.
Note that values can repeat in the right column – in older versions of HMS they had to be strictly increasing. Now they just have to be non-decreasing.

## Slide 44: Synthetic Hyetograph
Midwest Region 3
2nd Quartile, 50%
Volume matches area-reduced subbasin amount

## Slide 45: Area Reduction
10 mi2 maximum:
5 in
200 mi2 average:
4.2 in
10 mi2 maximum:
100%
200 mi2 average:
4.2/5 = 84%
Precipitation Depth (in)
Percent of Maximum
100 mi2
500 mi2
1,000 mi2

## Slide 46: Area Reduction
Usually assumed that storm area = watershed area
Conservative assumption
Assumes the worst rainfall perfectly coincides with watershed
Area (mi2)
Percent of Point (%)
24-hour
6-hour
3-hour
1-hour
30-min

## Slide 47: Evapotranspiration
Overview
Historic Precipitation
Hypothetical Storm
Evapotranspiration
Precipitation Methods

## Slide 48: Role of Evapotranspiration
ET comprises two processes:
  Transpiration from plants
  Evaporation from surfaces
Key component of continuous hydrologic models
  Significant moisture is lost to the atmosphere
  Deficits created through ET
Notes: A good continuous hydrologic model requires evapotranspiration modeling, especially for multi-year simulations. ET removes water from the soil and transmits it to the atmosphere, which can create a moisture deficit prior to flood events that reduces or eliminates direct runoff early during a precipitation event. HMS can simulate surface evaporation, plant canopy evaporation, and plant transpiration.

## Slide 49: Evapotranspiration Basics
Source: WMO FAO56
Notes: Evaporation and transpiration occur simultaneously. The figure on this slide shows the seasonal fluctuations of evaporation and transpiration. When plants are small in size or dormant, water is lost mainly due to evaporation. As they grow and become active, transpiration dominates.
Factors affecting evapotranspiration (ET) include weather, vegetation characteristics, and environmental factors.
The main weather characteristics affecting ET are radiation, temperature, humidity, and wind speed. Many equations for estimating ET use these parameters.
Vegetation characteristics affecting ET include vegetation type and stage of development.
Salinity, soil characteristics, the use of fertilizers, and disease are some of the many environmental factors affecting ET.
The Leaf Area Index (LAI), a dimensionless quantity, is the leaf area (upper side only) per unit area of soil below it.

## Slide 50: Evapotranspiration Basics
Credit: Figure drawn by Gigi Richard, adapted from Bates, R.L. &amp;amp; J.A.Jackson, Glossary of Geology, Second Edition, American Geology Institute, 1980
Notes: The amount of evapotranspiration depends on multiple factors:
Atmospheric conditions
  Temperature
  Solar radiation
  Windspeed
  Relative humidity
Plant species and density
Life stage of the plants
Available water

## Slide 51: ET Modeling Requirements
Meteorologic model method
  Computes potential/reference ET
Canopy method in basin model
  Computes actual ET
  Creates moisture deficit
Notes: In order to simulate the ET part of the water cycle in HMS, two components are needed.
The meteorologic model allows HMS to use atmospheric data to estimate the potential evapotranspiration. PET is dependent on the energy input and the ability to transport evaporated water vapor away from the surface, but is not limited by the supply of water.
Actual evapotranspiration is handled by the basin model. Within the subbasin component is the canopy method, which serves two purposes. The first is to model canopy interception. The second is to compute the actual amount of water that can be evaporated and transpired. The maximum amount is the potential evapotranspiration, but this amount is reduced depending on the type of vegetation (controlled by the crop coefficient) and is also reduced by the availability of water. At the maximum deficit, no more water can be transpired to the atmosphere.

## Slide 52: Simple Canopy Settings
Evapotranspiration timing
  Wet and dry periods
  Only dry periods
Uptake method
  Simple
  Tension reduction
    SMA only!
Notes: The simple canopy method is what you should use in the vast majority of cases. The storage terms control interception. The ET settings are below – you can choose your crop coefficient, during which periods actual ET is computed, and the uptake method. Unless you are using the SMA loss method, use the simple uptake method.

## Slide 53: ET Impact
Initial
Deficit
Max Deficit
Daily Actual ET
Notes: When performing continuous modeling using loss methods, for example deficit and constant or SMA, deficit increases when plant uptake draws water from soil storage. If no method for increasing deficit is specified, soil storage will fill up and infiltration will only occur at the specified constant rate.
Here is an example of the impact of modeling ET on the soil moisture deficit. The initial deficit is zero. No water is input to this system. The diurnal cycle of ET creates a stair-step shaped accumulation of deficit until the maximum deficit is reached. The steepness of the growth is controlled by atmospheric conditions and the crop coefficient. The initial and maximum deficit are controlled by the subbasin loss method.

## Slide 54: HMS – a spectrum of ET methods
Monthly Average
Hamon
Hargreaves
Priestly-Taylor
Penman-Monteith
Complex
Simple
Typical Methods
+ gridded options
Notes: HMS includes a range of evapotranspiration methods. The simplest is to choose the monthly average value, which for some regions may be published data. Data and modeling requirements go up as you move to the right. The Hamon method is a temperature-based PET method, which approximates the energy balance using temperature data. The other methods begin to require radiation, wind speed, and relative humidity data. In data limited environments, the first two methods are usually adequate. Consider the role of ET in your model – if you are most interested in large flood peaks, then spending a lot of time on additional details for ET may not make sense.
Most of these methods have gridded counterparts as well, where the input data is specified with grids instead of time series.

## Slide 55: Data Requirements
Method | Temperature | Wind speed | Humidity | Shortwave
Monthly Average | No | No | No | No
Hamon | Yes | No | No | No
Hargreaves | Yes | No | No | Yes
Penman-Monteith | Yes | Yes | Yes | Yes

## Slide 56: Hamon ET
ETo reference evapotranspiration
C Hamon evapotranspiration coefficient
D possible hours of daylight in units of 12 h
ρt saturated water vapor density at daily mean temperature
Notes: Reference Hamon 1960, 1961, 1963.

## Slide 57: Hamon ET

## Slide 58: Calibration Considerations
Changing ET parameters can change overall water volumes
Two primary changes:
  ET method coefficients
  Crop coefficients
Notes: Only consider making adjustments to ET parameters if there is volume error that you suspect is attributable to a mismatch in the type of vegetation in play. In some locations, using a crop coefficient equal to 1.0 is not reasonable when the vegetation tends towards higher ET, for example corn during the peak of its growth. You can also toggle between whether or not HMS will compute ET during periods when precipitation occurs.

## Slide 59: Dynamic Canopy
In long hydrologic simulations where vegetation changes drastically throughout the year, a dynamic canopy method may help
Notes: For long-term continuous hydrologic modeling, HMS is capable of simulating a dynamic canopy, which varies the crop coefficient throughout the simulation using a time series gage or a gridset that you provide. I would only suggest using this approach in situations when modeling soil moisture deficits throughout the year can’t be captured with a single crop coefficient.

## Slide 60: Takeaways
Evapotranspiration
  Important for continuous hydrology models
  Requires a canopy method in the subbasin
  Simple methods typically adequate
Notes: Here are the three key takeaways for evapotranspiration modeling in HMS. First, ET is an important part of continuous hydrology models. Second, in order to compute actual evapotranspiration, a canopy method is required for your subbasins. Finally, the simplest methods for ET and canopy are typically adequate – use methods with fewer data requirements where you can.

## Slide 61: Snow Modeling
Overview
Precipitation
Evapo-transpiration
Snow

## Slide 62
Importance of Snow for Water Resources
Snow represents a volume of water storage distributed over a watershed, that when melted into liquid water contributes a significant inflow into rivers, streams and reservoirs that must be dealt with in an efficient & effective manner.
Notes: In some regions, snow represents a significant volume of water storage within the watershed that can produce powerful impacts as it melts, contributing significant additional inflow into rivers streams and reservoirs.

## Slide 63: Importance of Snow within USACE
Reservoir Operation
  Timing, volume, optimization
  Release schedules, gate settings
Snowmelt Flooding
  Peak Runoff, Timing, Rain on snow
Planning & Design Studies
Source: https://atlas.niu.edu/klot/snowclimatology/USSnowContours.png
Notes: A large portion of the United States is impacted by the effects of snowmelt. Within USACE, the effects of snowmelt can impact reservoir operations, produce flooding and impact planning & design studies.

## Slide 64: Snow Hydrology Goals
Snow Accumulation
  Estimation of the distribution of watershed snow water equivalent (SWE)
Snow Melt (Ablation)
  Timing and magnitude of snowmelt
Routing of Meltwater
  Where, When, How Much?

## Slide 65: Snowmelt Methods
Temperature Index
Gridded Temperature Index
Gridded Hybrid
Energy Balance
Gridded Energy Balance
Notes: The Temperature Index method is based on a degree-day model, where there is a fixed amount of snowmelt for each degree above freezing. This method uses air temperature as a proxy for total heat transfer. There are both banded and gridded implementations.
The Hybrid method, also called the Radiation-derived Temperature Index or RTI, uses a radiation balance rather than temperature as a proxy for available energy in the snowpack. This method can be difficult to parameterize as measurements of solar radiation are not always available. This method accounts for some modes of heat transfer.
The Energy Balance method is a physically-based energy and mass balance model, where energy is exchanged between the snowpack, the air above, and the soil below. There are both banded and gridded implementations. This method accounts for each mode of heat transfer.

## Slide 66
Temperature
Index Method
Yes
No
Precipitation
Air Temperature
Rain or Snow?
Add to Liquid Water
Add to Snowpack
Above Freezing?
Melt Snowpack
Add to Liquid Water
Snowpack
Below Freezing?
Refreeze Liquid Water
Liquid Water Limit
Groundmelt
Liquid Water to
Soil Surface
Rain
Snow
Yes
No
Notes: HMS utilizes the Temperature Index Method to simulate snowmelt processes.
The Temperature Index Method essentially looks at falling precipitation with respect to air temperature to determine whether the precipitation is falling as rain or snow. If the temperature is over a specified limit, it’s considered rain and falls as liquid water; if the temperature is under the set threshold, the precipitation volume is added to the snowpack.
Next, the temperature index method determines if the air temperature is above freezing. If it is below freezing, no change in snowpack occurs; if it’s above freezing, the snowpack begins to melt and is added to the liquid water volume within the snowpack.
Then it considers—is the Snowpack temperature below freezing? If yes, the liquid water within the snowpack re-freezes; if the temperature of the snowpack is above freezing, the amount of liquid water within the snowpack is considered. If the liquid water volume within the snowpack exceeds a specified percentage of the overall snowpack (ex: 5%), the “Liquid Water Limit” is exceeded and water is released from the snowpack.
Additional melt may occur due to groundmelt and the melted snowpack is released as liquid water to the soil’s surface as runoff.
The flow chart for the temperature index snowmelt model shows how the information on the following slides comes together as a simulation algorithm.

## Slide 67
Snowmelt - Temperature Index Method Parameters
Temperature Index (TI)
Snowmelt Calibration Parameters
Lapse Rate: 0 for most; >0 for mountainous regions
*Px Temp: 32-34F
Base Temp: 32F
ATI-Meltrate Coefficient: 0.98-1.0 (typ.=1.0)
* Wet Meltrate: 0.05-0.15 in/F-day
* Rain Rate Limit: 0.25-0.50 in/day
* Dry-Meltrate: 0.015-0.15 in/F-day
Cold Limit = 0.2 in/day
ATI-Coldrate Fn: 0.01-0.045
ATI-Coldrate Coeff: 0.2-0.5
  0.2=Shallow Snowpack to 0.5=Deep Snowpack
Water Capacity: 3-5%
Groundmelt: Typically = 0 in/day
*Common Calibration Parameter
Notes: Temperature index method parameters must be assigned by subbasin within the Meteorologic Model.
The figure in the center of this slide shows the (lumped parameter) Temperature Index dialog.
The far right of the page includes common parameter values as well as which parameters are typically adjusted during calibration.
The meltrate is the most sensitive parameter that will always have a direct impact on the snow calibration.

## Slide 68
Snowmelt – Gridded Temperature Index Method Parameters
Gridded Temperature Index (GTI)
Snowmelt Calibration Parameters
Initial SWE, CC = Observed Data Grids
Initial Liquid, CC ATI, Melt ATI = Zero (acceptable assumption)
*Px Temp: 32-34 F
Base Temp: 32 F
* Wet Meltrate: 0.05-0.15 in/F-day
* Rain Rate Limit: 0.25-0.50 in/day
ATI-Meltrate Coefficient: 0.98-1.0 (typ.=1.0)
* ATI-Meltrate Fn: 0.015-0.15 in/F-day
Cold Limit = 0.2 in/day
ATI-Coldrate Coeff: 0.2-0.5
  0.2=Shallow Snowpack to 0.5=Deep Snowpack
ATI-Coldrate Fn: 0.01-0.045
Water Capacity: 3-5%
Groundmelt: Typically = 0 in/day
*Common Calibration Parameter
Notes: Gridded temperature index method parameters must be assigned by subbasin within the Meteorologic Model.
The figure in the center of this slide shows the (distributed parameter) Gridded Temperature Index (GTI) dialog.
Initial Values for the GTI method can be set to spatially distributed parameter grids (as shown above) or can be set to default values (which reverts the initial conditions similar to the general TI method, but still determines future snowmelt on a gridded distribution).
The far right of the page includes common parameter values as well as which parameters are typically adjusted during calibration. Observed data is desirable for initial Snow Water Equivalent (SWE) and Cold Content (CC), but Zero-value grids can be used for the remaining gridded initial conditions (liquid water, cold contend ATI, Meltrate ATI) if no observed initial data is available.
Once again, the meltrate is the most sensitive parameter in the GTI approach (just like in the TI approach)--it will always have a direct impact on the snow calibration.

## Slide 69
Snowmelt – Approach to Calibration
Calibrate snowmelt SWE first (before runoff calibrations).
Compare Modeled to Observed Snow Water Equivalent (SWE) Values.
Once melt of snowpack is calibrated, proceed with runoff calibration.
Notes: When modeling snowmelt within HMS, you must first calibrate the melting of the snow component. To do this, we consider the Snow Water Equivalent (SWE) within the model and calibrate the modeled SWE to closely mirror the actual observed SWE. Once the snowpack is melting similarly to the observed data, you can proceed with the runoff calibration (infiltration, routing, etc.) to complete the event.

## Slide 70
Snowmelt – Snow Observation Data
Source: https://www.wcc.nrcs.usda.gov/snow/snow_map.html
Notes: Where can you find observed snow data?
Luckily, several snow observation sites are available throughout the Western United States—shown here in Blue. Western US sources include both Snow Telemetry (SNOTEL) automated data collection sites as well as Snow Course sites where data is manually collected.
Unfortunately, observed snow data is more difficult to come by in the Midwest and Eastern United States—with just a handful of SCAN (Soil Climate Analysis Network) sites available—shown here in Red.

## Slide 71
Snowmelt – Alternate “Observed” Snow Data
Snow Data Assimilation System (SNODAS)
PROS
Available nationwide (CONUS)
Includes HMS snowmelt distributed inputs
  SWE, Cold Content, etc.
Model is updated with observed data
  Gamma flights
  Point observations
  Corrections documented at: NOHRSC SNODAS Adjustments
CONS
SWE is a model output (not observed)
Observational updates not always timely
Still lack of “observed” data
Notes: In regions where observed snow data is scarce, an alternate source may be adopted as “observed” snow data—the Snow Data Assimilation System (SNODAS).
SNODAS is actually a snow simulation model produced by the National Operational Hydrologic Remote Sensing Center (NOHRSC).
Benefits of the SNODAS data is that it’s available nationwide and includes information required for the HMS Temperature Index and Gridded Temperature Index snowmelt methods. While the SNODAS data is actually model output, the SNODAS model is corrected with observed data from gamma flights and point observations. Model corrections are then documented online.
Drawbacks of using the SNODAS data is that it is in itself model output and not actually observed. Updates made to the SNODAS model from field observations are not always timely and there’s still a large discrepancy of “observed” data availability in the non-Western United States.

## Slide 72: Takeaways
Snowmelt
  Important driver in several watersheds
  Calibrated 1st (before runoff calibration)
  Several parameters required
  Observed (or est. observed) data are available

## Slide 73: Gage Weights
Gage Weights
Gridded Precip
Overview
Precipitation
Other Meteorologic Processes
Evapotranspiration

## Slide 74: Setting Up A Gage Weights Model
Notes: First, as always, create a new meteorologic model, by selecting one of the options in the Components menu. Then, in the met model component editor, select the Gage Weights method for precipitation.

## Slide 75: Include Subbasins
Notes: This step is often forgotten, but what it does is tells the met model which subbasin elements are going to be controlled. Switch to the Basins tab of the met model editor. Here, you can decide which basin models are usable with the met model by selecting Yes for Include Subbasins. When the subbasins are included, they appear beneath the met model in the watershed explorer.
If you want to use multiple basin models with a met model, this can get cluttered sometimes, especially if your basin models have a lot of elements. For organization purposes, it can make more sense to make a copy of the met model and set up met models so they are 1:1 with basin models.

## Slide 76: Use Gages
Notes: This step tells the subbasin which gages will be used in the computation step. Expand the subbasin node of the watershed explorer, then select Gage Weights underneath it. On first click it will take you to the weights tab, where you will notice that there are no gages listed. Don’t panic, you need to switch over to the Selections tab and turn on any gages. If you don’t see any gages on this tab, that means you haven’t set up any precipitation gages yet. To do that you’ll need to create some time series components. Review that video if you need a refresher on how to do that.

## Slide 77: Weights
Notes: After enabling some gages, you’ll be able to give them weights on a subbasin-by-subbasin basis. There are two types of weights: depth, and time.
Depth weights set what the total volume of rainfall will be for the simulation.
Time weights set how the time pattern will be computed for the simulation.
These values don’t have to add up to 1, but HEC-HMS will normalize the values during the simulation so that they do.

## Slide 78: Estimating Depth Weights
Notes: You are free to determine the depth weights in whatever method you find appropriate, but a good starting point is to use the Thiessen polygon method. This method tells you how much of the watershed is closest to each precipitation gage you are using. The percents can be used as weights directly. If you have a shapefile of your watershed and the gage locations, generating Thiessen polygons and intersecting them with the basin polygon is trivial in GIS.

## Slide 79: Estimating Time Weights
Best practice: use a weight of 1 for the “best” gage, considering:
  Granularity of data – finer is better
  Location of gage – near the center of subbasin is better
Use 0 for the rest
Notes: For time weights, the best practice is to not average together gages to get a time pattern. If your precipitation stations have different time resolutions (for example one at daily level, and one at hourly), consider choosing the one with the finer time step to give you better estimates for the precipitation at shorter time steps. Also consider the location of the stations – if you have one near the center of the subbasin, it probably represents the rainfall inside the subbasin better than ones outside of it.
The effect of time-averaging is shown in the graph. Here, two completely made-up gages (in dark blue and light blue) were given an equal depth weight and time weight. When HMS computed the basin-averaged precipitation, the result is the grey Mayan Pyramid…
If you want to make sure you’re capturing the peak intensity of this storm, then time-averaging two non-coincident peaks will result in a hyetograph with a broad, flat peak, which may not be what you desire. If this helps describe the storm as it occurred in your watershed, feel free to break with best practices. However, if you’re finding that you’re underestimating peak storm intensity and you’re using time averaging, consider trying something else.

## Slide 80: Total Storm Gages
Total precipitation known
Time distribution unknown
Notes: In some situations, especially when modeling the most extreme of extreme floods, there are observations for total storm depth, but no time information was captured. Sometimes these are called “bucket surveys” and are literally an open container of some kind that was left outside (intentionally or not) during a storm event and filled up with water. You can add a total storm gage by filling in the row of the Total Storm Gages table under the Precipitation Gages node. It asks for a name, and a total depth. When you add this information, this gage will be selectable in the Selections tab, and then you can give it a depth weight, but not a time weight, because it has no timing information.

## Slide 81: Optional Settings in Met Model Editor
Use Indexing
  Adjust for climatology, regional trends in precipitation patterns
Total Override
  Override total depth for a gage
Notes: If you click on the met model and switch over to the Options tab, you’ll see two options: “Use Indexing” and “Total Override”. These give you even more control over how HMS computes properties of the storm.
The Indexing option is used to adjust gage data when there are regional trends in precipitation patterns. Using the index option requires the specification of an index value for each precipitation gage and each subbasin. The average annual precipitation total is often used as the index at a gage, and the estimated average annual precipitation over a subbasin area is often used as the index for a subbasin. Alternately, the monthly average values may be used at each gage and each subbasin. The index values are used to adjust the precipitation data for regional trends before calculating the weighted depth and weighted timing.
For small project areas this may not be necessary, but for larger project extents where the behavior of precipitation varies significantly, this allows you to adjust the estimated precipitation for the subbasins of interest.
Total override allows you to set the total depth for the gage instead of letting HMS compute it by taking the total of all timesteps in the gage entry.

## Slide 82
Watershed Explorer
Component Editor
Basin Map
Message Console
Notes: Before we start discussing the Meteorologic Model, let’s go over a brief review of the HEC-HMS user interface.
The top bar of the window contains several menus. The most important menu for working with the Meteorologic Model is the Components menu.
Beneath the menu bar is a collection of toolbars. Aside from the well-known buttons on the left, these buttons and menus are mainly for working with the basin map and for viewing results.
The watershed explorer in the top-left contains an organized tree of all the components in the project. Components include things like basin models, meteorologic models and so on. As you add complexity to your project, the tree grows, and keeps everything organized.
The component editor in the bottom left lets you edit the component that you have selected in the watershed explorer. This is the most common way to change settings or parameters for components.
The basin map in the top right gives you a view of the basin model that you are currently working with.
The message console in the bottom right alerts you to what HEC-HMS is doing. It will display warnings and errors if they occur.

## Slide 83: Gage Weights Precipitation Method
Pros
  Flexible
  Accounts for space and time variation
  Can be calibrated
Cons
  Still dependent on gage data
  Up to you to determine weights
Notes: Gage weights is recommended for the general case of dealing with multiple imperfect precipitation gages used to estimate precipitation in a subbasin. Consider the figure on the right – there are three gages, which is fortunate. However, it’s hard to say if any of these will represent the rainfall for the watershed well. It’s likely that a combination of the three could work, because the three gages span the basin. Gage weights let you decide how these three gages will combine to estimate the precipitation over the subbasin of interest. You can specify how each of these gages combine into the basin average estimate.
For events where radar data aren’t available, this method offers the most control over using gages for watershed modeling. It gives you options to combine gage data in various ways, account for gauges with varying time resolution or no time information at all, and adjust for variations in climatology.
However, there is a significant hitch in all of this – gages have to be available for the event you are trying to model. In some areas, gages are sparse, and you must do your best to find the best available information. For small watersheds, there may not be any gages inside the boundary at all, and you may be making estimates using gages that are distant. Luckily, this method gives you several controls that let you adjust how these gages are combined to achieve the optimal result.

## Slide 84: Historical Storm Methods
Gridded precipitation
Gage weights
Interpolated precipitation
Inverse distance
Specified hyetograph
Notes: Inverse distance is also a method for combining information from multiple precipitation gages using inverse distance interpolation.
Inverse distance weights the gages based on their location, which means the latitude and longitude information must be specified.
This method can be useful when you want to take the work out of estimating how gages contribute to a basin average, and want the inverse distance routine to figure it out. It can run into challenges when dealing with averaging time patterns, so the gage weights method can be preferable.

## Slide 85: Meteorologic Model Processes
  Precipitation
  Temperature
  Shortwave radiation
  Longwave radiation
  Wind speed
  Pressure
  Dew point/Humidity
  Evapotranspiration

## Slide 86: Meteorologic Model Processes
Notes: Met Model processes are models and are not simply inputted data. Here’s one example – the FAO56 Longwave Radiation method. This method computes long radiation emission from temperature, solar properties, cloud cover, etc. The user inputs the subbasin location but the longwave radiation is a modeled process.