## Slide 1: HEC-HMS Surface Runoff Unit Hydrograph Derivation

## Slide 2: Unit Hydrograph
Defined as the “basin outflow resulting from 1.0 inch (1.0 mm) of direct runoff generated uniformly over the drainage area at a uniform rainfall rate during a specified period of rainfall duration.”
Often used for “lumped” parameter modeling
User Specified Unit Hydrograph, User-Specified S-Graph, Clark and ModClark, SCS, and Snyder’s

## Slide 3: Unit Hydrograph Assumptions
Rainfall excesses of equal duration are assumed to produce hydrographs with equivalent time bases regardless of the intensity of the rain
Direct runoff ordinates for a storm of given duration are assumed directly proportional to rainfall excess volumes. Twice the rainfall produces a doubling of hydrograph ordinates (superposition)
The time distribution of direct runoff is assumed independent of antecedent precipitation (time invariance)
Excess precipitation is spatially distributed uniformly and has a constant intensity throughout the time interval

## Slide 4: UH - Limitations
Normally do not see proportional behavior in river flow.
Time-invariance can be affected by the seasons
Areal distribution of rainfall rarely uniform over time and space

## Slide 5: Unit Hydrograph – Derivation Example

## Slide 6: Unit Hydrograph - Derived
Separate interflow and base flow
Time
Flow
Direct runoff
Excess precip depth (d)
Base flow
Direct runoff
Interflow
Time
Flow
Excess precip depth (d)

## Slide 7: Unit Hydrograph - Derived
Measure the total volume of direct runoff under the hydrograph and convert this to depth over the watershed
Time
Flow
Direct runoff (V)
Excess precip depth (d)
Area (A)

## Slide 8: Unit Hydrograph - Derived
Divide the ordinates of the direct runoff by the depth of runoff (d)
Time
Flow
Direct runoff
Flow/u
Direct runoff
Time
Excess precip depth (d)
Unit precip depth (u)

## Slide 9: Unit Hydrograph - Derived
Estimate the duration of the unit hydrograph
Time
Precip
Φ index
Excess Rainfall Duration

## Slide 10: Unit Hydrograph – Derivation Example
Notes: 1958400/(10 〖𝑚𝑖〗^2 ) 10 〖𝑚𝑖〗^2×("27 878 400" 〖𝑓𝑡〗^2)/(1 〖𝑚𝑖〗^2 )

## Slide 11: Unit Hydrograph – Derivation Example
Rainfall total depth (5 hours) = 3.34 inches
Time
Precip
Φ index = 0.5 in/hr
Excess Rainfall Duration
= 0.84 inches (Step 2)
Rainfall duration = 3-hr

## Slide 12: Unit Hydrograph in HEC-HMS

## Slide 13: Unit Hydrograph – Convolution Example

## Slide 14: Thank you for listening!
Visit our website!
https://www.hec.usace.army.mil/confluence/hmsdocs/hmsum/4.7
https://www.hec.usace.army.mil/software/hec-hms/