## Slide 1
Matt Fleming, P.E.
Hydrologic Engineering Center
HEC-HMS Presentation for NRCS
8 March 2022
U.S. Army corps of engineers

## Slide 2: Outline
Background
Documentation
Tech support
Tech transfer
HEC-HMS basics
New features NRCS staff should know about
Questions

## Slide 3: HEC-HMS
Latest Release
  Version 4.9
Beta Release
  Version 4.10
MacOS and Linux versions available
HEC-HMS Webpage

## Slide 4: Documentation
Release Notes
User’s Manual
Technical Reference Manual
Applications Guide
Validation Guide
HEC-HMS Documentation

## Slide 5: Tech Support
Discourse

## Slide 6: Tech Transfer
Tutorials and Guides

## Slide 7: Tech Transfer
Basic HEC-HMS Class Materials

## Slide 8: Tech Transfer
The HEC-HMS team has been providing quarterly webinars since 18Feb2021
Increase awareness of new features and materials
Focus on 2 to 3 new features and demo their usage
Dedicated time for Q&A
Next webinar: April 2022

## Slide 9: Tech Transfer
HEC-HMS USACE HH&C CoP Webinar Series

## Slide 10: Outline
Background
Documentation
Tech support
Tech transfer
HEC-HMS basics
New features NRCS staff should know about
Questions

## Slide 11: Hydrologic Modeling System

## Slide 12: Empirical, conceptual, or physically based

## Slide 13: Subbasin-average or Gridded

## Slide 14: Event OR Continuous

## Slide 15: Deterministic or Stochastic

## Slide 16: GIS Processing
Terrain modification
Sink fill and flow direction
Subbasin and reach delineation
Subbasin and reach splitting and merging
Subbasin and reach characteristics
Parameter estimation

## Slide 17: User Interface
Watershed Explorer
Component Editor
Basin Model Map
Message Window
Menus
Toolbars

## Slide 18: Simple Basin Model
Non-georeferenced models can be created by added element icons and connecting them to form a network.
Parameters are manually entered in the component editors or global editors.

## Slide 19: Georeferenced Basin model
GIS tools can be used to Georeference an existing basin models or create a new basin model using terrain data and shapefiles.
Parameter are manually entered in the component editors or global editors. GIS parameter estimation tools are available.
Gridded meteorologic variables can be applied.
Spatial results can be computed and visualized.

## Slide 20: Meteorologic Model
Meteorologic model is used to compute boundary conditions for the basin model
  Precipitation
  Temperature
  Evapotranspiration potential
  Snowmelt (moving to the basin model)

## Slide 21: Simulations
Compute tab, Watershed Explorer
Compute Toolbar
Managers

## Slide 22: Simulation Run
Simulation Run
Meteorologic Model
Basin Model
Control Specifications

## Slide 23: Five Result Displays in HEC-HMS
Global summary tables
Element graph
Element summary table
Element time series
Spatial Results

## Slide 24: Spatial Results
Precipitation, excess, loss, snow, 2D output, etc.
Feature within v4.7 release
0
50
Precip Depth (in)

## Slide 25: Spatial Results
Visualize time series of spatial results
Feature within v4.9 release

## Slide 26: Spatial Results
Visualize flow and SWE statistical metrics
Feature within v4.10-beta.1 release

## Slide 27: Spatial Results
Export static map (e.g. .tif)
Export animation (e.g. .mp4)
Feature within an upcoming v4.10-beta release

## Slide 28: Six WAYS to Access results
Watershed Explorer Results tab
Right-click option in basin map
Compute toolbar
Results menu
Animation Toolbar
Reports

## Slide 29: Outline
Background
Documentation
Tech support
Tech transfer
HEC-HMS basics
New features NRCS staff should know about
Questions

## Slide 30: New features NRCS staff should know about
GIS delineation (including reconditioning)
GIS characteristics
GIS parameterization
Hypothetical storm
  Atlas 14 grid
  User-defined temporal pattern
  User-defined area-reduction curve
Reports
PMP (HMR 52) optimization
Online documentation and training material

## Slide 31: HEC-HMS GIS Tools
TauDEM GIS library is used to define the flow direction, flow accumulation, and stream grids
The user defines the stream threshold
A default delineation is performed
Tools are available to customize the delineation by merging elements or splitting subbasins and reaches
GIS tools are available for computing physical characteristics
GIS tools are available for estimating model parameters

## Slide 32: Automated Delineation
Flow direction codes
71
56
44
53
69
74
78
72
69
71
47
68
58
55
21
31
67
58
49
46
37
38
64
22
61
16
Digital elevation model (DEM)
4
4
4
4
4
4
5
5
5
5
3
3
4
5
6
2
2
3
4
5
3
3
5
3
2
Flow direction grid
Stream Network
Flow accumulation grid
0
0
0
0
0
0
1
1
2
1
0
0
0
0
1
3
8
5
2
1
0
19
0
2
24
3
4
5
6
7
8
1
2
8-point pour model

## Slide 33: Automated Delineation
Stream Network
Flow accumulation grid
0
0
0
0
0
0
1
1
2
1
0
0
0
0
1
3
8
5
2
1
0
19
0
2
24
How many subbasins and reaches would be delineated if the stream threshold was set to 3 cells?

## Slide 34: Define the Coordinate System
There are three ways to define the coordinate system:
Choose from a predefined system; UTM or Albers projections
Choose an existing projection file with well known text
Use the terrain data’s projection

## Slide 35: Choose a Terrain Dataset for the Basin Model
Once the projection has been defined and the terrain data selected, the terrain is displayed in the basin model map
The draw properties for the terrain can be modified from the Map Layers editor
GIS delineation tools can now be applied to the terrain data

## Slide 36: Terrain Reconditioning
Original Terrain with desired subbasin boundaries (red) and a stream network (blue)
Reconditioned Terrain

## Slide 37: Terrain Reconditioning
Auto = 17.9
NRCS = 17.8
Auto = 35.7
NRCS = 35.7
Auto = 62.9
NRCS = 61.2
Total
Auto = 809
NRCS = 798
Auto = 69.6
NRCS = 78.8
Automated delineation tools can result in subbasin boundaries and reach lines that do not match published information
The terrain reconditioning tool in HEC-HMS can be used to modify the terrain so subbasin and reach delineation better matches published information

## Slide 38: Burning Streams with a Smooth and Sharp Drop
Buffer = 2 cells
Smooth drop = 5 ft
Sharp drop = 1 ft
5 ft
1 ft

## Slide 39: Terrain Reconditioning

## Slide 40: Preprocess Sinks
Preprocess Sinks automatically fills in low spots that prevent water from flowing across the terrain
A Sink Fill terrain layer is created, this is the hydrologically corrected DEM
A Sink Location raster is created showing the locations of the sinks and amount of fill needed

## Slide 41: Preprocess Drainage
Preprocess Drainage runs the flow direction and flow accumulation processes
New grid layers are added to the project and displayed in the basin model map
The flow accumulation grid shows the detailed stream network
Notes: After

## Slide 42: Identify Streams
The user must define the drainage area threshold for initiating a stream segment
Once the drainage area exceeds the threshold, the program will identify a stream segment
A new stream segment is identified when there is a confluence
A subbasin will be created for the drainage area of each stream segment
Notes: After

## Slide 43: Break Points
Break points are used to define the outlet of the basin model and any location where the user knows a subbasin outlet is required, like at a gage location
The break point must be added so that it falls on top of the identified streams layer
Use the break point creation tool and click within the basin model map to add a new break point

## Slide 44: Delineate Elements
Delineate Elements will create the default element network (based on the stream threshold)
There are options to set prefix names for subbasins, reaches, and junctions
Insert junction elements between subbasin and reach elements is a user option
Converting break points to computation points is a user option

## Slide 45: Merging Subbasin and Reach Elements
Subbasin and reach elements must be hydrologically adjacent in order to merge
Select the elements to merge in the watershed explorer or through the basin model map
Two or more elements can be merged at one time
The program automatically names the new element

## Slide 46: Merging Subbasin and Reach Elements
Check reach elements after merging subbasin elements
HEC-HMS will automatically delete reach elements when merging headwater subbasins
There can be multiple reach elements within interior subbasins, these can be merged
Four reach segments in this interior subbasin

## Slide 47: Split Subbasin and Reach Elements
New subbasin and reach elements can be added using the Split Element tool
First, select an element in the basin model
Then, select the Split Element option on the GIS menu
Zoom into the location where the split will occur and click on an existing identified stream grid cell (or on a stream identified in the flow accumulation grid)

## Slide 48: Split Subbasin and Reach Elements
A temporary GIS feature will show the results of the split
Accept the action and a new subbasin and reach elements will be added to the project
A new junction will be added if that option was selected when initially delineating the network

## Slide 49: Split Subbasin and Reach Elements
HEC-HMS will add a new subbasin element with an outlet at the split subbasin point

## Slide 50: GIS Data Management
Manually add background shapefiles to the maps folder before adding them to a basin model (makes the files relative to the project)
HEC-HMS will save GIS files created during automated delineation to the gis folder
HEC-HMS will save terrain files to the terrain folder
The *.sqlite file contains information for georeferenced elements, including discretization
Typical HEC-HMS Project Directory

## Slide 51: Subbasin Characteristics
Longest Flowpath Length
Longest Flowpath Slope
Centroidal Flowpath Length
Centroidal Flowpath Slope
10-85 Flowpath Length
10-85 Slope
Basin Slope
Basin Relief
Relief Ratio
Elongation Ratio
Drainage Density

## Slide 52: Reach Characteristics
Reach Length
Reach Slope
Reach Sinuosity
Reach Relief

## Slide 53: Parameter Expression Calculator
HEC-HMS has a built-in Expression Calculator that can be used to facilitate canopy, surface, loss, transform, baseflow, and routing parameter estimation from GIS data.
The Expression Calculator can be launched from global editors.

## Slide 54: Parameter Expression Calculator
When clicking “Calculate” within the Expression Calculator, the parameter estimates are computed and automatically populated in the Global Editor table.

## Slide 55: Parameter Expression Calculator
In the Expression Calculator, grids can also be used as variables if they have been previously imported into HEC-HMS. Grids are available from the Grids tab. When a grid is included in the expression, a zonal average value of the feature on the grid is used in the calculation.

## Slide 56: Hypothetical Storm
User-specified temporal pattern (could be NRCS patterns)
Storm duration
User-specified storm depth or extract from a grid
Depth-area reduction
  TP 40 or user-specified
  Enter storm area or choose a computation point

## Slide 57: Hypothetical Storm
Download precipitation-frequency grids from https://hdsc.nws.noaa.gov/hdsc/pfds/pfds_gis.html

## Slide 58: Hypothetical Storm
New Precipitation-Frequency Grid Importer
Choose the grid, name, units and scale factor
The program will copy the file into the project directory and create the grid object

## Slide 59: Hypothetical Storm
User-specified temporal patterns can be created using Percentage Curves

## Slide 60: Hypothetical Storm
Depth Area Reduction – TP40 or User-Specified

## Slide 61: Frequency Analysis Compute
Frequency Analysis Compute
Combines multiple Met/Basin combinations to compute a frequency curve
Presentation

## Slide 62: Basin Model Reports
Standard Report Option

## Slide 63: Simulation Results Report
Statistics Report Option

## Slide 64: HMR 52 Storm Optimization
HMR 52 Storm parameters can be automatically adjusted to maximize peak flow, volume, and reservoir stage

## Slide 65: Link to Training Material
GIS related tutorials:
https://www.hec.usace.army.mil/confluence/hmsdocs/hmsguides/creating-a-georeferenced-model-using-hec-hms-gis-tools
https://www.hec.usace.army.mil/confluence/hmsdocs/hmsguides/gis-tutorials-and-guides
GIS Parameter Estimation tutorials:
https://www.hec.usace.army.mil/confluence/hmsdocs/hmsguides/applying-hec-hms-gis-parameter-estimation-tools
Hypothetical Storm tutorials:
https://www.hec.usace.army.mil/confluence/hmsdocs/hmsguides/working-with-hypothetical-precipitation-methods-in-a-meteorologic-model
HMR 52 Storm tutorials:
https://www.hec.usace.army.mil/confluence/hmsdocs/hmsguides/developing-probable-maximum-precipitation-pmp-estimates

## Slide 66: Conclusion
Latest release: v4.9
More enhancements are being delivered within version 4.10 (April 2022)
Documentation is continuously updated
HEC-HMS training is continuously updated
We would appreciate any feedback and ideas for improvement

## Slide 67: Questions?
Docs: https://www.hec.usace.army.mil/confluence/hmsdocs
To be added to the list, send an email to hec.hms@usace.army.mil with “subscribe” in the title or body.