## Slide 1: GREEN & AMPT LOSS MeTHOD IN HEC-HMS FOR POST-WILDFIRE HYDROLOGY MODELING APPLICATIONS
Presenter:
Jay Pak (HEC)
Jose Paredez (SPL)
Jackie Oehler (SPL)
How ?
Pre-Wildfire Condition
Post-Wildfire Condition
SCS-CN
G&A
Etc.
HEC-HMS FY25 Q2 Webinar, 25 Mar 2025

## Slide 2: overview
    Fire Impacts on Debris Basins/Reservoirs
    Study Motivation
    Modification of Green & Ampt Equation with “Wetting Front Suction” & “Sorptivity” (Guidance Table: Work in Progress by Dr. Ross Shillito (CHL))
    Guidance Table using Walnut Gulch Rainfall Simulator Dataset
    Validation through Arroyo Seco Case Study
    Improvements Needed for Guidance Table
    Summary
    Case Study: 2025 Los Angeles Eaton Fire - Bailey Canyon
      SCS-CN Method
      G&A Method with “Wetting Front Suction” option
    Questions & Feedback

## Slide 3: Fire Impacts on Reservoir
Source: https://www.kunc.org/science/2019-09-24/how-wildfires-may-muck-up-the-wests-reservoirs
  What’s happening here?
    Indicators
      Early Snowmelt
      Longer Dry Seasons
      Wildfire Pattern: More Extreme Wildfires
        Water Repellence
      Storm Pattern: extreme short-duration high-intensity rainfall values
    Flash Flood (Faster & Higher Peak, More Volume)
    Sediment/Debris Flow
    Decreased Reservoir Capacity
    And other related impacts
How do flow and sediment inflow change under post-fire conditions?

## Slide 4: High Park Fire (June-July, 2012), Colorado Estimated pre-and post-fire hydrographs
Source: USGS NRCS Hydrology Technical Note 4 -Hydrologic Analyses of Post-Wildfire Conditions, August 2016

## Slide 5: Study Motivation
Current Guidance for the Post-Wildfire Hydrology:
USDA, Hydrology Technical Note No. 4
“Existing methods for adjusting CNs to account for wildfire effects are for the most part based heavily upon the hydrologic judgment of practitioners who have studied burned watersheds.”
- USDA (2016)
    To develop a physically based post-wildfire hydrological method using the Green & Ampt infiltration model as an alternative solution.
    This alternative approach is crucial in cases where no data is available for mountain watersheds affected by wildfires.

## Slide 6: Post-Fire Curve Number Adjustments
Condition | CN Value
High Burn Severity | pre-fire CN + 15
Moderate Burn Severity | pre-fire CN + 10
Low Burn Severity | pre-fire CN + 5
Higginson and Jarnecke (2007)
Livingston and others (2005)
Method 1
Method 2

## Slide 7
Modification of G & A Equation in HEC-HMS with Wetting Front Suction & Sorptivity
Green & Ampt infiltration equation (1911)
Using
Chart: Time [sec]
| 0 | 60 | 300 | 360 | 600 | 720 | 900 | 1200 | 1500 | 1800
S (42 deg sand) | 0 | 42.0379 | 103.7497 | 115.5404 | 157.4165 | 176.3247 | 203.0742 | 244.6623 | 283.6922 | 320.9327
S (88 deg sand) | 0 | 14.9545 | 34.759 | 38.3288 | 50.577 | 55.9157 | 63.2938 | 74.4107 | 84.5084 | 93.8845
Where:
I = cumulative infiltration, K = hydraulic conductivity, ψ = the effective suction at the wetting front, Δθ= change in soil water content, S = sorptivity, and t = time
(Philip, 1957)
Sorptivity is a function of contact angle

## Slide 8: 1st Question?
Condition | CN Value
High Burn Severity | pre-fire CN + 15
Moderate Burn Severity | pre-fire CN + 10
Low Burn Severity | pre-fire CN + 5
How can the G&A Loss Method with “Wetting Front Suction” & “Sorptivity” in HEC-HMS be used to develop a post-fire hydrology model from the pre-fire model?
Answer: "Absolutely, simpler guidance is essential for effectively applying this approach as like the SCS-CN method!"
?

## Slide 9: Development of Guidance Table using Walnut Gulch Rainfall Simulator Dataset
Source: Earth Syst. Sci. Data, 10, 19–26, 2018, https://doi.org/10.5194/essd-10-19-2018

## Slide 10: Walnut Gulch Case Studies: Abar Ranch
Site name | Site | Coordinates |  | Soil | Soil | Slope | MLRA | Ecological | Precipitation | Vegetation | State | Plot | Plot # | Slope, % |  |  |  |  |  |  | Simulation year |  |  |  |  | 
 | ID | Latitude | Longitude | series | texture | aspect |  | site | zone, in |  | STM | condition |  |  | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Abar ranch | Ab | 31.4411516 | -110.52191 | White house | gravely loam | E | 41-1 | Loamy Upland | 16-20 | oak savana | HCPC | natural | 1 | 9.3 |  |  | x |  |  |  |  |  |  |  |  | 
 | 2003 Fire |  |  |  |  |  |  |  |  |  |  | natural | 2 | 9.2 |  |  | x |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | natural | 3 | 12.5 |  |  | x |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | natural | 4 | 14.2 |  |  | x |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | burn | 1 | 10.2 |  | x | x | x |  | x |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | burn | 2 | 9.1 |  | x | x | x |  | x |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | burn | 3 | 8.1 |  | x | x | x |  | x |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | burn | 4 | 9.8 |  | x | x | x |  | x |  |  |  |  |  | 
Chart: Years After Burn (Year)
| 0 | 1 | 2 | 3 | 5
Ab-Plot4 | 41 | 18 | 11 | 20 | 41
Ab-Plot3 | 43 | 28 | 19 | 40 | 50
Ab-Plot1 | 49 | 39 | 8.7 | 25 | 49
Ab-Plot2 | 32 | 10 | 7 | 25 | 26
Chart: Years After Burn (Year)
| 0 | 1 | 2 | 3 | 5
Ab-Plot4 | 170 | 138 | 135 | 143 | 135
SA-Plot 1 | 175 | 140 | 155 | 165
Ab-Plot3 | 170 | 138 | 134 | 136 | 140
Ab-Plot1 | 170 | 128 | 131 | 151 | 147
Ab-Plot2 | 165 | 138 | 135 | 132 | 156
Table | 167 | 134.46
Chart: Year After Burn
| 0 | 1 | 2 | 3 | 5
Ab-Plot4 | 0.09 | 0.11 | 0.03 | 0.07 | 0.08
Ab-Plot3 | 0.035 | 0.12 | 0.07 | 0.04 | 0.06
Ab-Plot1 | 0.0001 | 0.08 | 0.03 | 0.04 | 0.05
Ab-Plot2 | 0.047 | 0.09 | 0.0001 | 0.03 | 0.095
Post-Fire Parameters For the 1st year after fire (Arid & Semi-Arid Areas) | Actual Range for 1st Year after Fire | 
 | Min | Max
Moisture Deficit Values | 0.12 | 0.08
Sorptivity Multiplier | 0.84 | 0.75
Hydraulic Conductivity Multiplier | 0.8 | 0.31
Note: The recommended range was developed based solely on the Abar ranch within the Walnut Gulch Area. Further research is needed with more data.
20 cases

## Slide 11: Walnut Gulch Rainfall simulator data
Calibration for 5 locations & 84 events with measured data
Wet Condition: 68 events & Dry Condition: 16 events (need more data)

## Slide 12: Moisture Deficit Values (all Conditions)

## Slide 13: Moisture Deficit Values (Wet Condition)

## Slide 14: Sorptivity multiplier (Wet Condition)
(Philip, 1957)
Conversion from Sorptivity to Wetting Front Suction using

## Slide 15: Hydraulic conductivity multiplier (wet Condition)

## Slide 16: 2nd Question?
Is this guidance table applicable using “Wetting Front Suction” to other events?
Answer: Yes, it is ready to be applied to case studies.
Sources: Rawls, Brakensiek, and Miller’s Table (1983) / Highway Drainage Design Manual, ADOT, 2014

## Slide 17: validation: Arroyo Seco Watershed
Watershed | County | Drainage Area (mi2) | Wildfire | Percent Burned | Burn Severity
Arroyo Seco | Los Angeles | 16.0 | Station Fire (August 2009) | 95% | Unburned: 5% Low: 18% Moderate: 42% High: 36%

## Slide 18: Step 1: Estimate initial G & A parameters for pre-wildfire hydrology using gSSURGO data and Table B-2 (Highway Drainage Design Manual, ADOT, 2014).

## Slide 19: Step 2: Calibrate the pre-wildfire hydrology model using the precipitation and flow gage data.

## Slide 20: Step 3: Prepare Post-Wildfire Hydrology Model using the guidance Table

## Slide 21: Step 4: Compare post-wildfire results with measured data & SCS-CN Methods

## Slide 22: Need To Improve for Guidance Table
Update the guidance table with more case studies, especially dry condition & different areas to generate the better direction for the post-fire hydrology
Seeking a dataset to update the guidance table with varying soil burn severities (Minor, Moderate, and Severe)
Prepare the guidance table for 2nd, 3rd, 4th, and 5th year
Post-Fire Parameters | 1 st Year Actual Range For G&A-Sorptivity (Wet Condition) |  |  |  | 
For the 1st year after fire | Min | 1Q Percentile | Medium | 3Q Percentile | Max
Moisture Deficit Values | 0.12 | 0.08 | 0.07 | 0.021 | 0.001
Sorptivity Multiplier | 0.94*(Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) | 0.91*(Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) | 0.91*(Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) | 0.84*(Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) | 0.75*(Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value)
Wetting Front Suction Multiplier | 0.942 * (Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) 2 | 0.912 * (Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) 2 | 0.912 * (Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) 2 | 0.842 * (Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) 2 | 0.752 * (Pre-Fire Moisture Deficit Value/Post-Fire Moisture Deficit Value) 2
Hydraulic Conductivity Multiplier | 1.91 | 1.23 | 0.87 | 0.46 | 0.14

## Slide 23: Case Study
Post-Wildfire Hydrology Modeling Application for Bailey Debris Basin in Eaton Fire Areas
  CN Application – Jose Paredez
  G&A Loss Method Application with “Wetting Front Suction” – Jackie Oehler
Source: California Geological Survey (CGS)

## Slide 24: NRCS (SCS) Curve number
The SCS-CN Method is an event-based, lumped rainfall-runoff model, based on the water balance equation. Originally developed for small agricultural watersheds
  Apply to drainage areas ranging in size from 1 to 2,000 acres (0.001 to 3 mi2)
  Does not cover modeling runoff from snowmelt or rain on snow events
  Primarily uses precipitation-frequency data (rainfall amount by return period)
  Uses a storm duration of 24 hours for the synthetic rainfall distributions
for P > Ia
for P ≤ Ia
Q = runoff, in
P = rainfall, in
Ia = initial abstraction, in
S = potential maximum retention after runoff begins, in
Ia = Initial Abstraction
CN = Curve Number
Tl = Lag Time
L= Longest Flow Path (ft)
Y = Mean Basin Slope (%)
λ = initial abstraction ratio, unitless
(λ = 0.2 is a standard value based on studies)

## Slide 25: Loss Method: Initial abstraction (Ia)
Initial abstraction is the amount of rain that falls before runoff begins.
It includes all losses such as water retained in surface depressions, water intercepted by vegetation and other cover, and water lost to evaporation and infiltration
Ia is highly variable
λ = 0.2 is a standard value based on studies of many small agricultural watersheds
λ = initial abstraction coefficient, unitless
S = potential maximum retention after runoff begins, in
1-in
Precipitation (5 in)
Losses (1 in)
Ia = 1 in
CN = 100 (no infiltration)
Notes: The NRCS CN method assigns a representative runoff curve number for a given soil and cover type for design purposes.

## Slide 26: Loss Method: Initial abstraction ratio
Due to the uncertainty and unknown origin, several investigators have re-evaluated the selection of the initial abstraction ratio (Baltas et al., 2007;Mishra et al., 2006; Mishra & Singh, 2004; Woodwardet al., 2004; Hawkins et al., 2002; Jiang, 2001).
Runoff estimates are inaccurate where watershed retention is a large fraction of the rainfall, as in semiarid watersheds.
The use of a universal (λ = 0.2) initial abstraction ratio may not be appropriate.
Studies found that the initial abstraction ratio varied from storm to storm and from watershed to watershed.
λ = initial abstraction ratio, unitless
S = potential maximum retention after runoff begins, in

## Slide 27: Post-Wildfire Application
CN
*CN estimated based on land use/cover and hydrologic soil group

## Slide 28: Post-Wildfire Application
CN
*CN estimated based on land use/cover and hydrologic soil group

## Slide 29: Post-Wildfire Application
Burn Severity | CN Adjustment
Unburned | Pre-fire CN + 0
Low | Pre-fire CN + 5
Moderate | Pre-fire CN + 10
High | Pre-fire CN + 15
Higginson and Jarnecke (2007)
*Adjust initial abstraction ratio (λ) based on antecedent conditions.

## Slide 30: Case study – 2025 Eaton Fire
Eaton Fire
Los Angeles District Hydrologic Engineering Center
Albuquerque District
Los Angeles District | CA DWR | HEC | Albuquerque District
Tim Fairbank Michael Thompson Van Crisostomo Moosub Eom Nick Olsen Jackie Oehler Jose Paredez | Essayas Ayana Om Prakash | Jay Pak | Jonathan AuBuchon Lavonna Begay Adam Jones

## Slide 31: Background – CWMS Model
Whittier Narrows Dam
Santa Fe Dam
Sepulveda Dam
Whittier Narrows Dam
Santa Fe Dam
Sepulveda Dam
Eaton Fire

## Slide 32: HEC-HMS Model
Whittier Narrows
Dam
Santa Fe Dam
Eaton Fire
Bailey Canyon Bailey Debris Basin
Bailey
Canyon

## Slide 33: Pre-Fire Model “Calibration”
Eaton Fire
Arroyo Seco
Roberts Canyon
Whittier Narrows
Dam

## Slide 34: Pre-Fire Model “Calibration”
85
85
65
86
86
86
86
Initial Curve Number Estimates
Curve Number
68
69
69
52
68
69
69
Adjusted Curve Number Estimates* (Pre-Fire Curve Number)
*Based on similar watersheds (Arroyo Seco & Roberts Canyon)
Bailey
Canyon
Bailey
Canyon

## Slide 35: Post-Wildfire Estimates
Burn Severity | CN Adjustment
Unburned | Pre-fire CN + 0
Low | Pre-fire CN + 5
Moderate | Pre-fire CN + 10
High | Pre-fire CN + 15
Higginson and Jarnecke (2007)
Bailey
Canyon
+9.5
+9
+9.6
+9.2
+8.6
+9.4
+9.1

## Slide 36: Post-Wildfire Estimates
Bailey
Canyon
+9.5
+9
+9.6
+9.2
+8.6
+9.4
+9.1
77.5
Bailey
Canyon
78.2
78.6
61
76.6
78.4
78.1
Bailey Canyon = 68 + 9.5 = 77.5

## Slide 37: Validation – February 13, 2025, Event

## Slide 38: Green & Ampt Method
Initial Storage Method
  Initial Content
  Initial Deficit
Capillarity Parameter
  Wetting Front Suction (Suction)
  Sorptivity
Saturated Hydraulic Conductivity (Conductivity)
Impervious (%)

## Slide 39: Surface Texture Data
Surface texture data was downloaded from the NRCS Web Soil Survey.
Bailey subbasin consists of:
  Loam
  Very Gravelly Loam
  Sandy Loam
  Gravelly Loam
Bailey
Subbasin

## Slide 40: Green & Ampt Parameters
Table is from the ADOT Highway Drainage Design Manual (2014)
An area weighted average for each parameter was computed.
 | Conductivity (IN/HR) | Suction (IN)
Initial Parameters | 0.2 | 8.12

## Slide 41: Pre-Fire Calibration
Observed data was not available to calibrate the model.
Arroyo Seco model ratios were applied to the Bailey subbasin initial parameters.
 | Conductivity (IN/HR) | Suction (IN) | Initial Deficit
Calibrated Pre-Fire Parameters | 0.18 | 8.73 | 0.02

## Slide 42: Post-Wildfire Estimates

## Slide 43: Post-Wildfire Estimates
Bailey_Sub Parameters |  |  |  | 
 | Conductivity (IN/HR) | Suction (IN) | Initial Deficit | % Burned
Post-Fire Min | 0.34 | 0.26 | 0.12 | 99.5
Post-Fire Median | 0.16 | 0.63 | 0.07 | 99.5
Post-Fire Max | 0.03 | 157.00 | 0.001 | 99.5

## Slide 44: Burn Severity
Green & Ampt post-fire method does not take burn severity into consideration.
However, we expect areas with high burn severity to be closer to the maximum scenario and areas with low burn severity to be closer to the minimum scenario.
Bailey
Subbasin

## Slide 45: Validation - February 13, 2025 Event (Min)

## Slide 46: Validation - February 13, 2025 Event (Med)

## Slide 47: Validation - February 13, 2025 Event (MAX)

## Slide 48: Comparison of Results

## Slide 49: Questions & Feedback
Funding Sources:
Code Development: Post-Wildfire Hydrology R&D Program (CHL)
Walnut Gulch Rainfall Simulator Calibration & Guidance Table: GI Fund (HQ) & Innovation Fund (HEC)
Acknowledgments: Rose Shillito (CHL), Markus Berli (DRI), David Ho (HEC), Jose Paredez (SPL), Moosub Eom (SPL), Jonathan AuBuchon (SPA), Jackie Oehler (SPL)
!
Thank You!