## Slide 1: Reservoir Sedimentation Management Hydrosuction
John Shelley, Ph.D., P.E.
August 2024
Tuttle Creek Lake prior to filling.
“The views, opinions and findings contained in this report are those of the authors(s) and should not be construed as an official Department of the Army position, policy or decision, unless so designated by other official documentation.”

## Slide 2: Bucket and Sand Model
Nathan and Trey collecting sand from the Arkansas River. Picture by Mark Morris.

## Slide 4: El Canada Reservoir (Guatelama) Hydrosuction
El Canada Graphics: SediCon

## Slide 5
El Canada Hydrosuction- Connecting to Existing Conduit

## Slide 7: Analysis
Will coarser sediments settle out in the pipe and plug it?
How much sediment will the hydrosuction system transport out of the lake?

## Slide 8: Limit Velocity (From ICOLD Bul. 193)

## Slide 9: Limit Velocity
Answers the question: What is the slowest velocity in the pipe to avoid sediment settling (which could lead to plugging)?
Really only applies to non-cohesive sediment (sands and gravels).
FL

## Slide 10: Limit Velocity Exercise
What is the limit velocity for d50 = 0.25 mm in a 0.5 m hydrosuction pipe that is 10% solids by volume?
FL

## Slide 11: Limit Velocity Exercise
What is the limit velocity for d50 = 0.25 mm in a 0.5 m hydrosuction pipe that is 7% solids by volume?
FL
FL 0.84
VL = 0.84 * sqrt (2 * 9.8 * 0.5 (2.65-1))
= 3.38 m/s

## Slide 12: Analysis
Will coarser sediments settle out in the pipe and plug it?
How much sediment will the hydrosuction system transport out of the lake?
Compute the flow of the water out of the pipe, with some adjustment to viscosity
Assume a % solids

## Slide 14
1
2
Z1
Z2
y1
y2

## Slide 15: Losses Depends on the Pipe And the Fluid
Smooth pipe = less losses
Rough pipe = high losses
Low viscosity liquid (i.e. water) = low losses
High viscosity liquid (i.e. honey) = high losses
Friction losses: (hL/L) * length of the pipe

## Slide 16
https://www.youtube.com/watch?app=desktop&v=WMtiH5LyOYI
M x v2/2g

## Slide 17: Workshop: LPP
Data:
Time series of pool elevations
Sediment characterization
Pipe length
Pipe type
Analysis Steps
Assume a concentration of sediment
Calculate viscosity
Create a pool height—water flow rating curve using pipe flow equations
Multiply by concentration to generate a pool height—sediment discharge rating curve
Use bulk density to convert from sediment discharge to volume of sediment removed
Use the time series of pool heights and the rating curve to compute a time series of sediment removal

## Slide 18: Workshop Pre-Requisites
The workshop assumes you know how to do various tasks in Excel, including:
Plot a trendline
Use the solver tool
Do a “sumif” function

## Slide 19: What Concentration of Sediment in the Pipeline?
% Solids (By Volume) | Reservoir | Location | Sediment Type | Entrainment Mechanism | Reference
12 | El Canada (Year 1) | Guatemala | Clay | Water-jetting | Jimenez, Figueroa, and Jacobsen, 2015
9 | El Canada (Year 2) | Guatemala | Clay | Water-jetting | Jimenez, Figueroa, and Jacobsen, 2015
8 | El Canada (Year 3) | Guatemala | Clay | Water-jetting | Jimenez, Figueroa, and Jacobsen, 2015
3 | Djindiouia | Algeria | Silt and clay | Cutter-head powered by a turbine on the outlet pipe | Fan, 1985
15 | Xiao Hua-shan | China |  | Water-jetting | Hotchkiss and Huang, 1995.
We will assume 10% solids for the workshop.

## Slide 20: Questions?

## Slide 21: Practical Constraints
Minimum releases
Volume of deposition till pre-impoundment
Distance from dam

## Slide 22: Example- John Redmond, KS

## Slide 23: Environmental Limit

## Slide 24: How much deposition is available for removal?

## Slide 25: The further away you are, the less effective your hydrosuction system will be
John Redmond

## Slide 26: John Redmond- Storage Impacts Over Time

## Slide 27: Other Kansas Lakes
Note: Equivalent costs based on 2018 John Redmond dredging rates without adjusting for inflation.