## Slide 1
Dry Period
Wet Period
Annual Peak Flow Record

## Slide 2
Figure 10 Estimated peak discharge for the Lower Red River basin at Winnipeg and flood signatures in the Upper Red River basin.
from: St. George, S. and Nielsen, E. “Palaeoflood records for the Red River, Manitoba, Canada, derived from anatomical tree-ring signatures,” The Holocene, 13,4 (2003) pp. 547-555.
Suggestion of wet/dry cycle
Tree-ring evidence of historical flood peaks suggests a reoccurrence of wet and dry periods in the last few centuries
gaged

## Slide 3
1941
1961
Where to split the record? – Pettitt Test
Two samples are compared to test whether the means are significantly different. The Pettitt Test repeats the comparison for every possible break point between the samples, and finds the one with the greatest evidence of difference
Statistical Evidence of Difference between samples
5% significance level

## Slide 4
Dry Period
Wet Period
Annual Peak Flow Record
Split record in 1941

## Slide 5
Frequency Analysis on Wet and Dry Records
The standard deviation (slope of curve) is much less for the wet and dry records than for the full record, because in either period, range of observed flow is less

## Slide 6
Theorem of total probability:
P(Q>q) = P(Q>q|wet) * P(wet) + P(Q>q|dry) * P(dry)
Re-Combining the Wet and Dry Frequency Curves
where:
P(Q>q) =
exceedance probability for a given flow, q
P(Q>q|wet) =
exceedance probability given that we're in the wet condition
P(wet) =
probability we're in the wet condition.

## Slide 7
Analysis requires a single frequency curve for any future year.
Recombining the wet and dry frequency curves with the total probability theorem requires, for every year, the probability that year is in wet part of cycle, and complementary probability year is in dry part of cycle
Year 0: seem to be in the wet period now, 100% wet, 0% dry
Year 25: between 0 and 50, chose 80% wet, 20% dry
Year 50: far enough in the future that we can’t make any statement about which part of the cycle it might be, so steady-state probability of 65% wet, 35% dry (following ratio in observed record)
Choosing P[wet] and P[dry] for future years