## Slide 1: Mixed Populations
Flood Frequency Analysis PROSPECT Course
May 2024
Avital Breverman, P.E.
Some slides borrowed from Greg Karlovits and Mike Bartles
US Army Corps of Engineers
Hydrologic Engineering Center

## Slide 2: Outline
Why mixed populations?
What are mixed populations?
How do we model mixed populations?
Challenges
Who is working on mixed populations?
Goal: Take steps toward “homogenizing” flood series and frequency analyses

## Slide 3: Activity Time
Open HEC-SSP and start a new project
Import annual peak flows from one of the following gages:
  Pembina River at Neche, ND (05100000)
  Merced River at Happy Isles Bridge near Yosemite, CA (11264500)
  East Branch Delaware River at Margaretville, NY (1413500)
Right click on the dataset and select the Year-Over-Year Plot
Question: What observations can you make about the causes and seasonality of floods at this site?

## Slide 4
Notes: Pembina:
  The vast majority of floods occur in the early spring (March – April) but vary a lot in magnitude
  There are less annual peak floods in the summer and none in the fall and winter month
Merced:
  The vast majority of floods occur in the late spring/early summer months and tend to be smaller in magnitude
  There are a few, larger floods that occur in the November – February time period
  There are no floods in the summer through early fall months
East Branch Delaware
  Floods occur almost any time of year
  The largest concentration of floods occurs in the springtime
  The summer and fall floods can be significantly larger than springtime floods
You may have guessed that the seasonality of flood peaks is a good indicator of different flood mechanisms

## Slide 5: Why do we need to consider mixed populations?

## Slide 6: Is this a population or a sample?
Notes: In flood frequency, we are typically concerned with the annual peak flows at a gage site.
The annual peak flows at a site is a sample of all possible annual peak flows at that location.
The population is all possible annual peak flows at a site.

## Slide 7: Populations vs. Samples
Notes: The sample is the set of observed values (e.g. annual peak flows at a gaging site).
The sample that we work with is one possible subset from the population.

## Slide 8: Populations vs. Samples
Population
Entire group you want to draw conclusions about
May be unknowable
Parameter
  Example: all annual maximum flows on the Mississippi River at Vicksburg
Sample
Part or subset of the population
Data you have or can collect
Statistic
  Example: annual maximum flow observations on USGS/NWIS
Notes: The distinction between populations and samples is crucial.
Often, samples are what you have, and populations are what you want to know.
The population is the entire group that you want to answer questions about.
However, it may be unknowable.
An example of the difference is on the Mississippi River at Vicksburg, Mississippi.
There exists some population of all annual maximum flows on the Miss at Vicksburg, but it’s an unknowable collection of flows because we can’t observe it forever.
We only have a sample of annual maximum flows through the National Water Information System (NWIS) hosted by the USGS.
Even though we want to answer questions about all the annual maximum flows, we only have a limited sample to work with.
What you are often doing is taking a sample, which is a part or a subset of that population, and using the statistics of that sample to estimate quantities in the population, which are called parameters.

## Slide 9: Assumptions
Sample is representative
  Not always easy to determine
Observations are IID
  Independent
  Identically-distributed
Ω
S
Notes: When we use the sample to make inferences about the population, we are making a few assumptions.
The most important one is that the sample we have is representative of the population.
In some circumstances it can be difficult to ascertain whether the sample is representative or not because the population is completely unknowable.
For surveys, where people are polled for their opinions, the sample can be checked for representation by comparing the demographics of the respondents in the sample to the general population demographics to see how representative a sample is.
For streamflow, if we have a limited record of flows, we would have to look at other variables such as climate to tell us if the period containing our sample is a good representation of the entire population.
The other major assumptions fall under the IID acronym, which stands for independent and identically distributed.
These assumptions have to do with the way that the observations that make up the sample were taken.
We want the observations to be independent of one another – that is, that they are not dependent on each other in some way.
We also want them to be identically-distributed, which is similar in nature to the representative sample assumption.
Think of identical distribution as the assumption that the samples come from the same population.

## Slide 10: Independence
Serial (in)dependence?
Hydrologic processes have long memories
“Overcount” certain ranges of observation
Notes: Sequent observations in time are likely to have a lot in common.
This occurrence is referred to as “serial dependence,” and in hydrology and other geosciences the occurrence of long “memory” of a system is referred to as the Hurst Phenomenon.
What happens is that in a finite record, depending on the strength of the serial dependence, is that our observations may not be truly representative of the full population, instead it is clustered to smaller regions of the population due to the slow evolution of the system in time.

## Slide 11: Independence
Generally safe by using annual maximum series
Consequence may be small
  Depends on strength of serial dependence
  Depends on the sample size
Notes: Recall that we use the AMS to model floods, primarily this is so we can make sure that the observations are sufficiently independent.
By breaking apart our record at the water year, we generally are able to take one flood per year that is far enough from the last flood that they are functionally independent.
That’s not always true, such as the site shown in the image. WY 1986 and 1987 annual peak flow events occurred 5 days apart, right around the October 1 WY demarcation.
Check your data!
With partial duration series (PDS) we can include more observations per year but have to be particularly careful that they are independent of each other.
AMS makes this easier but is made of fewer observations and some of these observations may not truly be floods.
Samples with high serial dependence may not represent the whole population well.
We can extract samples with smaller serial dependence, but very small sample sizes may have the same problem.
This comes up in volume frequency analyses that are concerned with longer durations (e.g., 60, 90, 120, 180 days)

## Slide 12: Identical Distribution
A single distribution can be used to model the values
But are all floods at a site from the same population?
Just because a flow is an annual maximum, does not guarantee it was created the same way as the others
Notes: This is the question we’re really getting at.
Nature isn’t on some sort of schedule – it doesn’t drop one flood in a watershed per year, pulled from the distribution of annual maximum floods.
Often, many physical processes have to occur together in order to create the largest flood in a year.
If a river discharge is the largest in a year, it is not guaranteed to be caused by the same thing as the largest in other years.
Orestimba Creek (one of those pathological examples) has 12 years with no flow at all, thus, 0 is the annual maximum.
There are also years that very much do not look like the rest.
Klemes, V., 1986, Dilettantism in hydrology; Transition or destiny?: Water Resources Research, v. 22, no. 9, p. 177S–188S.
“For it is by no means hydrologically obvious why the regime of the highest floods should be affected by the regime of flows in years when no floods occur, why the probability of a severe storm hitting this basin should depend on the accumulation of snow in the few driest winters, why the return period of a given heavy rain should be by an order of magnitude different depending, say, on slight temperature fluctuations during the melting seasons of a couple of years (p. 183S).”

## Slide 13
Population A
Sample
Observation
Population B
Observation
Inference?
Notes: When the sample contains observations from multiple populations, it may not be clear which population each sample value comes from.
If it’s assumed that the sample comes from a single population when there are in fact multiple populations being sampled, the sample no longer meets the ID assumption.
Here is an example of a mixture. Imagine you want to know what the distribution of the height of adults is. You take a sample of 200 adults and look at the distribution of the sample. Is this sample from a single population? At first blush this seems reasonable – we are sampling adult humans which could be thought of as one population. One issue is that the distribution of the height of females and males is likely to be pretty different (the average female in the US is 5’-4” and male 5’-9”). If you look at the sample values of just females and just males (assuming you have recorded this information) you can identify the impact of a mixture on your sample. However if the only value you wrote down is the height, then you may not be able to evaluate the impact of the mixture.
Streamflow is similar. If your flows are caused by different things, for example snow floods and rain floods, floods of each type are likely to have different distributions.
Recording only the flow values means that we can’t evaluate the impact of this mixture without extra work.

## Slide 14: Why Do We Care?
Violation of IID assumption
Trends
Regionalization
Prediction of rare events
Better modeling improves investment decisions!
?
Notes: Beyond federal guidance, consideration of mixed populations has important implications.
Most importantly, at site where we know floods are causal by different processes, we are violating the IID assumption (specifically, the identically distributed portion) by fitting a single probability distribution (i.e. statistical model) to flood peaks.
  Can result in very very positive skew values
Investigating trends in precipitation, floods, and the response of floods to changes in precipitation suggests that separating storms and floods by causal mechanism is important.
In hydrology, we often trade space for time since measurement records at a single location are often short. We aggregate or pool this data using regionalization. The index flood procedure is one example of regionalization wrt floods. Regionalizing is predicated on the assumption that regions or samples are similar so regionalizing by flood type is more defensible.
The impact of mixed populations is most profound at the upper (righthand) tail of the distribution. This where design events live.
And this is also where our largest investment in infrastructure occurs – rare events.

## Slide 15: What are mixed populations?

## Slide 16: Mixed Populations
Some locations unfortunate (or lucky?) enough to have multiple causes for flooding
  Makes the hydrology interesting!
What causes mixed populations?
  Meteorology
  Watershed Processes
  Disturbance
Notes: In some locations, the meteorology can create several kinds of flood hazards.
What are some properties of watersheds that may make it that floods occur in different ways which makes it more challenging to still assume IID for an AMS?

## Slide 17: Some Warnings
Day of year/season is a consequence, not a driver!
Regional skew is almost always developed from mixed flood series
Notes: Floods do not occur because the date happens to be May 15.
They occur because of snowmelt, prolonged precipitation on ground with high soil moisture content, hurricanes, etc.
Flood types should be assigned based on physical processes, not calendar convenience.
In some areas, the flood causal mechanisms might align well with day of year or season. But don’t make this assumption without investigation!
Regional skew studies almost always used mixed flood series, that is flood series that are not separated by causal mechanism (or even by seasons).
These regional skew values should not be used with individual flood type subsets

## Slide 18: Some Warnings
“Hydrologically reasonable”
“Flooding in some watersheds is caused by different types of meteorological events associated with distinct physical processes.”
Notes: See the Mixed Populations section of Bulletin 17C

## Slide 19: Watershed Processes
Snowmelt
Rain-on-snow
Saturation-excess runoff
  Antecedent soil moisture
  Frozen ground
Ice jams
HELP
Cahill (2023)
Notes: The falling precipitation itself may not cause floods.
Rather, combinations of solid water on the ground (in the form of snow or ice) and falling precipitation may be the cause.
Saturation-excess runoff occurs when the ground is saturated and cannot infiltrate any more precipitation.
Top image shows ice jams along the Yellowstone River in Glendive, MT. Horse was carried 35 miles in 2 days on a block of ice!
Multiple mechanisms can occur within a single watershed (e.g., the Columbia River)
  Image credit to Ryan Cahill (NWP)
  Higher elevation areas (Canada, Cascades) accumulate significant snowpack
  Precipitation typically falls as rain in lower elevation portions and causes limited flooding
  Warmer years: shallower snowpack, precipitation falls as rain rather than as snow, winter flooding
  Cold, wet years: deep snowpack, spring snowmelt flooding
  Occasionally, a slow-melting snowpack meeting a warm, wet springtime storm will result in the dreaded rain-on-snow flooding which has water from both sources.

## Slide 20: Meteorological Scale
    Climatic cycles
    Synoptic scale
      Tropical cyclones
      Mid-latitude cyclones
    Mesoscale
      Squalls
      Mesoscale convective systems)
    Local scale
      Thunderstorm
Notes: Differing scales of meteorology can dominate the precipitation mechanism.
Mesoscale meteorology can cause extremely heavy rainfall in small areas, largely driven by intense convective activity, while synoptic scale meteorology can affect much larger areas.
Much of the middle of the country (east of 100°W generally) has precipitation driven by more than one scale.
Some examples you’ve probably heard of:
  Hurricanes are tropical cyclones that occur in the Atlantic Ocean or the northern Pacific Ocean
  Nor’easters are a type of extratropical/mid-latitude cyclone
  Mid-latitude cyclones are characterized by rapid changes in temperature along fronts
  Lake effect snow, which occurs in the Great Lakes region, is an example of mesoscale to synoptic scale meteorology
  Thunderstorm complexes act as a system (Mesoscale Convective Complexes)

## Slide 21: Moisture Source
Tropical cyclone
Atmospheric River
Notes: Atmospheric rivers are caused by moisture transported from the tropics to poles
Tropical cyclones are characterized by low pressure centers and in the United States, these events originate in the western North Atlantic Ocean, the Gulf of Mexico, and the Caribbean Sea and to a lesser extend, the eastern North Pacific Ocean.
The tropical nature of Hurricane Harvey (plus the additional synoptic complexities) made the extreme floods in Houston possible.
Notice the stationary front north of Houston.

## Slide 22: Climatic Cycles
El Niño
La Niña
Pacific
Decadal
Oscillation
Atlantic
Multidecadal
Oscillation
North Pacific
Oscillation
Notes: https://storymaps.arcgis.com/stories/d62f89509b504633a2c7516ab12d7767
https://oceanservice.noaa.gov/facts/ninonina.html
Long-period climatic cycles, such as the El Niño-Southern Oscillation (ENSO) and Pacific Decadal Oscillation, shown here, change continental-scale meteorology depending on their phase.
Many cycles have phases measured by sea surface temperatures (SST) in particular patches of ocean.
ENSO warm phase = La Niña
ENSO cool phase = El Niño
Neutral phase
Since these cycles have long periods (e.g. ENSO typically 1-5 years, or PDO on the scale of multiple decades) several years in a row may fall into the same sort of cycle, resulting in several dry or wet years in a row. The effects can add up, and also affects our previous assumption of independence.

## Slide 23: Wildfire
Notes: Vegetation and soil absorb rainwater.
Fire destroys vegetation and creates a hydrophobic (water-repelling) surface layer which reduces the infiltration capacity of the land.
Watersheds experience increased runoff response/flood risk post-fire.
  A given storm depth will result in increased runoff post-fire compared to pre-fire.
Land surface recovers post-fire but that can take a few to many years. Wetter climates tend to recover more quickly than arid climates since more rain and higher intensity rain erodes the hydrophobic soil layer.
Division of floods into pre-fire and post-fire (until recovery occurs).

## Slide 24: Multiple Events
Sequencing of events may cause the biggest floods
Frequency of tropical storm counts in Lake Okeechobee watershed:
  Tropical Storms
Notes: Tropical storms per year in the Lake Okeechobee watershed, Florida.
The Lake’s level is sensitive to large volumes of inflow accumulated over long periods, and the biggest source of heavy rainfall is tropical storms.
The window is fairly large, so the possibility of multiple events bringing heavy rain is high.

## Slide 25: Identifying Mixed Populations
Streamflow data by itself usually not enough information
Need additional data to identify causal mechanism
Meteorological data most important
Sometimes simple rules work well

## Slide 26: Nonstationarity
Both mixed populations and nonstationarity deal with differences in the properties of floods
Causes:
  Urbanization
  Land use changes
  Climate change
Non-stationarity: rate of flood events per year changes
Mixed populations: rate of flood events per year does not change
Notes: In a mixed population paradigm, each source of floods exists in varying numbers every year.
In any year a sample of floods can contain 0 to many floods from each mechanism.
However in a nonstationarity paradigm, we are generally seeing the rate of flood events per year change (increase/decrease) in one direction.
This means information from past floods is no longer relevant to the future.
In mixed populations, we still assume future floods will look like the past, even if there are multiple sources.

## Slide 27: How do we model mixed populations?

## Slide 28: A Model for Mixed Populations
Determining the dominant flood mechanisms/types
Identifying the annual maximum series for each type
Fitting a distribution to each AMS
Probability of union!
Notes: EM 1110-2-1415 Hydrologic Frequency Analysis provides guidance on modeling mixed populations.
We need to fit distributions to each flood type sample separately before we can combine to produce a single frequency curve.
We use the probability of union (remember that from set theory) to combine the distributions.

## Slide 29: Probability of Union
What is the probability that a flood of magnitude X is exceeded by type 1 or type 2?
+ -
+
-
=

## Slide 30: Probability of Union
If C = max(A, B), then:
A: largest rain flood in a year
B: largest snow flood in a year
C is the larger of the two
Thus, C is the annual maximum
CDF
Non-exceedance
probability
Any flood
magnitude
Notes: Reference: EM 1110-2-1415 Hydrologic Frequency Analysis

## Slide 31
Flood Type B
Flood Type A
Mixed
Notes: Flood mechanism A has a higher mean, lower variance and lower skewness than flood mechanism B.
Nearly every flood in the record for A is larger than for B, except for the two largest on record, which are both flood B.
How do the individual mechanisms look compared to just doing the AMS without breaking it down? If you extrapolate the combined curve, is it capturing the behavior of the largest floods well?

## Slide 32
1 -
For 2 flood types:
+ -
Oopsies…
Notes: What is the probability of a rain flood exceeding 10,000 cfs?
What is the probability of snow flood exceeding 10,000 cfs?
What is the probability of either a rain flood or a snow flood exceeding 10,000 cfs (combined probability)?
Rain flood is shown in green, snow flood is shown in blue, the combined curve is shown by a red dashed line, and the mixed (i.e. no separation) curve is shown in gray
Notice that the curves cross at AEP ~ 0.1 (1/10 annual exceedance probability)
The equations shown are for exceedance probability

## Slide 33: Challenges

## Slide 34: Defining the Mixed Populations
What flood types are worth considering?
How do we attribute a flood event to a type?
Coincident causal mechanisms
WY 1949
WY 1979
WY 1951
WY 1993
WY 1987
WY 2011
Notes: Each flood is unique but we have to strike a balance between (1) improving the performance of our statistical model and (2) dividing floods into too many subsets
We want to divide floods when the difference in the frequency-magnitude relationship is meaningful!
If the distribution parameters of two flood types are the same/similar, then it’s not worth dividing those flood types.
Attribution of flood events to causal mechanisms
  We typically know what physical processes caused the top 5-10 floods at a site
  What is a relevant antecedent time period?
  What is a relevant spatial window (larger for synoptic scale, smaller for local events)?
  Coincident causal mechanisms may mean that flood(s) do not fit neatly into one type
  Manual vs. automated approaches
  What data do we use? Snow, temperature, surface analysis maps, etc.
  There is only 1 USGS peak flow qualification code that describes flood causal mechanisms

## Slide 35: Data Intensive
Gridded Data Sources
Reanalysis products
Variables to consider:
  Precipitation
  Temperature
  Snow water equivalent
  Soil moisture
  Discrete storm tracks
  Ice jams
  Geopotential heights
  Mean sea level pressure
  Integrated vapor transport
Notes: Here is a list of some useful spatially distributed/gridded products that can be used for understanding and classifying flood types.
The first link is an HEC-HMS tutorial & guides page on gridded data sources.
This table is geared towards hydrologic modeling applications so the products have relatively fine spatial and temporal resolution.
In addition, the products generally provide precipitation, temperature, and snow water equivalent (SWE) estimates.
You may need other variables to help with flood typing and you may not need products with as fine spatial resolution.
Reanalysis products often have longer periods of availability that those listed in the Gridded Data Sources table.
Reanalysis products are produced through a process known as data assimilation, which combines observations and weather forecasts.

## Slide 36: Fitting Distributions
Annual Non-hurricane Events 1929-85
Computed Frequency Curves, Non-hurricane Series
Annual Hurricane Events, 1929-85
Graphical Frequency Curve, Hurricane Series
103
104
105
106
Flow (cfs)
% Chance Exceedance
99.99
99.9
99
90
50
10
1
0.1
0.01
What do you do with flood subsets?
What about rare events that drive the right tail of the probability distribution?
What about flood types that do not occur every year?
Notes: How do you think an LP3 would fit to this kind of data?
How do we implement a B17C analysis with a divided flood record?
What about floods caused by extreme events (atmospheric rivers, tropical cyclones, others)?
We may not have a large enough flood sample to reasonably fit an analytical probability distribution to these floods, but they are often the largest in the flood record.
The figure shows a gage in Pennsylvania. Four of the 8 largest floods were caused by tropical cyclones but the gage record only includes these 4 tropical cyclone-driven floods.

## Slide 37: Samples
Split the AMS by flood type
  Pros:
    Easiest
  Cons:
    Small sample sizes
    Egregious number of periods with “missing” data
Original AMS
Rain-only Events
Snowmelt Events
Notes: How do we develop samples for each flood types?
There’s at least 3 approaches
The first is to split your annual maximum series by flood types
This poses some problems
If you have an 80 year POR with 80 annual maxima, if you split the record by two different flood types, you wind up with two much shorter records
Using the split AMS in a Bulletin 17C approach results in many, many perception threshold (far too many)

## Slide 38: Samples
Develop an annual maximum series for each flood type
  Pros:
    Larger sample sizes (N years  N events in each flood type) except that…
  Cons:
    Not all flood types occur every year (maybe this is a pro?)
    More time-consuming
125 years
~10-15 tropical storm events
Notes: The second approach is the one recommended in Bulletin 17C and EM 1110-2-1415: develop an AMS for each flood type
This results in N*x events, where N is the number of years of record and x is the number of flood types
However, not all flood types occur every year!
  Tropical storms
  Snowmelt (in some locations)
  Rain-on-snow (in some locations)
Some flood types occur infrequently but produce the largest events at a site

## Slide 39: Samples
Use a peaks over threshold approach
u
excess
x – u
  Cons:
    Selecting a threshold is subjective
    Ensuring independence requires some effort
    We rarely have continuous sub-daily time series
    Implementation in HEC-SSP is in progress
    No federal guidance (maybe this is a pro?)
  Pros:
    Larger sample sizes
    Eliminates the need for perception thresholds when dividing the AMS by flood type
    Only concerned with actual floods
Notes: The third approach is to use a peaks over threshold approach to develop a partial duration series
Greg will talk about PDS tomorrow

## Slide 40: Who is working on mixed populations? (State of Research)

## Slide 41
Bulletin 17B (1982)
Notes: Identification and treatment of mixed populations/distributions was included in the Future Studies section of Bulletin 17B (1982)

## Slide 42
More supporting details, but no recipe
Also identifies potential issues with independence (serial correlation)
Familiar language
Bulletin 17C (2019)
Notes: And again in Bulletin 17C (2019)
Bulletin 17C does include more supporting details, such as referenced mixed population studies, but still no recipe

## Slide 43
Time to face the music…
The Federal Government

## Slide 44
Federal Inter-agency Work Unit
USGS and USACE collaboration supporting FEMA Future of Flood Risk Data (FFRD) initiative
FY 2023-2027
Four priorities:
  Identify improved flood frequency analysis methods for mixed populations
  Develop automated methods for flood type classification
  Account for future changes in causal mechanisms
  Prescribe a plan for national implementation

## Slide 45
End Goals
Provide algorithm/criteria for separating records
Integration with National Water Information System (NWIS)
  Inclusion of type-codes for each USGS site
Detailed procedures for modeling mixed populations for any site
Water Year | Streamflow (cfs) | Qualification Code | Type Code
1851 | 65,000 | 2,7,Bd | A
… |  |  | 
2016 | 81,600 |  | C
2017 | 25,700 |  | A
2018 | 61,900 |  | C
2019 | 61,800 |  | A
2020 | 48,100 |  | B
2021 | 23,700 |  | C

## Slide 46
Status
Literature review
Pilot region selection
Data source identification
Currently (FY24):
  Manual flood typing to inform…
  Automated flood typing procedures
  Statistical approaches to mixed population analysis
  Gridded data validation

## Slide 47: Questions?