## Slide 1: Monte Carlo Simulation
Hydrologic Engineering Center
Beth Faber
Statistical Methods 2023
Lecture 7

## Slide 2: Monte Carlo Simulation/Analysis
“Stochastic techniques” based on the use of random numbers to evaluate questions and problems, generally by simulating random occurrences
A lot of probability theory was developed around gambling … hence the name Monte Carlo!
First published by this name in 1949
  Metropolis, Nicholas and Stanislaw Ulam (1949). The Monte Carlo method, Journal of the American Statistical Association, 44 (247), 335-341.
Notes: Using random numbers to do things…. Explore probability, compute functions of random numbers, integrate, etc

## Slide 3: Monte Carlo Simulation/Analysis
Allows us to explore many possible outcomes, having seen only a few, if we can describe the probabilistic structure of the process.
Examine error in estimates by creating many small samples of a known distribution and estimating parameters (introductory lecture)
Compute a function of a random variable: Replace a RV with a large sample from its probability distribution (ie, randomly generated values), and use each member of the sample in computation.
  It is easier to do math on a member of a sample than on a distribution,
  Can perform deterministic analysis on sample member, then recombine the resulting sample into a new probability distribution
  Can evaluate any number of input variables without added complexity

## Slide 4: Outline
Introduction
Example: Estimate of p
Theory of Monte Carlo Simulation
  what we’re doing
  how we generate samples
  convergence
Workshop / Demo
Applications
  Flood Risk Analysis (HEC-WAT/FRA)
  Stochastic Streamflow Generation for Water Supply
  Uncertainty Analysis (next lecture)

## Slide 5: Buffon’s Needle Problem
Method to estimate p
A needle of length l is dropped at random on a horizontal surface with parallel lines a distance d > l apart
What is the probability that the needle will cross one of the lines?
first stated in 1777
2 variables, A and 
requirement for cross: A < l sin…
from trig and calculus
Notes: Monte Carlo analysis includes activities that use random outcomes to solve problems and answer questions.
This is an example that allows us to use a random experiment to solve a problem. In this case, it will allow us to estimate the value of pi by performing the experiment described in Buffon’s Needle Problem.
If a needle were to be dropped between 2 drawn lines, the geometry of the problem tells us that the probability of the needle crossing one of the lines, given the dimensions shown, is 2*l / d*pi.

## Slide 6: Buffon’s Needle Problem
Can approximate this probability by repeatedly dropping the needle onto the surface and counting the number of times it crosses a line relative frequency
  where: M = number of times needle crosses a line
  n = number of times needle is dropped
Therefore,
And so This is an estimator of p
Notes: We can also estimate the probability of the needle crossing the line by experiment, actually dropping the needle on a page with 2 lines drawn. Thus, we can solve the original equation for pi, and estimate its value.

## Slide 7: Buffon’s Needle Problem
In 1864, an injured sea captain tried this experiment during his convalescence…
We see only Captain Fox’s final results, but if we could plot the estimate of p against number of trials, we’d see it improve as he continued
pi = 3.14159265…
search “buffon’s needle problem” on the web to find some neat simulations
Notes: Nearly 100 years after the problem was first described, the diary of an injured sea captain tells of his experience with trying this experiment.
He first tried 500 needle drops with a 3 inch needle and lines 4 inches apart. He determined that his drops were not completely random because of the limitation of the angle he could turn his hand. So he tried the experiment again placing the paper with the lines on a rotating surface (like a lazy susan). The experiment done this way, with outcomes that were more random, gave a better estimate of pi.
The final version of the experiment used a longer needle and lines closer together, so a single drop could have the needle cross twice, once or not at all (with the required changes to the geometry and the equation for pi). This version provided the best estimate of pi.

## Slide 8: Another way to estimate p
Consider a unit square,
area = r * r = 1 * 1 = 1
Inscribe a quarter of a unit circle inside,
area = pr2/4 = p*12/4 = p/4
The ratio of the area of the circle to the area of the square is
ratio = p/4 / 1 = p/4
so p = ratio-of-areas * 4
r = 1
r = 1
area = p/4
area = 1
If randomly dropped grains of sand are equally likely to fall anywhere in the square, occurrence of grains in the ¼ circle is proportional to the area of the ¼ circle
Notes: Here’s another, simpler way to estimate pi, using a quarter unit circle inscribed in a unit square. With side length = 1, the area of the square is 1. With radius 1, the area of the quarter circle is pi/4. The ratio of these areas is pi/4.
The ratio of the areas can also be estimated by counting how many randomly dropped grains of sand fall in the circle but not the square. Thus, we can again solve for pi and estimate it’s value with a random experiment.

## Slide 9: Another way to estimate p
Set the shapes on a Cartesian coordinate system
Generate pairs of random U[0,1] values, one for each axis x and y, to produce randomly dropped points
If y ≤ sqrt(1 – x2), then the point is in the quarter circle
x = 0.14, y = 0.89
x = 0.91, y = 0.78
x = 0.40, y = 0.71
x = 0.61, y = 0.28
x = 0.32, y = 0.19
with 1,000 random pairs, 79% are in quarter circle, so
p = 0.79*4 = 3.16
^
X
Y
Notes: In order to avoid actually dropping grains of sand, we describe the problem using a Cartesian coordinate system and generating a pair of pseudorandom U[0,1] values to represent the x and y locations of a “random” drop. All values fall in the square, and values for which y < sqrt (1-x^2) are also in the circle.
An experiment of 1000 random “drops” showed 79% within the quarter circle, estimating pi as 3.16.

## Slide 10: Repeating the Experiment….
The experiment with 1,000 points was repeated 100 times.
Then, an experiment with 10,000 points was repeated 100 times…
Note from the histogram the improved accuracy with 10,000 points
But Buffon’s method was
better!
Notes: These histograms show repeated trials of the entire experiment, with the blue showing 1000 points, and the pink showing 10,000 points. This shows the uncertainty in the estimate of pi, assuming that we didn’t already know the true value.
10,000 points performs notably better than 1,000 points, but not as well as Buffon’s problem.

## Slide 11: Outline
Introduction
Example: Estimate of p
Theory of Monte Carlo Simulation
  what we’re doing
  how we generate samples
  convergence
Workshop!
Applications
  Flood Risk Analysis (HEC-WAT/FRA)
  Stochastic Streamflow Generation for Water Supply
  Uncertainty Analysis (next lecture)

## Slide 12: The Basic Idea
We’re interested in a variable Y (damage) which is a complex function of variable X (flow) ie, Y = g(X)
X is a random variable, described
by a probability distribution…
So Y is also a random variable
Can determine the distribution of
Y analytically…
…or can use Monte Carlo Simulation
Notes: We have a variable of interest, Y, that is a complex function of another variable we know more about, X. But X is a random variable. Therefore Y is also a random variable. It can be difficult to route a probability distribution through a complex function g(X) to solve this problem analytically, so we can instead solve it with Monte Carlo Simulation.

## Slide 13: The Monte Carlo Concept…
Replace the probability distribution of random variable X (flow) with a large random sample of values from that distribution
For each member of the sample, compute damage Y = g(X)
This process creates a large sample of variable Y (damage)
Value
of X
Relative Frequency
histogram
PDF of X
Notes: The pink PDF is the distribution of X, and the pink histogram is the large random sample of values of X meant to replace the distribution. The complex function Y = g(X) is performed on every sample member, producing a sample of Y.

## Slide 14: The Monte Carlo Concept…
From the generated sample of Y (damage), infer the probability distribution of Y
NOTE: Monte Carlo adds no information, it just integrates the random variables with the specified distributions
Value
Relative Frequency
of Y
distribution of Y
Notes: The orange histogram is the sample of Y values produced by evaluating Y = g(X) for every member of X, and the orange PDF is the distribution of Y inferred by a statistical analysis of the sample of Y.
Note, Monte Carlo simulation is just processing the random values and the relationship defined between X and Y. It adds no information to the problem.

## Slide 15: with Multiple Input Variables…
When variable Y (damage) is a function of 2 random variables, X and Z i.e., Y = h(X, Z)
  e.g. flow and reservoir level…
    Create a random sample of variable X (flow)
    Create a random sample of variable Z (reservoir level)
    Compute Y = h(X, Z) for every pair of X and Z
    …still end with a large random sample of variable Y(damage)
  if X and Z are correlated, can use correlated random sampling
Notes: We are not limited to a single input random variable, or even a single output random variable. Here is a case where the Y variable is based on 2 input random variables, X and Z. Large random samples are created for both X and Z, and with each pair of values (one member from each sample), Y = h(X,Z) is computed, with one member of Y for every pair X and Z. A large sample of Y is still created, no matter how many input random variables were involved, and thus the probability distribution of Y estimated.
In this case, flood damage may be dependent on both flow, and the starting pool level of an upstream reservoir that can intercept some of the flow.
If another variable W can be computed from X, Z and Y, a sample of W can also be developed in the same way (based on every triplet X, Y and Z), and a distribution of W estimated.
Note, the simplest case creates the random samples of X and Z independently. However, if there is a relationship between X and Z that must be maintained, correlated random sampling can be used to maintain a linear relationship.

## Slide 16: with Dependent Input Variables…
When variable Y (damage) is a function of dependent or conditional random variables:
  e.g. season, then flood event flow and reservoir level…
    Create a random sample of RV S (flood event date or season)
    For each event, the sampled date or season defines conditional distributions of X and Z for that event
    Create a random sample of X (flow) from g(X|S)
    Create a random sample of Z (reservoir level) from g(Z|S)
    Compute Y = h(S, X, Z) for every S, X and Z
    …still end with a large random sample of variable Y (damage)
Notes: We can also do Monte Carlo simulation with random variables whose distributions are dependent on other random variables, if we can describe the conditional probability distributions.
Here, we sample a flow, and also the date of the flood event. The probability distribution of the reservoir pool level is then conditional on the sampled date.
We still compute variable Y for each set of sample members, ending with a sample of Y and so a distribution of Y.

## Slide 17: Generating the Sample
How do we generate a random sample of values from a particular probability distribution?
First, switch from a PDF to a CDF, ie cumulative probability…
1
0
f(x)
F(x)
CDF:
F(x) = P[X<x]
Notes: We can generate a random sample from any probability distribution. In this class, we first did it by generating rolls of a 6-sided die. The first step is using the cumulative form of the probability distribution, the CDF.

## Slide 18: Monte Carlo Simulation
Generate pseudo-random values, Ui ~ Uniform[0,1]
  “random number generators” usually produce U[0,1]
Use Ui as the cumulative probability, and compute xi as the inverse of the CDF of X
A frequency analysis on the sample xi provides the original probability distribution, ie P[X ≤ x]
Ui
X
F(X)
CDF, F(X)
xi
Ui = F(xi), xi = F-1(Ui)
Quantile function

## Slide 19: Monte Carlo Simulation
Generate pseudo-random values, Ui ~ Uniform[0,1]
  “random number generators” usually produce U[0,1]
Use Ui as the cumulative probability, and compute xi as the inverse of the CDF of X
A frequency analysis on the sample xi provides the original probability distribution, ie P[X ≤ x]
Ui
X
F(X)
CDF, F(X)
xi
Ui = F(xi), xi = F-1(Ui)
6-sided die example

## Slide 20: How Large a Sample?
We know the random sample is large enough if can reproduce correct distribution parameters with sample estimators, such as mean and standard deviation.
Accuracy of the MC increases as the size of the random sample increases, meaning the sample becomes more representative as it gets larger
Let’s try an experiment with generating a sample from a Standard Normal Distribution
Notes: Monte Carlo simulation does not add information. But it can lead to error if the samples used are not large enough to represent the distributions they are replacing.

## Slide 21: Sample from Standard Normal Distribution N(0,1)
N(m,s)
sample size = 25
Notes: This is a 25-member sample from the standard Normal distribution. The table has a column of U[0,1], and another column of the subsequent N[0,1] that results. Two values are shown as reflected through the standard Normal CDF.

## Slide 22: Histogram (Class Interval Analysis)
Mean = -0.04
StDev = 0.74
Skew = 0.78
Was the sample size adequate?
sample size = 25
Notes: This is the histogram of the 25-member sample, plotted in front of the original PDF we’re attempting to replace. The histogram doesn’t replace the PDF well.
The sample mean = -0.4 and sample standard deviation is 0.74. Population values were mean = 0 and standard deviation = 1. So the distribution parameters are not well-maintained.

## Slide 23
sample size = 100
sample size = 10,000
sample size = 1000
input sample is large enough when it adequately reproduces the input probability distribution
output sample is large enough when statistics of interest stabilize, stop changing with new sample member within d
How large a sample?
or, how many iterations?
Convergence!
Notes: This slide shows samples of 100, 1000 and 10000, moving left to right. Note that 100 captures the middle of the distribution accurately, and gives some idea of spread. 1000 captures a good representation of spread, and gives an idea of the distribution tails. 10000 captures the tails fairly well. The sample size needed really depends on what aspects of the distribution are relevant.
If we change our attention to the output sample (which is of course the same size as the input sample), we can base the sample size on the statistics of interest in the analysis. If we compute the statistic of interest with each new sample member (rather than choosing the sample size in advance), we can stop adding member when the statistic stops changing within some specified delta. The point at which the change falls below delta is called convergence.

## Slide 24: How many is enough? Convergence
We continue creating and evaluating new random sample members until the statistic of interest stabilizes
  average damage
  1% exceedance damage, …
100 members
100 members
average of damage
1% exceedance damage
avg
1%
Notes: This shows two different values of the output distribution we might be interested in – the mean and a 1% exceedance quantile.
Repeatedly recomputing the output sample mean on the left and 1% exceedance value on the right, we can see that mean is stable in the first 100 sample members, but the 1% quantile is not. (NOTE, the vertical axes are not the same.)
It is not surprising that the estimate of a value exceeded in every 100 values has not stabilized within only 100 values….

## Slide 25: How many is enough? Convergence
average of damage
1% exceedance damage
avg
1%
1000 members
1000 members
We continue creating and evaluating new random sample members until the statistic of interest stabilizes
  average damage
  1% exceedance damage, …
Notes: This shows two different values of the output distribution we might be interested in – the mean and a 1% exceedance quantile.
Repeatedly recomputing the output sample mean on the left and 1% exceedance value on the right, we can see that mean is stable in the first 100 sample members, but the 1% quantile is not. (NOTE, the vertical axes are not the same.)
It is not surprising that the estimate of a value exceeded in every 100 values has not stabilized within only 100 values….

## Slide 26: Outline
Introduction
Example: Estimate of p
Theory of Monte Carlo Simulation
  what we’re doing
  how we generate samples
  convergence
Workshop! / Demo
Applications
  Flood Risk Analysis (HEC-WAT/FRA)
  Stochastic Streamflow Generation for Water Supply
  Uncertainty Analysis (next lecture)

## Slide 27: Cell Phone Experiment
3 cell phone plans with increasing allotted minutes, and decreasing cost for exceeding allotted minutes
You have an estimate of family’s monthly minute usage based on historical average
  Plan A would seem best
Given uncertainty in the estimate of monthly minutes, which plan is best…?
see spreadsheet…

## Slide 28: Game Show Example
Game Show!
There are 3 doors, with a prize behind one of them
You are asked to choose a door
After your choice, the host opens another door, and you see there is no prize behind it
You are given another choice:
  Stay with your chosen door, OR
  Switch to the other unopened door
What should you do?
see spreadsheet…

## Slide 29
1
2
3
1
2
3
1
2
3
Better to stay with the original choice
Better to switch
Better to switch
Host shows either door 1 or door 3
Player can stay or switch to the other
Host must show door 1
Player can stay or switch to door 3
Host must show door 3
Player can stay or switch to door 1
1
3

## Slide 30: How about a gambling example?
Let’s test a betting strategy for Roulette
38 numbers on the wheel: 0, 00, and 1 through 36
18 numbers are red, 18 numbers are black, and 0 and 00 are green
    Prob(red) = 18/38 Prob(each number) = 1/38
    Prob(black) = 18/38
    Prob(green) = 2/38
Strategy: always bet red, repeat bet if win, double previous bet if loose
see spreadsheet…

## Slide 31: Outline
Introduction
Example: Estimate of p
Theory of Monte Carlo Simulation
  what we’re doing
  how we generate samples
  convergence
Workshop / Demo
Applications
  Flood Risk Analysis (HEC-WAT/FRA)
  Stochastic Streamflow Generation for Water Supply
  Uncertainty Analysis (next lecture)

## Slide 32: Expected Annual flood Damage (EAD)
One metric for economic decisions on flood risk management is the expected value of annual flood damage
  the mean of the damage-frequency curve
Expected Annual Damage can be interpreted as the average annual damage over a very long period of time. This annualized value can be compared to an equivalent annual cost in cost/benefit analysis.
  benefits of project = EAD reduced

## Slide 33: Expected Annual Flood Damage
expected annual damage
EAD
Notes: Expected Annual Damage, or mean annual damage, can be thought of as the average damage over a long period of time. In this time series, there is rarely any damage at all. But if we average all of the zeroes along with the times there was some damage, we get the blue line. It’s a value that would probably never actually occur, but it is an annualized value.

## Slide 34: Computing EAD with summary curves
The traditional way of computing EAD was to condense the flood frequency information, the hydraulics, and the economics into summary relationships, and combine them.
flow-frequency curve
flow-stage rating curve
stage-damage function
The mean of the damage-frequency curve is the expected value of annual damage, or EAD.
combine to obtain a:
damage-frequency curve
Notes: One way to estimate a damage frequency curve is to start with a flow frequency curve, and transform it with summary relationships for flow versus stage and for stage versus damage. The resulting damage frequency curve rarely has any analytical form, but is a graphical frequency curve.

## Slide 35
Area = mean
Summary Curves for Frequency, Hydraulics and Economics
Economics
Stage (ft)
Damage ($)
Stage-Damage
Hydraulics
Stage (ft)
Flow (cfs)
Stage-Flow
Hydrology
Peak Flow (cfs)
Exceedance Prob
1
Flow-Frequency
0
summarizes the result of hydraulic modeling of the channel, overbanks, and interior
summarizes the aggregated result of structural inventory, including value and damage assessments, and the topography
Probability distribution of annual peak flow
1
2
3
CDF
PDF
Notes: The basic and derived evaluation relationships are shown in Figure 1. Concepts important to their construction are described below.
Stage-Damage Relationship: This is the economic counterpart to the stage-flow function and represents the damage which will occur for various river stages. Usually the damage represents an aggregate of the damage, which could occur some distance upstream and downstream from the specified location. It is usually developed from field damage surveys.
Stage-Flow Relationship: This is a basic hydraulic function that shows, for a specific location, the relationship between flow rate and stage. It is frequently referred to as a 'rating curve' and is normally derived from water surface profile computations.
Flow-Frequency Relationship: This defines the relationship between exceedance frequency and flow at a location. It is the basic function describing the probability nature of streamflow and is commonly determined from either statistical analysis of gaged flow data or through watershed model calculations.

## Slide 36
AREA = mean = expected annual damage, EAD
Peak Flow (cfs)
Exceedance Probability
1
0
Exceedance Probability
1
0
Stage (ft)
Flow (cfs)
Stage (ft)
Damage ($)
Damage ($)
Computing EAD with Summary Curves
p
p
Flow-Frequency Curve
captures year-to-year variability in flow
captures year-to-year variability in damage
CDF
CDF
1
2
3
Notes: Arranging the 3 summary relationships with their axes line up, we can see how they combine into a damage frequency curve.
One method of estimating the mean of a non-analytical probability distribution is computing the area below the CDF along the probability axis, similar to a probability weighted sum if the distribution were discrete. So, the mean of the damage frequency curve, the EAD, is estimated by the area in red.

## Slide 37
Peak Flow (cfs)
Exceedance Probability
1
0
Stage (ft)
Flow (cfs)
Stage (ft)
Damage ($)
Computing EAD with Monte Carlo Simulation
using an “event sampling” approach
choose random probability U[0,1]
to “generate” event
replace flow-frequency curve with a sample…
Damage(i)
One Event (sample member)
…end with a sample of damages
Damage ($)
Relative Frequency
CDF
Notes: We switch the problem to a Monte Carlo simulation by replacing the flow frequency curve by a large sample of values from it. This is called an “event sampling” approach. Reflecting through the other summary relationships produces a value of damage for each flow, ending in a sample of damage. The sample average is an estimate of the EAD.

## Slide 38: Replacing Flow-Frequency Curve with a Large Sample of Peak Flows
Annual Peak Flow (cfs)
annual peak flows, or annual max X-duration flows, 1000 events
each point is an “event”
PDF form
(histogram)
CDF form (frequency curve)
Notes: This image shows a 1000-member sample of flows, first as a histogram against the PDF, and then as a frequency plot against the frequency curve form of the CDF.

## Slide 39: From each flow, compute a damage, create a sample of damages
1000 event damages the average or mean of these is the EAD
PDF form
(histogram)
each point is an “event”
CDF form (frequency curve)
PDF form
(histogram)
Notes: Similarly, this slides shows the 1000 subsequent damages, as a histogram and as a frequency plot. The average of the 1000 values is the estimate of EAD.

## Slide 40
Peak Flow (cfs)
Exceedance Probability
1
0
Stage (ft)
Flow (cfs)
Stage (ft)
Damage ($)
Computing EAD with Monte Carlo Simulation
using an “event sampling” approach
choose random probability U[0,1]
to “generate” event
replace flow-frequency curve with a sample…
Damage(i)
One Event (sample member)
…end with a sample of damages
Damage ($)
Relative Frequency
CDF
Notes: We switch the problem to a Monte Carlo simulation by replacing the flow frequency curve by a large sample of values from it. This is called an “event sampling” approach. Reflecting through the other summary relationships produces a value of damage for each flow, ending in a sample of damage. The sample average is an estimate of the EAD.

## Slide 41
Damage ($)
Relative Frequency
Peak Flow (cfs)
Exceedance Probability
1
0
Reservoir Analysis
Channel Hydraulics
Levee Behavior
Spreading Model
Inundation Mapping
Structure Inventory
Damage to Structures
Damage(i)
One Event (sample member)
hydrographs
stage
damage
Using models rather than summary curves
Replace summary relationships with models
choose random probability U[0,1]
to “generate” event
replace flow-frequency curve with a sample…
…end with a sample of damages
CDF
Notes: We use the event sampling Monte Carlo approach to allow us to replace the simple summary relationships with more careful modeling of each generated flood event.
The sampled flow is turned into a hydrograph (based on a randomly chosen shape), and routed through a reservoir model (with a randomly chosen starting pool). It then goes through a channel model to see if stage exceeds a randomly chosen levee breach height, and a spreading model if breach occurs. Next, inundation is mapped and compared against a structure inventory to determine damage to structures.
The resulting sample of damages is more carefully formulated than the version that depended upon summary relationships.
When the system being modelled is a watershed, rather than a single index point like this, there are further benefits to this approach. Flows can be provided for various streams, and damage areas at confluences, that can be inundated by each reach, will show inundation by one side or the other or both at the appropriate frequencies. Another benefit is upstream levees. If a levee breaches, and thus decreases the flow volume below it, the lower system will show that lower flow against its levees and damage areas.

## Slide 42: Knowledge Uncertainty?
What we’ve looked at so far has used Monte Carlo simulation, but is still computing a best estimate of EAD (or of pool stage frequency)
  The MC sampling is only addressing variability in flood magnitude
It has not yet included uncertainty in the summary relationships, or in the model parameters
Notes: Thus far, replacing the frequency curve, and perhaps a reservoir starting pool frequency curve, have only captured natural variabilities that contribute to the damage frequency curve. Thus, we produce only one estimate of the damage frequency curve an its mean, the EAD.
However, we have a great deal of knowledge uncertainty about various aspects of the system such as model parameters and especially parameters of the flow frequency curve.

## Slide 43: Variability and Uncertainty
Natural Variability (Aleatory) = some variables are random and unpredictable by nature, and their values change with time (event to event) or in space
Knowledge Uncertainty (Epistemic) = some variables do not change with time or space, but we do not know their values accurately
Both variability and uncertainty
are described as random variables
by probability distributions
PDF
Notes: Reminder of the definitions.

## Slide 44: How do these affect EAD?
We estimate average damage (EAD) because the natural variability in occurrence of floods prevents us from knowing what future damages will be
Natural Variability: All random variables that vary event-to-event or vary spatially are part of the distribution of annual damage, and so in the mean damage
  flood magnitude, starting reservoir storage, bridge debris
annual damage PDF
mean = EAD
Notes: All natural variabilities must be incorporated into each estimate of the damage distribution and so the EAD.

## Slide 45: How do these affect EAD?
Knowledge Uncertainty: Watershed parameters that we do not know exactly, and modeling simplifications, introduce uncertainty into the damage
distribution, and so into the mean damage
  flood likelihood, hydraulic coefficients, foundation height
This uncertainty creates a probability distribution of EAD
EAD distribution
EAD distribution
annual damage PDFs
mean = EAD
Notes: Knowledge uncertainties make us uncertain about the damage distribution and the EAD, and are captured as spread in the estimate.

## Slide 46: We’re Interested in Uncertainty in EAD
histogram
estimated probability distribution
Notes: Rather than a single estimate of EAD, we are looking for a distribution of the uncertainty around the EAD, as shown in this histogram.

## Slide 47: How do we capture a distribution of uncertainty in EAD?
Nested Monte Carlo:
Sample instances of natural variabilities as flood events, with enough events to capture the distribution of damage
Sample instances of knowledge uncertainties in model parameters to get their impact on the damage distribution
inner loop A varies natural variabilities, computes EAD
A
B
outer loop B varies knowledge uncertainty, computes EAD distribution
1 outer loop B = a realization
HEC-WAT/FRA
Notes: The Monte Carlo simulation is performed as a nested loop, and natural variability and knowledge uncertainty are separated into different levels.
On the inside loop, enough flood events are simulated to replace the flow frequency curve and all other variables whose values change event to event.
Prior to performing the inside loop, a value is randomly sampled for each of the knowledge uncertainties. Those values populate the model parameters, and are held for all the events in the inside loop. This outer loop, is called a realization, and includes all the flood events of the inner loop.

## Slide 48
Exceedance Probability
1
0
Sampling Variability and Uncertainty
Corps of Engineers
IWR-HEC
Reservoir Analysis
Channel Hydraulics
Levee Behavior
Spreading Model
Inundation Mapping
Structure Inventory
Damage to Structures
Damage(i)
One Event: sample member i
hydrographs
stage
damage
Nested Monte Carlo Simulation
sample variabilities
sample new frequency curve (uncertainty)
sample uncertain model parameters
For each realization, get an EAD estimate:
…still end with a sample of damages
One Realization
Peak Flow (cfs)
CDF
After repeating for many realizations:
EAD
Random choice of probability ~ Ui[0,1]
to “generate” event
and then sample events (variability)
Notes: This slide is easier to see when animated. The outer loop is the orange values including a “new” possible version of the flow frequency curve, sampled from within its uncertainty, and “new” values of the uncertain model parameters. Then the inner loop is performed, with each event sampled from the “new” frequency curve routed through the watershed models, populated with any naturally variable values (like starting reservoir level.)
The sample of damages from the inside loop forms one damage frequency curve and one estimate of EAD.
Going back to the outer loop and incrementing all knowledge uncertainties, and then going back and repeating the inner loop produces another damage frequency curve and estimate of EAD. After many outer loops, we have a large sample of EAD, reflecting its uncertainty.

## Slide 49
sample of annual damage from one realization
(spans natural variability)
provides 1 estimate of EAD
mean = average = EAD
sample of mean damage (EAD) from all realizations
(spans knowledge uncertainty)
provides distribution of EAD
Annual Damages
EAD estimates
A
B
Notes: At the top of the slide, one inner loop spans all natural variabilities and produces a sample of damages, with one estimate of the mean, EAD. This is a realization. That inner loop lives within one pass of the outer loop, which had individual values of knowledge uncertainties.
At the bottom of the slide, many passes of the outer loop (and subsequent inner loops) spans the knowledge uncertainties and produces a sample of EAD estimates, one from each realization.

## Slide 50: Outline
Introduction
Example: Estimate of p
Theory of Monte Carlo Simulation
  what we’re doing
  how we generate samples
  convergence
Workshop / Demo
Applications
  Flood Risk Analysis (HEC-WAT/FRA)
  Stochastic Streamflow Generation for Water Supply
  Uncertainty Analysis (next lecture)

## Slide 51: Water Supply Yield Analysis
1 KAF/mo = 16.5 cfs = 10.7 mgd
= 4,857 cfs
Without storage, historical “safe” yield = min flow = 24.5 KAF/mo
Most of the annual volume comes in a 2 to 3 month Spring snowmelt season. Flow is very low in summer.
Notes: This problem demonstrates the relationship between storage volume and yield for some purpose like water supply that requires a constant flow rate. This is a flow time series in a location with low flow in summer and most of the volume arriving during a wetter winter and spring snowmelt. With no storage available, the only constant flow rate that can be “guaranteed” is the lowest flow level seen in the time series.

## Slide 52: When water from storage is needed…
1 KAF/mo = 16.5 cfs = 10.7 mgd
Demand = 100 KAF/mo
demand = 100 KAF/mo
Notes: With a larger demand, it must be possible to storage some water to provide during the times that the flow is less than the demand. In this image, the pink shaded areas are times of deficit, and are the required storage volumes to supply the demand in those times. The blue shaded areas are available to refill storage after use.

## Slide 53: Storage required to meet a demand/yield
demand = 100 KAF/mo
Iterative simulation: trial & error on volume to exactly empty given withdrawal 100 KAF/mo
Notes: Adding to the previous slide, the lower graphic shows a storage routing in which water is taken from storage to meet the demand when flow (inflow to this reservoir) is less than demand. Storage capacity is defined as the volume needed to get through the greatest deficit. The storage level is drafted during the pink shaded deficits, and refilled by the blue shaded surplus. The complete draft in 1976 is the critical period for this demand & storage combination.

## Slide 54: When water from storage is needed…
Demand = 100 KAF/mo
demand = 100 KAF/mo
demand = 200 KAF/mo
Demand = 200 KAF/mo
1 KAF/mo = 16.5 cfs = 10.7 mgd
Notes: This slide shows a demand twice the size as the last. With this higher demand, the orange shaded areas are times of deficit, and are the required storage volumes to supply the demand in those times. Note these deficit volumes are much greater, and happen more frequently. The blue shaded areas are available to refill storage after use, and there is a period when there is little blue to refill a reservoir between oranges periods of draft, meaning there will be storage drawn over years.

## Slide 55: Storage required to meet a demand/yield
demand = 200 KAF/mo
Notes: Adding to the previous slide, the lower graphic shows a storage routing in which water is taken from storage to meet the demand when flow (inflow to this reservoir) is less than demand. Storage capacity is defined as the volume needed to get through the greatest deficit. Note that a much larger storage was needed to get through the period of record with this larger demand. Storage is drafted during orange deficits and refilled during blue surplus. The period in the middle of the record shows the expected over-year draft, and is the more critical period for this demand & storage combination.

## Slide 56
Storage / Yield Relationship for Each Critical Period
669
4068
Firm Yield
Firm Yield
Notes: This is a storage/yield curve, showing the storage required to meet demand of increasing size. The blue version was created based on the first critical period, and the pink version was created based on the second critical period. The lower of the two curve is the actual storage/yield curve, showing the first period was controlling for lower demands and the second period was controlling for larger demands.
This curve was created based on dry period or droughts that occurred during the period of record that was available. However, there is some likelihood of worse droughts occurring. One way to consider the reliability of a given storage volume for a given demand is to consider a longer streamflow record produced randomly.

## Slide 57: Use Monte Carlo…
There’s only one real inflow time series to work with for estimating yield, sizing reservoirs or reallocating reservoir pools for supply
It would be nice if we could create more time series, in the same way we numerically played roulette…
  Stochastic Streamflow Generation!

## Slide 58
Initial 41-year record of annual volumes (first example)
Use autoregression AR(1) to generate longer record
More examples of drought events
serial correlation = r = 0.24
Generated 100-year record of annual volumes
Q(t) = m + (Q(t-1)-m)*r + random error(s,g)
compute m, s, g, r
Notes: This slide shows a method of stochastic data generation called lag 1 AutoRegression. The statistical structure of the streamflow is estimated from the 41-year record of annual flow volumes shown at the top. Parameters estimated are mean, standard deviation, skew and serial correlation.
Serial correlation is the relationship between one year’s flow volume and the next. Higher serial correlation is seen as extended departures from the mean, where smaller serial correlation looks more random in whether the value is above or below the mean from one year to the next.
The streamflow model, AR(1), is shown in the center of the slide and has 3 terms: (1) the distribution mean, (2) the previous year’s departure from the mean times the serial correlation, and (3) a random error value.
This model produced the 100-year record in the lower figure based on the streamflow structure in the upper figure. Note they look consistent, and show another feasible set of dry periods that can affect the storage/yield computation.

## Slide 59
1000 years
Notes: This slide uses the model of the previous slide to produce 1000 years of possible flows from the stream. This record contains even more examples of potential dry periods.
The annual flow volumes are disaggregated into monthly volumes to perform the reservoir routing in the next slide.

## Slide 60
Reliability is 99.9% (1 failure in 1,000 years)
Reservoir Storage trace for 1000 years, volume needed for 100 kaf/month
Release = 100 KAF/mo
1 failure in 1000 years, reliability = 99.9%
Required Volume = 1,434 KAF
Disaggregated annual to monthly, then preformed reservoir simulation
Notes: This is the storage trace resulting from performing a simple 1-reservoir yield analysis, determining what volume of storage is needed to satisfy a certain demand. This trace represents no failure or 100% reliability in 1000 years.
The driest in 1000 years is much more extreme than the driest in any record we might observe. But, we can now work with the reliability. If we allow1 failure in 1000 years, we’re aiming for 99.9% reliability…

## Slide 61
10 failures in 1000 years Reliability is 99% (1 in 100)
Reservoir Storage trace for 1000 years, volume needed for 100 kaf/month
2 years
Release = 100 KAF/mo
10 failures in 1000 years, reliability = 99%
Required Volume = 783 KAF
Notes: … if we allow 10 failures in 1000 years, we’re targeting 99% reliability. Now we have some estimate of return period for shortage.
We can produce as many 1000 year records as needed to estimate yield with a particular reliability, and the uncertainty in that reliability given the limited record we’re starting with.

## Slide 62: Required Storage vs Reliability
Notes: This reliability curve is created by determining the storage required to meet demand with the specified percentage of failures across 1000 years. The original record needed 669 KAF to meet the 100 KAF/mo demand, show is shown to provide almost 99% reliability with this analysis.

## Slide 63: Long-term Reliability
500 examples of 50-year record
Calculate storage requirement for each of the 500 traces
Histogram or PDF
Demand = 100 KAF/mo
CDF
For 90% 50-year reliability, need 943 KAF
669 KAF
669 KAF
Notes: Here is an example of a long-term reliability calculation using many 50-year long traces. We can calculate the yield for each trace, and plot them all as a histogram.
We can then transform this into a cumulative distribution function that will show the reliability vs. yield.
We can determine the yield for a given reliability level, or we could determine the reliability of a given yield.

## Slide 64: Why Monte Carlo?
Repeat an experiment to estimate probability
  Dice rolling, Buffon’s needle to estimate p
Replace probability distribution with a large sample to avoid calculus
Create many small samples of known distributions to examine error in estimates (introduction lecture)
Create outcomes we haven’t seen before, but could
Create larger samples to see extreme outcomes, with correct frequency
Notes: Summary.