## Slide 1
Coincident Frequency Analysis
Beth Faber, PhD, PE
Statistical Methods in Hydrology
Hydrologic Engineering Center

## Slide 2: Coincident Frequency
Coincident Frequency =
the probability of a given outcome resulting from several processes, because they all influence the single variable of interest
  Sometimes an occurrence of interest is dependent on 2 or more other processes
  To estimate probability of the occurrence of interest, probabilities of each of those primary processes must be considered

## Slide 3: Topics
Examples of Coincident Frequency Problems
Theory
  Situations and assumptions
  Total Probability Theory
  When variables are not independent
Using HEC-SSP
Monte Carlo Approach

## Slide 4: Problems requiring Coincident Frequency Analysis
Tributary
River
A = Flow in the Tributary
B = Stage on the Main Stem
C = Stage on the Tributary
Flooding on Tributary
A
B
C
River
Channel
Levee
A = Local Runoff
B = Flow in the River Channel
C = Stage behind the Levee
Interior Flooding
Conduit with
Flap Gate
B
A
C
Interior Pond
Local Runoff
Notes: These are examples of problems which tend to require coincident frequency analysis. The variable of interest in the analysis is variable C, and it is affected by variables A and B.
Variable A is defined as the more influential, for which we assume the annual maximum is occurring for the highest each year at C. B is the less influential.
For interior flooding, we modeling the runoff interior to the levee (the land side) and the stage in the channel on the exterior. Generally we’re designing an interior pond, with gravity drainage or pumps.
For flooding on a tributary, we’re looking at an event on a tributary with a damage area that experiences backwater from the main step at high flow.

## Slide 5
River
Ocean or
Lake
A = Flow in the River
B = Stage of the Water Body
C = Stage on the River
Stage on Lake Tributary
Peak Reservoir Pool
Flood Control Storage
A = Flood Inflows
B = Initial Reservoir Level
C = Flood Control Storage Used
A
B
C
B
A
C
Problems requiring Coincident Frequency Analysis
Notes: Stage on a lake tributary is similar to the river tributary, experiencing backwater at the data area when levels are high
Final peak flood pool stage is influenced by the event inflow, and the starting level of the reservoir pool.

## Slide 6
Ocean
Bay or Estuary
A = Storm Surge (Wind or Wave Setup) Stage
B = Rainfall Runoff
C = Estuary Stage
A = Conveyance Reduction
Due to Ice
B = Flow in the River
C = River Stage
Ice-Affected Flows
Bridge
ICE
Combined Runoff / Storm Surge
A
B
C
A
B
C
Runoff
River
Problems requiring Coincident Frequency Analysis
Notes: In an ice jam, the stage at the location of interest in influence by the impact of the ice, and the flow at the site.
Stage in a storm surge situation is influenced by the storm surge stage and the inflow to the estuary.

## Slide 7
Cazanovia Creek, South Buffalo
Notes: Here’s an image of an ice jam in South Buffalo.

## Slide 8: Example: Tributary Flooding
tributary peak flow
mainstem stage
tributary stage near confluence
B
C
A
In this example, the variable of interest, C, is the tributary stage near the confluence with the mainstem.
We’d like a frequency curve for the tributary stage, C.
This stage is a function of BOTH the tributary flow, A and the stage on the mainstem, B (ie, backwater effects.)
variable C can be computed with backwater analysis, given A and B
Notes: For this lecture, tributary flooding will be used as the example. We’re interested in the stage C at the damage area, and it is influence by both the tributary flow going by and the backwater from the mainstem.
Variable A is annual maximum flow on the tributary, variable B is the stage on the mainstem that can cause backwater, and variable C is the stage at the damage area.

## Slide 9
Q5
Q100
Q100
P(A)
P(B)
P(C)=?
Variable A = more influential
Variable B = less influential
Variable C = variable of interest
A
B
C
mainstem channel
tributary channel
Q5
Q25
Example: Tributary Flooding
Notes: This example demonstrates the effect of the stage on the mainstem on the stage at C. Knowing you have the 100-year flow on the tributary is not enough to define the stage at C if there is backwater.
If we want to model the situation, and define the a flow at A, what should we define as the stage at B? The choice affects the stage at C.

## Slide 10: Should we assume worst case for variable B?
In problems like interior flooding, we could just assume the gravity drain is always blocked – worst case
The problem with assuming worst case for variable B is that we lose the probabilistic description we were trying to create.
What appears to be the 1%-chance event no longer has a 1% chance, because we’ve attached a condition, and the joint probability is no longer 1%…
So what assumptions do we make about the flood event on the tributary and the stage on the mainstem?
It depends on whether we see flood events on both at the same time (or, coincident), and how they are related.
Notes: If we do assume worst case, we ruin out probabilistic descriptions of the resulting damages. A 1% chance has become something with probability other than 1%, because it is combined with another condition that has its own likelihood of occurrence.

## Slide 11: Questions to ask
Coincidence: Do notable events (extremes) happen for both variables at the same time?
answer defines probability descriptions
  Flood event or extreme on both A and B
    need annual frequency curve for each variable
    annual max for A, not necessarily annual max for B…
  Flood event on A, “just another day” on B
    If just another day on B, would use daily duration curve for B
Correlation: If notable events on both, are their magnitudes related or independent?
answer defines approach

## Slide 12: 5 Possibilities for Tributary & Mainstem Relationship
Always coincident & strong positive correlation (r ≈ 1)
  1% tributary event always happens with the 1% mainstem stage.
  the drainage areas are small and similar size (same weather)
Never coincident
  Tributary and mainstem events never happen at the same time.
Can be coincident, but not correlated (r ≈ 0)
  1% tributary event might happen with any mainstem stage.
  mainstem drainage area is greater than tributary (different weather)
Usually coincident, but not correlated (r ≈ 0).
  1% tributary event happens with mainstem event, not similar
  Seasonal events, but impacted by different weather patterns
Usually coincident, and correlated (r not ±1 or 0)…
Notes: We must define the relationship between the likelihoods of interior and exterior events. The first 2 descriptions above lead to the simplest analyses. In the first case, we have perfect correlation between interior and exterior events, so when the 1%-chance exceedance event is happening on the interior, we are also experiencing a 1% event on the mainstem channel. This might occur with small and similarly-sized drainage areas. At every likelihood, and interior and exterior event are modeled to define the stage of the same likelihood.
In the second case, a strong negative correlation means flood events never happen on the interior and exterior together. Therefore, we could always assume a low mainstem stage and unblocked gravity drain. This is uncommon.
In the third case, interior and exterior events sometimes occur together, but they are independent, such that large is no more likely to occur with large than small. Correlation is near zero. This state requires a consideration of the separate probabilities of events on the interior and exterior. This relationship might occur when the exterior drainage area is much larger than the interior.
In the forth case, there is some correlation between interior and exterior events, but it is not 1 or -1. Analysis is similar to the third case, but without some simplifying assumptions the third case allows.

## Slide 13: Easier Cases conditions (1) or (2)
If we could assume variables A and B are perfectly correlated (r ≈ 1)…
  ie, 1/100-year flow on tributary always coincides with 1/100-year stage on mainstem
  then the 1/100-year level of variable C could be computed with A100 and B100
If events A and B never coincident…
  1/100-year flow on tributary A100 always occurs with low mainstem stage, no backwater
easy!
also easy!
Notes: Case one requires many fewer model runs. Just one for each frequency ordinate using that frequency for both A and B.
Case two also requires fewer model runs, because each frequency ordinate for A is paired with low B.

## Slide 14: More Challenging Cases condition (3), (4) or (5)
Variables A and B usually coincident, might have some correlation, though not perfect
3, 4. Little or no correlation, convenient to say INDEPENDENT
  knowing the value of B tells us nothing about the value of A,
    P(A|B) = P(A), or
    probability of A given B equals probability of A
  difference in 3 and 4 is whether an event for B, or just another day
It is easier to assume independence…
less easy, but OK
hard…
Notes: We’ll defer the more difficult case 4 for later, and discuss case 3 where it is acceptable to assume independence between A and B.

## Slide 15: Total Probability Method
Information we have:
  variable A, data for annual tributary flood peaks (more influential)
  variable B, data for daily and annual peak mainstem stage (less influential)
Information we want:
  variable C, frequency curve (probability distribution) for stage above confluence
(Coincident Frequency Analysis)
Notes: An example of combining probabilities using the coincident frequency analysis approach, documented in EM 1110-2-1413 and 1110-2-1415. We define the more influential variable as A, in this case tributary annual peak flood flow, and the less influential variable as B, in this case the mainstem stage. By combining these two variables we will estimate a frequency curve for variable C, the stage at the confluence.
We must define tributary peak flow across all annual exceedance probabilties, and mainstem stages that span the range and are defined by daily % of time exceeded.
For each value of annual peak flow (defined at regular exceedance probabilities) and each chosen mainstem stage, model the maximum resulting confluence stage at C. This run provides variable C, confluence stage, conditioned on variable B, mainstem stage. This resulting stage is given the exceedance probability of A, but conditioned on the associated value of B. The set of these model runs defines a matrix that defines the “response function” – ie, the response of variable C to variables A and B.

## Slide 16: Total Probability Method
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
Annual Peak Flow
% of time B is exceeded
Mainstem Stage
P(A)
P(B)
0.10 0.30 0.50 0.70 0.90
Tributary Annual Peak Flow Frequency Curve for A
using annual extremes
Mainstem Stage Daily Duration Curve for B
using daily stages
NOT assuming peaks/events happen for both variables at the same time
Initial Probability Distributions
more influential
less influential
“any given day”
Notes: We must define tributary peak flow across all annual exceedance probabilties, and mainstem stages that span the range and are defined by daily % of time exceeded.

## Slide 17: Total Probability Method
Duration Curve for B, stage on mainstem
Choose index values for B that each represent a portion of the range and probability -- INCREMENTAL
Frequency Curve for A, tributary peak flow
Choose quantiles along the curve (flow for each probability) to use in computation -- CUMULATIVE
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
A=a0.01
A=a0.5
P(A)
Annual Peak Flow
% of time B is exceeded
0.10 0.30 0.50 0.70 0.90
20%
40%
20%
10%
7%
b3
b1
b2
b4
b5
b6
P(B)
Mainstem Stage
A=a0.1
Processing the Probability Distributions
P(b5)=0.2
P(b3)=0.2
more influential
less influential
3%
P(b6)=0.1
P(b1)=0.03
Notes: We choose discrete points for each variable. For variable A, it is the range of frequency ordinates. For variable B, we define a series of index values, and define a portion of the probability range as being represented by each index value.

## Slide 18: Computing the “Response Function”
 | a0.9 | a0.5 | a0.2 | a0.1 | a0.05 | a0.01
b1 | c0.9¦b1 | c0.5¦b1 | c0.2¦b1 | c0.1¦b1 | c0.05¦b1 | c0.01¦b1
b2 | c0.9¦b2 | c0.5¦b2 | c0.2¦b2 | c0.1¦b2 | c0.05¦b2 | c0.01¦b2
b3 | c0.9¦b3 | c0.5¦b3 | c0.2¦b3 | c0.1¦b3 | c0.05¦b3 | c0.01¦b3
b4 | c0.9¦b4 | c0.5¦b4 | c0.2¦b4 | c0.1¦b4 | c0.05¦b4 | c0.01¦b4
b5 | c0.9¦b5 | c0.5¦b5 | c0.2¦b5 | c0.1¦b5 | c0.05¦b5 | c0.01¦b5
b6 | c0.9¦b6 | c0.5¦b6 | c0.2¦b6 | c0.1¦b6 | c0.05¦b6 | c0.01¦b6
Tributary Annual Peak Flow, variable A
Mainstem Stage, variable B
value of C that has exceedance probability of 5%, given that B = b6
Notes: For each value of annual peak flow (defined at regular exceedance probabilities) and each chosen mainstem stage, model the maximum resulting confluence stage at C. This run provides variable C, confluence stage, conditioned on variable B, mainstem stage. This resulting stage is given the exceedance probability of A, but conditioned on the associated value of B. The set of these model runs defines a matrix that defines the “response function” – ie, the response of variable C to variables A and B.

## Slide 19: Total Probability Method
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
0.99 0.90 0.50 0.10 0.05 0.01
B = b1
B = b3
B = b4
B = b5
B = b2
C=c0.01|b6
C=c0.5|b6
exceedance probability of C
B = b6
A=a0.01
A=a0.5
P(A)
P(C|B)
for each index value of B
and various values (and probabilities) of A,
compute variable C.
Step 1
Annual Peak Flow
Annual Peak Stage at C
A=a0.1
C=c0.1|b6
note that the “response” for C adopts the exceedance probability of A, but conditioned on B
Notes: For the confluence stage resulting from a given tributary flow A and mainstem stage B, we assign the tributary stage C exceedance probability, but condition it on the associated exterior stage B.

## Slide 20: Now what?
What do we do with this family of conditional frequency curves for C?
Our interest is in a single (marginal) frequency curve for variable C that is not conditional on B
Make use of the Law of Total Probability
P(C) = ΣB P(C|B) * P(B)
  ‘prob of C’ equals ‘prob of C given B’ times ‘prob of B’ summed for all B
What is the probability of each value of B?
  from duration curve – daily “% of time exceeded”
Notes: The probability of C given B, P(C|B) is the curves we’ve just created. The marginal probability of B is based on the duration curve, and having divided up the probability range among the index values of B.

## Slide 21: Law of Total Probability
The Law of Total Probability
Pe(C) = ΣB Pe(C|B) * P(B)
Venn Diagram:
area = probability
C is the sum of the 5 intersections with Bi (intersection ∩ means AND)
We have conditional probabilities, C|Bi
C|B1 = C∩B1 / B1
B1
B5
B4
B3
B2
C
C∩B1
C∩B2
C∩B3
C∩B4
C∩B5
Bi are mutually exclusive and exhaustive
Notes: This example defines the law of total probability more clearly using a Venn Diagram. The “universe” is divided among 5 sections of B. The Bi are mutually exclusive (no overlap) and exhaustive (span the entire universe). C is a part of the universe we are interested in. C can be found by adding together C∩Bi (read “C AND Bi”) for each of the Bi. But the information we have is the conditional “C given Bi” or C|Bi for each of the Bi.
The meaning of the condition-Bi is that we know Bi has occurred, and are now interested in the likelihood of C occurring. The part of C we are looking for is therefore C∩Bi. So once we condition on B1, for example, we no longer have the whole universe, but rather B1 becomes the universe. Since B1 is the universe, it’s likelihood becomes 1. Therefore, to scale C∩Bi up to reflect it’s portion of the new B1 universe, we divide C∩Bi by Bi. This provides the expression C|B1 = C∩B1 / B1
We can convert from the C|Bi that we have to the C∩Bi we want by rearranging into C∩Bi = C|Bi * Bi, therefore scaling back down the reflect it’s portion of the original universe. Having the statement for this intersection for each Bi, we can sum them to get C.

## Slide 22: Law of Total Probability
The Law of Total Probability
Pe(C) = ΣB Pe(C|B) * P(B)
B1
B5
B4
B3
B2
C
C∩B1
C∩B2
C∩B3
C∩B4
C∩B5
Venn Diagram:
area = probability
C is the sum of the 5 intersections with Bi (intersection ∩ means AND)
We have conditional probabilities, C|Bi
C|B1 = C∩B1 / B1
so C∩B1 = C|B1 * B1
Notes: This example defines the law of total probability more clearly using a Venn Diagram. The “universe” is divided among 5 sections of B. The Bi are mutually exclusive (no overlap) and exhaustive (span the entire universe). C is a part of the universe we are interested in. C can be found by adding together C∩Bi (read “C AND Bi”) for each of the Bi. But the information we have is the conditional “C given Bi” or C|Bi for each of the Bi.
The meaning of the condition-Bi is that we know Bi has occurred, and are now interested in the likelihood of C occurring. The part of C we are looking for is therefore C∩Bi. So once we condition on B1, for example, we no longer have the whole universe, but rather B1 becomes the universe. Since B1 is the universe, it’s likelihood becomes 1. Therefore, to scale C∩Bi up to reflect it’s portion of the new B1 universe, we divide C∩Bi by Bi. This provides the expression C|B1 = C∩B1 / B1
We can convert from the C|Bi that we have to the C∩Bi we want by rearranging into C∩Bi = C|Bi * Bi, therefore scaling back down the reflect it’s portion of the original universe. Having the statement for this intersection for each Bi, we can sum them to get C.

## Slide 23: Law of Total Probability
The Law of Total Probability
Pe(C) = ΣB Pe(C|B) * P(B)
B1
B5
B4
B3
B2
C
C∩B1
C∩B2
C∩B3
C∩B4
C∩B5
Venn Diagram:
area = probability
C is the sum of the 5 intersections with Bi (intersection ∩ means AND)
We have conditional probabilities, C|Bi
C|B1 = C∩B1 / B1
so C∩B1 = C|B1 * B1
then C = Si C∩Bi
Notes: This example defines the law of total probability more clearly using a Venn Diagram. The “universe” is divided among 5 sections of B. The Bi are mutually exclusive (no overlap) and exhaustive (span the entire universe). C is a part of the universe we are interested in. C can be found by adding together C∩Bi (read “C AND Bi”) for each of the Bi. But the information we have is the conditional “C given Bi” or C|Bi for each of the Bi.
The meaning of the condition-Bi is that we know Bi has occurred, and are now interested in the likelihood of C occurring. The part of C we are looking for is therefore C∩Bi. So once we condition on B1, for example, we no longer have the whole universe, but rather B1 becomes the universe. Since B1 is the universe, it’s likelihood becomes 1. Therefore, to scale C∩Bi up to reflect it’s portion of the new B1 universe, we divide C∩Bi by Bi. This provides the expression C|B1 = C∩B1 / B1
We can convert from the C|Bi that we have to the C∩Bi we want by rearranging into C∩Bi = C|Bi * Bi, therefore scaling back down the reflect it’s portion of the original universe. Having the statement for this intersection for each Bi, we can sum them to get C.

## Slide 24: Law of Total Probability
the Law of Total Probability
P(C) = ΣB P(C|B) * P(B)
  ‘prob of C’ equals ‘prob of C given B’ times ‘prob of B’ summed for all B
Example:
  if a cold front arrives, there’s a 70% chance of rain
  if not, there’s 10% chance of rain
  What’s the chance of rain?
  Depends on chance of cold front arriving
  if there’s a 20% chance the cold front will arrive…
  prob of rain = (70%)(20%) + (10%)(100%-20%) = 22%
I need to know the probability of my condition….
Notes: Here’s another example of using the total probability theorem…

## Slide 25
% of time B is exceeded
Exterior Stage
P(B)
0.10 0.30 0.50 0.70 0.90
Note, this curve is NOT formed from annual peaks. It represents daily data. We are interested in what the stage might be when an interior flood happens, and it might not be the annual peak stage or even an event.
Probability of the “Condition” – River Stage
0.10 0.30 0.50 0.70 0.90
20%
40%
20%
10%
7%
b3
b1
b2
b4
b5
b6
P(B)
P(b6)=0.1
P(b3)=0.2
3%
Exterior Stage
% of time B is exceeded
Notes: This shows where the marginal probability of B, P(B) comes from. The duration curve for B is made from all daily stages, and represents what stage might be on any given day in the future, when an event occurs on the tributary, and not necessarily the annual maximum stage. This choice, made earlier in the example, reflects the fact that the annual maximum doesn’t necessarily happen on the mainstem when it is happening on the tributary.
There are 2 ways to proceed. The probability range for B can be divided up, and an index value chosen to represent each probability segment. Or, a range of relevant index values of B can be chosen, and the probability range divided up to given some amount to each index value. In the end, the probabilities of the index values, Bi, must sum to 1.0.

## Slide 26
For every level of C, the exceedance probability given all levels of B can be determined with the
Law of Total Probability:
P(C) = ΣB P(C|B) * P(B)
0.99 0.90 0.50 0.10 0.05 0.01
exceedance probability of C
0.99 0.90 0.50 0.10 0.05 0.01
c1
c1
B = b1
B = b3
B = b4
B = b5
B = b2
B = b6
P(c1|b5)=0.35
P(c1|b2)=0.70
exceedance probability of C
P(C)
P(C|B)
Step 2
P(c1) = [P(c1|b1)*P(b1)] + [P(c1|b2)*P(b2)] + [P(c1|b3)*P(b3)] + [P(c1|b4)*P(b4)] + [P(c1|b5)*P(b5)] + [P(c1|b6)*P(b6)]
P(c1) = [0.9*0.03] + [0.7*0.07] + [0.65*0.2] + [0.52*0.4] + [0.35*0.2] + [0.2*0.1]
P(c1) = 0.51
Annual Peak Stage at C
Annual Peak Stage at C
We can view the single P(C) curve as a probability-weighted average horizontally
Notes: We implement the total probability theorem for a series of values of variable C. We choose a value of Ci, and draw a line across the family of P(C|B) curves, interpolating the exceedance probability of C|B from each of the curves. Then the total probability equation has each of those values of P(C|B) for Ci is multiplied by the associated P(Bi), and summed. The result is the marginal P(Ci) and plots as one point on the P(C) frequency curve. This process is repeated for the full range of C.
For a value of C that is below a frequency curve from the family of curves, P(C|B) is 1.0. For a value of C that is above a frequency curve from the family of curves, P(C|B) is 0. These values must still be included in the total probability equation.

## Slide 27: Case 4, Event on A and B
Sometimes due to events during a certain season, or being close enough to experience the same weather system, we see an event on B, though not necessarily annual max
Replace duration curve for B with frequency curve for B
  annual max, or
  “coincident events” – sample for B is value of B while A having annual peak
Discretize frequency curve for B in the same way as the duration curve

## Slide 28: Total Probability Method
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
Annual Peak Flow
exceedance probability of B
P(A)
P(B)
0.10 0.30 0.50 0.70 0.90
Tributary Annual Peak Flow Frequency Curve for A
using annual extremes
Mainstem Stage Annual Frequency curve for B
using annual extremes, or value of B while A is annual extreme (conditional)
more influential
less influential
Mainstem Stage
A=a0.01
A=a0.5
A=a0.1
20%
40%
20%
10%
7%
b3
b1
b4
b5
b6
P(b5)=0.2
P(b2)=0.2
Initial Probability Distributions
3%
b2
Notes: We must define tributary peak flow across all annual exceedance probabilties, and mainstem stages that span the range and are defined by daily % of time exceeded.

## Slide 29: Case 5, Not Independent
Often, A and B are not perfectly correlated, BUT it is not reasonable to assume that they are independent
What if there is some
correlation between
A and B ≠ 0 or 1?
Correlation is too strong to
ignore by assuming
independence
B
A
Notes: The method just described assumes that A and B are independent. When correlation is close enough to 0, this assumption is fine, but when correlations are above 0.3 or so, independence can’t be assumed. If possible, a continuous simulation approach that provided a time series of variable C would allow a direct frequency analysis on C, and not require coincident frequency analysis. Here, we’ll discuss how tackle the coincident frequency analysis with non-zero correlation.

## Slide 30: With Some Correlation
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
A=a0.01
A=a0.5
P(A)
Annual Peak Flow
A=a0.1
Where before we used the marginal probability of A, (i.e., a single variable)
now we must define a joint (or conditional) probability of A and B
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
B = b1
B = b2
A=a0.01|b6
A=a0.5|b6
P(A|B)
B = b3
B = b4
B = b5
B = b6
A=a0.1|b6
Annual Peak Flow
P(A|B) is read as
“probability of A given B”
Notes: When there is notable correlation between A and B – too much to be ignored – we need a joint distribution between A and B, shown here as a conditional distribution of A given B. This family of conditional curves, one for each index value of B, is used in place of the marginal distribution of A used previously.

## Slide 31: Total Probability Method
Frequency Curve for B
Choose index values for B that each represent a portion of the range and probability
Conditional Probability Curves of A given B
exceedance probability of A
0.99 0.90 0.50 0.10 0.05 0.01
B = b1
B = b2
A=a0.01|b6
A=a0.5|b6
P(A|B)
B = b3
B = b4
B = b5
A=a0.1|b6
Annual Peak Flow
B = b6
more influential
Processing the Probability Distributions
exceedance probability of B
0.10 0.30 0.50 0.70 0.90
20%
40%
20%
10%
7%
b3
b1
b2
b4
b5
b6
P(B)
Mainstem Stage
P(b5)=0.2
P(b3)=0.2
less influential
3%
P(b6)=0.1
P(b1)=0.03
Notes: In addition to the family of conditional curves for P(A|B), we use a frequency curve for B (either annual peak, or values “coincident” with each A peak), divided into probability ranges and index values.

## Slide 32: Maintaining Correlation
exceedance probability of A
B = b1
B = b3
B = b2
A=a0.01|b6
A=a0.5|b6
0.99 0.90 0.50 0.10 0.05 0.01
B = b1
B = b3
B = b4
B = b5
B = b2
C=c0.01|b6
C=c0.5|b6
exceedance probability of C
B = b6
Note that the “response” for C adopts the probability of A, but it’s the conditional probability of A given B.
0.99 0.90 0.50 0.10 0.05 0.01
P(A|B)
P(C|B)
B = b4
B = b5
B = b6
Step 1 is slightly different
Annual Peak Flow
Annual Peak Stage at C
Using the conditional distribution of A given B
Notes: When developing the response function for C given A and B, we now use the quantile value of A from each of the curves, along with the index value of B the curve is associated with. In this example of 6 quantiles of A and 6 index values of B, there are still 36 model runs to determine C from A and B, but they now use 36 different values of A, as the 1% quantile of A, for example, now has a different value for each value of Bi.
The computation in the step shown here is the same, however. For each value of A, the value of C that results from combining with the appropriate value of Bi assumes the exceedance probability of A, and remains conditional on Bi.

## Slide 33
0.99 0.90 0.50 0.10 0.05 0.01
exceedance probability of C
For every level of C, the exceedance probability given any level of B can be determined with the
Law of Total Probability:
P(C) = ΣB P(C|B) * P(B)
exceedance probability of C
0.99 0.90 0.50 0.10 0.05 0.01
P(c1|b5)=0.30
B = b1
B = b3
B = b4
B = b5
B = b2
B = b6
P(c1|b2)=0.90
c1
c1
P(C)
P(C|B)
Step 2 is exactly the same
Annual Peak Stage at C
Annual Peak Stage at C
Available in
HEC-SSP
Notes: The total probability step is exactly the same as the previous without-correlation description.
Note, the biggest impact of considering the correlation between A and B is that the upper end of the frequency curve is higher. If we acknowledge that large tend to occur at the same time for both variable, it means that larger combined events are more likely.

## Slide 34: Coincident Frequency Analysis in HEC-SSP
Notes: A coincident frequency analysis can be performed on any data type, flow, stage, precipitation, wind, etc. The coincident frequency analysis requires both duration and frequency curves. These can be computed by existing analyses in the HEC-SSP study or they can be entered manually in the coincident frequency analysis.
The Coincident Frequency Analysis is designed following guidelines in EM 1110-2-1415. This analysis tool can be used to compute the exceedance frequency relationship for a variable that is a function of two other variables. An example is illustrated above. In this example, the stage at the damage site on the tributary, variable C, is a function of stream flow from the tributary, variable A, and the stage in the mainstem river, variable B.

## Slide 35: Variable A
If A and B are independent then only 1 frequency curve is needed for Variable A.
  Variable A frequency curve can be imported from existing analyses or entered manually
If A and B are not independent then a conditional frequency curve of Variable A is needed for each Variable B index.
Notes: The Variable A tab is used to define the frequency curve for variable A. This tab will look different based on the user selection on the General Tab. When the Manual Entry option is selected, the user must define the Data Name and Data Units. Then the user must enter the frequency curve for variable A. A frequency curve value must be defined for each percent chance exceedance ordinate in the table. When the Existing Study Analysis option is selected, the dropdown list will be active and the user can choose any Bulletin 17B or General Frequency analysis in the HEC-SSP study. The variable A frequency curve table will be populated with the frequency curve when an analysis is selected.

## Slide 36: Variable B
The duration curve for Variable B must be imported from an existing Duration Analysis,
But, it can be defined manually in a Duration Analysis.
Then discretize the duration curve to determine index values for variable B.
Notes: The Variable B tab is used to define the duration curve for variable B and the index points with an associated probability. The index points will be used by the user when developing the response curves (response of variable C to each combination of variables A and B). The associated probability represents the proportion of time we’ve assign to each index point.

## Slide 37: Response Curves
Notes: The Response Curves tab is used to define the response of variable C to each combination of variable A and variable B. This analysis is performed outside of HEC-SSP. For example, a hydraulics model could be used to apply flow values from the variable A frequency curve to the tributary and the index flow (or stage) from the variable B duration curve would be applied to the mainstem. The hydraulics model would be used to compute the variable C stage at some reference point on the tributary for multiple combinations of variable A and variable B. The peak variable C stage is the value to input into the Response Curves table.
Note the response function table has the rows and columns reversed from what was shown earlier in this lecture.

## Slide 38: Coincident Frequency Results
Notes: Once the new analysis has been defined, and the user has all of the information defined on the General, Variable A, Variable B, Response Curves tabs, performing the computations is simply a matter of pressing the Compute button at the bottom of the Coincident Frequency Analysis editor.
The following describes how the variable C coincident frequency curve is computed.
1) The program uses the variable A frequency curve(s) and the variable A values in the response curves table to assign a frequency of exceedance to each variable C value in the response curves table.
2) The program finds the minimum and maximum values of variable C in the response curves table.
3) The program defines 20 evenly spaced values of variable C in between the minimum and maximum values (20 values include the minimum and maximum values).
4) For each variable C from step 3, the program will look-up the exceedance frequency value from each response curve in step 1 and multiply by the corresponding proportion of time (using the probability defined on the Variable B tab) obtained from the variable B index value. These “weighted” values from each response curve are summed to compute the variable C frequency curve.
5) The curve is interpolated to the selected exceedance ordinates defined on the General tab.

## Slide 39: Other ways…
Often the assumption of independence is not valid (ie, correlation it too high to ignore).
We want a joint distribution between A and B, but it requires at least an order of magnitude more data
Other options
  Continuous simulation of time-series of A and B to get time-series of C, do frequency analysis for C
  Estimate distributions for A and B, and a correlation, and do correlated random sampling in a Monte Carlo simulation

## Slide 40: Monte Carlo Simulation
Replace the probability distributions for A and B with large samples, to create “events” with a value of A and of B
  Use correlated sampling to maintain observed correlation
Evaluate C for each “event” to get an output
Resulting output sample of C can be used to infer the distribution of C
Notes: Another way to incorporate correlation is to use correlated sampling in a Monte Carlo simulation.

## Slide 41
Peak Flow (cfs)
Exceedance Probability
1
0
Corps of Engineers
IWR-HEC
Reservoir Analysis
event or
sample
member
hydrograph
To generate Pool Stage Frequency Curve
…end with a sample of Pool Stages
CDF
choose random probability U[0,1]
to “generate” event
replace flow-frequency curve with a sample…
peak pool level
another random U[0,1] to sample starting pool
Pool Stage (ft)
Relative Frequency
simulate each event to determine pool stage
Peak Stage(i)
Notes: The upper left corner is the flow frequency curve, and the right side is the starting reservoir pool stage. A random value is chosen for each to create an event, which is simulated in the reservoir model, producing a peak pool stage for each event. The Monte Carlo simulation ends with a large sample of peak pool stages in the lower right.

## Slide 42: Replacing Flow-Frequency Curve with a Large Sample of Peak Flows
1000 events (annual peak flows, or annual max X-duration flows)
each point is an “event”
CDF form (frequency curve)
PDF form
(histogram)
events are ranked and plotted against relative frequency of exceedance (plotting positions for N=1000)
Notes: This is the sample of flows that replaces the flow frequency curve, as a histogram and a frequency plot. There is also a sample of reservoir starting pools to replace the starting pool duration curve, which is not shown.

## Slide 43: From each flow & initial stage, compute peak reservoir stage, get sample of stages
1000 event peak stages
each point is an “event”
CDF form (frequency curve)
PDF form
(histogram)
Notes: This is the output sample of peak pool stages, as a histogram and as a peak pool stage frequency curve.

## Slide 44: Need to Sample Correlated Values?
If suspect there is enough correlation between the variables to make independence a poor assumption:
Evaluate coincidence:
  Do they experience annual max at same time?
Study and estimate correlation:
  For flow, consider relationship for log as well as linear
Estimate probability distributions for each variable
Notes: To determine if need to do correlated sampling…

## Slide 45: Two Flow Locations
Variable A
Variable B
Notes: Here is an example of a flow confluence problem. Variable A is the tributary and variable B is the mainstem. It was determined that annual maximums for thse basins coincide. These figures show an annual maximum flow frequency curve of each. Variable B uses the annual maximum distribution when it’s determined that annual maximums coincide.

## Slide 46: Make Correlation Plots
Linear Flow, r = 0.74
Log Flow, r = 0.84
A
B
A
B
Notes: These are correlation plots of A versus B, with linear axes on the left, and log axes on the right. In this case, the relationship between A and B is more linear (ie, have greater linear correlation) with log flow, at r = 0.84. Correlation of flow was only r = 0.74, on the left.

## Slide 47: Sampling Correlated Flows
Linear Flow, r = 0.74
Log Flow, r = 0.84
1000 pairs
1000 pairs
A
B
A
B
0.74
Notes: Correlated random sampling of 1000 pairs of A and B are shown here, with linear axes on the left, and log axes on the right. Note that the point scatter of the samples resembles the point scatter of the actual data on the previous slide.

## Slide 48: Sampling Correlated Flows
1000 flows
1000 flows
Variable A
Variable B
Notes: This shows the 1000 pairs of A and B, each plotted on its frequency plot.

## Slide 49: Correlated Sampling
Can generate correlated random values by bringing independent random value through a joint Normal distribution
  Want X ~ MN(0, S) multivariate normal
    where S is the correlation matrix of the variables
  Generate Zi ~ N[0,1] for Z = (Z1, Z2, …, Zn)
  Find matrix C such that CTC = S
    Can use Cholesky decomposition for matrix C from S
  Then, CTZ ~ MN(0, S)
Gaussian Copula
Notes: Correlated random sampling is performed using a standard multivariate Normal distribution having correlation matrix Sigma. For 2 variables, 2 arrays of independent U[0,1] are generated and transformed to N{[0,1] (Z). The arrays together form the Z matrix. A matrix C is developed such that C transpose times C equals matrix Sigma. Using it, C transpose times Z has a multivariate Normal distribution with correlation Sigma. The two columns of the multivariate Normal matrix are arrays that have the defined correlation.

## Slide 50
Peak Flow at A & B (cfs)
Exceedance Probability
1
0
Hydraulic Analysis
event
To generate Tributary stage frequency Curve
…end with a sample of stages at C
CDF
Damage Area Stage (ft)
Relative Frequency
simulate each event to determine stage
Tributary
Mainstem
A
B
C
A
B
choose correlated random probabilities U[0,1] to “generate” event
replace flow-frequency curves with samples…
Corps of Engineers
IWR-HEC
hydrographs at A and B
the sample is a stage frequency curve:
Stage at C (ft)
Notes: The upper left corner shows the two correlated flow frequency curves, one for A and one for B. A correlated pair of values is sampled, and sent to the RAS model on the right side of the screen. Stage at C is computed, in the same way the response surface values were computed in the standard coincident frequency analysis. The Monte Carlo simulation ends with a sample of stages at C in the lower right., which is also shown as a stage frequency curve in the bottom center.

## Slide 51: Knowledge Uncertainty?
What we’ve looked at so far has computed a best estimate of stage frequency curve at C
  The Monte Carlo sampling is only addressing natural variability in flood magnitudes
It has not yet included uncertainty in the flow distributions, or in the model parameters
Notes: Thus far, only natural variabilities have been included in this analysis. But knowledge uncertainty is also important.

## Slide 52: How do we capture knowledge uncertainty in MC event modeling?
Two-level Nested Monte Carlo:
Sample instances of natural variabilities as flood events, with enough events to capture the distribution of flow
Sample instances of knowledge uncertainties in model parameters for each realization of the stage distribution
inner loop 2 varies natural variability, computes stage-freq
2
1
outer loop 1 varies knowledge uncertainty, computes stage-frequency uncertainty
outer loop 1 = a realization
Corps of Engineers
IWR-HEC
Notes: A way to incorporate knowledge uncertainty is to do a nested Monte Carlo.
In an outer loop, we sample knowledge uncertainty, and initialize all the models (including frequency curves) with the resulting value(s). Then we do an inner loop in which we sample natural variabilities as flood events. We sample only once in the outer loop, and we sample enough flood events on the inner loop to converge. The combination of once around the outer loop and a converged inner loop is called a realization.
We go back to the outer loop and again sample knowledge uncertainties once and initialize the models again. Then return to the inner loop to do enough flood events to converge.
We do enough outer loops to capture the knowledge uncertainty distributions, doing a full inner loop of natural variabilities for each of them.

## Slide 53
sample of peak stage at C from one realization
(spans natural variability)
provides 1 estimate of peak frequency
sample of frequency curves from all realizations
(spans knowledge uncertainty)
provides distribution peak C stage quantiles
2
1
Peak Stage at C (ft)
Annual Peak Stage at C (ft)
Notes: After an inner loop has converged (one realization), we have a sample of peak stages at C. After all realizations, we have a collection of frequency curve for C, from which we can create confidence intervals.

## Slide 54: Sampling Correlated Flows
We can also estimate a stage frequency curve by combining a trib peak flow frequency curve with a mainstem flow or stage frequency (or duration) curve
How does the Monte Carlo (WAT/FRA) analysis differ?
  Can explicitly incorporate uncertainty in flow frequency curve and other variables
  Can easily capture more random variables than peak flow and channel stage if they are relevant, rather than just two.
  Can consider a range of event shapes with differing volumes for a given peak magnitude
  Correlation!

## Slide 55
Precip (inches)
Exceedance Probability
1
0
Reservoir Analysis
event or
sample
member
hyetographs
Starting with Precipitation
…end with a sample of Pool Stages
CDF
choose random probability U[0,1]
to “generate” event
replace precip-frequency curve with a sample…
peak pool level
new randoms U[0,1] to sample starting pool
Damage ($)
Relative Frequency
add rainfall/runoff model w/uncertainty to the sequence
Peak Stage(i)
Rainfall/Runoff Analysis
new randoms U[0,1] to sample infiltration rate, etc
hydrographs
Notes: This slides shows the same sampling and modeling process, but starting the hydrology one step earlier with a precipitation frequency curve and a rainfall/runoff analysis.

## Slide 56: Questions?