## Slide 1: Developing a Watershed Schematic
The Watershed Setup Module

## Slide 2: Watershed Setup Tasks
Draw Stream Alignment
Define Configurations
Place Project Elements
  Reservoirs
  Diversions
  Etc.
Place Computation Points
Draw other model elements…

## Slide 3: Configure ResSim
Watershed Location
  an alias or logical name for a place on your disk where you will put your watersheds
  You can identify several watershed locations.

## Slide 4: Creating a Watershed…
The File Menu
  New
  Open
  Save
Must Provide:
  Name & Description
  Location
  Units
  Time Zone

## Slide 5: Preparing the map region…
View -> Layers…
The Layer Selector
  Add Map Layer…
  Order Layers
  Edit layer properties

## Slide 6: The Stream Alignment…
Represents the river system in
the watershed
Composed of…
  Stream Elements
  Stream Nodes
  Stream Junctions
Defines flow direction…
  The stream alignment typically should be drawn from upstream to downstream
  By default, the station at the downstream end of an element is Station zero, and the stationing increases upstream along the stream element

## Slide 7: A Stream Element…
A “polyline” - a series of line segments defined by vertex points.
  Typically begins or ends at a confluence, bifurcation, or at the boundary of a river system.
The level of the detail of the stream alignment is dependent on the needs of the overall study.
  If you are going to be using another model that will provide a geo-referenced layer (such as RAS) then the stream alignment needs to be fairly detailed.
  If geo-referencing is not an issue, the stream alignment can be as simple as a “stick figure”.
Stream Alignment Tool - is used to create, delete, and edit stream elements.
Notes: Stream element default color is orange.

## Slide 8: A Stream Node…
Used to establish the stationing for a stream element.
  Default Nodes: Upstream & Downstream endpoints of a stream element.
  Intermediate: Added by user to set the station of known landmarks.
Stream Node Tool - used to create, delete, and edit stream nodes on the stream alignment.
Notes: Default color is green.

## Slide 9: A Stream Junction..
A stream junction is automatically created where stream elements connect.
  Stream nodes are created on each stream element associated with a junction.
  You can edit the stream nodes located at a junction to establish stream stationing for all associated streams
  Use the Stream Node tool to edit stream junctions.
Notes: Default color is green.

## Slide 10: Before you start drawing…
It will be useful to display a background map of the river system as a guideline for creating the stream alignment.
If your alignment is based on a map layer, the map layer should already be in the watershed.
If the shapefile of the streams map layer is available, it is possible to “import” the stream alignment from it.

## Slide 11: To Draw a Stream Element
From the map toolbar, press the Stream Alignment tool .
Find a location on the display area where you want to start a stream element.
Hold down the CTRL key while clicking the left mouse button. Each click creates a vertex point as you point to locations on the display area. To place the last vertex point release the CTRL key, and then click the mouse button.

## Slide 12: Drawing Order…
Draw streams from upstream to downstream.
  Use the “Reverse Direction” option to reverse the direction of the stream element
Draw mainstem first, then the major tributaries, and then the minor tributaries.
Remember that this stream alignment may be shared by other models and needs to encompass the streams needed by all models.

## Slide 13: Functions of.. The Stream Alignment Tool
Draw Mode – ctrl-click
Select Mode – single click
  Rename a Stream Element
  Delete a Stream Element
Edit Mode – double click
  Add Vertex Points to a Stream Element (ctrl-click)
  Move Vertex Points of a Stream Element (select and drag)
  Delete Vertex Points (ctrl-shift-click)
Stream Alignment Popup Menu

## Slide 14: Stream Alignment Properties
Stream element properties (stream width, color, font, tic mark lengths and font,...)
Node properties (color, outline color, width)
Junction properties (color, width)
Notes: To access the Stream Alignment Properties dialog, on the View menu, click
Layers. From the Layer Select dialog, right-click on Stream Alignment, from
the shortcut menu click Properties and the Stream Alignment Properties dialog
will open.

## Slide 15: Configurations
The physical arrangement of elements that will be modeled by the set of programs to be used for the study of the watershed.
Developed by the whole modeling team, this will reduce the possibility of incompatible model data sets.
Elements in a Configuration are identification shells. They only store name and location.
A configuration does not have time-window specific information nor model data.
Study is NOT a configuration. It is the “bucket” that holds the entire set of all project elements that have been defined in the watershed.

## Slide 16: How does ResSim use a Configuration?
A Reservoir Network will inherit the project elements from a selected configuration.
The physical and operational data associated with the elements are added and stored in the Reservoir Network.

## Slide 17: Configuration Editor
From the Configuration menu, click New. The Create a New Configuration dialog box will open. Enter a name and click OK. Then save the configuration and close the editor by pressing OK again.
The Configuration Editor is used to create and edit configurations.
On the Watershed menu, click Configuration Editor. The Configuration Editor will open.

## Slide 18: Projects
A project is a man-made structure that reduces flood damage by reducing flood stages (e.g. a reservoir) or by protecting property from flood stages (e.g. levee).
Project Tools are used to create, delete, and edit projects in the display area.
Available Project Types:
  Reservoirs
  Levees
  Diversions
  Channel Modifications
  Storage Areas
  Other

## Slide 19: Drawing a Reservoir
In the Watershed Setup Module…
On the stream alignment, starting at the upstream end of the reservoir, hold down the CTRL key and click the left mouse button.
Release the CTRL key and move the mouse to the downstream end of the reservoir and click. You will be asked to give the reservoir a name.

## Slide 20: Drawing a Reservoir, cont’d.
The reservoir will appear in the display area. It is represented by
  a (light blue) triangle,
  a (grey) dam,
  and a (light blue) storage reach.
Two computation points are added to identify the reservoir’s inflow and outflow points. Don’t forget to rename these points!

## Slide 21: Reservoir Complexity
Simple
  1 in, 1 out
Branched
  Multi in – 1 out
Multiple Dams
  1 or more in, 2 or more out
Diverted Outlets

## Slide 22: Drawing a Diversion
In the Watershed Setup Module…
On the stream alignment, starting at the upstream end of the diversion, hold down the CTRL key and click the left mouse button.
While continuing to hold the CTRL key, click the mouse to add “shaping points” to the diversion as you move toward the downstream end of the diversion.
Release the CTRL key and move the mouse to the downstream end of the diversion and click. You will be asked to give the diversion a name.

## Slide 23: Drawing a Diversion, cont’d.
The diversion will appear in the display area. It is represented by a heavy black polyline with an arrowhead at the downstream end.
The color of the arrowhead denotes connectivity
  blue for connected
  black for unconnected
Up to two computation points may also be added.
  As with a reservoir, when a diversion is drawn, if the upstream or downstream computation points are not already in the watershed, they will be created with the diversion to identify the diversion’s inflow and outflow points.
Don’t forget to rename the computation points!

## Slide 24: Computation Points
Computation points are locations where time-series information is to be exchanged between models.
Some computation points are automatically generated for the watershed based on the projects and impact area placement.
Remember the two points added at the reservoir?

## Slide 25: Computation Points
Computation Point Tool - allows you to add your own computation points.
Add computation points at locations where the models need information but may not have been automatically generated by the placement of projects.
  Gage Locations
  Control Points
  Confluences or Inflow points

## Slide 26: Placing Computation Points
In the Watershed Setup Module
Using the computation point tool, move the cursor to the location in the map region where you want to place the computation point, then hold down the CTRL key and click.
You will be prompted to enter a name for the computation point.
A black dot and the name will appear where you placed the point.

## Slide 27: Placing Computation Points
Special Case: Stream Junctions
  When you place a computation point at a confluence (stream junction), an extended form of the “Name new Computation Point” window will appear.
  You must select WHERE the
  computation point will be placed…
    At the stream junction – TYPICAL
    On one of the connecting reaches
    None – off the streams completely

## Slide 28: Points to Remember…
The Watershed Setup Module is where you…
  Create Watersheds.
  Define the basic model schematic of your watershed.
The Stream Alignment is…
  The skeleton for your model schematic.
A Configuration is..
  The selection of project elements that will be represented by a set of models for this watershed.
Project Elements and Computation Points are…
  Identification placeholders for model elements.