## Slide 1: Scripting HEC-ResSim

## Slide 2: Topics
Scripts Executed During Simulations
  State Variable Scripts
  Scripted Rule Scripts
Scripts Executed Outside Simulations
  Static Scripts
Jython

## Slide 3: Two Categories of Scripts – 1 of 2
Scripts executed during simulations
  These scripts can:
    Compute and store the state of some (concrete or abstract) portion of the model at each simulation time step
    Compute a flow limit (minimum, maximum, or specified) at each simulation time step
  These scripts cannot:
    Know when they execute in relation to other scripts

## Slide 4: Two Categories of Scripts – 2 of 2
Scripts executed outside simulations
  These scripts can:
    Pre-process data for simulations
    Run simulations (some or all alternatives)
    Post-process data from simulations, generate plots, reports, etc…
  These scripts cannot:
    Interact with a running simulation

## Slide 5: Scripts Executed During Simulations
There are two types of HEC-ResSim scripts that are executed during simulations
  State Variable Scripts
    Scripts that set the value of a state variable, which can be used by rules and IF-THEN-ELSE blocks to specify flow constraints
      A model variable represents the state of some element of the network with a value at each time step of the simulation (thus, a time series)
      A state variable is a model variable-like time series whose values are computed by a script instead of the static rule-based logic; it doesn’t necessarily represent the state of a single element
  Scripted Rules
    Scripts that directly specify flow constraints

## Slide 6: Scripts Executed During Simulations
Common Properties of State Variable and Scripted Rule Scripts
  Scripts are executed at every iteration of every timestep
  Computation at any time step may depend on any model variables at previous time steps, and may depend on other State Variables at the current or previous timestep
  The main scripts must “return” a value.
Notes: Scripts that depend on other State Variables at the same time step must manually ensure they have been executed before the current script

## Slide 7: Model Variables vs. State Variables
Represent the state of single elements within a ResSim model.
Standard output of a ResSim model.
Globally accessible Time Series objects that belong to the network.
Not associated with a specific network element, so can represent complex or abstract concepts involving one or more model elements – such as basin wetness, system drought state, etc.
Defined by the modeler.
Globally accessible Time Series objects that belong to the network.

## Slide 8: More about State Variables
HEC-ResSim computes a state variable by executing a Jython script for that variable at every time step throughout the simulation period.
The script can access model variables and other state variables for the current and prior time steps.
  Scripts that depend on other State Variables at the same time step must be manually ensured to be executed after the script they depend upon
The script can also perform any function available to Jython to compute the variable.
  Care must be taken not to perform lengthy tasks (e.g. disk or network access) because of the number of times the script is executed!
Notes: Jython is a Java implementation of the Python programming language and provides the common basis for ResSim, DssVue, and CWMS scripting.
State Variable definition scripts do not return anything. They must “set” the value of the TimeSeries object for the current time step, or have set it in an earlier time step. The script may optionally set values into the future (through the end of the computation time window).

## Slide 9: Creating a New State Variable
To create a new State Variable script:
  Edit menu, State Variables…
    The State Variable Editor will open.
  State Variable menu, New…
    Enter a name and an optional description, Click OK.
  Enter a parameter (DSS C Part) in the Parameter Name field.
  Select the parameter type from the Parameter Type list.
  Edit the script text as desired.
  Press the Compile Script button to check for syntax errors.
    Fix any errors and repeat this step.
  Save the script by selecting Save from the State Variable menu or by pressing Ctrl-S.

## Slide 10: The State Variable Editor
State Variable Selector
Script Tabs
API Tree
Edit Pane
API Preview
Cursor Position

## Slide 11: Using the State Variable API Tree
Selecting a node (not a folder) in the API Tree causes the API insertion text for the selected node to be displayed in the API preview bar.
Double-clicking on a node in the API Tree causes its API text to be inserted at the current cursor position in the Edit Pane.
  The same can be accomplished by selecting a node in the API and then selecting the Insert in Script button under the API Pane.
Dragging a node in the API Pane to some position in the Editor Pane causes its API text to be inserted at that location in the Editor Pane.

## Slide 12: Scripted Rules…
Are Release Function Rules defined by a script
Are evaluated with the other rules in the rule stack
Allow the modeler to define a more complex or abstract rule than the standard rule set allows
Have an init function (initRuleScript) and a main function. (runRuleScript)
A value for the rule limit must be defined and set in the script.

## Slide 13: Creating a Scripted Rule
To create a Scripted Rule:
  Open the Reservoir Editor, Operations tab
  In the Zone-Rules tree on the Zone-Rules tab, right-click the desired zone and select Add New Rule… from the context menu.
  Give the rule a name, select the release element
  Select Script for the Rule Type.
  Press the OK button.
  The Scripted Rule Editor appears in the rule’s Edit pane. It is very similar to the State Variable Editor.

## Slide 14: Scripted Rule Editor
API Tree
Edit Pane
API Preview

## Slide 15: Scripts Executed Outside Simulations
There is only one type of script executed outside simulations, which we call static scripts or utility scripts.
ResSim Static scripts resemble HEC-DSSVue scripts:
  They can be executed from the Script Selector, Script Pane, or Script Editor.
  They are created, edited, and tested in the Script Editor.
  Their location in the Tree Pane of the Script Editor corresponds to a file in your user profile’s AppData area on disc.
ResSim Static scripts go beyond HEC-DSSVue scripts:
  Script location in the Tree Pane determines script visibility.
  Scripts can have knowledge of the current module and current simulation.

## Slide 16: The Script Selector
The Script Selector is accessed by the ToolsScripts menu item in any module.
The Script Selector is titled according to the current module.
Execute a script by pressing its button.

## Slide 17: Accessing the Script Editor
The Script Editor is accessed by the ToolsScript Editor… menu item on the HEC-ResSim menu bar, or by ScriptScript Editor menu item on the Script Selector.

## Slide 18: The Script Editor
Tree Pane
Editor Pane
Script Name
File Name
Dismissal Buttons
Description Pane
Edit/Save/Test Buttons
Icon Selector
Pre-Defined Variables
Location & Mode Indicators
Visibility Switches

## Slide 19: Static Script Visibility
For a static script to be visible:
  its position in the Tree Pane:
    must be in the All Watersheds folder or Current Watershed folder
    must be in Modules folder or folder corresponding to the current module
  its Show in Script Selector switch must be checked to be visible in the Script Selector
  its Display Script to User switch must be checked to be visible in the script pane

## Slide 20: Creating a New Static Script
To create a new static script:
  right-click on one of the folders under either the All Watersheds or Current Watershed:
    Modules
    Watershed Setup
    Reservoir Network
    Simulation
  select New Script from the context menu
  enter a name in the Label field
  enter the script text in the Editor Pane
  press the Save or Save and Test button

## Slide 21: Editing Existing Static Scripts
To edit an existing Static Script, do one of the following:
  double-click on its entry in the Tree Pane
  right-click on its entry in the Tree Pane and select Edit Script from the context menu
  select its entry in the Tree Pane and do one of the following:
    select FileOpen from the menu bar
    press Ctrl-O
    press the Edit button

## Slide 22: Testing Existing Static Scripts
To test an existing Static Script from the Script Editor, select its entry in the Tree Pane and do one of the following:
  select FileTest from the menu bar
  press the Save and Test button

## Slide 23: Adding Scripts to the Control Panel
To add a script to the simulation module script pane:
  right-click in the scripts area
  select Edit Script List from the context menu
  use the Edit Scripts dialog to move desired scripts to the Selected list

## Slide 24: The hec.script package
These hec.script package contains some “wrapper” classes that simplify some common functions for the scripter. Just identify the classes you need on an include statement in your script such as:
  from hec.script include ResSim, MessageBox
For example, the ResSim class, a subclass of ClientAppWrapper provides the following functions:
  isWatershedOpened()
  getWatershed()
  getWatershedName()
  openWatershed(watershedName)
  closeWatershed()
  getCurrentModule()
Also Available is MessageBox

## Slide 25: What is Jython?
Jython is a Java-based implementation of the Python programming language. This means:
  You learn the Python language to learn Jython.
  Jython code can work seamlessly with Java code.
Anybody programming experience will pick it up quickly.
Others can quickly become effective by mimicking examples.
http://jython.org

## Slide 26: What is Python?
Python is a programming language that is
  interpreted
  open source
  object oriented
and has
  simple syntax
  high level dynamic data types
http://python.org

## Slide 27: Some Books Available

## Slide 28: Review
Scripts Executed During Simulations
  State Variable Scripts
  Scripted Rule Scripts
Scripts Executed Outside Simulations
  Static Scripts
Jython