## Slide 1: Mixed Populations
SPL Partial Duration Series Workshop
June 2023
Avital Breverman, E.I.T.
Hydraulic Engineer
US Army Corps of Engineers
Hydrologic Engineering Center

## Slide 2: Outline
Why mixed populations?
What are mixed populations?
How do we model mixed populations?
Challenges
Goal: Take steps toward “homogenizing” flood series and frequency analyses

## Slide 3: Why do we need to consider mixed populations?

## Slide 4: Populations vs. Samples
Notes: The sample is the set of observed values (e.g. annual peak flows at a gaging site).
The sample that we work with is one possible subset from the population.

## Slide 5: Populations vs. Samples
Population
Entire group you want to draw conclusions about
May be unknowable
Parameter
  Example: all annual maximum flows on the Mississippi River at Vicksburg
Sample
Part or subset of the population
Data you have or can collect
Statistic
  Example: annual maximum flow observations on USGS/NWIS
Notes: The distinction between populations and samples is crucial.
Often, samples are what you have, and populations are what you want to know.
The population is the entire group that you want to answer questions about.
However, it may be unknowable.
An example of the difference is on the Mississippi River at Vicksburg, Mississippi.
There exists some population of all annual maximum flows on the Miss at Vicksburg, but it’s an unknowable collection of flows because we can’t observe it forever.
We only have a sample of annual maximum flows through the National Water Information System (NWIS) hosted by the USGS.
Even though we want to answer questions about all the annual maximum flows, we only have a limited sample to work with.
What you are often doing is taking a sample, which is a part or a subset of that population, and using the statistics of that sample to estimate quantities in the population, which are called parameters.

## Slide 6: Assumptions
Sample is representative
Observations are IID
  Independent
  Identically-distributed
Ω
S
Notes: When we use the sample to make inferences about the population, we are making a few assumptions.
The most important one is that the sample we have is representative of the population.
In some circumstances it can be difficult to ascertain whether the sample is representative or not because the population is completely unknowable.
For surveys, where people are polled for their opinions, the sample can be checked for representation by comparing the demographics of the respondents in the sample to the general population demographics to see how representative a sample is.
For streamflow, if we have a limited record of flows, we would have to look at other variables such as climate to tell us if the period containing our sample is a good representation of the entire population.
The other major assumptions fall under the IID acronym, which stands for independent and identically distributed.
These assumptions have to do with the way that the observations that make up the sample were taken.
We want the observations to be independent of one another – that is, that they are not dependent on each other in some way.
We also want them to be identically-distributed, which is similar in nature to the representative sample assumption.
Think of identical distribution as the assumption that the samples come from the same population.

## Slide 7: Independence
Serial (in)dependence?
Hydrologic processes have long memories
“Overcount” certain ranges of observation
Notes: Sequent observations in time are likely to have a lot in common.
This occurrence is referred to as “serial dependence,” and in hydrology and other geosciences the occurrence of long “memory” of a system is referred to as the Hurst Phenomenon.
What happens is that in a finite record, depending on the strength of the serial dependence, is that our observations may not be truly representative of the full population, instead it is clustered to smaller regions of the population due to the slow evolution of the system in time.

## Slide 8: Independence
Generally safe by using annual maximum series
Consequence may be small
  Depends on strength of serial dependence
  Depends on the sample size
Notes: Recall that we use the AMS to model floods, primarily this is so we can make sure that the observations are sufficiently independent.
By breaking apart our record at the water year, we generally are able to take one flood per year that is far enough from the last flood that they are functionally independent.
That’s not always true, such as the site shown in the image. WY 1986 and 1987 annual peak flow events occurred 5 days apart, right around the October 1 WY demarcation.
Check your data!
With partial duration series (PDS) we can include more observations per year but have to be particularly careful that they are independent of each other.
AMS makes this easier but is made of fewer observations and some of these observations may not truly be floods.
Samples with high serial dependence may not represent the whole population well.
We can extract samples with smaller serial dependence, but very small sample sizes may have the same problem.

## Slide 9: Identical Distribution
A probability distribution represents the relative likelihood of all outcomes in a population
Each sample in a record of streamflow is assumed to come from the same population
Identical distribution = same population
Notes: The annual maximum for each year is a random variable.
We assume that each realization of a sequence of those random variables makes up our annual maximum series.

## Slide 10: Identical Distribution
Are all floods at a site from the same population?
Just because a flow is an annual maximum, does not guarantee it was created the same way as the others
Notes: This is the question we’re really getting at.
Nature isn’t on some sort of schedule – it doesn’t drop one flood in a watershed per year, pulled from the distribution of annual maximum floods.
Often, many physical processes have to occur together in order to create the largest flood in a year.
If a river discharge is the largest in a year, it is not guaranteed to be caused by the same thing as the largest in other years.
Orestimba Creek (one of those pathological examples) has 12 years with no flow at all, thus, 0 is the annual maximum.
There are also years that very much do not look like the rest.
Klemes,ˇ V., 1986, Dilettantism in hydrology; Transition or destiny?: Water Resources Research, v. 22, no. 9, p. 177S–188S.
“For it is by no means hydrologically obvious why the regime of the highest floods should be affected by the regime of flows in years when no floods occur, why the probability of a severe storm hitting this basin should depend on the accumulation of snow in the few driest winters, why the return period of a given heavy rain should be by an order of magnitude different depending, say, on slight temperature fluctuations during the melting seasons of a couple of years (p. 183S).”

## Slide 11
Population A
Sample
Observation
Population B
Observation
Inference?
Notes: When the sample contains observations from multiple populations, it may not be clear which population each sample value comes from.
If it’s assumed that the sample comes from a single population when there are in fact multiple populations being sampled, the sample no longer meets the ID assumption.
Here is an example of a mixture. Imagine you want to know what the distribution of the height of adults is. You take a sample of 200 adults and look at the distribution of the sample. Is this sample from a single population? At first blush this seems reasonable – we are sampling adult humans which could be thought of as one population. One issue is that the distribution of the height of females and males is likely to be pretty different (the average female in the US is 5’-4” and male 5’-9”.) If you look at the sample values of just females and just males (assuming you have recorded this information) you can identify the impact of a mixture on your sample. However if the only value you wrote down is the height, then you may not be able to evaluate the impact of the mixture.
Streamflow is similar. If your flows are caused by different things, for example snow floods and rain floods, floods of each type are likely to have different distributions.
Recording only the flow values means that we can’t evaluate the impact of this mixture without extra work.

## Slide 12: What are mixed populations?

## Slide 13: Mixed Populations
Some locations unfortunate enough to have multiple causes for flooding
What causes mixed populations?
  Meteorology
  Watershed Processes
  Disturbance
Notes: In some locations, the meteorology can create several kinds of flood hazards.
What are some properties of watersheds that may make it that floods occur in different ways which makes it more challenging to still assume IID for an AMS?

## Slide 14: Meteorological Scale
Storm Duration
Mesoscale ~6 hour
Synoptic ~48 hour
Notes: Differing scales of meteorology can dominate the precipitation mechanism.
Mesoscale meteorology can cause extremely heavy rainfall in small areas, largely driven by intense convective activity, while synoptic scale meteorology can affect much larger areas.
Much of the middle of the country (east of 100°W generally) has precipitation driven by more than one scale.

## Slide 15: Climatic Cycles
https://www.nature.com/articles/srep06651/figures/3
(Whitfield et al., 2010)
Notes: Long-period climatic cycles, such as the El Nino-Southern Oscillation and Pacific Decadal Oscillation, shown here, change continental-scale meteorology depending on their phase. Many cycles have phases measured by sea surface temperatures (SST) in particular patches of ocean.
Left image shows year-over-year snowpack (snow water equivalent) during cool and warm phase Pacific Decadal Oscillation (PDO).
Right image shows the fraction of global land area with significant drying and wetting induced by El Nino-Southern Oscillation during warm and cold PDO regimes.
There are four categories: ENSO+/PDO+, ENSO+/PDO-, ENSO-/PDO+ and ENSO-/PDO-. Then, the proportion of years that are either wet or dry are evaluated.
ENSO warm phase = La Nina
Since these cycles have long periods (e.g. ENSO typically 1-5 years, or PDO on the scale of multiple decades) several years in a row may fall into the same sort of cycle, resulting in several dry or wet years in a row. The effects can add up, and also affects our previous assumption of independence.

## Slide 16: Moisture Source
Notes: The tropical nature of Hurricane Harvey (plus the additional synoptic complexities) made the extreme floods in Houston possible.

## Slide 17: Watershed Processes
Rain-on-snow
Snowmelt
Saturation-excess runoff
  Antecedent soil moisture
  Frozen ground
Ice jams
Notes: The falling precipitation itself may not cause floods.
Rather, combinations of solid water on the ground (in the form of snow or ice) and falling precipitation may be the cause.
Saturation-excess runoff occurs when the ground is saturated and cannot infiltrate any more precipitation.
Top image shows ice jams along the Yellowstone River in Glendive, MT. Horse was carried 35 miles in 2 days on a block of ice!
Multiple mechanisms within a single watershed: Columbia River
  Lower Columbia River dominate flooding mechanisms (Ryan Cahill, NWP)
  Higher elevation areas (Canada, Cascades) accumulate significant snowpack
  Precipitation typically falls as rain in lower elevation portions and causes limited flooding
  Warmer years: shallower snowpack, precipitation falls as rain rather than as snow, winter flooding
  Cold, wet years: deep snowpack, spring snowmelt flooding
  Occasionally, a slow-melting snowpack meeting a warm, wet springtime storm will result in the dreaded rain-on-snow flooding which has water from both sources.

## Slide 18: Wildfire
Notes: Vegetation and soil absorb rainwater.
Fire destroys vegetation and creates a hydrophobic (water-repelling) surface layer which reduces the infiltration capacity of the land.
Watersheds experience increased runoff response/flood risk post-fire.
  A given storm depth will result in increased runoff post-fire compared to pre-fire.
Land surface recovers post-fire but that can take a few to many years. Wetter climates tend to recover more quickly than arid climates since more rain and higher intensity rain erodes the hydrophobic soil layer.
Division of floods into pre-fire and post-fire (until recovery occurs).

## Slide 19: Multiple Events
Sequencing of events may cause the biggest floods
Notes: Tropical storms per year in the Lake Okeechobee watershed, Florida.
The Lake’s level is sensitive to large volumes of inflow accumulated over long periods, and the biggest source of heavy rainfall is tropical storms.
The window is fairly large, so the possibility of multiple events bringing heavy rain is high.

## Slide 20
Annual Nonhurricane Events 1929-85
Computed Frequency Curves, Nonhurricane Series
Annual Hurricane Events, 1929-85
Graphical Frequency Curve, Hurricane Series
103
104
105
106
Flow (cfs)
% Chance Exceedance
99.99
99.9
99
90
50
10
1
0.1
0.01
Many zero years
Notes: How do you think an LP3 would fit to this kind of data?

## Slide 21: Identifying Mixed Populations
Streamflow data by itself usually not enough information
Need additional data to identify causal mechanism
Meteorological data most important
Sometimes simple rules work well

## Slide 22: Some Warnings
Day of year/season is a consequence, not a driver!
Regional skew is almost always developed from mixed flood series
Notes: Floods do not occur because the date happens to be May 15.
They occur because of snowmelt, prolonged precipitation on ground with high soil moisture content, hurricanes, etc.
Flood types should be assigned based on physical processes, not calendar convenience.
In some areas, the flood causal mechanisms might align well with day of year or season. But don’t make this assumption without investigation!
Regional skew studies almost always used mixed flood series, that is flood series that are not separated by causal mechanism (or even by seasons).
These regional skew values should not be used with individual flood type subsets

## Slide 23: Some Warnings
Notes: See the Mixed Populations section of Bulletin 17C

## Slide 24: Nonstationarity
Both mixed populations and nonstationarity deal with differences in the properties of floods
Key difference: nonstationarity is a one-way process
Notes: In a mixed population paradigm, each source of floods exists in varying numbers every year.
In any year a sample of floods can contain 0 to many floods from each mechanism.
However in a nonstationarity paradigm, we are generally seeing the rate of flood events per year change (increase/decrease) in one direction.
This means information from past floods is no longer relevant to the future.
In mixed populations, we still assume future floods will look like the past, even if there are multiple sources.

## Slide 25: Modeling Mixed Populations

## Slide 26: A Model for Mixed Populations
If C = max(A,B), then:
A: largest rain flood in a year
B: largest snow flood in a year
C is the larger of the two
Thus, C is the annual maximum
CDF
Any flood
magnitude
Notes: Reference: EM 1110-2-1415 Hydrologic Frequency Analysis

## Slide 27: A Model for Mixed Populations
What does this require?
  Determining the dominant flood mechanisms/types
  Identifying the annual maximum series for each type
  Fitting a distribution to each AMS
Notes: The first one requires some local knowledge and a little historical investigation. Look at the floods of record, what caused them? Do any of the flood variation mechanisms we identified before come into play? One exploratory mechanism would be to split a daily flow record (or IDA-scale data if you’re willing to deal with that much data) into seasons, extract the AMS for each season, and see if the empirical frequency plots cross. Crossing indicates that the mechanism might change by frequency.
The process of splitting the record by type “homogenizes” the record – that is, we work with subsamples that are much more likely to be identically-distributed.

## Slide 28
Flood A
Flood B
Notes: Flood mechanism A has a higher mean, lower variance and lower skewness than flood mechanism B.
Nearly every flood in the record for A is larger than for B, except for the two largest on record, which are both flood B.

## Slide 29
Flood A
Flood B
AMS (all)
Notes: How do the individual mechanisms look compared to just doing the AMS without breaking it down? If you extrapolate the combined curve, is it capturing the behavior of the largest floods well?

## Slide 30
1 -
For 2 flood types:
+ -
Notes: What is the probability of a type 1 flood exceeding 10,000 cfs?
What is the probability of type 2 flood exceeding 10,000 cfs?
What is the probability of either a type 1 or type 2 flood exceeding 10,000 cfs (combined probability)?
Flood type 1 is shown in green, flood type 2 is shown in red, the combined curve is shown in yellow, and the mixed (i.e. no separation) curve is shown in blue
The equations shown are for exceedance probablity

## Slide 31: Challenges

## Slide 32: Data Intensive
What flood types are worth considering?
How do we attribute a flood event to a type?
Coincident causal mechanisms
Notes: Each flood is unique but we have to strike a balance between (1) improving the performance of our statistical model and (2) dividing floods into too many types
We want to divide floods when the difference in the frequency-magnitude relationship is meaningful!
If the distribution parameters of two flood types are the same/similar, then it’s not worth dividing those flood types.
Attribution of flood events to causal mechanisms
  We typically know what physical processes caused the top 5-10 floods at a site
  What is a relevant antecedent time period?
  What is a relevant spatial window (larger for synoptic scale, smaller for local events)?
  Coincident causal mechanisms may mean that flood(s) do not fit neatly into one type
  Manual vs. automated approaches
  What data do we use? Snow, temperature, surface analysis maps, etc.
  There is only 1 USGS peak flow qualification code that describes flood causal mechanisms

## Slide 33: Sample Sizes
Splitting the annual maximum series by type can result in small sample sizes for each flood type
Consider applying peaks-over-threshold
Original AMS
Rain-only Events
Snowmelt Events
Notes: The usual challenges with flood frequency:
  Short data records
  We may have a peak flow that was recorded by WY, without a recorded date
If you have an 80 year POR with 80 annual maxima, if you split the record by two different flood types, you wind up with two much shorter records.
Bulletin 17C approach results in many, many perception threshold (far too many)
If you apply a peaks-over-threshold approach, the partial duration series by type might have much larger sample sizes.

## Slide 34: Fitting Distributions
What do you do with flood subsets?
What about rare events that drive the right tail of the probability distribution?
Flood Type
Notes: How do we implement a B17C analysis with a divided flood record?
What about floods caused by extreme events (atmospheric rivers, tropical cyclones, others)?
We may not have a large enough flood sample to reasonably fit an analytical probability distribution to these floods, but they are often the largest in the flood record.
The figure shows a gage in Pennsylvania. Four of the 8 largest floods were caused by tropical cyclones but the gage record only includes these 4 tropical cyclone-driven floods.

## Slide 35
Bulletin 17B (1982)
Notes: Identification and treatment of mixed populations/distributions was included in the Future Studies section of Bulletin 17B (1982)

## Slide 36
More supporting details, but no recipe
Also identifies potential issues with independence (serial correlation)
Familiar language
Bulletin 17C (2019)
Notes: And again in Bulletin 17C (2019)
Bulletin 17C does include more supporting details, such as referenced mixed population studies, but still no recipe

## Slide 37: Questions?