## Slide 1: Graphical Frequency Analysis & Plotting Positions
Beth Faber, PhD, PE
May 2024
Flood Frequency Analysis
Lecture 11

## Slide 2: Goals
Know how a graphical frequency curve differs from an analytical frequency curve
Understand plotting positions, what they estimate, and how they differ from each other
  and that plotting positions are the basis for a graphical frequency curve
Become familiar with the methods of developing graphical frequency curves for regulated flow and stage

## Slide 3: Graphical Frequency Analysis
Used for estimating an empirical or just non-analytical frequency curve with no assumed distribution
Used for regulated flows, channel or pool stages, partial duration series

## Slide 4: Outline
Graphical Frequency Analysis
Plotting Positions
  Statistical estimation theory
  Sampling Distributions to define uncertainty
Non-analytic (Graphical) Frequency Curves
  Regulated Flow Frequency Curves
  Stage Frequency Curves
Partial Duration Series (peaks over threshold)
  as graphical, rather than analytical
Graphical Frequency Analysis

## Slide 5: What Is Graphical Frequency Analysis?
Graphical analysis involves fitting a curve “by hand” to observed data plotted on probability paper (i.e., on a Normal probability axis)
  The horizontal location at which a data point is plotted is based on a selected plotting position — an empirical estimate of exceedance probability
Or, we might form a graphical frequency curve with quantile estimates from another source

## Slide 7: Why Use Graphical Analysis?
Plotting the data is a useful visual check on analytical frequency curves (e.g., frequency curves based on LPIII)
Sometimes, plotted frequencies of stage and regulated flow data cannot be adequately described by an analytical distribution such as Normal, or LPIII
  Under these circumstances, we use a graphical frequency curves – also called non-analytic

## Slide 8: Plotted Annual Maximum Regulated Flows
20
100
10
5
2
1.01
Return Period
Annual Exceedance Probability
1
0
max hydropower
channel capacity

## Slide 9: Does an Analytical Curve Make Sense?
20
100
10
5
2
1.01
Return Period
1
0
Annual Exceedance Probability
max hydropower
channel capacity

## Slide 10: Graphical Curve is Better for this
20
100
10
5
2
1.01
Return Period
1
0
Annual Exceedance Probability
max hydropower
channel capacity

## Slide 11: Outline
Graphical Frequency Analysis
Plotting Positions
  Statistical estimation theory
  Sampling Distributions to define uncertainty
Non-analytic (Graphical) Frequency Curves
  Regulated Flow Frequency Curves
  Stage Frequency Curves
Partial Duration Series (peaks over threshold)
  as graphical, rather than analytical

## Slide 12: Plotting Position – basic idea
A plotting position is an estimate of the exceedance probability for some observation of a random variable, such as flow or stage
For a period of record, plot each observation on the probability axis at the estimate of its exceedance probability based on its relative frequency
Estimated Probability = # of Occurrences
# of Trials → # years
= Relative Frequency

## Slide 13: a 30-year record of annual peak flows
1962-1991

## Slide 14: Rank the annual events…
1962-1991

## Slide 15: Estimate Exceedance Probability by Relative Frequency
exceeded
1 year of 30 ≈ 1/30
≈ .032
exceeded
2 years of 30 ≈ 2/30 ≈ .065
flow vs plotting position
Review from Intro Lecture

## Slide 16: Use log(flow) and frequency scale
flow vs plotting position
exceeded
2 years of 30 ≈ 2/30 ≈ .065
exceeded
1 year of 30 ≈ 1/30 ≈ .032
how do we extrapolate?
Review from Intro Lecture

## Slide 17: Remember the simple plotting position?
Rank the N observed flows from largest to smallest
The top ranked event has rank m = 1
The second largest event has rank m = 2
...
The smallest event has rank m = N
Estimate cumulative frequency based on the relative frequency of observations within the sample
incremental probability of each 1/N
exceedance probability of each m/N
simple Plotting Position m/N
the rank is the number of times the observation has been equaled or exceeded…
Review from Intro Lecture

## Slide 18: A Problem with simple PP = m/N
Probability of exceeding the smallest value is N/N = 1.0
  this is unreasonable
  it also implies a problem with the exceedance probability estimates for other values
Plotting position m/N is therefore statistically biased
Review from Intro Lecture

## Slide 19
EXAMPLE:
MILL CREEK, LOS MOLINOS, CALIFORNIA
simple
PLOTTING POSITION m/N

## Slide 20
99.5 99 95

## Slide 21: Choosing a Plotting Position
How Should a Plotting Position Be Chosen?
Plotting position is an estimator of exceedance probability
  an estimator is generally a function of the data
  two plotting position estimators seen so far are the Median and Weibull plotting positions
Other estimators discussed so far have been for the MEAN, standard deviation and skew
Remember that an estimator for the mean was given as:
Review from Uncertainty Lecture

## Slide 22: Creating a Sampling Distribution
Consider the sample mean, an unbiased estimator of the pop. mean
Let’s examine properties of estimating the mean from 10 data points
  There exists an actual “population” probability distribution of X
  The distribution of X has a mean m and standard deviation s
  As an experiment, we’ll generate 10-member random samples of flow X from the distribution of X above, 100 times
X
m
s
here, distribution of X is Normal
Review from Uncertainty Lecture
Notes: We’re going to construct the sampling distribution – this is the Monte Carlo simulation. We’re going to generate random samples, compute and estimate of the mean, and see how wrong they are.
The idea of the sampling distribution will be developed by looking at an estimate of the mean from 10 sample members. We can do a statistical experiment with a know distribution to examine the formation and properties of the sampling distribution of this estimator.
The experiment will start with a known distribution, and create random samples of 10 members each.

## Slide 23: Creating a Sampling Distribution
  Generate 100 different 10-member samples of flow X
  Compute an estimate of the mean, X, from each sample of 10
  A frequency analysis of the 100 estimates of X (one from each 10-member sample) would result in this histogram
  the average of 100 X would be close to the population value of the mean, m
  the histogram of X could be approximated by a Normal distribution
m = Population Mean
histogram of X
with N = 10
estimate of X
Review from Uncertainty Lecture
Notes: The experiment will start with a known distribution, and create random samples of 10 members each, and estimates the mean (using the sample average) of each sample. Done 100 times, this produces 100 estimates of the mean, each from a sample of size 10. This pink histogram is made up of the 100 estimates of the mean. It will be centered at the population values, because the estimator is unbiased.

## Slide 24: Sampling Distribution for the Mean
  CENTRAL LIMIT THEOREM: Since the estimator adds identical RVs, as N becomes very large, the distribution of X is Normal, with mean equal to the population value.
  The pink distribution to the right is the sampling distribution for the sample mean, X
The standard deviation of the distribution-of-sample-means is equal to
distribution of sample means, X
estimate of X
Review from Uncertainty Lecture
Notes: Because the Central Limit Theorem tells us that our sample of sample means is asymptotically Normal, we switch the histogram to a Normal distribution. It is centered on the known mean of the original distribution. It’s variance is equal to sigma-squared/N.

## Slide 25
sampling distribution for X, with N=10
Sampling Distribution for the Mean
for N = 10
for N = 50
X
population distribution
of X
m
Review from Uncertainty Lecture

## Slide 26: Sampling Distribution for Plotting Position
exceeded
1 year of 30 ≈ 1/30 ≈ .033
N = 30 ordered events
The sampling distribution for the estimate of exceedance probability is NOT symmetrical.
Not Normal because Central Limit Theorem does not apply. RVs are not summed
sampling distribution for exceedance probability of X1

## Slide 27: What are we uncertain about?
The estimated exceedance probabilities of events in the record are based on rank and the record length
  i.e., the largest event in N=30 years is assigned a likelihood near 1/30, or 0.033 annual likelihood
In what time period is it actually the largest? Longer than N? Shorter?
Can do a sampling experiment to see what the actual exceedance probability might be for the largest event in 30 years….
  Sample 30 years from U[0,1] as the AEP of each event
  Choose the smallest AEP = largest event from each sample
  Repeat for 1,000 samples
Source:
Dave Margo,
USACE / RMC

## Slide 28: What’s the real exceedance prob?
Sample 30 “years” as 30 AEPs ~ U[0,1]
Note the smallest AEP
Repeat for 1,000 samples
1 sample of 30 events as AEPs
smallest AEP from 1000 samples size N=30
approx ~U(0, 1)
1
0

## Slide 29: What’s the real exceedance prob?
Sample 30 “years” as 30 AEPs ~ U[0,1]
Note the smallest AEP
Repeat for 1,000 samples
1 sample of 30 events as AEPs
smallest AEP from 1000 samples size N=30
1
0
Linear Probability Axis
back to Linear Probability Axis to see direction of skew

## Slide 30: Weibull Plotting Position
For N=30,
PP1 = 0.032
Sampling Experiment
Smallest AEP of 30:
average of 1000
samples = 0.031
The Weibull plotting position is the mean of the sampling distribution at Xm, which results in an unbiased estimate of the exceedance probability
Sampling Distribution for Exceedance Probability
Exceedance Probability of Xm
Xm
mean
Return Period of largest event = N + 1
0
1

## Slide 31: Median Plotting Position
Area = probability = 50%
Xm
Median Plotting Position
Exceedance Probability of Xm
The Median plotting position is the median value of the sampling distribution for estimating the population probability of Xm
An approximation for N < 100 is:
Return Period of largest event = 1.5N + 1
For N=30,
PP1 = 0.023
Sampling Experiment
Smallest AEP of 30:
median of 1000
samples = 0.023
1
0

## Slide 32: Plotting Position Uncertainty, N=30
Plotting Positions versus Rank,
90% confidence interval for largest 3 of 30
Relative frequency of AEP of largest event (smallest AEP) in sample N=30
N=30
90% intervals

## Slide 33: Plotting Position Uncertainty, N=62
Plotting Positions versus Rank,
90% confidence interval for largest 3 of 62
Relative frequency of AEP of largest event (smallest AEP) in sample N=62
N=62
90% intervals

## Slide 34: Plotting Position Uncertainty, N=100
Plotting Positions versus Rank,
90% confidence interval for largest 3 of 100
Relative frequency of AEP of largest event (smallest AEP) in sample N=100
N=100
90% intervals

## Slide 35: Plotting Position Choice
Recommend using Weibull for graphical frequency curves when economic analysis involved
  Calculation of damages requires an expected or mean probability, so use Weibull to estimate graphical a curve
  The Weibull plotting position gives an expected value
Recommend using Median when comparing plotting positions to compute frequency curve such as LP3
Because comparing to a median estimate of LP3

## Slide 36
EXAMPLE:
MILL CREEK, LOS MOLINOS, CALIFORNIA
PLOTTING POSITION Comparison

## Slide 37
95

## Slide 38: Outline
Graphical Frequency Analysis
Plotting Positions
  Statistical estimation theory
  Sampling Distributions to define uncertainty
Non-analytic (Graphical) Frequency Curves
  Regulated Flow Frequency Curves
  Stage Frequency Curves
Partial Duration Series (peaks over threshold)
  as graphical, rather than analytical

## Slide 39: Regulated Frequency Curves
Two methods to produce a graphical regulated flow frequency curve:
Estimate a regulated frequency curve with regulated flow data and graphical frequency analysis
Develop unregulated flow frequency curve with LP3 fit. Combine it with reservoir regulation relationship to produce a graphical, regulated flow frequency curve
  Note the added uncertainty in the inflow/outflow relationship

## Slide 40: Regulated Frequency Curves
first method: graphical fit to annual peak regulated flow data
Source of regulated flow data:
  Observed data downstream of dam
  Route inflows through dam with reservoir model
    Use period of record inflows
    Estimate inflows from continuous simulation model
Hypothetical events are needed to estimate upper end of frequency curve
  define hypothetical inflow flood events (specified exc prob)
    exceedance probability of outflow assumed same as inflows
    starting water surface elevation is a critical consideration

## Slide 41
Unregulated Curve based on 100 years of record
Regulated Curve
Regulated Data

## Slide 42: Graphical Curve is Better for this
200
500
Cumulative Exceedance Probability
20
100
10
5
2
1.01
Return Period
42
max hydropower
channel capacity
Notes: Using synthetic events, we can estimate points higher on the frequency curve, to fill in the gap.

## Slide 43: Developing Regulated Flow-Frequency Curve
Second Method:
  Combine UNREGULATED flow-frequency curve with ‘unreg-regulated’ relationship

## Slide 44
PMF
250-yr
might instead create this relationship with a reservoir simulation model
Historical Reservoir Regulation Data
Regulated-Unregulated Relationship

## Slide 45
Unregulated Curve based on 100 years of record
Regulated Curve

## Slide 46: Additional Uncertainties in Regulation
Often, there is incidental flood management provided by reservoir water supply pool
  Reservoir starts with more flood space
  Non-flood reservoirs upstream might reduce peak
There are uncertainties in flood operation
  Real-time flood forecasts are sometimes used, and are contain a great deal of uncertainty
  Releases might be curtailed or diminished due to unforeseen contingencies, not using full capacities.
  Might reduce release to account for runoff below reservoir

## Slide 47: Outline
Graphical Frequency Analysis
Plotting Positions
  Statistical estimation theory
  Sampling Distributions to define uncertainty
Non-analytic (Graphical) Frequency Curves
  Regulated Flow Frequency Curves
  Stage Frequency Curves
Partial Duration Series (peaks over threshold)

## Slide 48: Stage-Frequency Curves
Two methods to produce a stage-frequency curve:
Estimate stage-frequency curve with stage data and graphical frequency analysis
Develop a flow frequency curve. Combine it with CURRENT flow-stage rating curve to produce stage-frequency curve
  requires a one-to-one relationship between flow and stage, which might not be feasible when complex water systems involved (backwater, tidal)
  better if flow is not regulated, and can use analytical fit

## Slide 49: Stage Frequency Analysis
first method, graphical fit to annual peak stage data:
  Use graphical frequency analysis, because analytical curve would smooth out relevant irregularities
  Pay attention to relevant stages: bottom, bankfull, etc
  A linear rather than log-scale is more reasonable
  Source of stage data:
    Observed gaged record (USGS peak flow file)
    Continuous simulation of hydraulic model, based on surrounding longer record gages

## Slide 50
Sometimes, it is not possible to define a one-to-one relationship between flow and stage
Sacramento-San Joaquin Delta, confluence of Sacramento and San Joaquin Rivers
Sacramento River
San Joaquin River

## Slide 51: Sacramento River at Walnut Creek, Stage-Frequency
1944 – 1988 annual peak stages
?
?

## Slide 52: Sacramento River at Walnut Creek, Stage-Frequency
?
?
90% confidence interval
1944 – 1988 annual peak stages
1944 – 1988 annual peak stages

## Slide 53
Sacramento Weir
Sacramento River
Sacramento River
American River
Sacramento Weir
ship channel
American River
Sacramento River
Sacramento
Hydraulic Modeling of the Period of Record
Yolo Bypass

## Slide 54
Sacramento Weir
Sacramento River
American River
Sacramento Weir
Fremont Weir
American River
Fremont Weir
Sacramento River
Feather River
Sutter Bypass
Sutter Bypass
Sacramento-SanJoaquin Delta
Delta
Sacramento
Feather River
Yolo Bypass
Yolo Bypass

## Slide 55
Non-exceedance Probability
Minimum Pool Elevation (ft)
boat dock at 385’
Others: Reservoir Min Stage vs frequency
might be reservoir stage rather than channel stage

## Slide 56: Others: Reservoir Max Stage vs frequency
Might extend curve with synthetic events and a reservoir model
could do Monte Carlo simulation for many synthetic events!
might be reservoir stage rather than channel stage

## Slide 57: Developing Stage-Frequency Curve
Second Method:
  Combine flow-frequency curve with flow-stage relationship

## Slide 58: Example Stage/Flow Rating Curve

## Slide 59: Resulting Stage-Frequency Curve
Stage Curve
Flow-Freq Curve based on 100 years of record
What uncertainties must we consider here?

## Slide 60: Outline
Graphical Frequency Analysis
Plotting Positions
  Statistical estimation theory
  Sampling Distributions to define uncertainty
Non-analytic (Graphical) Frequency Curves
  Regulated Flow Frequency Curves
  Stage Frequency Curves
Partial Duration Series (peaks over threshold)
  as graphical, rather than analytical

## Slide 61: Partial Duration Series
All peak events above a particular threshold
Annual Series vs Partial Duration
Review /preview from other lectures, only graphical

## Slide 62: Empirical Partial Duration Series (PDS)
Calculating plotting positions for AEP:
  If there are a total of k events in N years, then the plotting position for the smallest event (rank = k) is based on k/N
    However, if k > N, might be greater than 1.0
    can’t interpret as probability…
    The plotting position for this event is interpreted, not as exceedance probability, but as average of k/N events per year
Then the plotting position estimate states that on the average it is expected that 1.5 events per year will exceed 4 ft
  Example
  Smallest event = 4 ft
  k=61, N=42
62
Review /preview from other lectures, only graphical
Notes: It is possible to plot partial duration series empirically, with plotting positions. The exceedance probabilities are still interpreted as relative frequencies of equaling or exceeding a value, based on N years. The rank is interpreted the same way, as number of exceedances.
But, rank k might be higher than number-of-years N.
However, it is always possible to interpret as average number of exceedances per year, rather than likelihood of exceedance. This interpretation always makes sense.

## Slide 63: Frequency Analysis
Compute estimated probability as
relative frequency = # occurrences greater / # years
partial duration series
annual series
exceeded
1 year of 43
≈ 1/43 ≈ .023
exceeded
2 years of 43 ≈ 2/43 ≈ .046
Review from other lectures, only graphical
Notes: This is the same chart, with the probability axis changed to a Normal probability scale.

## Slide 64: Frequency Analysis
Generally, LP3 distribution does not fit a partial duration series frequency curve. Usually use graphical, or…..
partial duration series
annual series
Review from other lectures, only graphical
Notes: Generally, an analytical probability distribution will not fit the stage data. Instead, fit a graphical curve to the plotted data. Be careful about extrapolation.

## Slide 65: Why use Partial Duration Series?
Estimating expected damage when more than one damaging event per year
Concerned about the low end of the curve, for example for riparian ecosystem restoration studies
Lecture on Thursday!!

## Slide 66: Outline
Graphical Frequency Analysis
Plotting Positions
  Statistical estimation theory
  Sampling Distributions to define uncertainty
Non-analytic (Graphical) Frequency Curves
  Regulated Flow Frequency Curves
  Stage Frequency Curves
Partial Duration Series (peaks over threshold)

## Slide 67: Plotting Position Uncertainty
Plot with Weibull PP
Depiction of plotting position uncertainty for the largest three events
Source:
Dave Margo, USACE / RMC
j=1 (largest event) has almost 2 orders of magnitude uncertainty in 90% interval
0
1