## Slide 1: Analyzing Hydrologic Time-Series a potpourri
Flood Frequency Analysis
Hydrologic Engineering Center
Beth Faber, PhD, PE
Lecture 2
Notes: This lecture is a bit of a review and connect the dots of some material already covered, a preview of a topic that’s coming up, and then some new topics that fit within the theme.

## Slide 2: Goals
Review (or preview) some ways we might study a time-series, and what we can learn from it
What information we extract
What assumptions we make
What values or probabilities we can estimate
What type of analysis each requires

## Slide 3: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
No independence - persistence
independence
3
Assumption
independence
Annual Extremes
  annual maximums or minimums
  UNregulated
  instantaneous flows or longer duration avg flow/volume
Notes: These are the topics I’ll cover. We divide the time period of the data, and whether we use all the data or isolate the extremes. These choices affect the assumptions we can make about the data set. Isolating annual extremes provides enough time between values that we can assume independence. Using all the data at a daily step, the values are persistent, and can’t assume independence.

## Slide 4
often, annual peaks are instantaneous values
American River at Fair Oaks (unregulated)
Streamflow data, daily flow record
consider each year’s maximum flow
reservoir constructed
108 years of daily unregulated streamflow data
Notes: We extracted an annual max series by selecting the largest flow event in each year, based on some definition of “year,” such as calendar (starting Jan 1) or water (starting Oct 1).

## Slide 5
often, annual peaks are instantaneous values
Streamflow data, find annual max
consider each year’s maximum flow
Review from Intro Lecture
Notes: We extracted an annual max series by selecting the largest flow event in each year, based on some definition of “year,” such as calendar (starting Jan 1) or water (starting Oct 1).

## Slide 6: American River, ANNUAL MAX SERIES, AMS
annual maximum values are independent
6
Review from Intro Lecture
Notes: The data set is now 108 values of annual maximum/peak flows.

## Slide 7: Assumptions
What we have: series of annual maximum flows
Treat these flows as a random, representative sample from the flood population of interest
Generally, we assume the sample is IID
  annual peak flows are random and independent
  peak flows are identically distributed – homogeneous data set
  sample is adequately representative of the population
  (estimate of the distribution improves with sample size)
  NOTE, we’re assuming the data is homogeneous, stationary….
Review from Intro Lecture
Notes: IID = independent and identically distributed. Not so much that they ARE identically distributed as that we assume it is reasonable to fit a single distribution to them. Except when we can’t assume that….

## Slide 8: Histogram
divide data range into bins, count number of observations in each bin (frequency), divide by total (relative frequency)
this shape is similar to a PDF, probability density function
0 25 50 75 100 125 150 175 200 225 250 275
8
switch to log10(flow)
3.2 3.4 3.6 3.8 4.0 4.2 4.4 4.6 4.8 5.0 5.2 5.4 5.6
Log Flow (thousands of CFS)
Review from Intro Lecture
Notes: A histogram gives a good view of probability of the sample.

## Slide 9: Definition of PDF and CDF
A Probability Density Function (PDF), f(x), defines the probability of occurrence for a continuous random variable.
area under curve = probability
The Cumulative Distribution Function (CDF), F(x) is the probability the random variable is less than some value
curve = probability
p
p
X
X
9
PDF
CDF
of Variable X
of Variable X
Review from Intro Lecture

## Slide 10: Empirical Cumulative Distribution
Empirical or Graphical estimate: based on order statistics, using plotting position (estimated [non-]exceedance probability)
  Estimated probability of observation magnitude is based on its position within the sample
  Each observation has an equal incremental prob = 1/N
  mi = rank of ordered observation i (m=1 as smallest value, N as largest) N = total # of observations
P[X ≤ xi] =
mi
N
estimate probability that outcome will be smaller than observation xi by the fraction of the observed sample that is smaller
based on observation
i.e., relative frequency
10
Review from Intro Lecture
Notes: Rank is where that sample member is in the line-up of all sample members ordered by magnitude. So, it’s a way of counting the number of events less than or equal to.
Plotting position is the estimate of the cumulative prob of each observation, based on the sample size and the position of each observation within the sample that’s been sorted by magnitude. So, effectively we’re computing the relative frequency of being less than a given observation, based on how many values in the sample were less than that observation – defined by the rank.

## Slide 11: Empirical Cumulative Distribution
Year | Rank | Flow | Non-Excdnc Probability |  | Year | Rank | Flow | Non-Excdnc Probability
1997 | 108 | 252431 | 0.99 |  | 1955 | 14 | 10528 | 0.13
1955 | 107 | 189073 | 0.98 |  | 1975 | 13 | 10389 | 0.12
1964 | 106 | 183242 | 0.97 |  | 1972 | 12 | 10046 | 0.11
1986 | 105 | 170960 | 0.96 |  | 2008 | 11 | 9150 | 0.10
2005 | 104 | 161731 | 0.95 |  | 1966 | 10 | 8659 | 0.09
1963 | 103 | 152614 | 0.94 |  | 1939 | 9 | 8500 | 0.08
1950 | 102 | 132000 | 0.94 |  | 1907 | 8 | 8460 | 0.07
1980 | 101 | 124915 | 0.93 |  | 2001 | 7 | 8045 | 0.06
1928 | 100 | 119000 | 0.92 |  | 1931 | 6 | 7920 | 0.06
1982 | 99 | 113126 | 0.91 |  | 1990 | 5 | 7606 | 0.05
1907 | 98 | 105000 | 0.90 |  | 1961 | 4 | 6914 | 0.04
1909 | 97 | 98000 | 0.89 |  | 1988 | 3 | 5447 | 0.03
1970 | 96 | 88316 | 0.88 |  | 1994 | 2 | 5009 | 0.02
1969 | 95 | 83526 | 0.87 |  | 1977 | 1 | 2359 | 0.01
Plotting Position:
General Formula
Weibull: a = 0.0, b = 1.0
Median: a = -0.3175, b = 0.365
Median: a = -0.3, b = 0.4
Weibull plotting position
P =
m + a
N + b
largest 14 values
smallest 14 values
Notes: These are the largest 14 and smallest 14 values in the 108-year data set.

## Slide 12: Empirical Cumulative Distribution
CDF = cumulative distribution function
12
Review from Intro Lecture
Notes: First, plot in the typical CDF form, with flow on horizontal and cumulative probability on vertical. But, now can plot every observation, rather than every bin.

## Slide 13
Empirical Cumulative Distribution
for a Corps frequency curve, we switch axes...
13
annual
Review from Intro Lecture
Notes: Switch axes to probability on horizontal and probability on vertical. Note, annual probability because one value each year, and computing relative frequency based on years.

## Slide 14: Empirical Cumulative Distribution
0
1
...and adjust axis scales
Normal probability scale
…also called a frequency curve…
14
annual
Review from Intro Lecture
Notes: Switch probability axis from linear to Normal. Note, normal data would plot as a straight line on normal axis.
How to we create a normal axis?
the axis is linear in Zp, the standard normal deviate of probability p.
The axis is based on the normal PDF that you can see as a shadow along the horizontal, so
(2) we plot a given probability where the area under the PDF (from left to right) equals that probability.

## Slide 15: Empirical Cumulative Distribution
log scale
0
1
...and adjust axis scales
Normal probability scale
…also called a frequency curve…
15
annual
Review from Intro Lecture
Notes: Switch vertical axis to log(flow).
Note, the data becomes close to a straight line, so log(flow) is close to Normal, and flow is close to logNormal in this case.

## Slide 16: Empirical Cumulative Distribution
20
100
10
5
2
1.01
Return Period
Cumulative Exceedance Probability
1
0
log scale
largest in 108 years, probability ≈ 1/108 ≈ 0.9%
0.9%
equaled or exceeded 11 times in 108 years ≈ 10%
switch to exceedance
Normal probability scale
…also called a frequency curve…
16
Annual
Review from Intro Lecture
Notes: Switch from non-exceedance to exceedance probability. Note that return period = 1 / (exceedance prob).
Recall the interpretation of the plotting positions. The largest even is explicitly interpreted as equaled or exceeded once in 108 years, etc

## Slide 17: Empirical Graphical Cumulative Distribution
Cumulative Exceedance Probability
1
0
Normal probability scale
log scale
20
100
10
5
2
1.01
Return Period
17
Annual
Notes: With no further assumptions, we have an empirical or graphical curve only.

## Slide 18: Analytical Distribution
Cumulative Exceedance Probability
1
0
Normal probability scale
log scale
Log Pearson III per Bulletin 17B/C
20
100
10
5
2
1.01
Return Period
for unregulated, instantaneous annual maximums
18
Annual
Notes: Or, we can assume an analytical distribution, and estimate its parameters from the 108 member sample of values. This is the log Pearson type 3 distribution recommended in Bulletin 17B/C for unregulated annual maximum values

## Slide 19
Bulletin 17B
dated March 1982
Bulletin 17C
dated May 2019
19
Notes: Reference

## Slide 20: B17B/C: Frequency Analysis of Annual Peak Flows
Estimate LogPearson III distribution for unregulated annual peak flows
  Method of Moments
Data challenges:
  Missing Flows (Broken or Incomplete Record)
  Low and High Outliers
  Zero Flows
Additional information to improve estimates:
  Historical/Paleo Information
  Regional Skews (use a weighted skew)
  Allowing a longer record site to improve short record estimate
moments of sample used to estimate moments of distribution
many of the methods for handling data challenges and using additional information are improved in Bulletin 17C
20
Notes: Fitting an LP3 to annual maximums is the primary guidance. But the details are in dealing with difficulties in the data set, and in bringing in additional data that can provide more information.

## Slide 21: Analytical Distribution
Cumulative Exceedance Probability
1
0
Normal probability scale
log scale
90% confidence interval
Log Pearson III per Bulletin 17B/C
20
100
10
5
2
1.01
Return Period
for unregulated, instantaneous annual maximums
21
Annual
Notes: The fit of the LogPearson type 3 distribution (LP3) also includes estimating the 90% confidence interval. The interval can be interpreted simply as meaning there is a 90% change the correct population frequency curve is within this range.

## Slide 22: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
No independence - persistence
independence
22
Assumption
independence
Notes: These are the topics I’ll cover. We divide the time period of the data, and whether we use all the data or isolate the extremes. These choices affect the assumptions we can make about the data set. Isolating annual extremes provides enough time between values that we can assume independence. Using all the data at a daily step, the values are persistent, and can’t assume independence.

## Slide 23: Also Interested in Regulated Flow
Reservoir Storage Level
Inflow
Release
115,000 cfs
160,000 cfs
23
Notes: This figure shows the regulation of a flood event through a reservoir, where the reservoir stores all of the water volume in excess of the same channel flow or “objective release” and then releases that volume more slowly after the event.

## Slide 24: Streamflow data, regulated
Is this regulation homogeneous?
homogeneous = identically-distributed = stationary
24
reservoir constructed
period of record 1955 - 2009
Notes: The red line is the reservoir outflows, beginning when the reservoir was constructed (1955) and ending in 2005. These are regulated flows.
We can extract an annual maxima series of this data we have 2 issues:
  Are we looking at homogeneous data during the regulated period? Was the reservoir regulated the same way during this period? Usually not. Reservoir operations change. Not identically distributed and not stationary.
  Record lengths are different: 108 years of unregulated flow vs. 50 yrs of regulated flows
We can route our entire POR of data through our reservoir simulation model to ensure we have homogeneous data (the same and current reservoir operations) and expand data set

## Slide 25: Streamflow data, regulated
these are simulated outflows:
HOMOGENEOUS operation
2 benefits:
homogeneous operation, and longer period
25
Notes: Here, we see the unregulated record simulated with the current operation strategy. So, the operation is homogeneous. Hopefully, the inflow record is, too!
Light blue is modeled regulated record (from reservoir modeling)  plotting positions do not line up since we only simulated 80 years of record.
Longer period of record, same operations

## Slide 26: Streamflow data, regulated
regulated annual peaks are often daily values
26
consider each year’s maximum flow
Notes: Create the annual maximum series (AMS) in the same way we do for unregulated flows.
Note, in this case, the simulated period is not the complete unregulated record. So, the POR is a bit shorter.

## Slide 27: Folsom Release, ANNUAL MAX
27
annual maximum values are independent
Notes: Now we have a record of regulated peaks (81 regulated maxima). Channel capacity is 115000 cfs.
Frequency analysis of regulated flows by sorting them, ranking them, and computing plotting position

## Slide 28: Plotted Annual Maximums
Cumulative Exceedance Probability
1
0
28
20
100
10
5
2
1.01
Return Period
max hydropower
channel capacity
Notes: Hollow diamonds are the unregulated record.
Solid diamonds are the regulated record, plotted in the same way.
Note that there are relevant flow thresholds, such as channel capacity at the upper end, that are horizontal over a range of exceedance probability.
These thresholds are important
  Lower threshold of 4,000 cfs is hydropower release
  Upper threshold of 115,000 cfs is channel capacity
  We see that in our record, there were no events that exceeded the flood pool capacity and required a release above the channel capacity
  No regulated flows beyond 115,000 cfs in our record

## Slide 29: Does an Analytical Curve Make Sense?
Cumulative Exceedance Probability
1
0
20
100
10
5
2
1.01
Return Period
29
max hydropower
channel capacity
Notes: An analytical fit to this data would smooth through the important flat areas that represent flow thresholds. This is not what we want since it removes our thresholds!
Sometimes we do want to smooth through sampling error. But, in this case, the flats spots are meaningful.
Regulated flows are better represented by a graphical frequency curve.

## Slide 30: Graphical Curve is Better for this
Cumulative Exceedance Probability
1
0
20
100
10
5
2
1.01
Return Period
30
Cumulative Exceedance Probability
1
20
100
10
5
2
1.01
Return Period
how do we extrapolate?
max hydropower
channel capacity
Notes: It is better to do a graphical fit to this data, so we can capture the thresholds that are relevant, and smooth through the ones that are not.
Problem of extrapolation?

## Slide 31: Extending a Regulated Curve
To extend a regulated frequency curve, we can construct synthetic events with a specified frequency, e.g. 100-yr, 200-yr, etc, and regulate them
How?
  Estimate frequency curves for longer duration average flows or volumes (3-day, 7-day, 30-day, etc)
  Construct hydrograph for a given frequency
  Route through operation model to get peak outflow
  NOTE: will assume likelihood of peak release is related to likelihood of peak inflow
31
Notes: We extrapolate a graphical curve by estimating higher values (lower probability) regulated flows based on unregulated flood events of the desired probability.
Construct events with a particular exceedance probability
Estimate family of frequency curves (longer duration or volumes)
Scale up historical event to the given frequency curve based on longer duration average
Route event through reservoir model
Assumption: probability of peak release is equal to likelihood of peak inflow

## Slide 32: Graphical Curve is Better for this
Cumulative Exceedance Probability
1
32
200
500
20
100
10
5
2
1.01
Return Period
max hydropower
channel capacity
Notes: It is better to do a graphical fit to this data, so we can capture the thresholds that are relevant, and smooth through the ones that are not.
Problem of extrapolation?

## Slide 33: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
33
Assumption
No independence - persistence
independence
independence
Notes: We’ll move on to frequency analysis of longer durations of flow, for the purpose of generating scaled synthetic hydrographs.

## Slide 34: Longer Durations of Flow/Volume
Volume Frequency Analysis
Create a family of frequency curves for a given site that specify average flow across various durations
  Compute X-day moving average TS for various durations, X
    X might be 1-day, 5-day, 30-day etc.
  Extract annual maximums for each duration
  Perform frequency analysis for each duration
    Similar to Bulletin 17B/C procedure, but not instantaneous peak
    Compute plotting positions and distribution parameters from each period of record sample
34
Notes: Why are we looking at longer durations? When reservoir are involved for providing flood storage, we’re more interested in the volume of water that will arrive across some period of time than just the highest flow. So we want to estimate the likelihood of flow volumes.

## Slide 35: Longer Durations Max Average Flows
1-day Daily Average
5-day Daily Average
10-day Daily Average
1-day AMS
5-day AMS
10-day AMS
35
Notes: These are rain floods, that are shorter – only a few days. On the left is the time-series of moving X-day averages for 1 event, with the maximum values noted. On the right is the record of annual maximums generated this way across the record.

## Slide 36: Longer Duration Max Average Flows
36
Notes: This is a location where the highest flows are snow-melt floods that last longer than rain floods. It lets us see the annual maximum average flows more easily.

## Slide 37: Max Flow at Folsom Volume-Freq Curves
Percent Chance Exceedance
Average Flow (cfs)
shorter duration (1 day) is more extreme
Note: average flow easier to plot than volume – curves are closer
1DAY
3DAY
7DAY
15DAY
30DAY
37
Notes: This figure has both the sorted and plotted annual maximums, and fitted LP3 curves for each. Note, these are X-day average flows, because X-day volumes would be much higher for longer durations and not plot nicely. Showing average flows let’s us show them all on one plot this way.

## Slide 38: Note: it’s important to define the year
define a year that won’t break up longer high flow averages
what about for low flows?
38
Notes: It is important to choose a start date that captures all flood events from a certain hydrologic regime. If high flows generally occur between November and May, then the year should not start between these months. This will minimize the possibility that the same flood event is used for consecutive years.

## Slide 39: Synthetic Events
Create synthetic, low-frequency event hydrographs to model extremes, or other watershed conditions (e.g. regulated flow)
  perform volume frequency analysis
    produce the family of X-day average flow frequency curves
  choose an historical event as a hydrograph “shape”
  scale the hydrograph to match flow of chosen exceedance probabilities (e.g., the 1% chance event)
    read the average flow for each duration for the chosen exceedance probabilities
    scale the hydrograph up or down to match that avg flow
39

## Slide 40: Max Flow at Folsom Volume-Freq Curves
Percent Chance Exceedance
Average Flow (cfs)
shorter duration (1 day) is more extreme
200-year
1DAY
3DAY
7DAY
15DAY
30DAY
40
Notes: The average flow exceeded with a 0.005 (or, 0.5%) exceedance probability can be read for each curve. This value will allow us to create a synthetic event with that the desired estimated probability.

## Slide 41: Rescaling Historical Event
1997 flood event
0.97%
41
Notes: This is an historical event on the American River, from 1997. The exceedance probabilities of the maximum X-day average flows are noted.

## Slide 42: Rescaling Historical Event
1997 flood event, scaled to 3-day 1-in-200%
0.97%
42
Notes: This is the 1997 flood event scaled to the 0.5% (1 in 200 year) 3-day max average flow.

## Slide 43: Modeled Operations
Storage Level
115,000 cfs
Release
160,000 cfs
Inflow
43
Storage Level
Release
115,000 cfs
160,000 cfs
Actual 1997 event
Scaled 1/200-year 1997 event
Notes: Simulating the 1997 event through the reservoir shows it not exceeding the lower objective release.

## Slide 44: Graphical Curve is Better for this
200
500
Cumulative Exceedance Probability
20
100
10
5
2
1.01
Return Period

## Slide 45: Volume Frequency Analysis
  Sometimes there’s an additional step needed in the volume frequency analysis…
  Check curves for consistency
    Curves should not cross
    Smooth by plotting log moments vs duration, or versus each other
45
Notes: The curve have to make sense.

## Slide 46
When volume-frequency curve require adjustment
Note: average flow easier to plot than volume – curves closer
46
Notes: The sample for each duration is ranked and plotted separately, with an LP3 curve fitted to each. For high flow data, LP3 fit is generally successful.
The probability axis shows exceedance probability, and so extreme values plot to the right. Shorter durations are more extreme (in this case, higher) than longer durations.
When LP3 parameters are estimated for each separate data set (each duration column), the curves might not form a regular set, might cross. The parameters sometimes need to be adjusted…

## Slide 47
To prevent curves
from crossing…
47
Notes: Here standard deviation is plotted against mean, and smoothed.

## Slide 48
Resulting Volume Duration Frequency Curves
Note: average flow easier to plot than volume – curves closer
48
Notes: The sample for each duration is ranked and plotted separately, with an LP3 curve fitted to each. For high flow data, LP3 fit is generally successful.
The probability axis shows exceedance probability, and so extreme values plot to the right. Shorter durations are more extreme (in this case, higher) than longer durations.
When LP3 parameters are estimated for each separate data set (each duration column), the curves might not form a regular set, might cross. The parameters sometimes need to be adjusted…

## Slide 49
peak
1-day
3-day
7-day
15-day
30-day
Balancing across multiple durations
Notes: Using the 1% chance exceedance values of each duration, create a “balanced” hydrograph that has those flow volumes. Could be scaled from an historical event. Note, this historical event might not be the best model, as the 1% values show a greater difference between peak and 1-day average max flow.

## Slide 50: High vs Low Flows
High flows
  Can usually fit an analytical distribution function to unregulated high flows
  Generally not to regulated high flows - need graphical
Low flows
  can be more non-linear (effects of groundwater, etc),
  might only allow graphical (empirical) frequency curve
50
Notes: So far we have talked about annual maxima (high flows).
We are also interested in low flow frequency, with annual minima.
Unregulated high flows allow us to use a parametric model, or an analytical probability distribution.
Unregulated low flows very rarely fit an analytical distribution. We more often use a graphical frequency curve.

## Slide 51: Low Flow Frequency Analysis
Based on annual minimum flows
Estimate the probability that X-day average flow will not exceed a given value:
mQn: m consecutive day average,
n year return period
example: 7Q10, 7-day 10-year low-flow
 There is a 10% chance that the 7-day average low-flow will be less than this value in any year
As the duration increases to months, independence between events becomes less likely (7-day is common)
X
p
Notes: For low flows, we work with NON-exceedance probabilities.
A metric that’s sometimes used in watershed restoration analysis and low flow regulation is ….

## Slide 52: Regulated Low Flow Volume-Freq Curves
7Q10, 7DAY 10YEAR
7DAY
3DAY
1DAY
Average Flow (cfs)
Percent Chance Non-exceedance
note that
low-flow curves are closer...
510
15DAY
Notes: We’re interested in extremes. So, for annual minimums, we plot the NON-exceedance probability.
We usually keep the extremes on the right. So, zero non-exceedance probability is still on the right. The curves for different X-day average flows are closer, because low flows are not a peaky as high.

## Slide 53: Folsom Minimum Pool Frequency
Non-exceedance Probability
Folsom Minimum Pool Elevation (ft)
boat ramp at 385’
boat ramp at 320’
53
Notes: Also look at annual minimums (and maximums) for other variables. In this case, minimum reservoir pool.

## Slide 54: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
54
Assumption
No independence - persistence
independence
independence
Notes: We’ll take a quick look at partial duration series, or peaks over threshold.

## Slide 55: Annual Maximum Series (AMS)

## Slide 56: Partial Duration Series (PDS)
Peaks over Threshold
Choose not just the most extreme each year, but all INDEPENDENT events that fall beyond a defined threshold

## Slide 57: Empirical Partial Duration Series (PDS)
Calculating plotting positions for AEP:
  If there are a total of k events in N years, then the plotting position for the smallest event (rank = k) is based on k/N
    However, if k > N, might be greater than 1.0
    can’t interpret as probability…
    The plotting position for this event is interpreted, not as exceedance probability, but as average of k/N events per year
Then the plotting position estimate states that on the average it is expected that 2.0 events per year will exceed 1000 cfs
  Example
  Smallest event = 1000
  k=50, N=25
57
Notes: It is possible to plot partial duration series empirically, with plotting positions. The exceedance probabilities are still interpreted as relative frequencies of equaling or exceeding a value, based on N years. The rank is interpreted the same way, as number of exceedances.
But, rank k might be higher than number-of-years N.
However, it is always possible to interpret as average number of exceedances per year, rather than likelihood of exceedance. This interpretation always makes sense.

## Slide 58: Empirical Frequency Curves: American River unreg partial duration vs annual max
partial duration series
annual maximum series
annual peak flow (cfs)
can only plot the top N points on a probability axis
N=years
58
Notes: AMS and PDS curves are very similar at the top. But, they tend to differ quite a lot below the median, and often start to diverge below 10%.
We use PDS when we care about the lower end of the annual maximum frequency curve.

## Slide 59: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
59
Assumption
No independence - persistence
independence
independence
Notes: We’ll take a quick look at partial duration series, or peaks over threshold.

## Slide 60: Flow/Stage Duration Curve
Fraction of days exceeding a given value, referred to
as percent of time exceeded
OR
Estimate of the likelihood that a daily flow will exceed a
particular level (refers to future, not soon…)
Graphical display of stream characteristics
Navigation, run-of-river hydropower, water supply
not necessarily the annual extreme...
60
Notes: When using daily data, we compute percent of time exceeded.

## Slide 61: Flow- or Stage-Duration Curves
Plot of Flow vs Percent of time exceeded
(see Maidment, 1992, pg. 8.27, 18.53, 27.40)
Computation
  Rank all the daily flows for period of record from largest to smallest
  Percent of time exceeded for each = rank
  total number of
  days in record
relative frequency!

## Slide 62: Starting with a daily flow record…
Question: How much of the time can we expect future flows to be between 2,000 and 4,000 cfs?
Interested in hydropower generation
62
How often were past flows between 2,000 and 4,000 cfs?
the REGULATED record
Notes: Here’s the daily outflow record from the reservoir simulation we’ve been looking at.

## Slide 63: Order the data from low to high, and compute relative frequency of exceedance
2000 cfs
4,000 cfs
19%
70%
More than 4000 cfs is released 19% of the time, and
at least 2000 cfs is released 70% of the time,
so, 51% between 2000 and 4000 cfs
2000
4000
considering all flows, not just annual extremes
… but lost event DURATION
63
Notes: We can plot every value versus its percent of time exceeded.
Though this is called a “duration curve,” we do not maintain information about the duration of time of each exceedance of a given flow. All days of exceedance are clumped together.

## Slide 64: Comparing Unregulated to Regulated
2000 cfs
4,000 cfs
19%
70%
Regulated flows are between 2000 and 4000 cfs 51% of the time,
unregulated flows are in the range 14% of the time.
44%
30%
American River flows, unreg and reg
2000
4000
64
Notes: The red curve uses the same process of generating a duration curve, but for unregulated flow. By comparing, it’s clear that the reservoir allows release to be within the hydropower generation range much more often than a run-of-river hydropower plant would have.

## Slide 65: Flow Duration Analysis Cautions
Data points are not independent, so frequency does not approximate probability in the near term
  Only approximates probability in future
  An estimate of daily probability, not annual
Analytical distributions do not fit data
Need sufficient record length to estimate distribution tails
65

## Slide 66: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
66
Assumption
No independence - persistence
independence
independence
Notes: Moving on to summary hydrographs

## Slide 67: Summary “Hydrographs”
Rio Madeira @ Porto Velho, Brazil
Sept 1 of each year 1967 – 2015
4834
1967 - 2005
Sept 1 only
min = 2630
max = 11614
50%
90%
7750
67
called
“cyclic analysis” in HEC-DSS
Notes: Summary hydrographs look at day of year, to give an overall summary of flow at a site across seasons. The method does a frequency analysis for each day of the years, and either plots all values, or plots summary values.
This image shows the frequency analysis for Sept 1 on the right, as a histogram and a cumulative histogram.

## Slide 68: Summary “Hydrographs”
Sept 1 of each year 1967 – 2015
4834
1967 - 2005
Sept 1 only
min = 2630
max = 11614
50%
90%
7750
% of time less than
max
90%
75%
50%
25%
10%
min
68
called
“cyclic analysis” in HEC-DSS
Rio Madeira @ Porto Velho, Brazil
Notes: Given the frequency analysis for each day, the left plot can show percentiles, rather than all flow years. Note that the curves on the left are not really hydrographs. The daily values do not follow each other.

## Slide 69: Summary “Hydrographs”
Unregulated Regulated
% of time less than
90%
75%
50%
25%
10%
% of time less than
90%
75%
50%
25%
10%
American River blw Folsom
69
Notes: Summary “hydrographs” for American River, unregulated and regulated. Note wet winter and dry summer, and how regulated record shows lower high flows, and higher low flows.

## Slide 70: Summary “Hydrographs”
Unregulated Regulated
% of time less than
max
90%
75%
50%
25%
10%
% of time less than
max
90%
75%
50%
25%
10%
American River blw Folsom
70
Notes: Summary “hydrographs” for American River, unregulated and regulated.
This version includes maximums for each day. Note, we see nearly all winter flood events, because they usually happened on different calendar dates. However, it makes it more clear that the max “hydrograph” doesn’t represent a flow time-series that can occur.
Seeing the maximum flows makes it clear that the reservoir is able to maintain each of the historical events to the channel capacity.

## Slide 71: Summary “Hydrographs”
% of time less than
90%
75%
50%
25%
10%
% of time less than
90%
75%
50%
25%
10%
Unregulated Regulated
Columbia River at the Dalles
71
Notes: Summary “hydrographs” for Columbia River, unregulated and regulated. Note snowmelt in spring, and how regulated record shows a large decrease in the snowmelt flood flow.

## Slide 72: Summary “Hydrographs”
Unregulated Regulated
% of time less than
max
90%
75%
50%
25%
10%
% of time less than
max
90%
75%
50%
25%
10%
Columbia River at the Dalles
72
Notes: Seeing the maximum flows makes it clear that the reservoir system is able to maintain nearly all of each of the historical events to the channel capacity.

## Slide 73: Topics
Annual Extremes
  annual maximums or minimums
  UNregulated, or regulated
  instantaneous flows or longer duration avg flow/volume
Partial Duration (peaks over threshold, POT)
  graphical (non-analytical)
Daily flows or stages
  Duration Curves
  Summary Hydrographs
73
Assumption
No independence - persistence
independence
independence
Notes: These are the topics I’ll cover. We divide the time period of the data, and whether we use all the data or isolate the extremes. These choices affect the assumptions we can make about the data set. Isolating annual extremes provides enough time between values that we can assume independence. Using all the data at a daily step, the values are persistent, and can’t assume independence.