## Slide 1: Introduction to Block Maxima
Flood Frequency Analysis PROSPECT
May 2024
Melissa Mika, P.E.
(slides courtesy of Gregory Karlovits)
US Army Corps of Engineers
Hydrologic Engineering Center

## Slide 2: Purpose
Understand a fundamental technique in statistical hydrology

## Slide 3: Outline
Block maxima
Annual maximum series

## Slide 4: Block Maxima

## Slide 5: Block Maxima
Break a sample into equal sized parts
  Parts can’t overlap
Take the largest observation from each part
Sample
1
2
3
4
5
6
Block | Maximum Value
1 | 117.7
2 | 110.9
3 | 112.2
4 | 115.9
5 | 107.3
6 | 122.5

## Slide 6: Why?
Helps with the “IID” assumption
  Observations are:
    Independent
    Identically-distributed
Lets us look at behavior of large observations (i.e. floods)
The math is “friendly”

## Slide 7: Example
Kindergartners
Class 1
Class 2
Class 3
Class 4
Class 5
Class 6
Each kindergartner has a height of N(42.8, 1.76) inches
20 children / class
Children are randomly assigned to a class
Notes: I don’t have real class data so I used the CDC growth charts for 5 year olds and created a fake elementary school.

## Slide 8: Example
Class | Max Height (in)
1 | 47.5
2 | 46.2
3 | 46.6
4 | 45.7
5 | 45.9
6 | 46.2
Kindergartners

## Slide 9: Time Series Block Maxima
Selected block size is a unit of time
Blocks should be homogeneous
  Make sure the largest value in each block means the same thing
  If your process repeats with a regular cycle length, use that as the block size

## Slide 10: Annual Maximum Series

## Slide 11: Annual Maximum Series
Block maxima where the groups are years
  Water year
  Calendar year
Collect up the maxima and analyze them
1 observation per year

## Slide 13: Water Year
Split the year during the driest part
Make sure one flood event doesn’t create maximum in two years
October 1st is the traditional break point
Check your flow record!
Calendar Year
1947
Water Year
1947

## Slide 14: Year-Over-Year Plot

## Slide 15: Water Year
01Dec

## Slide 16: Limitations
Non-maximum events in a year can be larger than annual maxima
Some small annual maximum events will not be floods
Partial Duration Series is an alternative to Annual Maximum Series that addresses these limitations to some extent

## Slide 17: Questions?