## Slide 1
RasUnsteady64 for Linux and test case
2 April 2019

## Slide 2
HEC-RAS Muncie 1D/2D test case
Muncie.p04.tmp.hdf needed for run
rasUnsteady64 Linux executable and supporting libraries
Contents of RAS_507_linux.zip
The RAS_507_linux.zip contains the rasUnsteady64 Linux executable, supporting libraries and an example HEC-RAS test case.

## Slide 3
rasUnsteady64 Linux executable
Contents of /bin_ras
Intel Fortran supporting Libraries
Will need gfortran library if not installed. (Rename extension)

## Slide 4
Script for running test case
Contents of /Muncie_Linux
- Runs the standard HEC-RAS Muncie test case
Unsteady input text file
Binary geom file from Geometry Preprocessor
Input geometry HDF file
Input geometry text file
Required files, generated by HEC-RAS Windows GUI
Trimmed plan HDF file for run input
Result Files generated by Linux Compute
Plan HDF file with 2D results
DSS output file

## Slide 5
Files needed from HEC-RAS GUI run
Geometry based files
Muncie.c04
Muncie.x04
The HEC-RAS GUI will need to be run to provide a base set of the input files for the Linux compute. Text based files will need to have the ending carriage return character stripped to be Linux compatible (.x04 and b04).
Muncie.g04.hdf
Muncie.b04
Muncie.p04.tmp.hdf
Unsteady BCs for 1D part of grid
Unsteady BCs applied to 2D part of grid

## Slide 6
Input Plan HDF file (e.g. Muncie.p04.tmp.hdf)
The Muncie.p04.tmp.hdf is derived from an HEC-RAS GUI compute that produces the file Muncie.p04.hdf. The computed file includes bcs, plan and geometry data, and the results. The RasUnsteady64 compute requires a file named Muncie.p04.tmp.hdf for input. The Muncie.p04.hdf cannot simply be renamed to
Muncie p04.tmp.hdf
Results group must be deleted from the file

## Slide 7
Input Plan HDF file (e.g. Muncie.p04.tmp.hdf)
Below is a python script which copies all data groups but “Results” from the Muncie.p04.hdf into Muncie.p04.tmp.hdf

## Slide 8
Muncie test case
The script, run_test_1.sh, runs the rasUnsteady64 for the Muncie example. At the end of the compute, the Muncie.p04.tmp.hdf is renamed to Muncie.p04.hdf
Before running the test, remove the existing Muncie.p04.hdf from the directory. Also be sure there is the suitable Muncie.p04.tmp.hdf file. A copy of the file can be obtained from the Muncie_Linux/plan_hdf_tmp directory.

## Slide 9
Muncie test case, *.b04 file
The Muncie.b04 file contains the 1D boundary conditions and most the run parameters for the unsteady compute.
Of note in the provided example is line 45, the DSS output file path. The line generated from the HEC-RAS GUI has a typical Windows OS pathname:
This will need to be modified to the right path on the Linux environment. For the test case provided, the path was shortened to Muncie.dss to output in the test directory.